## Slide 1
C&S input to SLP for Proximity-1 extension (AI_23_04) - SLS-CS_23-08
C&S Working Group
CCSDS 2023 Fall technical meetings

## Slide 2: Introduction
As part of AI_23_04, the WGs, including C&S, had the AI to
a) provide comments to SLP about the Proximity-1 directives, and
b) provide a list of MODCODs to SLP
This input, coordinated at C&S level, is the formal response to AI_23_04, and input to the SLP WG in view of Fall 2023 meetings
The following (working) documents were provided for review

## Slide 3: Part a) provide comments to SLP about the Proximity-1 directives
For point a), C&S had comments about “Annex A - Session Access Control Parameters for Space Enterprises” that are provided in attachment for SLP review
Among these, the following open points (for possible discussion in Fall 2023) were identified:
  To review latest SFCG PROV REC 42-1, for then aligning rates, hailing, etc. of the Proximity-1 extension for the lunar environment (see attachment)
  To discuss about the possibility to assign dynamically the rates (see comment about coded symbol rate, in “A2.2 - Lunar Working channel Parameters” in the Word file above)

## Slide 4: Part b) provide a list of MODCODs
For point b), C&S identified the following combinations
  Bi-phase-L
    LDPC ½ (011)
    LDPC 2/3 (022)
    LDPC 7/8 (044)
    Uncoded (055)
  GMSK
    LDPC ½ (111)
    LDPC 2/3 (122)
    LDPC 7/8 (144)
    Uncoded (155)

## Slide 5: Part b) provide a list of MODCODs (cont’d)
For the MODCOD numbering, C&S proposes (as nice to have) the numbering in cyan in previous slide. The rationale is the following:
  To have empty spaces between MODCOD identifiers in case additional MODCODs (with slight variations) will be added later (e.g., manufacturers doing a tailored version of the standard)
  To follow a human intelligible logic (not to be standardized, just for explanation)
      1st digit: 0=bi-phase-L, 1=GMSK
      2nd digit: 0: reserved, 1=1/2, 2=2/3, 3=4/5 (not foreseen currently), 4=7/8, 5=uncoded
      3rd digit: 0: reserved, 1=1024, 2=4096, 3=16384, 4=7136, 5=n/a
Final MODCOD numbering can be agreed at Fall 2023 meeting