## Slide 1: A NEW LINK BUDGET PROCESSING METHOD
CNES
Hervé GUILLON, Marie VIALARD, Claire DURAND, Franck ROUSSEAU, Clément DUDAL
CCSDS Spring 2024

## Slide 2: SUMMARY
LINK BUDGET GENERAL PRESENTATION
CCSDS/ECSS STANDARDIZED METHOD
NEW METHOD BASED ON RANDOM DRAWS
PRESENTION OF CNES LINK BUDGET TOOLS
A NEW LINK BUDGET PROCESSING METHOD – CCSDS spring 2024

## Slide 3: LINK BUDGET
A NEW LINK BUDGET PROCESSING METHOD – CCSDS spring 2024
A Key problem for RF link design, but the generic processing is well known:
  Estimation of transmitted power
  Estimation of losses between the transmitter and the receiver
  Estimation of the received power
  Estimation of the noise level at receiver level
  Several calculations can be performed to estimate :
    received power,
    C/N0, Eb/N0, signal to noise ratio at various point in the reception chain processing,
    power flux level,
    etc…
    ex:
    working with dB leads to a generic formulation:
« + » for gain, « - » for loss

## Slide 4: AVAILABILITY
A NEW LINK BUDGET PROCESSING METHOD – CCSDS spring 2024
Mission safety analysis takes the RF link into account
  RF link is considered as a specific contributor in the availability estimation
  A single link budget does not consider that availability aspect
CCSDS/ECSS link budget processing method
  provides a way to estimate link budget at N-sigma
    Downlink: 2 σ for CCSDS, 3 σ for ECSS  depend on the safety hypothesis
    Uplink: 3 σ for CCSDS and ECSS
    ECSS provide a way to estimate worst case RSS link budget
  Each contributor is defined thanks to:
    its Design value Dk
    its Adverse value (Dk+Ak)
    its Favorable value (Dk+Fk)
    its distribution law (Triangular, Gaussian or Uniform)
calculation of mean (µk) and variance (σk2) values

## Slide 5: CCSDS/ECSS method limits
A NEW LINK BUDGET PROCESSING METHOD – CCSDS spring 2024
Several drawbacks of the method have been identified:
  Independence of the contributors in CCSDS/ECSS method
    actually, antenna gain and axial ratio are correlated
  Gaussian consideration (correspondance availability ↔ number of sigmas)
    does not work if a contributor has a range largely higher than the other contributors
    it is the case in survival mode (when satellite attitude is not controlled)
    the global behavior is not Gaussian
  Discrepancy between the modeled distribution and the actual one
    example: antenna gain (Triangular for CCSDS/ECSS)
  Hidden hypothesis about polarisation loss computation:
    The ground station is able to receive both LHCP and RHCP polarizations
    Method not adapted to single receiving chain ground stations
    => Details page 4 of the article

## Slide 6: NEW METHOD
A NEW LINK BUDGET PROCESSING METHOD – CCSDS spring 2024
Method based on random draws:
  Random draws using:
    the recommended distribution law if the actual one in not known (triangular, uniform, gaussian)
    the actual distribution law if this one is known (on-board antenna gain and axial ratio thanks to antenna description files)
    Since version 1.4 of this tool (version 1.3 and before it was CNES DLL propagation library) : uses of the CNES Matlab ITU model (june 2023) to compute atmospheric loss, either using a single value or the modeled distribution law of atmospheric loss
    use of a new distribution law: PLCKMOD (for antenna gain and axial ratio if no data are available)
  Sense of circular polarization can be considered (for single receiving/transmitting chain ground stations)
  Q independent link budgets (Q = 106 in our analysis)
  for an availability of p, estimation of the value respected with this probability
    ex: for 99.865% availability (equivalent of 3 σ), the value is the one respected in 99.865% of the calculated cases.
  Possibility to estimate the availability of the link

## Slide 7: PLCKMOD DISTRIBUTION LAW
A NEW LINK BUDGET PROCESSING METHOD – CCSDS spring 2024
Useful for Antenna Gain and Axial Ratio:
  Used with random draws
  Inspired by the black body radiation law
  Can be defined with Design/Favorable/Adverse values
  Generally speaking: Very good fit with actual antenna gain distribution
  Useful for analysis if the antenna description file is not available
parameter of the distribution
normalisation term

## Slide 8: CALCULATION TOOLS
A NEW LINK BUDGET PROCESSING METHOD - CCSDS spring 2024
Tools developed:
  Under Matlab environnement
    tool for downlink (TM, HDRTM)
    tool for uplink (TC)
    tool for Inter Satellite Link (ISL)
    tool for DVB-S2 still under development
  CCSDS/ECSS method calculation
  Random draws calculation
  Possibility to compare results
  First use: X-Band link for MICROCARB satellite with Kourou Ground Station, availability estimation
  Tools available in standalone version using Matlab runtime

## Slide 9: PERFORMANCES OF THE TOOL
A NEW LINK BUDGET PROCESSING METHOD – CCSDS spring 2024
Cross validation of processing:
  Using the previous budget link tool used in CNES (BeLeTTe) on previous CNES missions
  Comparision of results using CCSDS/ECSS recommended distribution for random draws (with limited range)
  Comparision of independent and parallel analyses using previous and new methods
Error statistics of the tool:
  better than 0.1 dB on the 3 σ link budget calculation
  better than 2·10-4 (TM/TC case) and 5·10-4 (ISL case) for availability estimation
  better than 0.1° for the elevation threshold where the targeted link budget is complied with (for TM/TC)
Notes: Précision au niveau de la restitution des résutats environ 300 simulations identiques comparées entre elles

## Slide 10: RESULTS OF THE TOOL (1/2)
A NEW LINK BUDGET PROCESSING METHOD – CCSDS spring 2024
Nadir pointed satellite (Microcarb – S-Band TM link)
  Results are comparable using CCSDS/ECSS method and random draws method
  Results differences ± 2 dB

## Slide 11: RESULTS OF THE TOOL (2/2)
A NEW LINK BUDGET PROCESSING METHOD – CCSDS spring 2024
Satellite in survival mode (Microcarb – S-Band TM link)
  Huge difference between random draws results and CCSDS/ECSS method: 6 to 8 dB
  main contributor of the difference: on-board antenna gain
  difference could be even higher for cubesat:
    up to 30 dB for Eyesat 3U cubesat
  for ISL where both spacecrafts can be considered « in survival mode », the difference could reach 60 to 90 dB using CCSDS/ECSS method

## Slide 12: CONCLUSION
A NEW LINK BUDGET PROCESSING METHOD – CCSDS spring 2024
A new method for link budget processing is proposed:
  More accurate modelization of physical phenomenon (Antenna Gain, polarization loss, propagation loss)
  Possibility to estimate the availability of the RF link
  Possibility to rationalize the margin and reduced the on-board power
  Tools available for TM, TC and ISL RF links (on www.connectbycnes.fr).

## Slide 13
A NEW LINK BUDGET PROCESSING METHOD – CCSDS spring 2024
Questions ?