Draft Recommendation for
Space Data System Standards

Optical Communications Physical Layer

Draft Recommended Standard

CCSDS 141.0-R-1revised-d
(Incorporating RID responses)

Red Book

April 09, 2019

AUTHORITY

|  | Issue: | Red Book, Issue 1revised |  |
| --- | --- | --- | --- |
|  | Date: | April 2018 |  |
|  | Location: | Not Applicable |  |

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF AUTHORITY:)

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and represents the consensus technical agreement of the participating CCSDS Member Agencies.  The procedure for review and authorization of CCSDS documents is detailed in Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-4), and the record of Agency participation in the authorization of this document can be obtained from the CCSDS Secretariat at the e-mail address below.

This document is published and maintained by:

CCSDS Secretariat

National Aeronautics and Space Administration

Washington, DC, USA

E-mail: secretariat@mailman.ccsds.org

STATEMENT OF INTENT

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF INTENT:)

The Consultative Committee for Space Data Systems (CCSDS) is an organization officially established by the management of its members. The Committee meets periodically to address data systems problems that are common to all participants, and to formulate sound technical solutions to these problems. Inasmuch as participation in the CCSDS is completely voluntary, the results of Committee actions are termed Recommended Standards and are not considered binding on any Agency.

This Recommended Standard is issued by, and represents the consensus of, the CCSDS members.  Endorsement of this Recommendation is entirely voluntary. Endorsement, however, indicates the following understandings:

o	Whenever a member establishes a CCSDS-related standard, this standard will be in accord with the relevant Recommended Standard. Establishing such a standard does not preclude other provisions which a member may develop.

o	Whenever a member establishes a CCSDS-related standard, that member will provide other CCSDS members with the following information:

--	The standard itself.

--	The anticipated date of initial operational capability.

--	The anticipated duration of operational service.

o	Specific service arrangements shall be made via memoranda of agreement. Neither this Recommended Standard nor any ensuing standard is a substitute for a memorandum of agreement.

No later than five years from its date of issuance, this Recommended Standard will be reviewed by the CCSDS to determine whether it should: (1) remain in effect without change; (2) be changed to reflect the impact of new technologies, new requirements, or new directions; or (3) be retired or canceled.

In those instances when a new version of a Recommended Standard is issued, existing CCSDS-related member standards and implementations are not negated or deemed to be non-CCSDS compatible.  It is the responsibility of each member to determine when such standards or implementations are to be modified.  Each member is, however, strongly encouraged to direct planning for its new standards and implementations towards the later version of the Recommended Standard.

FOREWORD

This document is a CCSDS Recommended Standard for the Physical Layer of signals to be used in free-space optical communications systems of space missions.  It was contributed to CCSDS by NASA.  The Physical Layer concepts described herein are intended for missions that are cross supported between Agencies of the CCSDS.

Through the process of normal evolution, it is expected that expansion, deletion, or modification of this document may occur.  This Recommended Standard is therefore subject to CCSDS document management and change control procedures, which are defined in the Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-4).  Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be sent to the CCSDS Secretariat at the e-mail address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- China National Space Administration (CNSA)/People’s Republic of China.

- Deutsches Zentrum für Luft- und Raumfahrt (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (FSA)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

- UK Space Agency/United Kingdom.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- China Satellite Launch and Tracking Control General, Beijing Institute of Tracking and Telecommunications Technology (CLTC/BITTT)/China.

- Chinese Academy of Sciences (CAS)/China.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- Danish National Space Center (DNSC)/Denmark.

- Departamento de Ciência e Tecnologia Aeroespacial (DCTA)/Brazil.

- Electronics and Telecommunications Research Institute (ETRI)/Korea.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Geo-Informatics and Space Technology Development Agency (GISTDA)/Thailand.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- Korea Aerospace Research Institute (KARI)/Korea.

- Ministry of Communications (MOC)/Israel.

- Mohammed Bin Rashid Space Centre (MBRSC)/United Arab Emirates.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic and Atmospheric Administration (NOAA)/USA.

- National Space Agency of the Republic of Kazakhstan (NSARK)/Kazakhstan.

- National Space Organization (NSPO)/Chinese Taipei.

- Naval Center for Space Technology (NCST)/USA.

- Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Scientific and Technological Research Council of Turkey (TUBITAK)/Turkey.

- South African National Space Agency (SANSA)/Republic of South Africa.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- Swiss Space Office (SSO)/Switzerland.

- United States Geological Survey (USGS)/USA.

PREFACE

This document is a draft CCSDS Recommended Standard.  Its ‘Red Book’ status indicates that the CCSDS believes the document to be technically mature and has released it for formal review by appropriate technical organizations.  As such, its technical contents are not stable, and several iterations of it may occur in response to comments received during the review process.

Implementers are cautioned not to fabricate any final equipment in accordance with this document’s technical content.

Recipients of this draft are invited to submit, with their comments, notification of any relevant patent rights of which they are aware and to provide supporting documentation.

# DOCUMENT CONTROL

| Document | Title | Date | Status |
| --- | --- | --- | --- |
| CCSDS 141.0-R-1 | Optical Communications Physical Layer, Draft Recommended Standard, Issue 1 | November 2017 | Superseded |
| EC1 CCSDS 141.0-R-1revised | Editorial update Optical Communications Physical Layer, Draft Recommended Standard, Issue 1revised | November 2017 April 2018 | Corrects a reference problem Current draft. Includes responses to RIDs from Red Book review, according to OPT WG consensus. |

# CONTENTS

Section	Page

1	Introduction	1-1

1.1	Purpose	1-1

1.2	Scope	1-1

1.3	Applicability	1-1

1.4	Rationale	1-2

1.5	Document Structure	1-2

1.6	Nomenclature	1-2

1.7	Conventions	1-3

1.8	References	1-4

2	Overview	2-1

2.1	architecture	2-1

2.2	Summary of functions	2-1

3	HPE Telemetry Signal Characteristics	3-1

3.1	Center frequency	3-1

3.2	Center frequency Tolerance	3-1

3.3	Laser linewidth	3-1

3.4	In-band and spillover emissions	3-1

3.5	Polarization	3-1

3.6	Modulation	3-2

3.7	Timing jitter	3-3

3.8	Slot Width	3-3

3.9	Pulse Repetition Rates	3-3

4	HPE Beacon and optional telecommand  Signal Characteristics	4-1

4.1	Center frequency	4-1

4.2	Center frequency Tolerance	4-1

4.3	Laser linewidth	4-1

4.4	In-band and spillover emissions	4-1

4.5	Modulation	4-1

4.6	Timing jitter	4-2

5	MANAGED PARAMETERS	5-1

# CONTENTS (continued)

Section	Page

ANNEX A	Protocol Implementation CONFORMANCE 
Statement (PICS) Proforma  (Normative)	A-1

ANNEX B	SECURITY, SANA, and Patent CONSIDERATIONS  (Informative)	B-1

ANNEX C	Abbreviations  (INFORMATIVE)	C-1

ANNEX D	INFORMATIVE REFERENCES	D-1

Figure

1-1	Bit Numbering Convention	1-3

2-1	Relationship with OSI Layers	2-1

3-1	Reference Pulse Shape for ƒ = 1 GHz	3-2

Table

5-1	Managed Parameters for HPE	5-1

# Introduction

## Purpose

The purpose of this Recommended Standard is to specify the Physical Layer characteristics of free-space optical communications systems used by space missions.  The primary application addressed in this issue of the Recommended Standard is space-to-ground and ground-to-space photon starved links through an atmospheric channel; use of the Recommended Standard for other applications or operating conditions is not precluded.  When provided with a sequence of pulsed and non-pulsed slots produced by the Coding and Synchronization sublayer (see reference [1]), this specification describes the required Physical Layer characteristics of the telemetry, beacon, and telecommand transmissions.

## Scope

This Recommended Standard defines Physical Layer schemes in terms of the signal characteristics and procedures involved in the physical transmission of the optical signals.  It does not specify:

- individual implementations or products;

- the methods or technologies required to perform the procedures; or

- the management activities required to configure and control the system.

Issue 1 of this Recommended Standard provides a specification for High Photon Efficiency (HPE) optical communications, in which the photon-efficiency of the link is of primary concern.  Details of the design and implementation of HPE systems can be found in references [D7], [D8], and [D9].

## Applicability

This Recommended Standard applies to the creation of Agency standards and to the future data communications over optical space links between CCSDS Agencies in cross-support situations.  It includes comprehensive specifications of the data formats and procedures for inter-Agency cross support.  It is neither a specification of, nor a design for, real systems that may be implemented for existing or future missions.

The Recommended Standard specified in this document is to be invoked through the normal standards program of each CCSDS Agency and is applicable to those missions for which cross support based on capabilities described in this Recommended Standard is anticipated.  Where mandatory capabilities are clearly indicated in sections of this Recommended Standard, they must be implemented when this document is used as a basis for cross support.  Where options are allowed or implied, implementation of these options is subject to specific bilateral cross support agreements between the Agencies involved.

## Rationale

The rationale for producing this Recommended Standard is that it facilitates cross support at the physical layer of optical communications systems used by CCSDS member agencies.  Such cross support requires specification of set of allowable center frequencies of transmission, along with other physical layer characteristics of the signal.

The CCSDS believes it is important to document the rationale underlying the recommendations chosen, so that future evaluations of proposed changes or improvements will not lose sight of previous decisions. The rationale for the specifications making up this Recommended Standard is expected to be documented in a forthcoming CCSDS Informational Report.

## Document Structure

This document is divided into five numbered sections and four annexes.

- section 1 presents the purpose, scope, applicability, rationale, document structure, definitions and references;

- section 2 provides an overview of the architecture and summary of functions of the Physical Layer;

- section 3 specifies HPE telemetry signal characteristics;

- section 4 specifies HPE beacon and optional telecommand signal characteristics;

- section 5 lists the managed parameters;

- annex A is a Protocol Implementation Conformance Statement (PICS) Proforma;

- annex B discusses security issues;

- annex C lists acronyms used within this document;

- annex D provides a list of informative references.

## Nomenclature

### Normative text

The following conventions apply throughout this Specification:

- the words ‘shall’ and ‘must’ imply a binding and verifiable specification;

- the word ‘should’ implies an optional, but desirable, specification;

- the word ‘may’ implies an optional specification;

- the words ‘is’, ‘are’, and ‘will’ imply statements of fact.

### Informative text

In the normative sections of this document, informative text is set off from the normative specifications either in notes or under one of the following subsection headings:

- Overview;

- Background;

- Rationale;

- Discussion.

## Conventions

In this document, the following convention is used to identify each bit in an N-bit field.  The first bit in the field to be transmitted (i.e., the most left justified when drawing a figure) is defined to be ‘Bit 0’,  the following bit is defined to be ‘Bit 1’, and so on up to ‘Bit N-1’.  When the field is used to express a binary value (such as a counter), the Most Significant Bit (MSB) shall be the first transmitted bit of the field, i.e., ‘Bit 0’ (see figure 1-1).

Figure 1-1:  Bit Numbering Convention

In accordance with standard data-communications practice, data fields are often grouped into 8-bit ‘words’ which conform to the above convention. Throughout this specification, such an 8-bit word is called an ‘octet’. The numbering for octets within a data structure starts with ‘0’.

NOTE	–	Throughout this document, ‘bit’ refers to the contents of the transfer frames.  A bit is a binary digit transferred between the Data Link Protocol sublayer and the Coding and Synchronization sublayer.  Other symbols, whether binary or nonbinary, will be referred to by other names, such as ‘binary digits’. It should be understood that the ordering conventions described above apply equally to other types of symbols.

## References

The following publications contain provisions which, through reference in this text, constitute provisions of this document.  At the time of publication, the editions indicated were valid.  All publications are subject to revision, and users of this document are encouraged to investigate the possibility of applying the most recent editions of the publications indicated below.  The CCSDS Secretariat maintains a register of currently valid CCSDS publications.

[1]	Optical Communications Coding and Synchronization. Proposed Draft Recommendation for Space Data System Standards (Proposed Red Book), CCSDS 142.0-R. Forthcoming.

[2]	IEEE Standard for Definitions of Terms for Antennas. Revision of IEEE Std 145-1993. IEEE Std 145-2013. New York: IEEE, 2014.

# Overview

## architecture

Figure 2-1 illustrates the relationship of this Recommended Standard to the Open Systems Interconnection reference model (reference [D1]). Two sublayers of the Data Link Layer are defined for CCSDS space link protocols. The Data Link Protocol sublayer provides functions for producing Transfer Frames; possible Space Data Link Protocols using optical communications are the TM Space Data Link Protocol, (reference [D2]) and the AOS Space Data Link Protocol (reference [D3]). The Optical Coding and Synchronization protocol (reference [1]) provides the functions of the Coding and Synchronization sublayer of the Data Link Layer for transferring Transfer Frames over an optical space link.  The Optical Communications Physical Layer specified in this Recommended Standard provides the required characteristics of the Physical Layer transmission from space to ground and from ground to space.

Figure 2-1:  Relationship with OSI Layers

## Summary of functions

The Optical Communications Physical Layer specifies the physical characteristics of the telemetry signal and, separately, the physical characteristics of the beacon and optional telecommand signal.  In a typical application, a spacecraft transmits telemetry to a ground station, and a ground station transmits a beacon and optional telecommands to the spacecraft.

For each of the telemetry and beacon/telecommand specifications, this Recommended Standard defines the transmission laser’s required center frequency, tuning range, linewidth, in-band and spillover emissions, polarization, modulation, pulse shape, timing jitter, and supported slot widths.

The overall architecture of the optical communications system is shown in Figure 2-2.  Throughout the communications session, the optical Terminal A transmits a beacon, together with optional AOS transfer frames.  The Terminal B  receiver locks onto the beacon and uses it to assist in accurately pointing its optical transmitter.  Any AOS transfer frames are also decoded onboard.  Telemetry is transmitted from terminal B and received by Terminal A.  This recommendation specifies the physical characteristics of the Terminal A and Terminal B transmitters.  In a typical application, Terminal A on the ground transmits an uplink beacon and optional AOS transfer frames to Terminal B in space, and Terminal B transmits a downlink telemetry signal to Terminal A.

Figure 2-2: Overall architecture of the optical communications system.

# HPE Telemetry Signal Characteristics

At the sending end, a binary vector is received from the Coding and Synchronization sublayer, as defined in [1], indicating a sequence of slots in which light pulses are to be present (1) or absent (0).  The physical characteristics of these pulses at the sending end are described below.  At the receiving end, the physical layer delivers slot measurements to the Coding and Synchronization layer.

## Center frequency

The center frequency shall be 193.1 + n×0.1 THz, where n is an integer ranging from -18 to 28.

NOTE	–	These center frequencies in the optical C-band are a subset of those defined in the ITU-T G.694.1 frequency grid with 100 GHz channel spacing (reference [D6]).  The frequencies range from 191.3 THz to 195.9 THz and correspond to wavelengths in vacuum ranging from 1530.33 nm to 1567.13 nm.

## Center frequency Tolerance

The transmitter center frequency shall be accurate to within a tolerance of ( 10 GHz.

## Laser linewidth

The modulated laser linewidth shall be less than 6.25 GHz, measured at full width, 1/e2 of maximum, over a time scale of 100 ms.

## In-band and spillover emissions

The laser shall transmit 95 percent of its energy within ( 10 GHz of its center frequency.

## Polarization

### Polarization type

Polarized laser emission is optional.  When polarized, the laser emission exiting the terminal aperture shall be Right-Hand Circularly Polarized (RHCP) as defined in reference [2].

### Polarization extinction ratio

When polarized emission is used, the polarization extinction ratio shall be greater than 10 dB.

## Modulation

The binary vector received from the Coding and Synchronization sublayer defined in [1] shall be used to modulate the intensity of emitted light within each slot, using On-Off Keying (OOK).

NOTE – A modulation of Pulse Position Modulation (PPM) at the Coding and Synchronization sublayer gives rise to OOK at the Physical Layer, in the sense that a light pulse is present or absent in each slot.

## Timing jitter

The Root Mean Square (RMS) pulse timing jitter shall be less than 10 percent of the slot width.

## Slot Width

The slot width T shall be 0.125, 0.25, 0.5, 1, 2, 4, 8, 16, 32, 64, 128, 256, or 512 ns.

## Pulse Repetition Rates

The laser shall support a range of Pulse Repetition Rates (PRRs) corresponding to the slot width(s) and PPM order(s) used by the communications link.

NOTE	–	For example, in a system using 1 ns slots with 16-PPM and 4 slots of guard time, pulses could be as close as 5 ns and as far apart as 35 ns, center to center, corresponding to a PRR range of 28.57 to 200 MHz.

# HPE Beacon and optional telecommand  Signal Characteristics

At the sending end, a binary vector is received from the Coding and Synchronization sublayer, as defined in [1], indicating a sequence of slots in which light pulses are to be present (1) or absent (0).  The physical characteristics of these pulses at the sending end are described below.  At the receiving end, the physical layer delivers slot measurements to the Coding and Synchronization layer.

## Center frequency

The center frequency shall be tunable to any frequency within ±26 GHz of 280.18 THz, 281.72 THz, or 291.06 THz.

NOTE	–	These center frequencies correspond to wavelengths in vacuum of 1070 nm, 1064.15 nm, and 1030 nm, respectively.

## Center frequency Tolerance

The transmitter center frequency shall be accurate to within a tolerance of ±26.5 GHz.

## Laser linewidth

The laser linewidth shall not exceed 53 GHz, measured at full width, 1/e2 of maximum, over a time scale of 100 ms.

## In-band and spillover emissions

The laser shall transmit 95 percent of its energy within ±50 GHz of its center frequency.

## Modulation

### Overview

Telecommand (data) transmission is optional.

### When Data Transmission Is Not Used

When data transmission is not used, the beacon transmission shall be a 3.8145 KHz square wave.  The period of the square wave is 262,144 ns, i.e., an alternating sequence of pulsed and non-pulsed slots of duration 131,072 ns.

### When Data Transmission Is Used

When data transmission is used, the binary vector received from the Coding and Synchronization sublayer defined in [1] shall be used to modulate the intensity of emitted light within each slot, using OOK.

NOTES

- A modulation of PPM at the Coding and Synchronization sublayer gives rise to OOK at the Physical Layer, in the sense that a light pulse is present or absent in each slot.

- The transmission is not required to be polarized

#### Slot widths

The slot width shall be 65,536 ns.

NOTE – This Recommended Standard can be compatible with systems using substantially narrower pulse shapes that convey additional, higher-rate telecommand data than is specified in this Recommended Standard.  Such ‘nested outer modulations’ are not specified by this Recommended Standard, nor are they necessarily precluded by this Recommended Standard.

## Timing jitter

The RMS pulse timing jitter shall be less than 10 percent of the slot width.

# O3K Telemetry signal characterstics

Chapter 5 and 6 are intended to enable vendors and operators to provide compatible laser communication equipment and services for optical on-off keying (O3K) systems, mainly but not limited to high-speed optical direct-to-earth (DTE) telemetry data downlinks. After the Coding and Synchronization layer, a binary vector is created which is to be modulated by absence (0) or presence (1) of pulse in the slot by the transmitter at physical layer. The physical characteristics of these pulses at end of transmitter are described below. At the receiver, physical layer demodulates the data and delivers the information to the Coding and Synchronization layer.

## Center Frequencies

The center frequency shall be 193.1 + n×0.1 THz, where n is an integer ranging from -18 to 28 for choosing one of 47 optional bands for communications downlink.

NOTE	–	The frequencies range from 191.3 THz to 195.9 THz and correspond to wavelengths in vacuum ranging from 1530.33 nm to 1567.13 nm

## Center Frequency Tolerance

The center wavelength’s tolerance shall be maximum (10GHz.

## Laser Line-Width

Maximum of laser line-width FWHM of the (10GHz measured over a time scale of 100 ms

## In-Band and spillover emissions

The laser shall transmit 95 percent of its energy within ( 20 GHz of its center frequency

## Modulation

### Modulation Scheme

Non-return-to-zero On-Off Keying (OOK-NRZ) with equal lengths of ones and zeros slots shall be used as a modulation scheme for telemetry.

### Pulse Shape/Eye Diagram

The base-band eye-pattern shall fulfill the requirement listed below: [D10].

Figure 5-1. Transmit Eye-pattern

For NRZ the Pulse width (T)=1/datarate. x1 = 0.1T, x2=0.15T, x3 = 0.85T, x4=0.9T, y1=0.10(mean level of logical 1) and y2=0.90(mean level of logical 1).

### Accuracy and Stability of pulse shape (e.g. jitter)

The stability of the pulse shape shall be within+-1% of the slot width

### Extinction Ratio

The extinction ratio shall be > 10dB ON/OFF ratio

## Channel Data Rates

The channel rate r shall be based on fractions of 10Gsym/s with

## Slot Width

The slot width T shall be 0.1, 0.2, 0.4, 0.8, 1.6, 3.2, 6.4, 12.8, 25.6, 51.2, 102.4, 204.8, 409.6 or 819.2 ns..

# O3K Beacon signal characterstics

After the Coding and Synchronization layer, a binary vector is created which is to be modulated by absence (0) or presence (1) of pulse in the slot by the transmitter at physical layer. The physical characteristics of these pulses at end of transmitter are described below. At the receiver, physical layer demodulates the data and delivers the information to the Coding and Synchronization layer.

## Center Frequencies

Basic uplink frequency a) shall be between 188.54075 THz (1590.07nm) to 188.65925 THz (1589.07nm)

Alternative Uplink b) shall be one frequency between 195.000THz (1537nm) to 195.900THz (1530 nm).

Alternative Uplink c) shall be one frequency between 281.543 THz (1064.5 nm) to 281.807 THz (1063.5 nm)

## Center frequency tolerance

The center frequency shall be accurate within a tolerance of (25GHz for beacon uplink for basic uplink frequency a), and alternative b), and (132.3GHz for alternative uplink frequency c).

## Laser Line Width

Maximum of laser line-width FWHM of the beacon uplink for basic uplink frequency a), and alternative b) shall be (0.2 nm ((25GHz), and for alternative uplink frequency c) shall be ( 0.25nm ((66GHz), measured over a time scale of 100 ms.

## In-band and spillover emissions

The laser shall transmit 95 percent of its energy within ( 50 GHz of its center frequency.

## Modulation

Terminal-A shall transmit its beacon signal either unmodulated (CW) or with either rectangular or sinusoidal pulses with a major spectral component at one predefined frequency.

### Pulse Repetition Rate

The beacon signal shall be either unmodulated (CW) or the modulating frequency shall be in the interval of [0, 20] kHz

### Accuracy and Stability (e.g. jitter)

The stability of the pulse shape shall be within+/-0.1% of the slot width.

### Extinction Ratio

The extinction ratio shall be >10dB max-min ratio.

# MANAGED PARAMETERS

The managed parameters for HPE signaling shall be those specified in table 5-1.

Table 7-1:  Managed Parameters for HPE

| Managed Parameter | Allowed Values |
| --- | --- |
| n, the telemetry signaling center frequency selection parameter | 0 to 43 |
| Telemetry signaling slot width | 0.125, 0.25, 0.5, 1, 2, 4, 8, 16, 32, 64, 128, 256, or 512 ns |
| Telemetry signaling polarized transmission | Used or Not Used |
| Beacon frequency | 280.18, 281.72, or 291.06 THz |
| Telecommand transmission | Used or Not Used |

Table 7-2:	Managed Parameters for O3K

| Managed Parameter | Allowed Values |
| --- | --- |
| n, the telemetry signaling center frequency selection parameter | -18 to 28 |
| k, channel symbol rate ratio factor | 0 to 13 |
| Telemetry signaling slot width | 0.1, 0.2, 0.4, 0.8, 1.6, 3.2, 6.4, 12.8, 25.6, 51.2, 102.4, 204.8, 409.6, 819.2. ns |
| Beacon frequency options | a) 188.54075THz to 188.65925THz b) 195.000THz to 195.900THz c) 281.543 THz to 281.807 THz |
| Beacon pulse rate | CW .. 20KHz |

Protocol Implementation CONFORMANCE Statement (PICS) Proforma

(Normative)

[To be supplied.]

SECURITY, SANA, and Patent CONSIDERATIONS

(Informative)

Security Considerations

SECURITY BACKGROUND

It is assumed that security is provided by encryption, authentication methods, and access control to be performed at a layer above the physical layer and coding and synchronization sublayer. Mission and service providers are expected to select from recommended security methods, suitable to the specific application profile. Specification of these security methods and other security provisions is outside the scope of this Recommended Standard. The Physical Layer has the objective of delivering data with the minimum possible amount of residual errors. The associated channel coding as described in reference [1] must be used to insure that residual errors are detected and the frame flagged. There is an extremely low probability of additional undetected errors that may escape this scrutiny. These errors may affect the encryption process in unpredictable ways, possibly affecting the decryption stage and producing data loss, but will not compromise the security of the data.

SECURITY CONCERNS

Security concerns in the areas of data privacy, authentication, access control, availability of resources, and auditing are to be addressed in higher layers and are not related to this Recommended Standard.

CONSEQUENCES OF NOT APPLYING SECURITY

There are no specific security measures prescribed for the Physical Layer. Therefore consequences of not applying security are only imputable to the lack of proper security measures in other layers. Residual undetected errors may produce additional data loss when the link carries encrypted data.

Sana Considerations

The recommendations of this document do not require any action from SANA.

Patent Considerations

No patents are known to relate to this Recommended Standard.

Abbreviations and Terms

(INFORMATIVE)

Introduction

This annex lists key abbreviations and terms that are used throughout this Recommended Standard.

Abbreviations

AOS		Advanced Orbiting Systems

HPE		high photon efficiency

ITU		International Telecommunication Union

MSB		most significant bit

OOK		on-off keying

OSI		Open Systems Interconnection

PPM 		pulse position modulation

PRR		pulse repetition rate

RHCP		right-hand circularly polarized

RMS		root mean square

RZ50		50-percent return-to-zero

TM		telemetry

Terms

center frequency: The central frequency of a laser beam occupying a range of frequencies.

laser linewidth: The spectral linewidth of a laser beam.

optical pulse: An emission of photons, often constrained with respect to its amplitude, shape, and duration.

polarization extinction ratio: The ratio of optical powers of perpendicular polarization.

pulse repetition rate: The number of emitted pulses per second, or the inverse temporal pulse spacing.

right-hand circular polarization: A circularly polarized wave in which the electric field vector rotates in a right-hand sense with respect to the direction of propagation.

spillover emissions: The energy of an emission that is outside of a defined spectral band.

INFORMATIVE REFERENCES

[D1]	Information Technology—Open Systems Interconnection—Basic Reference Model: The Basic Model. 2nd ed. International Standard, ISO/IEC 7498-1:1994. Geneva: ISO, 1994.

[D2]	TM Space Data Link Protocol. Issue 2. Recommendation for Space Data System Standards (Blue Book), CCSDS 132.0-B-2. Washington, D.C.: CCSDS, September 2015.

[D3]	AOS Space Data Link Protocol. Issue 3. Recommendation for Space Data System Standards (Blue Book), CCSDS 732.0-B-3. Washington, D.C.: CCSDS, September 2015.

[D6]	Spectral Grids for WDM Applications: DWDM Frequency Grid. ITU-T Recommendation G.694.1. Geneva: ITU, 2012.

[D7]	B. Moision and J. Hamkins. “Coded Modulation for the Deep-Space Optical Channel: Serially Concatenated Pulse-Position Modulation.” IPN Progress Report 42-161 (May 15, 2005).

[D8]	Robert M. Gagliardi and Sherman Karp. Optical Communications. 2nd ed. Hoboken, New Jersey: Wiley, March 1995.

[D9]	Hamid Hemmati, ed. Deep Space Optical Communications. Hoboken, New Jersey: Wiley, June 2006.

# Footnotes

A subsequent issue of this Recommended Standard may provide a specification for low-complexity and/or high-data-rate optical communications.

# Comments

remark: very high number, but can be accepted as a maximum

- Added k in the managed parameter

Gbps replaced by Gsym/s

Added new section in response to Jon’s comment.

(L-Band channel 26 ..... +/-59.25GHz  (1589.57+/-0.5nm)

Updated as per input from TAS (9th Nov 2018)

half a channel, or ~0.4nm width

Corresponding to +-+-0.5 nm (=132.3GHz)  as per comment from JW from TAS

deltaF = c*deltaWL/WL^2

also relaxed this

rectangular would cause power at other spectral components which  would be filtered off later anyway

Added k in the managed parameter