Update of Deep Space Frequency Channels in Recommendation 3.1.6B

Dennis Lee, NASA/JPL

# Introduction

CCSDS Recommendation (401) 3.1.6B provides the channel frequency plan for the 2, 7, 8, 32, and 34 GHz deep space research bands.  The channel center frequencies in Recommendation 3.1.6B follow those given in Recommendation SFCG 7-1.  At the SFCG meeting in July 2019, Recommendation SFCG 7-1 was updated to correct some minor frequency errors in the deep space channel plan.  This document proposes an update to CCSDS Recommendation (401) 3.1.6B to mirror the changes in Recommendation SFCG 7-1R6.

# Deep Space Channel Plan

It was noticed by one of the NASA deep space missions that the X-band uplink and Ka-band downlink frequencies for their channel assignment in Recommendation SFCG 7-1R5 did not match the X-up/Ka-down turnaround ratio (749/3328).  In fact the Ka-band downlink frequency for Channel 21 in both the SFCG and CCSDS Recommendations differed by 2 Hz from the downlink frequency computed from the ideal turnaround ratio.

The specific channel in this case was deep space Channel 21.  Per CCSDS Recommendation 3.1.6B and SFCG Recommendation 7-1R5, the Ka-band downlink center frequency for this channel is 31859.950622 MHz.  However if the uplink frequency for this channel (7170.403550 MHz) is multiplied by the inverse of the turnaround ratio, 3328/749, the corresponding downlink frequency is actually 31859.950620 MHz, which is 2 Hz less than what is given in the CCSDS and SFCG recommendations. Note that some deep space missions use transponders that can generate coherent downlink frequencies to within a fraction of a millihertz needed for precision Doppler measurements and radio science; for these missions a 2 Hz error in the coherent downlink frequency would be quite significant.  Further examination of the channel center frequencies in Recommendation SFCG 7-1R5 and CCSDS Recommendation 3.1.6B showed that in addition to Channel 21, there were a number of other channels with frequency errors on the order of 1 to 2 Hz.

After further investigation, it was discovered that these errors are due to rounding in the method used to generate the channel center frequencies.  The uplink and downlink frequencies for X- and Ka-band channels are generated separately, first by multiplying the S-band uplink channel frequency by the appropriate factor and then rounding the result to the nearest hertz.  Since the S-band uplink frequency is always used as the reference, this results in S-up/S-down, S-up/X-down, and S-up/Ka-down frequency channel pairs that correctly follow the ideal turnaround ratio.  However, frequency pairs that do not include the S-band uplink (e.g., X-up/X-down and X-up/Ka-band pairs) can deviate from the ideal turnaround ratio due to separate rounding of the uplink and downlink frequencies after multiplication of the S-band reference.

One solution that would avoid such rounding errors and correct all frequencies was presented in [1].  However this approach introduced somewhat large changes in the center frequency of some channels.  Since current deep space missions would still be using the old channel frequencies and introducing a new set might cause confusion, the decision was made to go with another solution that would only modify the channel center frequencies by a few hertz.  This solution involved referencing all channels to the X-band uplink rather than the S-band uplink.  The rationale for this approach is that deep space mission have been migrating away from using the 2110-2120 MHz uplink S-band, and most current deep space missions now rely on an X-band uplink in the 7145 – 7190 MHz band.  By referencing the X-band downlink and Ka-band downlinks to the X-band uplink, the X-up/X-down and X-up/Ka-down coherent channel frequency pairs will comply with the ideal turnaround ratio.  In addition, this approach will also not create any rounding errors in the S-up/S-down frequencies.

This approach has the advantage that changes to the channel center frequencies are generally quite small (≤ 2 Hz for X-band and ≤ 10 Hz for Ka-band).  However some K-up/K-down frequency channel pairs, there will still be a 1 Hz error in the turnaround ratio.  In Recommendation SFCG 7-1R6, this is taken care of by including a note in the recommendation that frequencies may deviate by 1 or 2 Hz from the exact turnaround ratio due to rounding.  This solution was accepted by the SFCG, and the recommendation was provisionally approved at the most recent SFCG meeting.

# Summary

Changes to the deep space frequency channel plan in CCSDS Recommendation 3.1.6B are proposed in order to align the recommendation with recent changes in SFCG Recommendation 7-1R6.  These changes were made to correct certain errors in the X-band and Ka-band frequencies in the previous version of the SFCG recommendation, which caused the uplink and downlink frequencies not to correspond with the CCSDS recommended turnaround ratios.  The proposed changes are shown in the Annex below.

References

[1]  	SF39-23/D, “Proposed Modification of Deep Space Frequency Plan (REC SFCG 07-1R5)”, SFCG-39, July 1-8, 2019.

### 3.1.6B	CHANNEL FREQUENCY PLAN FOR 2, 7, 8, 32, AND 34 GHZ, CATEGORY B

The CCSDS,

considering

- that channel frequency plans for Category B missions exist for the 2, 7, 8, 32, and 34 GHz bands;

- that the sets of channel frequency pairs in these existing plans are based upon the recommended turnaround ratios;

- that members of the Space Frequency Coordination Group (SFCG) have resolved to select frequencies for their Category B missions from the existing channel frequency plans;

- that most past, existing, and planned Category B missions have assigned frequencies that were selected on the basis of these existing channel frequency plans;

- that CCSDS agencies conducting Category B missions have coordinated the selection of frequencies from those embodied in the existing channel frequency plans in order to avoid interference between missions;

recommends

- that CCSDS agencies select frequencies for their Category B missions operating in the 2, 7, 8, 32, and 34 GHz bands from the channel frequency plan contained in Table 3.1.6B-1;

- that frequency selection be coordinated with an appropriate organization, such as the SFCG, to ensure the orderly use of the channel frequency plan.

TABLE 3.1.6B-1:  Channel Frequencies for Category B (Deep-Space) Missions

| BAND (GHz): | 2 E-S | 2 S-E | 7 E-S | 8 S-E | 32 S-E | 32 S-E | 32 S-E | 34 E-S |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| FACTOR: | 221 | 240 | 749 | 880 | 3328 | 3344 | 3360 | 3599 |
| CHANNEL |  | F2DN |  |  |  |  |  |  |
| 1 |  | 2290.185185 | 7147.286265 |  |  | # 31909.913578 | #32062.592591 | # 34343.235337 |
| 2 |  | 2290.555556 | 7148.442131 |  |  | # 31915.074080 | #32067.777784 | # 34348.789358 |
| 3 |  | 2290.925926 | 7149.597994 | 8400.061729 |  | # 31920.234569 | #32072.962964 | # 34354.343365 |
| 4 |  | 2291.296296 | 7150.753857 | 8401.419752 |  | # 31925.395057 | #32078.148144 | # 34359.897372 |
| 5 | 2110.243056 | 2291.666667 | 7151.909723 | 8402.777779 |  | 31930.555559 | 32083.333337 | 34365.451393 |
| 6 | 2110.584105 | 2292.037037 | 7153.065586 | 8404.135802 |  | 31935.716048 | 32088.518517 | 34371.005399 |
| 7 | 2110.925154 | 2292.407407 | 7154.221449 | 8405.493825 |  | 31940.876536 | 32093.703696 | 34376.559406 |
| 8 | 2111.266204 | 2292.777778 | 7155.377316 | 8406.851853 |  | 31946.037042 | 32098.888894 | 34382.113432 |
| 9 | 2111.607253 | 2293.148148 | 7156.533179 | 8408.209877 |  | 31951.197531 | 32104.074074 | 34387.667438 |
| 10 | 2111.948303 | 2293.518519 | 7157.689045 | 8409.567903 | 31803.456798 | 31956.358033 | 32109.259267 | 34393.221459 |
| 11 | 2112.289352 | 2293.888889 | 7158.844908 | 8410.925927 | 31808.592595 | 31961.518521 | 32114.444447 | 34398.775466 |
| 12 | 2112.630401 | 2294.259259 | 7160.000771 | 8412.283950 | 31813.728392 | 31966.679010 | 32119.629627 | 34404.329472 |
| 13 | 2112.971451 | 2294.629630 | 7161.156637 | 8413.641977 | 31818.864203 | 31971.839512 | 32124.814820 | 34409.883493 |
| 14 | 2113.312500 | 2295.000000 | 7162.312500 | 8415.000000 | 31824.000000 | 31977.000000 | 32130.000000 | 34415.437500 |
| 15 | 2113.653549 | 2295.370370 | 7163.468363 | 8416.358023 | 31829.135797 | 31982.160488 | 32135.185180 | 34420.991507 |
| 16 | 2113.994599 | 2295.740741 | 7164.624229 | 8417.716050 | 31834.271608 | 31987.320990 | 32140.370373 | 34426.545528 |
| 17 | 2114.335648 | 2296.111111 | 7165.780092 | 8419.074073 | 31839.407405 | 31992.481479 | 32145.555553 | 34432.099534 |
| 18 | 2114.676697 | 2296.481481 | 7166.935955 | 8420.432097 | 31844.543202 | 31997.641967 | 32150.740733 | 34437.653541 |
| 19 | 2115.017747 | 2296.851852 | 7168.091821 | 8421.790123 | 31849.679012 | 32002.802469 | 32155.925926 | 34443.207562 |
| 20 | 2115.358796 | 2297.222222 | 7169.247684 | 8423.148147 | 31854.814810 | 32007.962958 | 32161.111106 | 34448.761568 |
| 21 | 2115.699846 | 2297.592593 | 7170.403551 | 8424.506175 | 31859.950624 | 32013.123464 | 32166.296304 | 34454.315594 |
| Note – Channel frequencies marked “ # ” may be used in conjunction with the corresponding channel in a lower frequency band if that channel is available within the Category B allocation. F2DN = N(10/27) + 2295 MHz, where N is in the range −13 to +28 for this Table. The value of F2DN is rounded to the nearest Hz. Frequencies in the 8 GHz E-S band are then computed and rounded to the nearest Hz. Channel numbers are equal to N + 14. Frequencies in other bands are derived from the 8 GHz E-S frequencies by using the corresponding ratio of frequency factors, and then rounding to the nearest Hz. Due to rounding, ratios of the uplink to downlink frequency may differ by 1 or 2 Hz from the exact turnaround ratio in some cases. |

TABLE 3.1.6B-1 (Continued):  Channel Frequencies for Category B (Deep-Space) Missions

| BAND (GHZ): | 2 E-S | 2 S-E | 7 E-S | 8 S-E | 32 S-E | 32 S-E | 32 S-E | 34 E-S |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| FACTOR: | 221 | 240 | 749 | 880 | 3328 | 3344 | 3360 | 3599 |
| CHANNEL |  | F2DN |  |  |  |  |  |  |
| 22 | 2116.040895 | 2297.962963 | 7171.559414 | 8425.864198 | 31865.086422 | 32018.283952 | 32171.481483 | 34459.869601 |
| 23 | 2116.381944 | 2298.333333 | 7172.715277 | 8427.222221 | 31870.222219 | 32023.444441 | 32176.666663 | 34465.423607 |
| 24 | 2116.722994 | 2298.703704 | 7173.871143 | 8428.580248 | 31875.358029 | 32028.604943 | 32181.851856 | 34470.977628 |
| 25 | 2117.064043 | 2299.074074 | 7175.027006 | 8429.938271 | 31880.493826 | 32033.765431 | 32187.037036 | 34476.531635 |
| 26 | 2117.405092 | 2299.444444 | 7176.182869 | 8431.296295 | 31885.629624 | 32038.925920 | 32192.222216 | 34482.085642 |
| 27 | 2117.746142 | 2299.814815 | 7177.338735 | 8432.654321 | 31890.765434 | 32044.086422 | 32197.407409 | 34487.639663 |
| 28 | 2118.087191 |  | 7178.494598 | 8434.012345 | #31895.901231 | # 32049.246910 | #32202.592589 | # 34493.193669 |
| 29 | 2118.428241 |  | 7179.650464 | 8435.370372 | #31901.037042 | # 32054.407412 | #32207.777782 | # 34498.747690 |
| 30 | 2118.769290 |  | 7180.806327 | 8436.728395 | #31906.172839 | # 32059.567901 | #32212.962962 | # 34504.301697 |
| 31 | 2119.110339 |  | 7181.962190 | 8438.086418 | #31911.308636 | # 32064.728389 | #32218.148142 | # 34509.855703 |
| 32 | 2119.451389 |  | 7183.118057 | 8439.444446 | #31916.444451 | # 32069.888895 | #32223.333340 | # 34515.409729 |
| 33 | 2119.792438 |  | 7184.273920 | 8440.802469 | #31921.580248 | # 32075.049384 | #32228.518520 | # 34520.963736 |
| 34 |  |  | 7185.429783 | 8442.160493 | #31926.716045 | # 32080.209872 | #32233.703699 | # 34526.517742 |
| 35 |  |  | 7186.585649 | 8443.518520 | #31931.851856 | # 32085.370374 | #32238.888893 | # 34532.071763 |
| 36 |  |  | 7187.741512 | 8444.876543 | #31936.987653 | # 32090.530863 | #32244.074073 | # 34537.625770 |
| 37 |  |  | 7188.897378 | 8446.234570 | #31942.123463 | # 32095.691365 | #32249.259266 | # 34543.179791 |
| 38 |  |  |  | 8447.592593 | #31947.259260 | # 32100.851853 | #32254.444446 | # 34548.733798 |
| 39 |  |  |  | 8448.950616 | #31952.395058 | # 32106.012341 | #32259.629625 | # 34554.287804 |
| 40 |  |  |  |  | #31957.530868 | # 32111.172843 | #32264.814819 | # 34559.841825 |
| 41 |  |  |  |  | #31962.666665 | # 32116.333332 | #32269.999999 | # 34565.395832 |
| 42 |  |  |  |  | #31967.802462 | # 32121.493820 | #32275.185178 | # 34570.949838 |
| Note – Channel frequencies marked “ # ” may be used in conjunction with the corresponding channel in a lower frequency band if that channel is available within the Category B allocation F2DN = N(10/27) + 2295 MHz, where N is in the range −13 to +28 for this Table. The value of F2DN is rounded to the nearest Hz. Frequencies in the 8 GHz E-S band are then computed and rounded to the nearest Hz. Channel numbers are equal to N + 14. Frequencies in other bands are derived from the 8 GHz E-S frequencies by using the corresponding ratio of frequency factors, and then rounding to the nearest Hz. Due to rounding, ratios of the uplink to downlink frequency may differ by 1 or 2 Hz from the exact turnaround ratio in some cases. |