### 2.4.18	MODULATION METHODS AT HIGH SYMBOL RATE TRANSMISSIONS, EARTH EXPLORATION SATELLITES (EES) 8 GHZ BAND, SPACE-TO-EARTH

The CCSDS,

considering

- that efficient use of RF spectrum resources is becoming increasingly important with the increasing congestion of the frequency bands;

- that the 8025–8400 MHz band is heavily used and interference conflicts may become increasingly frequent in this band;

- that the SFCG has approved a Recommendation which specifies a spectrum mask for emissions with symbol rates below and above 2 Ms/s;

- that the SFCG has approved a Recommendation on the use of the 8025–8400 MHz band recommending that bandwidth- and power-efficient modulation and coding techniques be used;

- that CCSDS 131.0-B-3, CCSDS 131.2-B-1, and CCSDS 131.3-B-1 foresee a number of coding schemes, some of which may be incompatible with the bandwidth-efficient use of the 8025–8400 MHz band;

- that contiguous to 8400 MHz, a particularly sensitive allocation to Space Research, deep space, requires adequate protection from unwanted emissions generated by EES;

- that only filtered suppressed carrier systems can meet the bandwidth efficiency of the SFCG spectrum mask Recommendation for symbol rates in excess of 2 Ms/s and limit unwanted emissions into the neighboring bands;1

- that Square Root Raised Cosine (SRRC) filtered 4-Dimensional 8PSK Trellis Coded Modulation (SRRC-4D 8PSK TCM), SRRC-QPSK, SRRC-OQPSK, SRRC-8PSK, SRRC-16APSK, SRRC-32APSK, and SRRC-64APSK, and some filtered OQPSK modulations spectra can meet the SFCG emission mask for symbol rates in excess of 2 Ms/s with acceptable end-to-end losses;

- that baseband filtered QPSK, OQPSK, and 8PSK receivers are readily available in most space agencies’ ground networks;

- that baseband filtered receivers for higher order modulations are available through a number of vendors;

- that a phase imbalance of less than 3 degrees and an amplitude imbalance of less than 0.5 dB should result in acceptable performance degradation;

2.4.18	MODULATION METHODS AT HIGH SYMBOL RATE TRANSMISSIONS, EARTH EXPLORATION SATELLITES (EES) 8 GHZ BAND, SPACE-TO-EARTH (Continued)

- that a channel with in-band ripple up to 0.1 dB, out-of-band rejection of at least 30 dB, and in-band (within channel symbol rate) group-delay variations up to 10 percent of the signal duration should result in acceptable performance degradations even in case no equalization is used at the receiver;

noting

- that filtered OQPSK signals can also be demodulated by unfiltered OQPSK receivers with some mismatching losses;

- that many missions are currently operating in this band with a signaling efficiency over 1.75 source bits/channel symbol;

- that recommended maximum values of phase noise and HPA linearity are needed to ensure small end-to-end losses;

- that linearization techniques (pre-distortion) or compensation (equalization, centroid tuning) or both can reduce the channel losses, especially for APSK modulations;

- that the use of a frame header and of pilot symbols can improve the acquisition time as well as tracking performance;

- that the constellation bit mapping for SRRC-4D 8PSK TCM is natural, while constellation bit mappings for SRRC-8PSK, SRRC-16APSK, SRRC-32APSK, and SRRC-64APSK are Gray coded and are different for coding in accordance with CCSDS 131.0-B-3, CCSDS 131.2-B-1 and CCSDS 131.3-B-1;

recommends

- that a mission planning to operate in the 8025–8400 MHz band shall use SRRC-4D 8PSK TCM10 or SRRC-QPSK, SRRC-OQPSK, SRRC-8PSK, SRRC-16APSK, SRRC-32APSK, and SRRC-64APSK or filtered OQPSK;

- that a mission planning to use this band should select the most bandwidth-efficient channel coding scheme from CCSDS 131.0-B-3 or 131.2-B-1 or 131.3-B-1 compatible with the mission constraints;

2.4.18	MODULATION METHODS AT HIGH SYMBOL RATE TRANSMISSIONS, EARTH EXPLORATION SATELLITES (EES) 8 GHZ BAND, SPACE-TO-EARTH (Continued)

- that Variable Coding and Modulation (VCM) or Adaptive Coding and Modulation (ACM) techniques should be used where practicable;

- that linearization techniques (pre‐distortion) at the transmitter or compensation (such as equalization or centroid tuning) at the receiver should be used to minimize the end-to-end losses at least for 16APSK and higher-order modulations, and in any case if the channel is worse than in considering (k);

- that a frame header (see A2.5) and pilot symbols should be used to improve the acquisition and tracking performance especially for modulations with order higher than 8PSK;

- that the phase noise of the communication chain should be limited according to the mask given in Annex 1 or Annex 2 depending on the selected scheme;

- that the modulator’s phase imbalance shall not exceed 5 degrees for SRRC-QPSK, SRRC-OQPSK, SRRC-4D 8PSK TCM, SRRC-8PSK, and SRRC-16APSK and 3 degrees for SRRC-32APSK and SRRC-64APSK, and the amplitude imbalance shall not exceed 0.5 dB between the constellation points;

- that the AM/PM slope for the non-linear amplifier shall be less than 5°/dB unless appropriate equalization at the receiver is performed.

2.4.18	MODULATION METHODS AT HIGH SYMBOL RATE TRANSMISSIONS, EARTH EXPLORATION SATELLITES (EES) 8 GHZ BAND, SPACE-TO-EARTH (Continued)

ANNEX 1

4-Dimensional 8PSK Trellis Coded Modulation Specifications

(Normative)

A1.1	General

The 4D-8PSK trellis-coded modulator consists of a serial-to-parallel converter, a differential coder, a trellis encoder (convolutional coder), a constellation mapper, and an 8PSK modulator (see figure 2.4.18-1). It should be noted that in this figure, ‘wi’ (with index i = 1, … , m) represent the uncoded bits and ‘xj’ (with index j = 0, … , m) are the coded bits.  The trellis encoder is based on a 64-state systematic convolutional coder and can be considered as the inner code if an outer block code is introduced. Carrier phase ambiguity is resolved by the use of a differential coder located prior to the trellis encoder. Spectral efficiencies of 2, 2.25, 2.5, and 2.75 bits/channel-symbol are achieved with four possible architectures of the constellation mapper. The output switch addresses successively one of the four symbols ( Z(0) – Z(3) ) from the constellation mapper to the 8PSK modulator.

The present standard is based on the following parameters:

- size of the constellation: M=8 phase states (8PSK);

- number of signal set constituents: L=4 (shown as Z(0) … Z(3) in figure 2.4.18-1);

- number of states for the trellis encoder: 64;

- rate of the convolutional coder used for the construction of the trellis: R=3/4;

- rate of the modulation: Rm=m/(m+1)  selectable to 8/9, 9/10, 10/11, or 11/12;

- efficiency of the modulation:

- Reff=2 bits per channel-symbol (for Rm=8/9);

- Reff=2.25 bits per channel-symbol (for Rm=9/10);

- Reff=2.5 bits per channel-symbol (for Rm=10/11);

- Reff=2.75 bits per channel-symbol (for Rm=11/12).

Figure 2.4.18-1:  Structure of the 4D 8PSK-TCM Coder/Mapper

2.4.18	MODULATION METHODS AT HIGH SYMBOL RATE TRANSMISSIONS, EARTH EXPLORATION SATELLITES (EES) 8 GHZ BAND, SPACE-TO-EARTH (Continued)

ANNEX 1 (Continued)

A1.2	Differential Coder

The differential coder is depicted in figure 2.4.18-2.  Table 2.4.18-1 gives the bit reference at input and output of the differential coder in each case.

Table 2.4.18-1:  Bit Mapping for Differential Coder with Modulo-8 Addition

| Efficiencies in bits /channel-symbol |
| --- |
| 2 | 2.25 | 2.5 | 2.75 |
| bit IN | bit OUT | bit IN | bit OUT | bit IN | bit OUT | bit IN | bit OUT |
| w1 | x1 | w2 | x2 | w3 | x3 | w4 | x4 |
| w5 | x5 | w6 | x6 | w7 | x7 | w8 | x8 |
| w8 | x8 | w9 | x9 | w10 | x10 | w11 | x11 |

An example of differential encoder connections is given in figure 2.4.18-2 for the 2 bits/channel-symbol case. The structure of the modulo-8 adder is also shown; it is applicable to both the coder mapper and differential coder.

|  | c0  a0 ⊕ b0 with carry r0 c1  a1 ⊕ b1 ⊕ r0 with carry r1 c2  a2 ⊕ b2 ⊕ r1 r0  a0.b0 r1  (a1.b1)(a1.r0)(b1.r0) where . corresponds to a logical AND, and to a logical OR |
| --- | --- |

Figure 2.4.18-2:  Differential Coder and Modulo-8 Adder Principle

2.4.18	MODULATION METHODS AT HIGH SYMBOL RATE TRANSMISSIONS, EARTH EXPLORATION SATELLITES (EES) 8 GHZ BAND, SPACE-TO-EARTH (Continued)

ANNEX 1 (Continued)

A1.3	Convolutional Coder

The convolutional coder used to implement the trellis is depicted in figure 2.4.18-3.  The shift registers of the encoder are clocked at the rate of RChS/4.

Figure 2.4.18-3:  Convolutional Coder Recommended for High Data Rates

A1.4	Constellation Mapper for 4D-8PSK-TCM

The constellation mapper principles are given in figures 2.4.18-4 to 2.4.18-7 for the four possible efficiencies of this modulation (i.e., 2 bits/channel-symbol, 2.25 bits/channel-symbol, 2.5 bits/channel-symbol, and 2.75 bits/channel-symbol).  These mappers implement the straightforward logical mapping described in the figures below.  The correspondence between the signals Z (i) at the input of the modular and the 8PSK phase states of the constellations follows a natural mapping (i.e., 0, 1, 2 …, 7 anticlockwise).

= line connected to differential coder

= line connected to serial-to-parallel converter or convolutional coder

Figure 2.4.18-4:  Constellation Mapper for 2 Bits/Channel-Symbol

2.4.18	MODULATION METHODS AT HIGH SYMBOL RATE TRANSMISSIONS, EARTH EXPLORATION SATELLITES (EES) 8 GHZ BAND, SPACE-TO-EARTH (Continued)

ANNEX 1 (Continued)

= line connected to differential coder

= line connected to serial-to-parallel converter or convolutional coder

Figure 2.4.18-5:  Constellation Mapper for 2.25 Bits/Channel-Symbol

= line connected to differential coder

= line connected to serial-to-parallel converter or convolutional coder

Figure 2.4.18-6:  Constellation Mapper for 2.5 Bits/Channel-Symbol

2.4.18	MODULATION METHODS AT HIGH SYMBOL RATE TRANSMISSIONS, EARTH EXPLORATION SATELLITES (EES) 8 GHZ BAND, SPACE-TO-EARTH (Continued)

ANNEX 1 (Continued)

= line connected to differential coder

= line connected to serial to parallel converter or convolutional coder

Figure 2.4.18-7:  Constellation Mapper for 2.75 Bits/Channel-Symbol

2.4.18	MODULATION METHODS AT HIGH SYMBOL RATE TRANSMISSIONS, EARTH EXPLORATION SATELLITES (EES) 8 GHZ BAND, SPACE-TO-EARTH (Continued)

ANNEX 1 (Continued)

A1.5	Coder/Mapper Implementation at 2, 2.25, 2.5, and 2.75 Bits/Channel-Symbol Efficiency

The principle of the coder-mapper for 2, 2.25, 2.5, and 2.75 bits/channel-symbol efficiency is given in figures 2.4.18-8 through 2.4.18-11.

Figure 2.4.18-8:  Coder and Mapper Implementation for 2 Bits/Channel-Symbol Efficiency

Figure 2.4.18-9: Coder and Mapper Implementation at 2.25 Bits/Channel-Symbol Efficiency

2.4.18	MODULATION METHODS AT HIGH SYMBOL RATE TRANSMISSIONS, EARTH EXPLORATION SATELLITES (EES) 8 GHZ BAND, SPACE-TO-EARTH (Continued)

ANNEX 1 (Continued)

Figure 2.4.18-10:  Coder and Mapper Implementation at 2.5 Bits/Channel-Symbol Efficiency

Figure 2.4.18-11:	Coder and Mapper Implementation at 2.75 Bits/Channel-Symbol Efficiency

2.4.18	MODULATION METHODS AT HIGH SYMBOL RATE TRANSMISSIONS, EARTH EXPLORATION SATELLITES (EES) 8 GHZ BAND, SPACE-TO-EARTH (Continued)

ANNEX 1 (Continued)

A1.6	SRRC Channel Filtering

The normalized transfer function of the SRRC filter shall be:,



where  is the Nyquist frequency and ( is the roll-off factor.

The specified values for the roll-off factor are α = 0.35 and 0.5.

A1.7	PHASE NOISE

The phase noise for all the oscillators of the communication chain shall be limited according to the mask given in figure 2.4.18-12 for channel symbol rates above 1 Ms/s.

NOTE	–	The figure shows the double sided phase noise mask 2L(f) in dBc/Hz versus frequency in Hz.

2.4.18	MODULATION METHODS AT HIGH SYMBOL RATE TRANSMISSIONS, EARTH EXPLORATION SATELLITES (EES) 8 GHZ BAND, SPACE-TO-EARTH (Continued)

ANNEX 1 (Continued)

Figure 2.4.18-12:  8PSK Phase Noise Mask Recommendation

2.4.18	MODULATION METHODS AT HIGH SYMBOL RATE TRANSMISSIONS, EARTH EXPLORATION SATELLITES (EES) 8 GHZ BAND, SPACE-TO-EARTH (Continued)

ANNEX 1 (Continued)

A1.8	bit mapping to constellation

The following convention is used to identify each bit in an N-bit field.  The first bit in the field to be transmitted (i.e., the most left justified when drawing a figure) is defined to be ‘Bit 0’,  the following bit is defined to be ‘Bit 1’, and so on up to ‘Bit N−1’.  When the field is used to express a binary value (such as a counter), the Most Significant Bit (MSB) shall be the first transmitted bit of the field, i.e., ‘Bit 0’ (see figure 2.4.18-13).

Figure 2.4.18-13:  Bit Numbering Convention

For instance, bits 3i, 3i+1, 3i+2 of the modulator input determine the ith 8PSK symbol, where i = 0, 1, 2,… (N/3)−1 and N is the block size to be transmitted.

The modulation shall employ a natural mapping constellation (i.e., 0, 1, 2, …, 7 anticlockwise) as in figure 2.4.18-14 with associated bit numbering convention as in figure 2.4.18-13.

Z(i) represents the signals (three lines) at the input of the modulator, with Z(0) being the signal set of the first constellation and Z(3) being the signal set of the fourth constellation.

|  | Phase state Phase angle (°) Z(i) A 0 000 B 45 001 C 90 010 D 135 011 E 180 100 F 225 101 G 270 110 H 315 111 |
| --- | --- |

Figure 2.4.18-14:  4D-8PSK-TCM Symbol Mapping into Constellation

2.4.18	MODULATION METHODS AT HIGH SYMBOL RATE TRANSMISSIONS, EARTH EXPLORATION SATELLITES (EES) 8 GHZ BAND, SPACE-TO-EARTH (Continued)

ANNEX 2

QPSK/OQPSK/8PSK/16APSK/32APSK/64APSK Modulation Specifications

(Normative)

A2.1	GENERAL

The modulation formats here specified shall follow the template provided in table 2.4.18-2, with the relevant parameters that define each constellation. For multi-circle constellations, and in particular for 16- and 32-APSK, different values are provided for the ratio of outer to inner circle radius, optimized based on the code rate used in CCSDS 131.2-B-1 and CCSDS 131.3-B-1.

Table 2.4.18-2: Modulation Definition

| Item | QPSK and OQPSK | 8PSK | 16APSK | 32APSK | 64APSK |
| --- | --- | --- | --- | --- | --- |
| Number of constellation concentric circumferences | 1 | 1 | 2 | 3 | 4 |
| Number of uniformly spaced points per circumference | N1=4 | N1=8 | N1=4, N2=12 | N1=4, N2=12, N3=16 | N1=4, N2=12, N3=20, N4=28 |
| Ratio of outer circle to inner circle radius | N.A. | N.A. | (1=R2/R1 as per CCSDS 131.2-B-1 and CCSDS 131.3-B-1; when codes from 131.0-B-3 are used as described in 431.0-B-1, the ratios in Table 2.4.18-3 shall be used. (See also ) | (1=R2/R1 and (2=R3/R1 as per CCSDS 131.2-B-1 and CCSDS 131.3-B-1; when codes from 131.0-B-3 are used as described in 431.0-B-1, the ratios in Table 2.4.18-3 shall be used. (See also ) | (1=R2/R1 = 2.73, (2=R3/R1= 4.52, (3=R4/R1= 6.31 |
| Radii relation for unit average symbol level (average symbol energy =1) | N.A. | N.A. | [R1]2+3[R2]2=4 | [R1]2+3[R2]2 +4[R3]2=8 | [R1]2+3[R2]2 +5[R3]2+7[R4]2=16 |
| Bit-to-symbol mapping | Bits 2i (MSB) and 2i+1 (LSB) determine the ith QPSK symbol | Bits 3i (MSB), 3i+1 and 3i+2 (LSB) determine the ith 8PSK symbol | Bits 4i (MSB), 4i+1, 4i+2 and 4i+3 (LSB) determine the ith 16APSK symbol | Bits 5i (MSB), 5i+1, 5i+2, 5i+3 and 5i+4 (LSB) determine the ith 32APSK symbol | Bits 6i (MSB), 6i+1, 6i+2, 6i+3, 6i+4 and 6i+5 (LSB) determine the ith 64APSK symbol |
| Constellation proper | (See figure 2.4.18-17) | (See figures 2.4.18-18 and 2.4.18-19) | (See figure 2.4.18-20) | (See figure 2.4.18-21) | (See figure 2.4.18-22) |

Table 2.4.18-3: Radii Ratios when codes from 131.0-B-3 are used as described in 431.1-B-1

| VCM Mode | Modulation | Code Rate | (1 = R2/R1 | (2 = R3/R1 |
| --- | --- | --- | --- | --- |
| 16 | 16-APSK | ½ | 3.15 | N.A. |
| 17 | 16-APSK | 2/3 | 3.15 | N.A. |
| 18 | 16-APSK | 4/5 | 2.75 | N.A. |
| 19 | 16-APSK | 223/255 | 2.60 | N.A. |
| 20 | 32-APSK | ½ | 2.84 | 5.27 |
| 21 | 32-APSK | 2/3 | 2.84 | 5.27 |
| 22 | 32-APSK | 4/5 | 2.72 | 4.87 |
| 23 | 32-APSK | 223/255 | 2.57 | 4.41 |

2.4.18	MODULATION METHODS AT HIGH SYMBOL RATE TRANSMISSIONS, EARTH EXPLORATION SATELLITES (EES) 8 GHZ BAND, SPACE-TO-EARTH (Continued)

ANNEX 2 (Continued)

A2.2	SRRC Channel Filtering

The transfer function of the SRRC filter shall be:,



where  is the Nyquist frequency and ( is the roll-off factor.	The specified values for the roll-off factor are α = 0.2, 0.25, 0.3, and 0.35.

A2.3	PHASE NOISE

The phase noise for all the oscillators of the communication chain shall be limited according to the mask given in figure 2.4.18-15 for channel symbol rates above 1 Ms/s.

NOTE	–	The figure shows the double-sided phase noise mask 2L(f) in dBc/Hz versus frequency in Hz.

2.4.18	MODULATION METHODS AT HIGH SYMBOL RATE TRANSMISSIONS, EARTH EXPLORATION SATELLITES (EES) 8 GHZ BAND, SPACE-TO-EARTH (Continued)

ANNEX 2 (Continued)

Figure 2.4.18-15:  Phase Noise Mask Recommendation

2.4.18	MODULATION METHODS AT HIGH SYMBOL RATE TRANSMISSIONS, EARTH EXPLORATION SATELLITES (EES) 8 GHZ BAND, SPACE-TO-EARTH (Continued)

ANNEX 2 (Continued)

A2.4	BIT MAPPING TO CONSTELLATION

The following convention is used to identify each bit in an N-bit field.  The first bit in the field to be transmitted (i.e., the most left justified when drawing a figure) is defined to be ‘Bit 0’,  the following bit is defined to be ‘Bit 1’, and so on up to ‘Bit N−1’.  When the field is used to express a binary value (such as a counter), the Most Significant Bit (MSB) shall be the first transmitted bit of the field, i.e., ‘Bit 0’ (see figure 2.4.18-16).

Figure 2.4.18-16:  Bit Numbering Convention

For instance, bits 3i, 3i+1, 3i+2 of the modulator input determine the ith 8PSK symbol, where i = 0, 1, 2,…, (N/3)−1, and N is the block size to be transmitted.

2.4.18	MODULATION METHODS AT HIGH SYMBOL RATE TRANSMISSIONS, EARTH EXPLORATION SATELLITES (EES) 8 GHZ BAND, SPACE-TO-EARTH (Continued)

ANNEX 2 (Continued)

A2.4.1 QPSK and OQPSK

Modulations in accordance with CCSDS 131.2-B-1, CCSDS 131.3-B-1 or when used with coding schemes specified in CCSDS 131.0-B-3, shall employ a conventional Gray-coded constellation with absolute mapping (no differential coding) as in figure 2.4.18-17 with associated bit numbering convention as in figure 2.4.18-16.

Figure 2.4.18-17:  QPSK and OQPSK Symbol Mapping into Constellation

2.4.18	MODULATION METHODS AT HIGH SYMBOL RATE TRANSMISSIONS, EARTH EXPLORATION SATELLITES (EES) 8 GHZ BAND, SPACE-TO-EARTH (Continued)

ANNEX 2 (Continued)

A2.4.2 8PSK

Modulation in accordance with CCSDS 131.2-B-1 shall employ a conventional Gray-coded constellation with absolute mapping (no differential coding) as in figure 2.4.18-18 with associated bit numbering convention as in figure 2.4.18-16.  Alternatively, modulation in accordance with CCSDS 131.3-B-1 or when used with coding specified in CCSDS 131.0-B-3 shall employ a conventional Gray-coded constellation with absolute mapping (no differential coding) as in figure 2.4.18-19 with associated bit numbering convention as in figure 2.4.18-16.

Figure 2.4.18-18:  8PSK Symbol Mapping into Constellation (CCSDS 131.2-B-1)

Figure 2.4.18-19:	8PSK Symbol Mapping into Constellation (CCSDS 131.3-B-1 and CCSDS 131.0-B-3)

2.4.18	MODULATION METHODS AT HIGH SYMBOL RATE TRANSMISSIONS, EARTH EXPLORATION SATELLITES (EES) 8 GHZ BAND, SPACE-TO-EARTH (Continued)

ANNEX 2 (Continued)

A2.4.3 16APSK

Modulations in accordance with CCSDS 131.2-B-1, CCSDS 131.3-B-1 or when used with coding schemes specified in CCSDS 131.0-B-3, shall employ a  constellation as in figure 2.4.18-20 and with associated bit numbering convention as in figure 2.4.18-16.

Figure 2.4.18-20: 16APSK Symbol Mapping into Constellation

2.4.18	MODULATION METHODS AT HIGH SYMBOL RATE TRANSMISSIONS, EARTH EXPLORATION SATELLITES (EES) 8 GHZ BAND, SPACE-TO-EARTH (Continued)

ANNEX 2 (Continued)

A2.4.4 32APSK

Modulations in accordance with CCSDS 131.2-B-1, CCSDS 131.3-B-1 or when used with coding schemes specified in CCSDS 131.0-B-3, shall employ a constellation as in figure 2.4.18-21 and with associated bit numbering convention as in figure 2.4.18-16.

Figure 2.4.18-21: 32APSK Symbol Mapping into Constellation

2.4.18	MODULATION METHODS AT HIGH SYMBOL RATE TRANSMISSIONS, EARTH EXPLORATION SATELLITES (EES) 8 GHZ BAND, SPACE-TO-EARTH (Continued)

ANNEX 2 (Continued)

A2.4.5 64APSK

Modulations in accordance with CCSDS 131.2-B-1 or when used with coding schemes specified in CCSDS 131.0-B-3, shall employ a  conventional Gray-coded constellation with absolute mapping (no differential coding) as in figure 2.4.18-22 and with associated bit numbering convention as in figure 2.4.18-16.

Figure 2.4.18-22: 64APSK Symbol Mapping into Constellation

2.4.18	MODULATION METHODS AT HIGH SYMBOL RATE TRANSMISSIONS, EARTH EXPLORATION SATELLITES (EES) 8 GHZ BAND, SPACE-TO-EARTH (Continued)

ANNEX 2 (Continued)

A2.5	FRAME HEADER MODULATION

The frame header shall consist of π/2-BPSK modulated symbols as defined below.

Assuming that the frame header binary sequence of length N is denoted as:

(x1,x2,...,xN)

then the in-phase (I) and the quadrature (Q) components of the N π/2-BPSK modulated symbols shall be determined according to the following rule:

for i = 1, 2, ..., N / 2

# Footnotes

See SFCG Recommendation 21-2R4 or latest version.

See SFCG Recommendation 14-3R10 or latest version.

See SFCG Recommendation 14-1R1 or latest version.

Square Root Raised Cosine ( = 0.35 and  = 0.5) 4D 8PSK Trellis Coded Modulation (see Annex 1).

Square Root Raised Cosine with α = 0.2, 0.25, 0.3, and  0.35 (see Annex 2).

Filtered (Square Root Raised Cosine  = 0.5) Offset QPSK; Butterworth 6 poles, BTS = 0.5; agencies may also utilize filtered OQPSK modulation with other types of bandpass filters provided that the equivalent baseband BTS is not greater than 0.5 and they ensure compliance with SFCG Recommendation 21-2R4 (or latest version) and interoperability with the cross-supporting networks. B refers to the one-sided 3-dB bandwidth of the filter.

1 ns at 100 Ms/s (channel symbol rate).

See annex B4 of CCSDS 413.0-G-3 for  SRRC and Butterworth filtered OQPSK mismatching losses.

Ratio of source data rate to channel symbol rate.

Available options are 2.0 b/s/Hz, 2.25 b/s/Hz, 2.5 b/s/Hz, and 2.75 b/s/Hz; Square Root Raised Cosine filter with  = 0.35 or  = 0.5 (see Annex 1).

Square Root Raised Cosine filter with α = 0.2, 0.25, 0.3, and  0.35  (see Annex 2).

Filtered (Square Root Raised Cosine α = 0.5) Offset QPSK; baseband Butterworth 6 poles, BTS = 0.5; agencies may also utilize filtered OQPSK modulation with other types of bandpass filters provided that the equivalent baseband BTS is not greater than 0.5 and they ensure compliance with SFCG Recommendation 21-2R4 (or latest version) and interoperability with the cross-supporting networks. B refers to the one-sided 3-dB bandwidth of the filter.

Relative Recommended Practices (Magenta Books) are under preparation.

For systems compliant with CCSDS 131.2-B-1 and CCSDS 131.3-B-1, the relevant standard should be consulted. For systems compliant with CCSDS 131.0-B-3 (see CCSDS 431.1-R-1).

For filtered OQPSK,12 Annex 2 applies.

SRRC filtering can be practically implemented either with baseband filters or with RF post-amplifier filters, each able to fulfill SFCG Recommendation 21-2R4 (see CCSDS 413.0-G-3).

This formulation yields an impulse-response function with dimensions of Hz (or 1/s). Sometimes in literature the transfer function is shown with a multiplication factor  in front.

For a multistandard system, the range to be covered for (1 varies from 2.57 to 3.15.

For a multistandard system, the range to be covered for (1 varies from 2.53 to 2.84 and the range for (2 varies from 4.30 to 5.27.

SRRC filtering can be practically implemented with baseband filters able to fulfill SFCG Recommendation 21-2R4 (see CCSDS 413.0-G-3).

This formulation yields an impulse response function with dimensions of Hz (or 1/s). Sometimes in literature the transfer function is shown with a multiplication factor  in front.

The mapping is the same as in recommendation 2.4.10.