DRAFT RECOMMENDATION FOR SPACE

DATA SYSTEM STANDARDS

PROXIMITY-1 SPACE LINK PROTOCOL— DATA LINK LAYER

CCSDS 211.0-P-2.1

PINK SHEETS

October 2003

AUTHORITY

|  | Issue: | Pink Sheets, Issue 2.1 |  |
| --- | --- | --- | --- |
|  | Date: | October 2003 |  |
|  | Location: | Washington D.C. |  |

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and represents the consensus technical agreement of the participating CCSDS Member Agencies.  The procedure for review and authorization of CCSDS Recommendations is detailed in Procedures Manual for the Consultative Committee for Space Data Systems, and the record of Agency participation in the authorization of this document can be obtained from the CCSDS Secretariat at the address below.

This Recommendation is published and maintained by:

CCSDS Secretariat

Office of Space Communication (Code M-3)

National Aeronautics and Space Administration

Washington, DC  20546, USA

| Bit 0 |  |  |  |  | Bit 15 |
| --- | --- | --- | --- | --- | --- |
| TX Mode 3 bits | TX Data Rate 4 bits | TX Modulation 1 bit | TX Data encoding 2 bits | TX Frequency 3 bits | Directive Type 3 bits |
| 0,1,2 | 3,4,5,6 | 7 | 8,9 | 10,11,12 | 13,14,15 |

Figure Error! No text of specified style in document.-1:  SET TRANSMITTER PARAMETERS Directive

A1.2.2	Directive Type

A1.2.2.1 Bits 13–15 of the SET TRANSMITTER PARAMETERS directive shall contain the Directive Type.

A1.2.2.2 The 3-bit Directive Type field shall identify the type of protocol control directive and shall contain the binary value ‘000’ for the SET TRANSMITTER PARAMETERS directive.

A1.2.3	Transmitter Frequency

A1.2.3.1	General

Bits 10–12 of the SET TRANSMITTER PARAMETERS directive shall be used to set the transmitter frequency of the partnered transceiver to the desired value.

A1.2.3.2	Return Transmitter Frequency (e.g., Orbiter as Initiator; Landed Asset as Responder)

In the context of the return link, this three-bit field shall define the transmit frequency of the Responder.  Actual frequency assignments are given in the Physical layer (see reference [9]).

| ‘000’ | ‘001’ | ‘010’ | ‘011’ | ‘100’ | ‘101’ | ‘110’ | ‘111’ |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Ch0R | Ch 1R | Ch2R | Ch3R | Ch4R | Ch5R | Ch6R | Ch7R |

Page A-3

c) ‘10’ = By-pass Convolution Code;

d) ‘11’ = Concatenated (RS(204,188), CC(7,1/2)) Codes.

NOTE	–	RS(204,188) with CC(7,1/2) code is an ETSI standard.  This option is not required for cross support.  See reference [F1] for more details.

A1.2.3.4	Transmitter Modulation

Bit 7 of the SET TRANSMITTER PARAMETERS directive shall contain the transmission modulation options:

a)	‘1’ = Non-coherent PSK;

b)	‘0’ = Coherent PSK.

A1.2.3.5	Transmitter Data Rate

A1.2.3.5.1	Bits 3–6 of the SET TRANSMITTER PARAMETERS directive shall contain one of the following transmission data rates (rates in kbps, i.e., powers of 10).

NOTE	–	Because of the NASA Mars Surveyor Project 2001 Odyssey implementation, there is an added constraint on the use of the values in the Data Rate field for 8, 32, 128, 256 Kbps.  Data rate selection is linked to the modulation field value as shown in the tables below.  NC indicates non-coherent PSK, and C indicates coherent PSK.  R1 through R4 indicate the field is reserved for future definition by the CCSDS.

A1.2.3.5.2	Ordered by Data Rate:

| ‘1000’ | ‘1001’ | ‘0000’ | ‘0001’ | ‘1100’ | ‘0010’ | ‘0011’ | ‘1101’ | ‘0100’ | ‘0101’ | ‘0110’ | ‘0111’ | ‘1010’ | ‘1011’ | ‘1110’ | ‘1111’ |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2 | 4 | 8 NC | 8 C | 16 | 32 NC | 32 C | 64 | 128 NC | 128 C | 256 NC | 256 C | R1 | R2 | R3 | R4 |

A1.2.3.5.3	Ordered by Bit pattern:

| ‘0000’ | ‘0001’ | ‘0010’ | ‘0011’ | ‘0100’ | ‘0101’ | ‘0110’ | ‘0111’ | ‘1000’ | ‘1001’ | ‘1010’ | ‘1011’ | ‘1100’ | ‘1101’ | ‘1110’ | ‘1111’ |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 8 NC | 8 C | 32 NC | 32 C | 128 NC | 128 C | 256 NC | 256 C | 2 | 4 | R1 | R2 | 16 | 64 | R3 | R4 |

A1.2.3.6	Transmitter Mode

A1.2.3.6.1	Bits 0–2 of the SET TRANSMITTER PARAMETERS directive shall contain the Transmitter Mode options. This field identifies the protocol utilized by the transmitter:

‘000’ = Reserved by CCSDS;

‘001’ = Proximity-1 Protocol;

‘010’ through ‘111’ = Reserved by CCSDS.

Note: See Annex C for NASA Mars Survey Project 2001 Odyssey Orbiter Transmitter Mode values.

A1.4.2.2	The three-bit Directive Type field shall identify the type of protocol control directive and shall contain the binary value ‘010’ for the SET RECEIVER PARAMETERS directive.

A1.4.3	Receiver Frequency

A1.4.3.1	General

Bits 10–12 of the SET Receiver PARAMETERS directive shall be used to set the Receiver frequency of the partnered transceiver to the desired value.

A1.4.3.2	Forward Receive Frequency (e.g., Orbiter as Initiator; Landed Asset as Responder)

In the context of the forward link, this three-bit field shall define the receive frequency of the Responder.  Actual frequency assignments are given in the Physical layer (see reference [9]).

| ‘000’ | ‘001’ | ‘010’ | ‘011’ | ‘100’ | ‘101’ | ‘110’ | ‘111’ |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Ch0F | Ch1F | Ch2F | Ch3F | Ch4F | Ch5F | Ch6F | Ch7F |

A1.4.4	Receiver Data Decoding

Bits 8–9 of the SET RECEIVER PARAMETERS directive shall contain the following coding options:

‘00’ = Reserved;

‘01’ = Convolutional Code(7,1/2) (G2 vector inverted) with attached CRC-32 (see reference [Error! Reference source not found.]);

‘10’ = By-pass Convolutional Code;

‘11’ = Concatenated RS(204,188), CC(7,1/2).

NOTE	–	RS(204,188) with CC(7,1/2) code is an ETSI standard.  This option is not required for cross support.  See reference [F1] for more details.

A1.4.5	Receiver Modulation

Bit 7 of the SET RECEIVER PARAMETERS directive shall contain the following transmission modulation options:

a)	‘1’ = Non-coherent PSK;

b)	‘0’ = Coherent PSK.

Page A-8

A1.4.6	Receiver Data Rate

A1.4.6.1	Bits 3–6 of the SET receiver PARAMETERS directive shall contain one of the following receiver data rates (rates in kbps, i.e., powers of 10).

NOTE	–	Because of the NASA Mars Surveyor Project 2001 Odyssey implementation, there is an added constraint on the use of the values in the Data Rate field for 8, 32, 128, and 256 Kbps.  Data rate selection is linked to the modulation field value as shown in the tables below (‘NC’ indicates non-coherent, and c indicates coherent).  R1 through R4 indicates the field is reserved for future definition by the CCSDS.

A1.4.6.2	Ordered by Data Rate:

| ‘1000’ | ‘1001’ | ‘0000’ | ‘0001’ | ‘1100’ | ‘0010’ | ‘0011’ | ‘1101’ | ‘0100’ | ‘0101’ | ‘0110’ | ‘0111’ | ‘1010’ | ‘1011’ | ‘1110’ | ‘1111’ |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2 | 4 | 8 NC | 8 C | 16 | 32 NC | 32 C | 64 | 128 NC | 128 C | 256 NC | 256 C | R1 | R2 | R3 | R4 |

A.1.4.6.3	Ordered by Bit pattern:

| ‘0000’ | ‘0001’ | ‘0010’ | ‘0011’ | ‘0100’ | ‘0101’ | ‘0110’ | ‘0111’ | ‘1000’ | ‘1001’ | ‘1010’ | ‘1011’ | ‘1100’ | ‘1101’ | ‘1110’ | ‘1111’ |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 8 NC | 8 C | 32 NC | 32 C | 128 NC | 128 C | 256 NC | 256 C | 2 | 4 | R1 | R2 | 16 | 64 | R3 | R4 |

A1.4.7	Receiver Mode

Bits 0–2 of the SET RECEIVER PARAMETERS directive shall contain the Receiver Mode options.   This field identifies the protocol utilized by the receiver:

‘000’ = Reserved by CCSDS;

‘001’ = Proximity-1 Protocol;

‘010’ through ‘111’ = Reserved by CCSDS.

Note: See Annex C for NASA Mars Survey Project 2001 Odyssey Orbiter Receiver Mode values.

A1.5	SET V(R) directive

A1.5.1	General

The SET V(R) directive shall consist of three fields, positioned contiguously in the following sequence (described from least significant bit, bit 15, to most significant bit, bit 0):

- Directive Type (3 bits);

- Spare (5 bits);

- Receiver Frame Sequence Number (SEQ_CTRL_FSN) (8 bits).

Page A-9

A1.8.10	Frequency Table

A1.8.10.1	General

Bit 1 of the SET PL EXTENSIONS directive shall indicate what set of frequencies shall be used:

a)‘0’ = Channels 0 – 7 defined in the Frequency Field of the Set Transmitter Parameters and Set Receiver Parameters Directives and specifically in the Proximity-1 Physical layer;

b)‘1’ = Channels 8 – 15 defined in the Extended Physical Layer Frequency Set defined below.

A1.8.10.2	Forward Link (e.g., Orbiter as Initiator; Landed Asset as Responder)

In the context of the forward link, this three-bit field shall define the receive frequency of the Responder.  Actual frequency assignments are given in the Physical layer (see reference [9]).

| ‘000’ | ‘001’ | ‘010’ | ‘011’ | ‘100’ | ‘101’ | ‘110’ | ‘111’ |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Ch8F | Ch9F | Ch10F | Ch11F | Ch12F | Ch13F | Ch14F | Ch15F |

A1.8.10.3	Return Link (e.g., Orbiter as Initiator; Landed Asset as Responder)

In the context of the return link, this three-bit field shall define the transmit frequency of the Responder.  Actual frequency assignments are given in the Physical layer (see reference [9]).

| ‘000’ | ‘001’ | ‘010’ | ‘011’ | ‘100’ | ‘101’ | ‘110’ | ‘111’ |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Ch8R | Ch 9R | Ch10R | Ch11R | Ch12R | Ch13R | Ch14R | Ch15R |

A1.8.11	Direction

Bit 0 of the SET PL EXTENSIONS directive shall indicate if the fields in this directive apply to the transmit or receive side of the transceiver.

- ‘0’ =  Transmit side;

- ‘1’ = Receive side.

Page A-17

From: Annex B (MIB Parameters)

| Hail_Wait_Duration | Mandatory. Used in the Hail persistent activity. Session static. See 6.2.4.11. | M |
| --- | --- | --- |
| Hailing_Channel | Mandatory. Channel assignment used in the Hail persistent activity during Link Establishment. Session static. See 6.2.4.15. | P,M |
| Hailing_Data_Rate | Mandatory. Data rate used in the Hail persistent activity during Link Establishment. Session static. See 6.2.4.16. | P,M |
| Interval_Clock | Mandatory. A frequency (e.g., 100 Hz) that is used for interval timing. Session static. See 6.3. | C |
| Local_Spacecraft_ID | Mandatory. Used as a frame validation check when Source-or-Destination ID equals source. Session static. See 3.2.2.9.3. | M |
| Maximum_Packet_Size | Mandatory if packets are used. Maximum size of a packet in octets. Used in the segmentation process. Session static. See 4.4.1.1. | I |
| Persistence_Wait_Time | Mandatory. Defines the maximum amount of time the initiating transceiver stays in persistence until either (1) it receives an acknowledgement from the remote transceiver that the Comm_Change was acted upon, or (2) the wait timer times out. See table 6-8, ‘Full Duplex Communication Change State Table’. | M |
| PLCW_Repeat | Mandatory. Used in COP-P. Session static. See 6.2.4.19. | D |
| Receive_Duration | Mandatory. Used in Half Duplex Data Services. Session static. See 6.2.4.18. | D |
| Remote_Spacecraft_ID | Mandatory. Used to address one or several remote spacecraft as opposed to the local spacecraft. Session dynamic. See 3.2.2.9.4. | F,M,D,I |
| Resync_Local | Mandatory. If Resync_Local equals false, it is the responsibility of the local controller to decide how synchronization will be re-established. Otherwise, if true, the Sender Node’s FOP-P forces synchronization by requesting a SET V(R) persistent activity. Session static. See 7.1.3.2, ‘SET V(R) Persistent Activity’. | D |
| Resync_Lifetime | Mandatory. Used in the FOP-P Set V(R) persistent activity. Session static. See 7.1.3.2. | M,D |
| Resync_Notification | Mandatory. Used in the FOP-P Set V(R) persistent activity. Session static. See 7.1.3.2. | M,D |
| Resync_Response | Mandatory. Used in the FOP-P Set V(R) persistent activity. Session static. See 7.1.3.2. | M,D |
| Resync_Waiting_Period | Mandatory. Used in the FOP-P Set V(R) persistent activity. Session static. See 7.1.3.2. | M,D |
| Send_Duration | Mandatory. Used in Half Duplex Data Services. Session static. See 6.2.4.17. | D |
| Synch_Timeout | Mandatory. Defines the value to which the SyncH_Timer is initialized or reinitialized. Session static. See 7.1.2. | D |
| Tail_Idle_Duration | Mandatory. Used in Full, Half Duplex, and Simplex session establishment. Session static. See 6.2.4.5. | M |
| Test_Source | Mandatory. Used in the verification of the spacecraft ID when the Source-or-Destination ID is source. Session static. See 6.2.4.2. | F |
| Transmission_Window | Mandatory. Sets the maximum size of the transmission window for the COP-P. Session static. See 7.1.3.3, note 3. | D |

C4.1	SET TRANSMITTER PARAMETERS Directive

C4.1.1	General

The SET TRANSMITTER PARAMETERS directive shall consist of six fields, positioned contiguously in the following sequence (described from least significant bit, bit 15, to most significant bit, bit 0):

- Set Directive Type (three bits);

- Transmitter Frequency (three bits);

- Transmitter Data Encoding (two bits);

- Transmitter Modulation (one bit);

- Transmitter Data Rate (four bits);

- Transmitter Mode (three bits).

NOTE	–	The structural components of the SET TRANSMITTER PARAMETERS directive are shown in figure Error! No text of specified style in document.-2.

| Bit 0 |  |  |  |  | Bit 15 |
| --- | --- | --- | --- | --- | --- |
| TX Mode 3 bits | TX Data Rate 4 bits | TX Modulation 1 bit | TX Data encoding 2 bits | TX Frequency 3 bits | Set Directive Type 3 bits |
| 0,1,2 | 3,4,5,6 | 7 | 8,9 | 10,11,12 | 13,14,15 |

Figure Error! No text of specified style in document.-2:  NASA Mars Surveyor Project 2001 Odyssey SET TRANSMITTER PARAMETERS Directive

C4.1.2	Set Directive Type

C4.1.2.1	Bits 13–15 of the SET TRANSMITTER PARAMETERS directive shall contain the Set Directive Type.

C4.1.2.2	The three-bit Set Directive Type field shall identify the type of protocol control directive and shall contain the binary value ‘000’ for the SET TRANSMITTER PARAMETERS directive.

C4.1.3	Transmitter Frequency

C4.1.3.1	Bits 10–12 of the SET TRANSMITTER PARAMETERS directive shall be used to set the transmitter frequency of the partnered transceiver to the desired value.

C4.1.3.2	This three-bit field shall contain the value ‘000’ indicating that the Responder’s transmit return frequency, 401.585625 MHz, shall be used.

C4.1.4	Transmitter Data Encoding

Bits 8–9 of the SET TRANSMITTER PARAMETERS directive shall contain the following coding options:

- ‘00’ = Scrambler;

- ‘01’ = Convolutional Code (7,1/2) without G2 inverter (CRC-32 attached);

- ‘10’ = By-pass Convolutional Code;

- ‘11’ = N/A.

C4.1.5	Transmitter Modulation

Bit 7 of the SET TRANSMITTER PARAMETERS directive shall contain the transmission modulation options:

a)	‘1’ = PSK;

b)	‘0’ = PSK Coherent.

C4.1.6	Transmitter Data Rate

Bits 3–6 of the SET TRANSMITTER PARAMETERS directive shall contain the transmission data rate.

| ‘0000’ | ‘0001’ | ‘0010’ | ‘0011’ | ‘0100’ | ‘0101’ | ‘0110’ | ‘0111’ | ‘1000’ | ‘1001’ | ‘1010’ | ‘1011’ | ‘1100’ | ‘1101’ | ‘1110’ | ‘1111’ |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 8 NC | 8 C | 32 NC | 32 C | 128 NC | 128 C | 256 NC | 256 C | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |

NOTE	–	Rates are in kbps, i.e., powers of 10; C indicates PSK coherent modulation, and NC indicates PSK non-coherent modulation.

C4.1.7	Transmitter Mode

C4.1.7.1	Bits 0–2 of the SET TRANSMITTER PARAMETERS directive shall contain the Transmission Mode options:

a)‘000’=Standby;

b)‘001’=Sequenced Controlled;

c)’010’=Expedited;

d)’011’=Unreliable Bit Stream;

e)‘100’=Tone Beacon

f) ‘101’=Canister Mode

C4.2	SET RECEIVER PARAMETERS Directive

C4.2.1	General

The SET RECEIVER PARAMETERS directive shall consist of six fields, positioned contiguously in the following sequence (described from least significant bit, bit 15, to most significant bit, bit 0):

- Set Directive Type (three bits);

- Receiver Frequency (three bits);

- Receiver Data Decoding (two bits);

- Receiver Modulation (one bit);

- Receiver Data Rate (four bits);

- Receiver Mode (three bits).

NOTE	–	The structural components of the SET RECEIVER PARAMETERS directive are shown in figure Error! No text of specified style in document.-3.

| Bit 0 |  |  |  |  | Bit 15 |
| --- | --- | --- | --- | --- | --- |
| RX Mode 3 bits | RX Rate 4 bits | RX Modulation 1 bit | RX Data Decoding 2 bits | RX Frequency 3 bits | Set Directive Type 3 bits |
| 0,1,2 | 3,4,5,6 | 7 | 8,9 | 10.11,12 | 13,14,15 |

Figure Error! No text of specified style in document.-3:  NASA Mars Surveyor Project 2001 Odyssey SET RECEIVER PARAMETERS Directive

C4.2.2	Set Directive Type

C4.2.2.1	Bits 13–15 of the SET RECEIVER PARAMETERS directive shall contain the Directive Type.

C4.2.2.2	The three-bit Set Directive Type field shall identify the type of protocol control directive and shall contain the binary value ‘010’ for the SET RECEIVER PARAMETERS directive.

C4.2.3	Receiver Frequency

C4.2.3.1	Bits 10–12 of the SET RECEIVER PARAMETERS directive shall be used to set the receiver frequency of the partnered transceiver to the desired value.

Page C-4

C4.2.3.2	This three-bit field shall contain the value ‘000’ indicating that the Responder’s receive forward frequency shall be set to 437.1 MHz.

C4.2.4	Receiver Data Decoding

Bits 8–9 of the SET RECEIVER PARAMETERS directive shall contain the following coding options:

a)	‘00’ = Scrambler;

b)	‘01’ = Convolutional Code (7,1/2) without G2 Inverter (CRC-32 attached);

c)	‘10’ = By-pass Convolutional Code;

d)	‘11’ = N/A.

C4.2.5	Receiver Modulation

Bit 7 of the SET RECEIVER PARAMETERS directive shall contain the transmission modulation options:

a)	‘1’ = PSK;

b)	‘0’ = PSK Coherent.

C4.2.6	Receiver Data Rate

Bits 3–6 of the SET RECEIVER PARAMETERS directive shall contain the Receiver Data Rate.

| ‘0000’ | ‘0001’ | ‘0010’ | ‘0011’ | ‘0100’ | ‘0101’ | ‘0110’ | ‘0111’ | ‘1000’ | ‘1001’ | ‘1010’ | ‘1011’ | ‘1100’ | ‘1101’ | ‘1110’ | ‘1111’ |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 8 NC | 8 C | 32 NC | 32 C | 128 NC | 128 C | 256 NC | 256 C | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |

NOTE	–	Rates are in kbps, i.e., powers of 10; C indicates PSK coherent modulation, and NC indicates PSK non-coherent modulation.

C4.2.7	Receiver Mode

Bits 0–2 of the SET RECEIVER PARAMETERS directive shall contain the Receiver Mode options:

a)‘000’=Standby;

b)‘001’=Sequenced Controlled;

c)’010’=Expedited;

d)’011’=Unreliable Bit Stream;

e)‘100’=Tone Beacon

#### Test_Source

The Test_Source parameter shall be used to determine whether the received frames whose Source-or-Destination IDs are set to source shall be tested for acceptance.  Test_Source=false means no test shall be performed.  Test_Source=true means a test shall be performed if the Receiving_SCID_Buffer is non-zero i.e., contains a valid SCID.  When the Receiving_SCID_Buffer is zero and Test_Source is true, the value of the SCID field in the header of the first received frame whose Source-or-Destination ID is source shall be loaded into Receiving_SCID_Buffer.

#### Carrier_Only_Duration

Carrier_Only_Duration represents the time that shall be used to radiate an unmodulated carrier at the beginning of a transmission.

#### Acquisition_Idle_Duration

Acquisition_Idle_Duration represents the time that shall be used to radiate the idle sequence pattern after carrier only to enable the receiving transceiver to achieve bit synchronization and decoder lock.

#### Tail_Idle_Duration

Tail_Idle_Duration represents the time that shall be used to radiate the idle sequence pattern at the end of a transmission to enable the receiving transceiver to process the last transmitted frame (i.e., push the data through the decoders).

#### Carrier_Loss_Timer_Duration

Carrier_Loss_Timer_Duration is the value loaded into the CARRIER_LOSS_TIMER based upon the conditions defined in 6.3.2 (CARRIER_LOSS_TIMER and Associated Events).

#### Comm_Change_Waiting_Period

Comm_Change_Waiting_Period represents the time that the caller will wait for the Comm_Change_Response to the Comm_Change directive.

#### Comm_Change_Response

The acknowledgement by the responder that the persistent activity has been accepted.  For the Full Duplex Comm_Change_Response see table 6-8, Events E17 and E20.  For the Half Duplex Comm_Change_Response, see table 6-11, Event E68.

Page 6-11

# Proximity-1 Timing Services

## 5.1	COUPLED NON-COHERENT PROXIMITY TIMING SERVICE

5.1.1	Timing Services are required for Proximity operations in order to provide the following three capabilities:

- on-board Proximity clock correlation between Proximity nodes;

- Universal Time Coordinated (UTC) time transfer to a Proximity node;

- coupled non-coherent time-derived ranging measurements between Proximity nodes.

5.1.2	All three of these capabilities require that MODE is active and the transceiver is operating in the Data Services sublayer.  Timing Services can occur in full duplex, half duplex, or simplex operations.

NOTE	–	Timing services can occur concurrently with other data-taking activities.  The method utilized to carry out the timing services is specified in 5.2.

## 5.2	Proximity Time correlation

### 5.2.1	Overview

The same time-tag capture method is used as the basis for all three time services capabilities.  The method requires that both the initiating and recipient transceiver shall have the capability of time tagging the trailing edge of the last bit of the Attached Synchronization Marker of every incoming and every outgoing Proximity frame.  This method allows for the simultaneous time tagging of transfer frames upon ingress to and egress from a Proximity transceiver (two-way) as well as one-way time tagging depicted in figure 5-1.  The time code format is provided in reference [Error! Reference source not found.], i.e., the unsegmented time code of 4 bytes of course time (> 1 sec) and 3 bytes of fine time (< 1 sec).  See figure Error! Reference source not found., Proximity Time Tagging and Time Correlation.

### 5.2.2	time TAG capture method

The time tag capture method shall be composed of the following steps:

- The vehicle controller shall issue a SET CONTROL PARAMETERS (local time tag) directive to the initiating transceiver, instructing it to capture its local time reference and associated frame sequence numbers over a commanded interval of frames.  Upon receipt of this directive, the MAC sublayer shall set the Time_Collection variable from inactive to collecting data, indicating that time collection has started.

- The initiating transceiver shall build and transmit the SET CONTROL PARAMETERS (Time Sample) directive.  Upon egress of each frame during the commanded interval (based upon the value of Time Sample), the initiating transceiver shall capture the

time and frame sequence number of every Proximity frame being radiated.  The application processes, which use the collected data, will also require information about any internal signal path delays associated with the radiation process.  Once the commanded interval has been reached (the prescribed number of frame time tags have been captured), the MAC sublayer shall set the Time_Collection variable to collection complete, indicating that those times and sequence numbers are available for transfer.  Coincidently upon receipt of the SET CONTROL PARAMETERS directive, the recipient transceiver shall identify and decode the directive and capture the subsequent time and frame sequence number of every Proximity frame received over the commanded interval.  The recipient transceiver shall also keep track of any internal signal path delays in the process.  Upon readout of the collected data set, Time_Collection shall be set to inactive.

- When the time collection process is completed, both the initiating and remote transceivers shall transfer their captured times, associated frame sequence numbers, and direction (indication of whether time tagging performed upon frame egress or ingress) of every transmitted and received Proximity-1 frame over the commanded interval to their respective vehicle controllers.

- The vehicle controller (CDS) shall create a Proximity time correlation packet consisting of the series of points (time tag, frame sequence number, direction) it received from its local transceiver collected over the commanded interval.  In addition, the internal signal path delays in the transmission and reception chains of the transceiver are required to be known a priori.

NOTES

- Time tag direction is labeled as either egress or ingress.

- The internal delays have coding and rate components.

- These time correlation packets need to be processed together.

- Simultaneous collections in both directions would increase the accuracy of the processing.

- By exchanging time correlation packets, either node can compute the correlation between the two Proximity clocks.

- The Report Request Directive (annex A) can be used to initiate a request to the remote transceiver to start up a time tag exchange.

- A separate TIME COLLECTION variable is required for two-way operations (simultaneous time tagging in both directions).

INFORMATIVE REFERENCES

(This annex is not part of the Recommendation.)

NOTE	–	The references in this annex define Physical layer techniques that are not part of the Proximity-1 Physical layer specification.  They are included here so that transceivers with an extended Physical Layer can interoperate.

[F1]	Digital Video Broadcasting (DVB); Framing Structure, Channel Coding, and Modulation for 11/12 GHz Satellite Services.  ETSI EN 300 421 V1.1.2 (1997-08). Valbonne:  ETSI, 1997.

[F2]	ITU-T Recommendations V.38, October 1996, “A 48/561/64 kbit/s Data Circuit-terminating Equipment Standardized for Use on Digital Point-to-Point Leased Circuits.”

[F3]	Performance Characteristics for Intermediate Data Rate Digital Carriers Using Convolutional Encoding/Viterbi Encoding and QPSK Modulation (QPSK/IDR) (Standard A, B, C, E and F Earth Stations).  Intelsat Earth Station Standard, IESS-308.  Rev. 10.  Washington, D.C.:  Intelsat, February 2000.

Page F-1