DRAFT RECOMMENDATION FOR SPACE

DATA SYSTEM STANDARDS

PROXIMITY-1 SPACE LINK PROTOCOL— DATA LINK LAYER

CCSDS 211.0-P-2.2

Pink Sheets

April 2004

AUTHORITY

|  | Issue: | Blue Book, Issue 2 |  |
| --- | --- | --- | --- |
|  | Date: | April 2003 |  |
|  | Location: | Matera, Italy |  |

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and represents the consensus technical agreement of the participating CCSDS Member Agencies.  The procedure for review and authorization of CCSDS Recommendations is detailed in Procedures Manual for the Consultative Committee for Space Data Systems, and the record of Agency participation in the authorization of this document can be obtained from the CCSDS Secretariat at the address below.

This Recommendation is published and maintained by:

CCSDS Secretariat

Office of Space Communication (Code M-3)

National Aeronautics and Space Administration

### Washington, DC  20546, USA

### Half Duplex Operations

Figure 6-2:  Half Duplex State Transition Diagram

Table 6-10:  Half Duplex Session Establishment and Data Services

| Event No. | Event Causing the Transition (Description) | Starting State (from) | Resulting State (to) | Action(s) in Addition to Tables 6-2, 6-4 and Comments |
| --- | --- | --- | --- | --- |
| E29 | Local Directive - Set Mode Connecting-L | S1 | S2 | - Set NEED_PLCW=true |
| E30 | HAIL Received | S2 | S51 | - WT=Carrier_Only_Duration - Set Receiver and Transmitter values per HAIL directives - Set Transmit = on - Send Hail_Notification to C&DH |
| E31 | Local Directive – Set Mode Connecting-T | S1 | S11 | - WT=Carrier_Only_Duration - Load HAIL directives to Comm Value Buffer - Set PERSISTENCE = true - Set Receiver Values per HAIL directive |
| E32 | WT=1 Carrier_Only_Duration Timeout | S11 | S12 | - WT=Acquisition_Idle_Duration - Set Modulation =on |
| E33 | WT=1 Acquisition_Idle_Duration Timeout | S12 | S13 | - Radiate HAIL |
| E34 | Output FIFO=empty | S13 | S14 | Hail Radiated - WT=Tail_Idle_Duration |
| E35 | WT=1 Tail_Idle_Duration Timeout | S14 | S36 | - WT=Hail_Wait_Duration - Set Modulation =off - Set Transmit = off |
| E36 | WT=1 Hail_Wait_Duration Timeout | S36 | S11 | - Set Transmit = on - WT=Carrier_Only_Duration - Set Load HAIL directives to Comm Value Buffer |
| E37 | Valid Transfer Frame Received (or BIT_INLOCK_STATUS = true)- implementation option See Hail_Response MIB parameter | S36 | S60 | - Set Transmitter values per Comm Value Buffer - Set PERSISTENCE=false (get ready for next transmit contact) - WT=Receive_Duration - Send Hail_Notification to C&DH |
| E38 | (Transmit Timer Event – End of Send Period) WT=1 Send_Duration Timeout | S50 | S50 | - Set PERSISTENCE=true Setting PERSISTENCE blocks the transmission of data from data services. Now only send from the MAC queue. Therefore, no frames pending will occur. |
| E39 | No Frames Pending.AND. Y=0 .AND. NEED_PLCW is false | S50 Y=0 | S56 | - Form and Load the Token via SET CONTROL PARAMETERS Directive into the MAC queue |
| E40 | WT=1 Carrier_Only_Duration Timeout | S51 | S52 | - WT=Acquisition_Idle_Duration - Set modulation=on |
| E41 | (End of Acquire) WT=1 Acquisition_Idle_Duration Timeout | S52 | S50 | - WT=Send_Duration |
| E42 | No Frames Pending (Y=0) | S56, Y=0 | S58 | - WT=Tail_Idle_Duration |
| E43 | WT=1 Tail_Idle_Duration Timeout .AND. Y(2 | S58 Y(2 | S62 | - WT=Receive_Duration - Set PERSISTENCE=false - Set Modulation =off - Switch transmit to receive |
| E44 | WT=1 Receive_Duration Timeout .AND. Carrier Lock=true | S60 | S60 | - WT=Receive_Duration - Notify vehicle controller: Sender exceeded prescribed transmission interval |
| E45 | WT=1 Receive_Duration Timeout .AND. Carrier Lock=true | S61 | S61 | - WT=Receive_Duration - Notify vehicle controller: No data transferred during contact period |
| E46 | Receive Valid frame .AND. Y(3 | S61 Y(3 | S60 |  |
| E47 | Carrier Lock = true | S62 | S61 |  |
| E48 | WT=1 Receive_Duration Timeout .AND. Carrier Lock = false | S60 | S51 | - WT=Carrier_Only_Duration back-up action for missed token - Switch receive to transmit |
| E49 | Receive Token - SET CONTROL PARAMETERS Directive | S60/S61 | S51 | - WT=Carrier_Only_Duration - Switch receive to transmit |
| E50 | WT=1 Receive_Duration Timeout .AND. Carrier Lock = false | S62 | S51 | - WT=Carrier_Only_Duration - Notify vehicle controller: No carrier received for contact period - Switch receive to transmit |
| NOTE – FOP-P Data operations occur within State 50 and are described in 7.1. FARM-P operations occur within States 60 and 61 are described in 7.2.1. |

Table 6-11:  Half Duplex Communication Change State Table

| Event No. | Event Causing the Transition (Description) | Starting State (from) | Resulting State (to) | Additional Action(s) and Comments |
| --- | --- | --- | --- | --- |
| E62 | Receive Local Comm_Change Directive (LCCD) | Any State other than State S50 Y=0=0 | No State Change Y=1 | - Load Set Transmitter/Set Receiver Parameters Directives values into Comm Value Buffer |
| E63 | Receive Local Comm_Change Directive (LCCD) | S50 | S50 Y=2 | - Set PERSISTENCE=true - Set Receiver Parameters from Comm Value Buffer |
| E64 | Transition to State 50 | Y=1 .OR. Y=3 | S50 Y=2 | - Set Y=2, Set PERSISTENCE=true - Set Receiver Parameters from Comm Value Buffer |
| E65 | No Frames Pending .AND. Y=2 | S50 Y=2 | S56 | - Form and load into the Comm Value Buffer the Comm_Change Directives |
| E66 | No Frames Pending | S56 Y=2 | S58 Y=2 | - WT=Tail_Idle_Duration Comm_Change Sent |
| E67 | WT=1 Tail_Idle_Duration Timeout .AND. Y=2 | S58 Y=2 | S62 Y=3 | -WT=Receive_Duration - Switch transmit to receive |
| E47 | Carrier Lock = true | S62 | S61 | Same event - provided for clarity |
| E68 | Receive Valid Frame | S61 Y=3 | S60 Y=0 | - Set Transmitter Parameters from Comm Value Buffer - Set Y=0 - PERSISTENCE=false |
| E69 | Receive Comm_Change (Not Shown in State Transition Diagram) | S60/S61 | S51 | - Set Transmitter & Receiver Parameters into Comm Value Buffer - Set NEED_PLCW=true |

Table 6-12:  Half Duplex Session Termination State Table

| Event No. | Event Causing the Transition (Description) | Starting State (from) | Resulting State (to) | Additional Action(s) and Comments |
| --- | --- | --- | --- | --- |
| E51 | Receive LNMD (can be received at any time) | X=0 | X=1 | - Set X=1 |
| E52 | Receive LNMD (can be received at any time) | X=3 | X=4 | - Set X=4 |
| E53 | No Frames Pending .AND. X=1 | S50 X=1 | S50 X=2 | - Form and Load RNMD into the MAC queue, - Set X=2 - Send RNMD |
| E55 | No Frames Pending .AND. X=4 | S50 X=4 | S54 X=5 | - Form and Load RNMD into the MAC queue, - Set X=5; Send RNMD |
| E56 | No Frames Pending .AND. X=5 | S54 X=5 | S55 X=0 | - WT=Tail_Idle_Duration - Set X=0 Transmission of RNMD complete |
| E57 | WT=1 Tail_Duration Timeout | S55 | S1 | - Set MODE Inactive - Notify vehicle controller: End of Session(# octets received) |
| E58 | Receive RNMD .AND. X=2 | S60/S61 X=2 | S1 X=0 | - Set MODE Inactive - Set X=0 Both nodes have no more data to send; Notify vehicle controller: End of Session(# octets received) |
| E59 | Receive RNMD .AND. X=0 | S60/S61 X=0 | S51 X=3 | - Set X=3 WT = Carrier_Duration_Only |
| E60 | Receive RNMD .AND. X=1 | S60/S61 X=1 | S51 X=4 | - Set X=4 WT = Carrier_Duration_Only |
| E61 | Receive a Local Set Mode Inactive directive | any | S1 | - SET MODE Inactive - Notify vehicle controller: End of Session(# octets received) Not shown on Half Duplex State Transition Diagram |