FOP-P State Diagram

Startup:

Initialize internal variables and enter state S1

While in state S1:

Frame sublayer is ready to send a frame

- Send highest-priority frame (if any).  Expedited frames take priority over retransmissions which take priority over new Sequence-controlled, etc

- Stay in state S1

Valid PLCW received

- Respond to feedback (e.g. initiate retransmission if requested)

- Clear Synch-timer

- Stay in state S1

Invalid PLCW received

- Start Synch-timer

- Stay in state S1

Synch-timer expired

- Report this problem to the vehicle controller

- If local-resync is enabled, send a “Set V(R)” directive to the FARM-P (i.e. request a resync), and go to state S2

While in state S2:

Valid PLCW received

- If the feedback indicates a resync of the FARM-P, go to state S1

- Otherwise, stay in state S2

Reset Request received

- Re-initialize and go to state S1

FARM-P State Diagram

Startup:

Initialize internal variables and enter state S1.

While in state S1:

(There is only one state, so no state changes occur)

Invalid frame received

- Discard it

Expedited frame received

- Accept it.

Sequence-controlled frame received in sequence

- Accept it.

- Update PLCW (frame accepted; no retransmission needed)

Sequence-controlled frame received out-of-sequence (“skips ahead”)

- Discard it

- Update PLCW (retransmission needed)

Sequence-controlled frame received out-of-sequence (“duplicate”)

- Discard it