Here is the essence of the proposal to change the signaling Field to augment the VC frame counter by a factor of up to 16:

Figure 4-2:  Transfer Frame Primary Header

Virtual Channel Frame Count Use Flag (1bit, mandatory)

0 = VC Frame Count Cycle Field NOT used;

1 = VC Frame Count Cycle Field used;

Reserved Spares (2 bits, mandatory)

Set to ‘00’;

Virtual Channel Frame Count Cycle (4 bits, optional)

If not used, set to ‘0000’;

If used, modulo 16 counter, used to extend the virtual channel frame count field.