Draft Recommendation for 
Space Data System Standards

Space Link Identifiers

Draft Recommended Standard

CCSDS 135.0-BP-2.2

BLUE BOOKPink Sheets

November 2005June 2006

AUTHORITY

|  | Issue: | Pink Sheets, Issue 2.1 |  |
| --- | --- | --- | --- |
|  | Date: | June 2006 |  |
|  | Location: | Washington, DC, USA |  |

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and represents the consensus technical agreement of the participating CCSDS Member Agencies.  The procedure for review and authorization of CCSDS Recommendations is detailed in the Procedures Manual for the Consultative Committee for Space Data Systems, and the record of Agency participation in the authorization of this document can be obtained from the CCSDS Secretariat at the address below.

This Recommendation is published and maintained by:

CCSDS Secretariat

Office of Space Communication (Code M-3)

National Aeronautics and Space Administration

Washington, DC  20546, USA

STATEMENT OF INTENT

The Consultative Committee for Space Data Systems (CCSDS) is an organization officially established by the management of its members. The Committee meets periodically to address data systems problems that are common to all participants, and to formulate sound technical solutions to these problems. Inasmuch as participation in the CCSDS is completely voluntary, the results of Committee actions are termed Recommended Standards and are not considered binding on any Agency.

This Recommended Standard is issued by, and represents the consensus of, the CCSDS members.  Endorsement of this Recommendation is entirely voluntary. Endorsement, however, indicates the following understandings:

o	Whenever a member establishes a CCSDS-related standard, this standard will be in accord with the relevant Recommended Standard. Establishing such a standard does not preclude other provisions which a member may develop.

o	Whenever a member establishes a CCSDS-related standard, that member will provide other CCSDS members with the following information:

--	The standard itself.

--	The anticipated date of initial operational capability.

--	The anticipated duration of operational service.

o	Specific service arrangements shall be made via memoranda of agreement. Neither this Recommended Standard nor any ensuing standard is a substitute for a memorandum of agreement.

No later than five years from its date of issuance, this Recommended Standard will be reviewed by the CCSDS to determine whether it should: (1) remain in effect without change; (2) be changed to reflect the impact of new technologies, new requirements, or new directions; or (3) be retired or canceled.

In those instances when a new version of a Recommended Standard is issued, existing CCSDS-related member standards and implementations are not negated or deemed to be non-CCSDS compatible.  It is the responsibility of each member to determine when such standards or implementations are to be modified.  Each member is, however, strongly encouraged to direct planning for its new standards and implementations towards the later version of the Recommended Standard.

FOREWORD

This document is a technical Recommendation for use in developing flight and ground systems for space missions and has been prepared by the Consultative Committee for Space Data Systems (CCSDS).

This Recommendation documents the identifiers used by the space link protocols developed by CCSDS, shows how these identifiers are managed, and lists the identifiers that are defined or reserved by CCSDS as part of the specification of the space link protocols.

Through the process of normal evolution, it is expected that expansion, deletion or modification to this document may occur.  This Recommendation is therefore subject to CCSDS document management and change control procedures, as defined in reference [B1].  Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be addressed to the CCSDS Secretariat at the address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- British National Space Centre (BNSC)/United Kingdom.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- Deutsches Zentrum für Luft- und Raumfahrt e.V.  (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (Roskosmos)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- Centro Tecnico Aeroespacial (CTA)/Brazil.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- Danish Space Research Institute (DSRI)/Denmark.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Korea Aerospace Research Institute (KARI)/Korea.

- MIKOMTEK:  CSIR (CSIR)/Republic of South Africa.

- Ministry of Communications (MOC)/Israel.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic & Atmospheric Administration (NOAA)/USA.

- National Space Program Office (NSPO)/Taipei.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- United States Geological Survey (USGS)/USA.

DOCUMENT CONTROL

| Document | Title and Issue | Date | Status |
| --- | --- | --- | --- |
| CCSDS 135.0-B-1 | Space Link Identifiers, Issue 1 | January 2002 | Original issue (superseded) |
| CCSDS 135.0-P-2.1 | Space Link Identifiers, Draft Recommended Standard, Issue 2.1 | June 2006 | Current issue |

CONTENTS

Section	Page

1	Introduction	1-1

1.1	Purpose	1-1

1.2	Scope	1-1

1.3	Applicability	1-1

1.4	Rationale	1-1

1.5	Document Structure	1-1

1.6	DEFINITIONS	1-2

1.7	References	1-2

2	MANAGEMENT OF SPACE LINK IDENTIFIERS	2-1

2.1	General	2-1

2.2	IDENTIFIERS Defined by CCSDS	2-1

2.3	IDENTIFIERS Assigned by CCSDS	2-2

2.4	IDENTIFIERS Managed by individual projects	2-2

3	IDENTIFIERS used by CCSDS File Delivery Protocol (CFDP)	3-1

4	IDENTIFIERS used by SCPS-TP	4-1

5	IDENTIFIERS used by Space PaCKET Protocol	5-1

5.1	APPLICATION PROCESS IDENTIFIER	5-1

5.2	RESERVED APPLICATION PROCESS IDENTIFIERS	5-1

6	IDENTIFIERS used by SCPS-NP	6-1

7	IDENTIFIERS used by SPACE DATA LINK PROTOCOLS	7-1

7.1	GENERAL	7-1

7.2	DEFINED TRANSFER FRAME VERSION NUMBERS	7-2

7.3	RESERVED VIRTUAL CHANNEL IDENTIFIERS	7-2

7.4	DEFINED FRAME SECONDARY HEADER VERSION NUMBERS	7-3

7.5	DEFINED CLCW VERSION NUMBERS	7-3

7.6	DEFINED PACKET VERSION NUMBERS	7-4

7.7	DEFINED PROTOCOL IDENTIFIERS	7-4

7.8	Reserved Proximity-1 Port Identifiers	7-5

CONTENTS (continued)

Section	Page

ANNEX A	ACRONYMS	A-1

ANNEX B	INFORMATIVE REFERENCES	B-1

ANNEX C	LOCATION OF PACKET LENGTH FIELD	C-1

Table	Page

3-1	Identifier Used by CCSDS File Delivery Protocol	3-1

4-1	Identifier Used by SCPS-TP	4-1

5-1	Identifier Used by Space Packet Protocol	5-1

5-2	Reserved Application Process Identifiers	5-1

6-1	Identifiers Used by SCPS-NP	6-1

7-1	Identifiers Used by Space Data Link Protocols	7-1

7-2	Defined Transfer Frame Version Numbers	7-2

7-3	Reserved Virtual Channel Identifiers (AOS Space Data Link Protocol Only)	7-2

7-4	Defined Frame Secondary Header Version Numbers	7-3

7-5	Defined CLCW Version Numbers	7-3

7-6	Defined Packet Version Numbers	7-4

7-7	Defined Protocol Identifiers	7-5

7-8a	Proximity-1 Port ID Assignments for the Forward Link for Both Physical Channels	7-6

7-8b	Proximity-1 Port ID Assignments for the Return Link for Both Physical Channels	7-6

C-1	Location of Packet Length Field	C-1

# Introduction

## Purpose

The purpose of this Recommendation is to document the identifiers used by the space link protocols developed by CCSDS, to show how these identifiers are managed, and to list the identifiers that are defined or reserved by CCSDS as part of the specification of the space link protocols.

## Scope

This Recommendation documents the identifiers currently used by the space link protocols and shows how these identifiers are managed at the CCSDS level.  It does not specify how these identifiers are managed in individual data systems of space projects.

## Applicability

This Recommendation constitutes provisions of the CCSDS Recommendations that refer to this Recommendation as a normative reference, to the extent that is specified in those Recommendations.

## Rationale

The goal of this Recommendation is to enable management of identifiers used by the space link protocols independently of management of protocol specifications themselves.

## Document Structure

This document is divided into seven numbered sections and four annexes:

- section 1 presents the purpose, scope, applicability and rationale of this Recommendation and lists the definitions and references used throughout the document;

- section 2 summarizes the methods used for managing space link identifiers;

- sections 3 through 7 list the identifiers used by each of the space link protocols, show how these identifiers are managed, and list the identifiers that are defined or reserved by CCSDS;

- annex A lists all acronyms used within this document;

- annex B provides a list of informative references;

- annex C summarizes the location of the length field of the packets for which Packet Version Numbers are defined by CCSDS.

## DEFINITIONS

For the purposes of this Recommendation, the following definitions apply.  Many other terms that pertain to specific items are defined in the appropriate sections.

Assigned by CCSDS: values of the identifier are assigned by CCSDS upon request by Agencies.

Defined by CCSDS: values of the identifier are defined by CCSDS as part of the specification of protocol.

Managed by projects: values of the identifier are managed independently by the projects that use the protocol.

space link:  a communications link between a spacecraft and its associated ground system, or between two spacecraft.

space link protocol: a communications protocol designed to be used over a space link (see above).  A space link protocol is not necessarily a protocol of the Data Link Layer of the OSI Basic Reference Model (reference [1]).

## References

The following documents contain provisions which, through reference in this text, constitute provisions of this Recommendation.  At the time of publication, the editions indicated were valid.  All documents are subject to revision, and users of this Recommendation are encouraged to investigate the possibility of applying the most recent editions of the documents indicated below.  The CCSDS Secretariat maintains a register of currently valid CCSDS Recommendations.

[1]	Information Technology—Open Systems Interconnection—Basic Reference Model: The Basic Model.  International Standard, ISO/IEC 7498-1.  2nd ed.  Geneva:  ISO, 1994.

[2]	Lossless Data Compression.  Recommendation for Space Data Systems Standards, CCSDS 121.0-B-1.  Blue Book.  Issue 1.  Washington, D.C.:  CCSDS, May 1997.

[3]	Space Communications Protocol Specification—File Protocol (SCPS-FP). Recommendation for Space Data Systems Standards, CCSDS 717.0-B-1.  Blue Book.  Issue 1.  Washington, D.C.: CCSDS, May 1999.

[4]	CCSDS File Delivery Protocol (CFDP).  Recommendation for Space Data System Standards, CCSDS 727.0-B-3.  Blue Book.  Issue 3.  Washington, D.C.: CCSDS, June 2005.

[5]	Space Communications Protocol Specification—Transport Protocol (SCPS-TP). Recommendation for Space Data Systems Standards, CCSDS 714.0-B-1.  Blue Book.  Issue 1.  Washington, D.C.: CCSDS, May 1999.

[6]	Space Packet Protocol.  Recommendation for Space Data System Standards, CCSDS 133.0-B-1.  Blue Book.  Issue 1.  Washington, D.C.: CCSDS, September 2003.

[7]	Space Communications Protocol Specification—Network Protocol (SCPS-NP). Recommendation for Space Data Systems Standards, CCSDS 713.0-B-1.  Blue Book.  Issue 1.  Washington, D.C.: CCSDS, May 1999.

[8]	TM Space Data Link Protocol.  Recommendation for Space Data System Standards, CCSDS 132.0-B-1.  Blue Book.  Issue 1.  Washington, D.C.: CCSDS, September 2003.

[9]	TC Space Data Link Protocol.  Recommendation for Space Data System Standards, CCSDS 232.0-B-1.  Blue Book.  Issue 1.  Washington, D.C.: CCSDS, September 2003.

[10]	AOS Space Data Link Protocol.  Recommendation for Space Data System Standards, CCSDS 732.0-B-1.  Blue Book.  Issue 1.  Washington, D.C.: CCSDS, September 2003.

[11]	Proximity-1 Space Link Protocol—Data Link Layer.  Recommendation for Space Data System Standards, CCSDS 211.0-B-3.  Blue Book.  Issue 3.  Washington, D.C.: CCSDS, May 2004.

[12]	CCSDS Global Spacecraft Identification Field Code Assignment Control Procedures.  Recommendation for Space Data System Standards, CCSDS 320.0-B-3.  Blue Book.  Issue 3.  Washington, D.C.: CCSDS, April 2003.

[13]	Encapsulation Service.  Draft Recommendation for Space Data System Standards, CCSDS 133.1-R-4.  Red Book.  Issue 4.  Washington, D.C.: CCSDS, September 2005.

[14]	TM Synchronization and Channel Coding.  Recommendation for Space Data System Standards, CCSDS 131.0-B-1.  Blue Book.  Issue 1.  Washington, D.C.: CCSDS, September 2003.

[15]	TC Synchronization and Channel Coding.  Recommendation for Space Data System Standards, CCSDS 231.0-B-1.  Blue Book.  Issue 1.  Washington, D.C.: CCSDS, September 2003.

[16]	Information Technology—Protocol for Providing the Connectionless-Mode Network Service: Protocol Specification.  International Standard, ISO/IEC 8473-1:1998.  2nd ed.  Geneva:  ISO, 1998.

[17]	J. Postel.  Internet Protocol.  STD 5, September 1981.  [RFC 791, RFC 950, RFC 919, RFC 922, RFC 792, RFC 1112]

[18]	S. Deering and R. Hinden.  Internet Protocol, Version 6 (IPv6) Specification. Draft Internet Standard, December 1998. [RFC 2460]

NOTE	–	Informative references are listed in annex B.

# MANAGEMENT OF SPACE LINK IDENTIFIERS

## General

The space link protocols developed by CCSDS use identifiers to identify protocols, addresses, and data formats.  Even though some of these identifiers are defined in the Recommendations that specify the protocols, management of identifiers should be performed independently of management of protocol specifications so that values of the identifiers can be defined (or re-defined) without changing the protocol specifications themselves.

With the aim described above, this document lists the identifiers currently used by the space link protocols developed by CCSDS, shows how these identifiers are managed, and lists the identifiers that are defined or reserved by CCSDS as part of the specification of the space link protocols.

NOTE	–	Since no identifier is used by the following CCSDS space link protocols, these protocols are not included in the following sections.

- Lossless Data Compression (reference [2]);

- SCPS-FP (reference [3]);

- TM Synchronization and Channel Coding (reference [14]);

- TC Synchronization and Channel Coding (reference [15]).

Each identifier is managed by one of the three methods listed below depending on its characteristics:

- defined by CCSDS as part of protocol specification;

- assigned by CCSDS upon request by Agencies;

- managed by individual projects.

The following subsections briefly describe these management methods.

## IDENTIFIERS Defined by CCSDS

The values of some identifiers are defined by CCSDS as part of the specification of protocols.  This method for managing identifiers is denoted ‘Defined by CCSDS’ in this document.

The values of the identifiers of this category that are currently defined by CCSDS are listed in the following sections of this document.

## IDENTIFIERS Assigned by CCSDS

The values of some identifiers are assigned by CCSDS upon request by Agencies. This method for managing identifiers is denoted ‘Assigned by CCSDS’ in this document.

The procedure for assigning values of each of the identifiers of this category is defined by a separate CCSDS Recommendation, which is referred to in the following sections of this document.

## IDENTIFIERS Managed by individual projects

The values of some identifiers are managed independently by the projects that use the protocols.  CCSDS does not specify how to manage these identifiers.  This method for managing identifiers is denoted ‘Managed by projects’ in this document.

Some values of the identifiers in this category may be reserved by CCSDS to be used for some specific purposes across Agencies.  The values of the identifiers reserved by CCSDS are listed in the following sections of this document.

## Security aspects of the Space Link Identifiers

### Security Background/introduction

The Space Link Identifiers Blue Book documents the identifiers used by the CCSDS space link protocols, CFDP, SCPS-TP and SCPS-NP, CCSDS space packet protocol, and the CCSDS encapsulation service.  It documents how these identifiers are managed and provides a list of these identifiers along with their defined and/or reserved values.

### Statements of security concerns

#### General

This subsection identifies Space Link Identifiers support for capabilities responding to security concerns in the areas of data privacy, data integrity, authentication, access control, availability of resources, and auditing.

#### Data Privacy (also known as Confidentiality)

This Space Link Identifiers specification does not define explicit data privacy requirements or capabilities to ensure data privacy. Data privacy is expected to be ensured either by encryption techniques applied at the data link layer or at a higher layer. For example, mission application processes might apply end-to-end encryption to the contents of the CCSDS space link data units carried as data by the applicable CCSDS data transfer service. Alternatively or in addition, the network connection between communicating entities might be encrypted to provide data privacy in the underlying communication network.

#### Data Integrity

The Space Link Identifiers specification does not define explicit data integrity requirements or capabilities to ensure data integrity.  See the individual protocol specifications listed in the References subsection (1.7) for such requirements.

#### Authentication

The Space Link Identifiers specification does not define explicit data integrity requirements or capabilities to ensure data integrity.  See the individual protocol specifications listed in the References subsection (1.7) for such requirements.

#### Access Control

The Space Link Identifiers specification does not define access control requirements or capabilities for access control.  See the individual protocol specifications listed in the References subsection (1.7) for such requirements.

#### Availability of Resources

This Space Link Identifiers specification does not define explicit capabilities to prevent denial of service. See the individual protocol specifications listed in the References subsection (1.7) for such requirements.

#### Auditing

This Space Link Identifiers specification does not define explicit security auditing requirements or capabilities.

### potential threats and attack scenarios

The Space Link Identifiers specification does not define potential threats and attack scenarios.

### Consequences of not applying security

The consequences of not applying security to the list of protocols whose identifiers are defined in the Space Link Identifiers Blue book is an issue covered by each individual protocol specification.

# IDENTIFIERS used by CCSDS File Delivery Protocol (CFDP)

Table 3-1 shows the identifier used by the CCSDS File Delivery Protocol (CFDP) (reference [4]) and how it is managed.

Table 3-1:  Identifier Used by CCSDS File Delivery Protocol

| Identifier | Management Method | Note |
| --- | --- | --- |
| Entity ID | Managed by projects | No value is reserved |

# IDENTIFIERS used by SCPS-TP

Table 4-1 shows the identifier used by SCPS-TP (reference [5]) and how it is managed.

Table 4-1:  Identifier Used by SCPS-TP

| Identifier | Management Method | Note |
| --- | --- | --- |
| Connection Identifier | Managed by projects | No value is reserved |

# IDENTIFIERS used by Space PaCKET Protocol

## APPLICATION PROCESS IDENTIFIER

Table 5-1 shows the identifier used by the Space Packet Protocol (reference [6]) and how it is managed.

Table 5-1:  Identifier Used by Space Packet Protocol

| Identifier | Management Method | Note |
| --- | --- | --- |
| Application Process Identifier (APID) | Managed by projects | See 5.2 for reserved values |

## RESERVED APPLICATION PROCESS IDENTIFIERS

Some values of the Application Process Identifier (APID) defined by the Space Packet Protocol (reference [6]) are reserved by CCSDS for special uses.  Table 5-2 lists the APIDs currently reserved by CCSDS.

Table 5-2:  Reserved Application Process Identifiers

| APID (decimal) | Utilization | Reference |
| --- | --- | --- |
| 2040 - 2044 | Reserved for possible future use |  |
| 2045 | CFDP | [4] |
| 2046 | ISO 8473 | [16] |
| 2047 | Idle Packet | [6] |

# IDENTIFIERS used by SCPS-NP

Table 6-1 shows the identifiers used by SCPS-NP (reference [7]) and how they are managed.

Table 6-1:  Identifiers Used by SCPS-NP

| Identifier | Management Method | Note |
| --- | --- | --- |
| Domain Identifier (D-ID) | Assigned by CCSDS | See NOTE below the table |
| End System Identifier (ES-ID) | Managed by projects | No value is reserved |
| Path Identifier (P-ID) | Managed by projects | No value is reserved |
| Transport Protocol Identifier (TP-ID) | Defined by CCSDS | See table 3-2 of reference [7] for defined values |

NOTE	–	No procedure is defined for assigning values of the Domain Identifier.  If SCPS-NP is intended to be used globally, one must be developed.

# IDENTIFIERS used by SPACE DATA LINK PROTOCOLS

## GENERAL

Table 7-1 shows the identifiers used by the Space Data Link Protocols (references [8]-[10]) and Proximity-1 Space Link Protocol (reference [11]), and how they are managed.

Table 7-1:  Identifiers Used by Space Data Link Protocols

| Identifier | Used by | Management Method | Note |
| --- | --- | --- | --- |
| Transfer Frame Version Number | TM [8], TC [9], AOS [10], Prox [11] | Defined by CCSDS | See 7.2 for defined values |
| Spacecraft Identifier (SCID) | TM [8], TC [9], AOS [10], Prox [11] | Assigned by CCSDS | See reference [12] for assignment procedure |
| Virtual Channel Identifier (VCID) | TM [8], TC [9], AOS [10], Prox [11] | Managed by projects | See 7.3 for reserved values |
| Frame Secondary Header Version Number | TM [8] | Defined by CCSDS | See 7.4 for defined values |
| MAP Identifier (MAP ID) | TC [9] | Managed by projects | No value is reserved |
| Port Identifier (Port ID) | Prox [11] | Managed by projectsDefined by CCSDS | No value is reservedSee tables 7-8a and 7-8b for defined values |
| CLCW Version Number | TC [9] | Defined by CCSDS | See 7.5 for defined values |
| Packet Version Number | TM [8], TC [9], AOS [10], Prox [11] | Defined by CCSDS | See 7.6 for defined values |
| Protocol Identifier | Encapsulation Packet [13] | Defined by CCSDS | See 7.7 for defined values |

## DEFINED TRANSFER FRAME VERSION NUMBERS

In the Transfer Frames defined by the Space Data Link Protocols (references [8]-[10]) and Proximity-1 Space Link Protocol (reference [11]), there is a field called the Transfer Frame Version Number to identify the Transfer Frame.  This is a two-bit field and its values are defined by CCSDS as part of the protocol specifications.

Table 7-2 lists the Transfer Frame Version Numbers currently defined by CCSDS.

Table 7-2:  Defined Transfer Frame Version Numbers

| Version Number | Binary Encoded Version Number | Transfer Frame | Reference |
| --- | --- | --- | --- |
| 1 | 00 | TM Transfer Frame | [8] |
| 1 | 00 | TC Transfer Frame | [9] |
| 2 | 01 | AOS Transfer Frame | [10] |
| 3 | 10 | Version 3 Transfer Frame | [11] |

NOTES

- Version Number ‘1’ is assigned to both TM Transfer Frame and TC Transfer Frame.  These two Transfer Frames are distinguished by the Attached Sync Marker defined in reference [14] or the Start Sequence defined in reference [15].

- In the field of Transfer Frame Version Number in the Transfer Frames, the Binary Encoded Version Number listed above must be used.

## RESERVED VIRTUAL CHANNEL IDENTIFIERS

A value of the Virtual Channel Identifier (VCID) is reserved by CCSDS for special use in the AOS Space Data Link Protocol (reference [10]).  Table 7-3 lists the VCID currently reserved by CCSDS.

No value of VCID is reserved by CCSDS for the other Space Data Link Protocols.

Table 7-3:  Reserved Virtual Channel Identifiers (AOS Space Data Link Protocol Only)

| VCID (binary) | Utilization | Reference |
| --- | --- | --- |
| 111111 | Idle Transfer Frames | [10] |

## DEFINED FRAME SECONDARY HEADER VERSION NUMBERS

In the optional Transfer Frame Secondary Header defined by the TM Space Data Link Protocol (reference [8]), there is a field called the Frame Secondary Header Version Number to identify the Transfer Frame Secondary Header.  This is a two-bit field and its values are defined by CCSDS as part of the protocol specification.

Table 7-4 lists the Frame Secondary Header Version Number currently defined by CCSDS.

Table 7-4:  Defined Frame Secondary Header Version Numbers

| Version Number | Binary Encoded Version Number | Frame Secondary Header | Reference |
| --- | --- | --- | --- |
| 1 | 00 | Version 1 Frame Secondary Header | [8] |

NOTE	–	In the field of Frame Secondary Header Version Number in the Transfer Frame Secondary Header, the Binary Encoded Version Number listed above must be used.

## DEFINED CLCW VERSION NUMBERS

In the CLCW defined by the TC Space Data Link Protocol (reference [9]), there is a field called the CLCW Version Number to identify the CLCW.  This is a two-bit field and its values are defined by CCSDS as part of the protocol specification.

Table 7-5 lists the CLCW Version Number currently defined by CCSDS.

Table 7-5:  Defined CLCW Version Numbers

| Version Number | Binary Encoded Version Number | CLCW | Reference |
| --- | --- | --- | --- |
| 1 | 00 | Version 1 CLCW | [9] |

NOTE	–	In the field of CLCW Version Number in the CLCW, the Binary Encoded Version Number listed above must be used.

## DEFINED PACKET VERSION NUMBERS

In the Packets carried by the Space Data Link Protocols, there is a field called the Packet Version Number to identify the Packets.  This is a three-bit field (see NOTE 2 below) and its values are defined by CCSDS as part of the protocol specifications.

Table 7-6 lists the Packet Version Numbers currently defined by CCSDS.

Table 7-6:  Defined Packet Version Numbers

| Version Number | Binary Encoded Version Number | Packet | Reference |
| --- | --- | --- | --- |
| 1 | 000 | Space Packet | [6] |
| 2 | 001 | SCPS-NP | [7] |
| 3 | 010 (See NOTE 2 below) | IP Version 4 Datagram | [17] |
| 8 | 111 | Encapsulation Packet | [13] |

NOTES

- In the field of Packet Version Number in the Packets, the Binary Encoded Version Number listed above must be used.

- The version number field of the IP version 4 Packet has four bits and contains the binary values of ‘0100’.  However, the CCSDS Space Data Link Protocols recognize only the first three bits of this field as the Packet Version Number.

## DEFINED PROTOCOL IDENTIFIERS

The Encapsulation Packet (reference [13]) is a data structure to encapsulate data units of some protocols so that they can be carried by a CCSDS Space Data Link Protocol.  In the Encapsulation Packet, there is a field called the Protocol Identifier to identify the protocol whose data units are encapsulated.  This is a three-bit field and its values are defined by CCSDS as part of the specification of the Encapsulation Packet.

When all of the values of the Protocol Identifier have been assigned, CCSDS has provided a mechanism for extending the Protocol Identifier: This is done by setting the Protocol Identifier field in the Encapsulation Packet header to ‘110’, which signals that the 4-bit Extended Protocol ID field within the Encapsulation Packet header (see table 7-7b) is used to define the protocol encapsulated by the Encapsulation Packet.

Table 7-7a lists the Sentifiers currently defined by CCSDS.

Table 7-7a:  Defined Protocol Identifiers

| Protocol Identifier (binary) | Protocol | Reference |
| --- | --- | --- |
| 000 | Fill (no encapsulation data) | N/A |
| 010 | IP Version 4 | [17] |
| 011 | CFDP | [4] |
| 100 | IP Version 6 | [18] |
| 110 | Protocol Extension (signals the use of the Extended Protocol ID for Encapsulation Service | [ 13 ] |
| 111 | Arbitrary Aggregations of Octets | N/A |

Table 7-7b lists the Extended Protocol Identifiers defined for the Encapsulation Service by CCSDS.

Table 7-7b:  Extended Protocol Identifiers

| Protocol Identifier (binary) | Protocol | Reference |
| --- | --- | --- |
| 0000 through 1111 | Reserved by CCSDS |  |

## Reserved Proximity-1 Port Identifiers

The Proximity-1 Port Identifier (reference [11]) provides the means to route user data internally (at the transceiver’s output interface) to specific logical ports, such as applications or transport processes, or to physical ports, such as on-board buses or physical connections (including hardware command decoders) on either the forward and/or return proximity links.

Table 7-8a:	Proximity-1 Port ID Assignments for the Forward Link for Both Physical Channels

| Port Identifier (binary) | Usage | Reference |
| --- | --- | --- |
| 000 | Bitstream | N/A |
| 001 | Hardware Commands | N/A |
| 010 | Space Packets | [6], [7], [13], [17] |
| 011 | Reserved by CCSDS | N/A |
| 100 | Reserved by CCSDS | N/A |
| 101 | Reserved by CCSDS | N/A |
| 110 | Reserved by CCSDS | N/A |
| 111 | Reserved by CCSDS | N/A |

Table 7-8b:	Proximity-1 Port ID Assignments for the Return Link for Both Physical Channels

| Port Identifier (binary) | Usage | Reference |
| --- | --- | --- |
| 000 | Bitstream | N/A |
| 001 | Reserved by CCSDS | N/A |
| 010 | Space Packets | [6], [7], [13], [17] |
| 011 | Reserved by CCSDS | N/A |
| 100 | Reserved by CCSDS | N/A |
| 101 | Reserved by CCSDS | N/A |
| 110 | Reserved by CCSDS | N/A |
| 111 | Reserved by CCSDS | N/A |

ACRONYMS

(This annex is not part of the Recommendation)

This annex lists the acronyms used in this Recommendation.

AOS	Advanced Orbiting Systems

APID	Application Process Identifier

CCSDS	Consultative Committee for Space Data Systems

CFDP	CCSDS File Delivery Protocol

CLCW	Communications Link Control Word

D-ID	Domain Identifier

ES-ID	End System Identifier

ID	Identifier

IP	Internet Protocol

ISO	International Organization for Standardization

MAP	Multiplexer Access Point

N/A	Not Applicable

P-ID	Path Identifier

Prox	Proximity-1 Space Link Protocol

SCID	Spacecraft Identifier

SCPS	Space Communications Protocol Standards

SCPS-FP	Space Communications Protocol Standards File Protocol

SCPS-NP	Space Communications Protocol Standards Network Protocol

SCPS-SP	Space Communications Protocol Standards Security Protocol

SCPS-TP	Space Communications Protocol Standards Transport Protocol

TC	Telecommand

TM	Telemetry

TP-ID	Transport Protocol Identifier

VC	Virtual Channel

VCID	Virtual Channel Identifier

INFORMATIVE REFERENCES

(This annex is not part of the Recommendation)

[B1]	Procedures Manual for the Consultative Committee for Space Data Systems.  CCSDS A00.0-Y-9.  Yellow Book.  Issue 9.  Washington, D.C.: CCSDS, November 2003.

NOTE	–	Normative references are listed in 1.7.

LOCATION OF PACKET LENGTH FIELD

(This annex is not part of the Recommendation)

Table C-1 summarizes the location of the length field of Packets for which Packet Version Numbers are defined by CCSDS.

NOTE	–	This information is used by the Space Data Link Protocols (reference [8]-[10]) and Proximity-1 Space Link protocol (reference [11]) to extract Packets from the Data Field of Transfer Frames.

Table C-1:  Location of Packet Length Field

| Version Number | Binary Encoded Version Number | Packet | Location of Length Field (See NOTE) | Interpretation of Length | Refer-ence |
| --- | --- | --- | --- | --- | --- |
| 1 | 000 | Space Packet | 32-47 | Binary count of number of octets in Packet Data Field minus 1. Must add 7 to get full packet length. | [6] |
| 2 | 001 | SCPS-NP | 3-16 | Binary count of total octets in Packet, including header. Shortest legal length is 4 (= 4 octets). | [7] |
| 3 | 010 | IP version 4 | 16-31 | Binary count of total octets in Packet, including header. | [17] |
| 8 | 111 | Encapsulation Packet | 8-15, 8-23, or 8-39 | Binary count of total octets in Packet, including header. | [13] |

NOTE	–	Counted in bits, from beginning of packet; first bit is numbered zero.

# Footnotes

Internet Request for Comments (RFC) texts are available on line in various locations (e.g., http://ietf.org/rfc/); Internet standards are made up of one or more RFCs, which are identified in square brackets following the entry.