Protocol Implementation Conformance 
Statement (PICS) Proforma

(normative)

  - Introduction

    - Overview

This annex provides the Protocol Implementation Conformance Statement (PICS) Requirements List (RL) for an implementation of Proximity-1 Space Link Protocol—Data Link Layer (CCSDS 211.0-B-4.1).  The PICS for an implementation is generated by completing the RL in accordance with the instructions below. An implementation claiming conformance must satisfy the mandatory requirements referenced in the RL.

The RL support column in this annex is blank. An implementation’s completed RL is called the PICS. The PICS states which capabilities and options have been implemented. The following can use the PICS:

- the implementer, as a checklist to reduce the risk of failure to conform to the standard through oversight;

- a supplier or potential acquirer of the implementation, as a detailed indication of the capabilities of the implementation, stated relative to the common basis for understanding provided by the standard PICS proforma;

- a user or potential user of the implementation, as a basis for initially checking the possibility of interworking with another implementation (it should be noted that, while interworking can never be guaranteed, failure to interwork can often be predicted from incompatible PICSes);

- a tester, as the basis for selecting appropriate tests against which to assess the claim for conformance of the implementation.

    - Abbreviations and Conventions

The RL consists of information in tabular form.  The status of features is indicated using the abbreviations and conventions described below.

Item Column

The item column contains sequential numbers for items in the table.

NOTE	–	The item-number prefix ‘DLL’ = ‘Data Link Layer’.

Feature Column

The feature column contains a brief descriptive name for a feature. It implicitly means ‘Is this feature supported by the implementation?’

Status Column

The status column uses the following notations:

M	mandatory.

O	optional.

O.<n>	optional, but support of at least one of the group of options labeled by the same numeral <n> is required.

Support Column Symbols

The support column is to be used by the implementer to state whether a feature is supported by entering Y, N, or N/A, indicating:

Y	Yes, supported by the implementation.

N	No, not supported by the implementation.

N/A	Not applicable.

The support column should also be used, when appropriate, to enter values supported for a given capability.

    - Instructions for Completing the RL

An implementer shows the extent of compliance to the Recommended Standard by completing the RL; that is, the state of compliance with all mandatory requirements and the options supported are shown. The resulting completed RL is called a PICS. The implementer shall complete the RL by entering appropriate responses in the support or values supported column, using the notation described in A1.2.  If a conditional requirement is inapplicable, N/A should be used. If a mandatory requirement is not satisfied, exception information must be supplied by entering a reference Xi, where i is a unique identifier, to an accompanying rationale for the noncompliance.

  - PICS Proforma for Proximity-1 Space Link Protocol—Data Link Layer (CCSDS 211.0-B-4.1)

    - General Information

      - Identification of PICS

| Date of Statement (DD/MM/YYYY) |  |
| --- | --- |
| PICS serial number |  |
| System Conformance statement cross-reference |  |

      - Identification of Implementation Under Test (IUT)

| Implementation name |  |
| --- | --- |
| Implementation version |  |
| Special Configuration |  |
| Other Information |  |

      - Identification of Supplier

| Supplier |  |
| --- | --- |
| Contact Point for Queries |  |
| Implementation Name(s) and Versions |  |
| Other information necessary for full identification, e.g., name(s) and version(s) for machines and/or operating systems; System Name(s) |  |

      - Identification of Specification

| CCSDS 211.0-B-4.1 |
| --- |
| Have any exceptions been required? NOTE – A YES answer means that the implementation does not conform to the Recommended Standard. Non-supported mandatory capabilities are to be identified in the PICS, with an explanation of why the implementation is non-conforming. | Yes [ ] No [ ] |

    - Requirements List

| Version-3 Transfer Frame |
| --- |
| Item | Description | Reference | Status | Values Allowed | Support |
| DLL-1 | Version-3 Transfer Frame | 3.2 | M |  |  |
| DLL-2 | Transfer Frame Header | 3.2.2 | M |  |  |
| DLL-3 | Transfer Frame Version Number | 3.2.2.2 | M | 2 |  |
| DLL-4 | Quality of Service Indicator | 3.2.2.3 | M | 0, 1 |  |
| DLL-5 | PDU Type ID | 3.2.2.4 | M | 0, 1 |  |
| DLL-6 | Data Field Construction ID | 3.2.2.5 | M | 0–3 |  |
| DLL-7 | Spacecraft Identifier (SCID) | 3.2.2.6 | M | 0–1023 |  |
| DLL-8 | Physical Channel Identifier (PCID) | 3.2.2.7 | M | 0, 1 |  |
| DLL-9 | Port Identifier | 3.2.2.8 | M | 0–7 |  |
| DLL-10 | Source-or-Destination Identifier | 3.2.2.9 | M | 0, 1 |  |
| DLL-11 | Frame Length | 3.2.2.10 | M | 4–2047 |  |
| DLL-12 | Frame Sequence Number (Sequence Controlled or Expedited) | 3.2.2.11 | M | 0–255 |  |
| DLL-13 | Transfer Frame Data Field | 3.2.3 | M | 0–2043 octets |  |
| DLL-14 | PACKETS in a U-Frame (DFC ID = 0) | 3.2.3.2 | O.1 |  |  |
| DLL-15 | SEGMENT DATA UNITS in a U-Frame (DFC ID = 1) | 3.2.3.3 | O.1 |  |  |
| DLL-16 | CCSDS RESERVED FIELD (U-Frame) (DFC ID = 2) | 3.2.3.4 | O.1 |  |  |
| DLL-17 | USER-DEFINED DATA in a U-Frame (DFC ID = 3) | 3.2.3.5 | O.1 |  |  |
| DLL-18 | Transfer Frame Data Field Contents in a P-frame | 3.2.3.6 | M |  |  |

o.1	For the Transfer Frame Data Field at least one must be chosen.

| Supervisory PDU (SPDU) |
| --- |
| Item | Description | Reference | Status | Values Allowed | Support |
| DLL-19 | SUPERVISORY PDU (SPDU) | 3.2.4 | M |  |  |
| DLL-20 | Fixed-length SPDU | 3.2.4.2.1 | M |  |  |
| DLL-21 | Variable-length SPDU | 3.2.4.4 | M |  |  |
| DLL-22 | Variable-Length SPDU Type 1 (Directives/Reports) | 3.2.4.2.2, B1 | M |  |  |
| DLL-23 | Variable-Length SPDU Type 2: Time Distribution | 3.2.4.4.3, B2 | O |  |  |
| DLL-24 | Variable-Length SPDU Type 3: Status Reports | 3.2.4.4.4 | O |  |  |

| Data Link Layer |
| --- |
| Item | Description | Reference | Status | Values Allowed | Support |
| DLL-25 | Frame Sub-Layer Functions | 4.1.1 | M |  |  |
| DLL-26 | Sending End Frame Selection for Output | 4.1.2 | M |  |  |

| Medium Access Control (MAC) Sublayer |
| --- |
| Item | Description | Reference | Status | Values Allowed | Support |
| DLL-27 | Persistent Activity Process | 4.2.2 | M |  |  |
| DLL-28 | MAC Control Mechanisms | 4.2.3 | M |  |  |
| DLL-29 | Directive Decoder | 4.2.4 | M |  |  |
| DLL-30 | MAC buffers | 4.2.5 | M |  |  |
| DLL-31 | Sent_Time_Buffer | 4.2.5.1 | M |  |  |
| DLL-32 | Receive_Time_Buffer | 4.2.5.2 | M |  |  |

| Data Services Sublayer |
| --- |
| Item | Description | Reference | Status | Values Allowed | Support |
| DLL-33 | Send Side Functionality | 4.3.1.1 | M |  |  |
| DLL-34 | Receive Side Functionality | 4.3.1.2 | M |  |  |
| DLL-35 | Order in which User Data is transferred | 4.3.2.1 | M |  |  |
| DLL-36 | Two Qualities of Service | 4.3.2.2 | M |  |  |

| I/O Interface Sublayer |
| --- |
| Item | Description | Reference | Status | Values Allowed | Support |
| Send Side |
| DLL-37 | Accept user data for transfer | 4.4.1.1 a) | M |  |  |
| DLL-38 | Form the Frame Data Unit and the Transfer Frame Header | 4.4.1.1 b) | M |  |  |
| DLL-39 | Expedited SDU is radiated | 4.4.1.1 c) | M |  |  |
| DLL-40 | Transfer of a Sequence Controlled SDU | 4.4.1.1 d) | M |  |  |
| Receive Side |
| DLL-41 | Output SDUs | 4.4.1.2 a) | M |  |  |
| DLL-42 | Assemble segments/verify packets | 4.4.1.2 b) | M |  |  |
| DLL-43 | Deliver only complete packets | 4.4.1.2 c) | M |  |  |
| DLL-44 | Deliver the packets/user-defined data | 4.4.1.2 d) | M |  |  |
| Interface to the Lower Sublayers |
| DLL-45 | SDUs to appropriate Queues (Sequence or Expedited) | 4.4.2.1 | M |  |  |
| DLL-46 | Existance of Expedited queue and Sequence Controlled queue | 4.4.2.2 | M |  |  |
| DLL-47 | Association between SDU and frame sequence number | 4.4.2.3 | M |  |  |
| DLL-48 | Evaluation of NNR for complete SDU transfer | 4.4.2.4 | M |  |  |
| I/O Sublayer Queues and Control Signals |
| DLL-49 | Data units stored within the Sequence Controlled Frame queue | 4.4.3.1 | M |  |  |
| DLL-50 | Data units stored within the Expedited Frame queue | 4.4.3.2 | M |  |  |
| DLL-51 | Frame extraction from either queue | 4.4.3.3 | M |  |  |

| Proximity-1 Timing Services |
| --- |
| Item | Description | Reference | Status | Values Allowed | Support |
| DLL-52 | Time Tag Recording | 5.2 | M |  |  |
| DLL-53 | Time Tagged Bit | 5.2.1 | M |  |  |
| DLL-54 | Time Tag Event | 5.2.2 | M |  |  |
| DLL-55 | Time Tags relationship to time reference point | 5.2.3 | M |  |  |
| DLL-56 | Enterprise defined time reference point | 5.2.4 | M |  |  |
| DLL-57 | Operational Mode | 5.2.5 | M |  |  |
| DLL-58 | Initiate Time Tag Collection | 5.2.6 | M |  |  |
| DLL-59 | Capture and Package Time Tags + Meta Data | 5.2.7 | M |  |  |
| DLL-60 | Time Correlation Process (notional) | 5.3 | O |  |  |
| DLL-61 | Transferring Time to a Remote Asset | 5.4 | O |  |  |
| DLL-62 | Time Distribution | 5.4.1 | O |  |  |
| DLL-63 | Method of Transfer | 5.4.2 | O |  |  |
| DLL-64 | Send Side: Time Distribution Directive | 5.4.2.2 | O |  |  |
| DLL-65 | Receive Side: Time Distribution Directive | 5.4.2.3 | O |  |  |

| State Control Variables |
| --- |
| Item | Description | Reference | Status | Values Allowed | Support |
| DLL-66 | Mode | 6.2.2.1 | M | inactive, connecting-T, connecting-L, active |  |
| DLL-67 | DUPLEX | 6.2.2.2 | M | full, half, simplex transmit, simplex receive |  |
| DLL-68 | TRANSMIT | 6.2.2.3 | M | on, off |  |
| DLL-69 | SUB-STATE | 6.2.2.4 | M | 0-7 |  |

| Operational Control Variables |
| --- |
| Item | Description | Reference | Status | Values Allowed | Support |
| DLL-71 | Session Termination | 6.2.3.1 | M | 0–5 |  |
| DLL-72 | Comm_Change | 6.2.3.2 | M | 0–5 |  |
| DLL-73 | SYMBOL_INLOCK_STATUS | 6.2.3.3 | M | 0, 1 |  |
| DLL-74 | Modulation | 6.2.3.4 | M | on, off |  |
| DLL-75 | Persistence | 6.2.3.5 | M | true, false |  |
| DLL-76 | NEED_PLCW and NEED_STATUS_REPORT | 6.2.3.6 | M | true, false |  |
| DLL-77 | REMOTE_SCID_BUFFER | 6.2.3.7 | M | 0–1023 |  |
| DLL-78 | COMMUNICATION_VALUE_BUFFER | 6.2.3.8 | M |  |  |
| DLL-79 | Receiving_SCID_Buffer | 6.2.3.9 | M | 0–1023 |  |
| DLL-80 | Receiving_PCID_Buffer | 6.2.3.10 | M | 0, 1 |  |

| Elements And Events That Affect State Status |
| --- |
| Item | Description | Reference | Status | Values Allowed | Support |
| DLL-81 | Interval_Clock | 6.3.1.1.1 | M |  |  |
| DLL-82 | WAIT TIMER (WT) and Associated Events | 6.3.1.2 | M |  |  |
| DLL-83 | CARRIER_LOSS_TIMER and Associated Events | 6.3.1.3 | M |  |  |
| DLL-84 | PLCW TIMER and Associated Events | 6.3.1.4 | M |  |  |
| DLL-85 | OUTPUT FIFO | 6.3.2.2 | M |  |  |
| DLL-86 | NO_FRAMES_PENDING | 6.3.2.3 | M |  |  |

| Directives |
| --- |
| Item | Description | Reference | Status | Values Allowed | Support |
| DLL-87 | Local Directives | 6.3.3.1 | M |  |  |
| DLL-88 | SET MODE | 6.3.3.1.1 | M |  |  |
| DLL-89 | SET INITIALIZE MODE | 6.3.3.1.2 | M |  |  |
| DLL-90 | LOCAL COMM_CHANGE (LCCD) | 6.3.3.1.3 | M |  |  |
| DLL-91 | LOAD COMMUNICATIONS VALUE BUFFER | 6.3.3.1.4 | M |  |  |
| DLL-92 | LOCAL_NO_MORE_DATA (LNMD) | 6.3.3.1.5 | O |  |  |
| DLL-93 | SET DUPLEX | 6.3.3.1.6 | M |  |  |
| DLL-94 | SET RECEIVING SCID BUFFER | 6.3.3.1.7 | M |  |  |
| DLL-95 | READ STATUS | 6.3.3.1.8 | O |  |  |
| DLL-96 | Remote directives | 6.3.3.2 | M |  |  |
| DLL-97 | SET TRANSMITTER PARAMETERS directive | 6.3.3.2.1 | M |  |  |
| DLL-98 | SET RECEIVER PARAMETERS directive | 6.3.3.2.2 | M |  |  |
| DLL-99 | SET PL_EXTENSIONS directive | 6.3.3.2.3 | M |  |  |
| DLL-100 | The Set CONTROL PARAMETERS directive (Time Sample Field) | 6.3.3.2.4 | M |  |  |
| DLL-101 | Initialized values of Proximity-1 control variables | 6.3.4 | M |  |  |

| Duplex/Simplex Operations |
| --- |
| Item | Description | Reference | Status | Values Allowed | Support |
| DLL-102 | Full duplex operations | 6.4.2, Tables 6-7, 6-8, 6-9 | M |  |  |
| DLL-103 | Half duplex operations | 6.4.3, Table 6-10, 6-11, 6-12 | O |  |  |
| DLL-104 | Simplex operations | 6.5, Table 6-13 | O |  |  |

| Interfaces with the Physical Layer |
| --- |
| Item | Description | Reference | Status | Values Allowed | Support |
| DLL-105 | Output Interfaces | 6.6.1 | M |  |  |
| DLL-106 | The TRANSMIT variable | 6.6.1.1 | M | On, Off |  |
| DLL-107 | The Output coded symbol stream | 6.6.1.2 | M |  |  |
| DLL-108 | The MODULATION signal | 6.6.1.3 | M | On, Off |  |
| DLL-109 | Input interfaces | 6.6.2 | M |  |  |
| Sending Operations |
| DLL-110 | Output symbol stream formulation | 6.7.2 | M |  |  |
| DLL-111 | Reset NEED_PLCW or NEED_STATUS_REPORT | 6.7.4.1–6.7.4.2 | M | True, False |  |
| DLL-112 | Setting No_Frames_Pending | 6.7.4.3 | M | True, False |  |
| DLL-113 | Setting OUTPUT_FIFO=empty | 6.7.4.4 | M | True, False |  |
| Receiving Operations |
| DLL-114 | The SET MODE (connecting-L) or SET MODE (connecting-T) local directives | 6.8.1 | M | connecting-L or connecting-T |  |
| DLL-115 | Processing the received bitstream | 6.8.2 | M |  |  |
| DLL-116 | Frame Validation Criteria | 6.8.3 | M |  |  |
| DLL-117 | Validated received U-Frames | 6.8.4 | M |  |  |
| DLL-118 | Validated received P-frames | 6.8.5 | M |  |  |

| Communication Operations Procedure for Proximity Links COP-P |
| --- |
| Item | Description | Reference | Status | Values Allowed | Support |
| DLL-119 | Implement COP-P Protocol | 7, 4.3.3 | M |  |  |
| DLL-120 | DATA SERVICES OPERATIONS (COP-P): Modulo-256 counters will be used for sequence number in the COP-P protocol | 7 | M |  |  |
| DLL-121 | SENDING PROCEDURES (FOP-P) | 7.1 | M |  |  |
| DLL-122 | The FOP-P Sent Frame Queue | 7.1.1 | M |  |  |
| FOP-P Variables |
| DLL-123 | VE(S) | 7.1.2 a) | M |  |  |
| DLL-124 | V(S) | 7.1.2 b) | M |  |  |
| DLL-125 | VV(S) | 7.1.2 c) | M |  |  |
| DLL-126 | N(R): | 7.1.2 d) | M |  |  |
| DLL-127 | NN(R): | 7.1.2 e) | M |  |  |
| DLL-128 | R(R): | 7.1.2 f) | M |  |  |
| DLL-129 | RR(R): | 7.1.2 g) | M |  |  |
| DLL-130 | NEED_PLCW/NEED_STATUS_REPORT | 7.1.2 h) | M |  |  |
| DLL-131 | SYNCH_TIMER | 7.1.2 i) | M |  |  |
| DLL-132 | RESYNC | 7.1.2 j) | M |  |  |
| DLL-133 | FOP-P General Procedures | 7.1.3.1 | M |  |  |
| DLL-134 | Set V(R) persistent activity | 7.1.3.2 | M |  |  |
| DLL-135 | Configure the SET V(R) persistent activity | 7.1.3.2.1 | M |  |  |
| DLL-136 | Execute the SET V(R) persistent activity | 7.1.3.2.2 | M |  |  |
| DLL-137 | FOP-P State Table | 7.1.3.3 | M |  |  |
| DLL-138 | DATA SERVICES RECEIVING OPERATIONS | 7.2 | M |  |  |
| DLL-139 | FARM-P STATE TABLE | 7.2.1 | M |  |  |
| INTERNAL FARM-P PARAMETERS |
| DLL-140 | V(R): | 7.2.2 a) | M |  |  |
| DLL-141 | R(S): | 7.2.2 b) | M |  |  |
| DLL-142 | N(S): | 7.2.2 c) | M |  |  |
| DLL-143 | EXPEDITED_FRAME_COUNTER | 7.2.2 d) | M |  |  |
| DLL-144 | INTERFACE TO THE I/O SUBLAYER | 7.2.3 | M |  |  |

| Input/Output (I/O) Sublayer Operations |
| --- |
| Item | Description | Reference | Status | Values Allowed | Support |
| DLL-145 | Sending Operations | 8.2 | M |  |  |
| DLL-146 | Receiving Operations | 8.3 | M |  |  |

| Variable-length Supervisory Protocol Data Field Formats |
| --- |
| Item | Description | Reference | Status | Values Allowed | Support |
| DLL-147 | SET TRANSMITTER PARAMETERS Directive | B1.2 | M |  |  |
| DLL-148 | SET CONTROL PARAMETERS Directive | B1.3 | M |  |  |
| DLL-149 | SET RECEIVER PARAMETERS Directive | B1.4 | M |  |  |
| DLL-150 | SET V(R) Directive | B1.5 | M |  |  |
| DLL-151 | REPORT REQUEST Directive | B1.6 | O |  |  |
| DLL-152 | SET PL EXTENSIONS Directive | B1.7 | M |  |  |
| DLL-153 | REPORT SOURCE SPACECRAFT ID Directive | B1.8 | O |  |  |

| Management Information Base (MIB) Parameters (alphabetical) |
| --- |
| Item | Description | Reference | Status | Values Allowed | Support |
| DLL-154 | Acquisition_Idle_Duration | 6.2.4.4 | M |  |  |
| DLL-155 | Carrier_Loss_Timer_Duration | 6.2.4.6 | M |  |  |
| DLL-156 | Carrier_Only_Duration | 6.2.4.3 | M |  |  |
| DLL-157 | Comm_Change_Lifetime | 6.2.4.10 | M |  |  |
| DLL-158 | Comm_Change_Notification | 6.2.4.9 | M |  |  |
| DLL-159 | Comm_Change_Response | 6.2.4.8 | M |  |  |
| DLL-160 | Comm_Change_Waiting_Period | 6.2.4.7 | M |  |  |
| DLL-161 | Hail_Lifetime | 6.2.4.14 | M |  |  |
| DLL-162 | Hail_Notification | 6.2.4.13 | M |  |  |
| DLL-163 | Hail_Response | 6.2.4.12 | M |  |  |
| DLL-164 | Hail_Wait_Duration | 6.2.4.11 | M |  |  |
| DLL-165 | Hailing_Channel | 6.2.4.15 | M |  |  |
| DLL-166 | Hailing_Data_Rate | 6.2.4.16 | M |  |  |
| DLL-167 | Interval_Clock | 6.3.1.1.1 | M |  |  |
| DLL-168 | Local_PCID | 3.2.2.7 | M |  |  |
| DLL-169 | Local_Spacecraft_ID | 3.2.2.9.3 | M |  |  |
| DLL-170 | Maximum_Failed_Token_Passes | 6.4.3, Table 6-10 | O |  |  |
| DLL-171 | Maximum_Frame_Length | 3.2.3.1 | M |  |  |
| DLL-172 | Maximum_Packet_Size | 4.4.1.1 | M |  |  |
| DLL-173 | Persistence_Wait_Time | 6.4.2, Table 6-8 | M |  |  |
| DLL-174 | PLCW_Repeat_Interval | 6.2.4.19 | M |  |  |
| DLL-175 | Receive_Duration | 6.2.4.18 | O |  |  |
| DLL-176 | Drop_Carrier_Duration | 6.2.1, Table 6-2 | M |  |  |
| DLL-177 | Remote_PCID | 3.2.2.7 | M |  |  |
| DLL-178 | Remote_Spacecraft_ID | 3.2.2.9.3 | M |  |  |
| DLL-179 | Resync_Local | 7.1.3.2.1,7.1.3.3 | M |  |  |
| DLL-180 | Resync_Lifetime | 7.1.3.2 | M |  |  |
| DLL-181 | Resync_Notification | 7.1.3.2 | M |  |  |
| DLL-182 | Resync_Response | 7.1.3.2 | M |  |  |
| DLL-183 | Resync_Waiting_Period | 7.1.3.2 | M |  |  |
| DLL-184 | Send_Duration | 6.2.4.17 | O |  |  |
| DLL-185 | Source_Destination_ID | 3.2.2.9 | M |  |  |
| DLL-186 | Synch_Timeout | 7.1.2 | M |  |  |
| DLL-187 | Tail_Idle_Duration | 6.2.4.5 | M |  |  |
| DLL-188 | Test_Source | 6.2.4.2 | M |  |  |
| DLL-189 | Transmission_Window | 7.1.3.3 | M |  |  |

| Notifications to Vehicle Controller |
| --- |
| Item | Description | Reference | Status | Values Allowed | Support |
| DLL-190 | 1 RESULT OF PERSISTENT ACTIVITY | Annex D #1 | M |  |  |
| DLL-191 | 2 STATE CONTROL STATUS | Annex D #2 | M |  |  |
| DLL-192 | 3 INVALID FRAME SOURCE | Annex D #3 | M |  |  |
| DLL-193 | 4 TIMING SERVICES INSTANCE | Annex D #4 | M |  |  |
| DLL-194 | 5 NO CARRIER RECEIVED - HALF DUPLEX | Annex D #5 | O |  |  |
| DLL-195 | 6 NO DATA TRANSFERRED - HALF DUPLEX | Annex D #6 | O |  |  |
| DLL-196 | 7 SENDER EXCEEDED PRESCRIBED TRANSMISSION PERIOD - HALF DUPLEX | Annex D #7 | O |  |  |
| DLL-197 | 8 COP-P LOSS OF SYNCHRONIZATION | Annex D #8 | M |  |  |
| DLL-198 | 9 CARRIER_LOSS_TIMER UNDERFLOWS | Annex D #9 | M |  |  |
| DLL-199 | 10 END OF SESSION(# octets received) | Annex D #10 | M |  |  |
| DLL-200 | 11 CARRIER ONLY RECEIVED | Annex D #11 | M |  |  |