## Slide 1: USLP Prototype Status
Sponsoring Org/Office Code: HP27
Name of Forum: CCSDS
Date: May 2017
Publicly Available – Distribution is Unlimited
Presenter Name R. Lee Pitts

## Slide 2: Outline
USLP implementation
  Overview
    Participants
    Test configuration
  Current status
  Plan for testing

## Slide 3
Two USLP implementations are being developed by DLR and MSFC/NASA
  Stefan Veit at DLR
  Kevan Moore at MSFC/NASA (Huntsville Operations Support Center)
The implementations are being conducted remotely over a VPN
Each end has been developing and testing incrementally
Current testing has been on Red-1 updates
Red -2 updates will be implemented after agreement
Overview

## Slide 4
Test configuration uses a reciprocal test mechanism
  Tester 1 generates a test pattern and transmits it to Tester 2
  Tester 2 receives and places it as data into frames and retransmits them to tester 1
  Tester 1 receives and decommutates data in frames
Allows multiple test
  Multiple independent test with only minor participation of a secondary tester.
We are in the process of generating the formal test plan for acceptance of USLP
Specific test areas
  Virtual channel frame service frames and master channel frame service frames, and their concurrent multiplexing with frames of USLP data for other master channels and VCIDs.
  Multiple packets in one frame to one-octet-per-frame spanning/reassembly
Current Status

## Slide 5
Specific test areas
  Length permutations to verify all boundary/spanning/optional field/encapsulated idle permutations (including all construction rules and data unit types) in transmitter and receiver, except for max frame size and truncated frame conditions.
  Timeouts are being temporarily simulated by event-driven methods to accommodate high speed automation and verification
  Automated length variations will be implemented to exercise all possible data unit, boundary condition, spanning, frame type, and idle fill permutations.
Current Status

## Slide 6
Goal is to complete before the next biannual CCSDS meeting
Incorporate Red-2 updates
Using a two pass scenario for testing
  First pass is a procedure check for completeness
  Second pass is on automatic and will vary conditions more widely
We will be incorporating fixed and variable length frames
  Using a known pattern for checking
  Use of CRC for automated checking
Plan for testing

## Slide 7
Backup
Backup

## Slide 8
Frame sequence control supported- switch for sequence control or whether it contributes to what ever is used (for sequence control or expedited integer)