## Slide 1
CCSDS Space Packet Protocol
APID Extension
11/01/2018
Jonathan Wilmot
Jonathan.J.Wilmot@NASA.gov
301-286-2623

## Slide 2: What Problem am I trying to Solve? In a standard way
ACS sensor data created on habitat
ACS sensor data
read on Orion
Orion applications need to know the data format and what system the data came from:
  Habitat.GNC.sensorData
I don’t want to see a repeat of Constellation

## Slide 3: APID Background
Many spacecraft systems use the CCSDS Space Packet Protocol (SPP) 133.0.x as the format of data exchange messages between onboard applications and over the space to ground interfaces
  As of 3/29/2016, version is 133.0.B-1 with Technical Corrigendum 2 dated September 2012
For commands, the APID is typically used to identify the consumer process/application. Can also be considered the command ‘topic”
For telemetry, the APID refers more to the name or “topic” of the packet
  One application (process) can send many different APIDs
  The APID identifies the data content and typically the format
  NASA, ESA, and CAST use this pattern
  CCSDS standard - APID is a process identifier
cFS SB has the subscriber set the QoS
  CCSDS standard - sender specifies QoS

## Slide 4: Standard CCSDS Secondary Headers
4.1.3.2.1.5 If present, the Packet Secondary Header shall consist of either:
  a) a Time Code Field (variable length) only;
  b) an Ancillary Data Field (variable length) only; or
  c) a Time Code Field followed by an Ancillary Data Field.
Cannot find original diagram but this format is still in use at GSFC, ARC, APL, JSC, GRC,…

## Slide 5: ESA PUS-C Use Of SPP
The CCSDS Space Packet Protocol (CCSDS 133.0-B-1) and the ECSS-E-ST-50 series of standards address the end-to-end transport of telemetry and telecommand data between user applications on the ground and application processes on-board the spacecraft, and the intermediate transfer of these data through the different elements of the ground and space segments.
This packet utilization standard (PUS) complements those standards by defining the application-level interface between ground and space, in order to satisfy the requirements of electrical integration and testing and flight operations.
The sequence flags are defined by CCSDS but not used by the space packet protocol. This Standard uses the binary value "11" for the sequence flags, to indicate a stand-alone packet. All telemetry packets and telecommand packets defined within this Standard are stand-alone packets
The telecommand packet sequence count or packet name field carries an identifier that used in combination with the source identifier
  This cannot be determined at run-time based on version.

## Slide 6: PUS-C Secondary Headers
Telecommand
Telemetry

## Slide 7
Assume PUS packets
on the Software Bus

## Slide 8: NASA cFS Use of SPP
cFS uses SPP as internal and external data exchange format
  cFS applications are not location aware
Uses APID as a topic identifier that defines the format of the message
APID (topic) is used in pub/sub protocol to help create a Logical Data Path in the underlying subnet

## Slide 9: What’s the Problem?
Allocation and management of APIDs during development
  Early block assignments to subsystems
  Ripple effects of APID changes to code, documentation, tests, ground systems…
Larger systems of systems are running out of APIDs
  Example: Habitat and Orion docked
Formation flying, distributed, cluster satellites, small satellites
  Includes multi-processor, multi-core, and partitioned systems
In CCSDS, the spacecraft ID is in the WAN frame and is stripped off as the packet goes up the protocol stack
Applications receiving Space Packets do not know how to interpret the packet unless the know the domain (i.e. spacecraft id)
  SPP Primary Header flag indicates there is a secondary header, but application cannot determine format

## Slide 10: Proposed Updates to CCSDS SPP

## Slide 11: Align with ESA ECSS PUS
European Cooperation for Space Standardization (ECSS) has a standard secondary header Packet Utilisation Standard (PUS)
We can assign a version to PUS and a version to cFS secondary header

## Slide 12: Primary Header Field Definitions (1)
CCSDS version – Version of CCSDS Space Packet Protocol used to create this packet (23 = 8) Currently set to 0 indicating version 1
Type ID – Indicates packet is a command or telemetry
Secondary Header Flag – Indicates packet contains a secondary header
  When combined with the Type ID format of secondary header is known
  For cFS always set to 1 indicating secondary header is present
Application ID (APID) – Indicates source application/process of that packet (211 = 2047) APID = 2047 is fill packet
  When combined with Type ID allows 4094 unique packet identifiers

## Slide 13: Primary Header Field Definitions (2)
Sequence Flags – Indicates that this packet encapsulates a larger packet
  ‘00’ if the Space Packet contains a continuation segment of User Data
  ‘01’ if the Space Packet contains the first segment of User Data
  ‘10’ if the Space Packet contains the last segment of User Data
  ‘11’ if the Space Packet contains unsegmented User Data.
  NASA cFS SB and ESA PUS use ’11’ to avoid complexities of encapsulation mechanisms
Packet Sequence Count - Continuous incrementing counter (modulo-16384)
  cFS implements this for telemetry packets
  Unused for cFS command packets
    Avoids issues with command from multiple applications (Many to one)
      Stored command and ground command sequencing

## Slide 14: Extended Header Field Definitions (1)
EDS version – Version of the EDS used to create this packet (25 = 32)
  Intended for ensuring data will be interpreted as encoded in plug and play type systems and archival playback both onboard and on ground
  Useful for CM of EDS
Endian – Indicates big or little endianness of encoded data
Playback – Indicates that this playback of archived data
  Intended to allow recorded data packet playback both onboard (crewed systems) and off board without unintended real time interpretation by systems or mission personnel

## Slide 15: Extended Header Field Definitions (2)
APID Qualifier (Subsystem Id) – Identifies the packet source subsystem (29 = 512 subsystems)
  A mission defined arbitrary number indicating a source software component, partition, processor, device or any combination of those.
  Can be inserted at runtime by SB (Not implemented)
APID Qualifier (System Id) – Identifies the packet source system (216 = 64k Spacecraft/Systems)
  A mission defined arbitrary number indicating the source system. Can be a software component, partition, processor, device, spacecraft, vehicle or any combination of those
    Default use is to encode the CCSDS Spacecraft ID and apply to multi-vehicle systems
      Ensures id is available to application level services
    Currently the CCSDS Spacecraft ID is encoded in the CCSDS frame which is striped off as a space packet is received by the application layer. Ground systems must archive the frame to retain that information.
  Can be inserted at runtime by SB (Not implemented)

## Slide 16: Issues
Is subsystem “logical” or absolute?
  Not dependent on location or physical address
  SBN routing would change but not SB
Is system “logical” or absolute?
  Not dependent on location or physical address
  SBN routing would change but not SB
If a subsystem (application) moves to a different processor what is the impact on subscribers?
  Should be transparent?