## Slide 1: SDLS – COP-1 Order Of Operations
Problem Statement:
  Current Order Of Operations
    SDLS – FOP – Coding > Physical Channel < Decoding – FARM - SDLS
  With this order nonce (Security Counter or IV) is numbered in the order of frame presentation to SDLS
  Anti-Replay Mechanism: nonce must always increase at Rcv side or frame will fail authentication
  A sequence of 10 type AD frames followed by a type BD frame will have nonces assigned by SDLS increasing in that same order: AD (nonce = 1)….AD (nonce = 10), BD (nonce = 11)
  Suppose AD frame 2 is missing. The BD frame will bypass the ARQ in the FARM and set the last received nonce value on the spacecraft SDLS to 11
  Re-transmission of the AD frames 2 through 10 by the FOP will be accepted by the FARM but fail the SDLS anti-replay mechanism on the spacecraft because nonce must be >=12 and result in false security event.
    COP-1 identifies BD frames as contingency frames
    Type AD Frames (sequence controlled): A – ARQ, D – Data (software command data to the spacecraft)
    Order is based on frame sequence number in the TF primary header
    Type BD Frames (expedited): B – Bypass ARQ, D – Data

## Slide 2: SDLS – COP-1 Order Of Operations
Alternative Order Of Operations:
  FOP – SDLS – Encoding < Physical Channel > Decoding – SDLS – FARM
  Eliminates problem created by BD frames since the nonces increment based on the order of transmission
  Use of the optional FECF CRC on secured TFs allows discrimination between transmission errors and security events
    All-Frames-Reception function discards frames (type A or B) which fail CRC prior to sending to SDLS or FARM
      Missing frame with no authentication failure (FSR) = transmission error
      Missing frame with authentication failure (FSR) = security event
  COP synchronization is maintained whether frames are missing due to transmission errors or security events (unlike current order) and recovery from either event is automatic
  *SDLS encrypts data field, adds security header and trailer, computes MAC on TF (excluding FECF) using incremented nonce (authenticated encryption option)
  **FECF optionally contains computed CRC based on secured TF (minus FECF field itself) prior to encoding/randomization