Draft Recommendation for
Space Data System Standards

Planning Data Formats

PROPOSED Draft Recommended Standard

CCSDS 902.2-W-0.04

White Book

November 2014

AUTHORITY

|  | Issue: | White Book, Issue 0.04 |  |
| --- | --- | --- | --- |
|  | Date: | November 2014 |  |
|  | Location: | Not Applicable |  |

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF AUTHORITY:)

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and represents the consensus technical agreement of the participating CCSDS Member Agencies.  The procedure for review and authorization of CCSDS documents is detailed in Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-3), and the record of Agency participation in the authorization of this document can be obtained from the CCSDS Secretariat at the address below.

This document is published and maintained by:

CCSDS Secretariat

Space Communications and Navigation Office, 7L70

Space Operations Mission Directorate

NASA Headquarters

Washington, DC 20546-0001, USA

FOREWORD

Attention is drawn to the possibility that some of the elements of this document may be the subject of patent rights. CCSDS shall not be held responsible for identifying any or all such patent rights. Attention is drawn to the possibility that some of the elements of this document may be the subject of patent rights. CCSDS shall not be held responsible for identifying any or all such patent rights.

Through the process of normal evolution, it is expected that expansion, deletion, or modification of this document may occur.  This Recommended Standard is therefore subject to CCSDS document management and change control procedures, which are defined in Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-3).  Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be addressed to the CCSDS Secretariat at the address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- China National Space Administration (CNSA)/People’s Republic of China.

- Deutsches Zentrum für Luft- und Raumfahrt e.V. (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (FSA)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

- UK Space Agency/United Kingdom.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- China Satellite Launch and Tracking Control General, Beijing Institute of Tracking and Telecommunications Technology (CLTC/BITTT)/China.

- Chinese Academy of Sciences (CAS)/China.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- CSIR Satellite Applications Centre (CSIR)/Republic of South Africa.

- Danish National Space Center (DNSC)/Denmark.

- Departamento de Ciência e Tecnologia Aeroespacial (DCTA)/Brazil.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Geo-Informatics and Space Technology Development Agency (GISTDA)/Thailand.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Korea Aerospace Research Institute (KARI)/Korea.

- Ministry of Communications (MOC)/Israel.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic and Atmospheric Administration (NOAA)/USA.

- National Space Agency of the Republic of Kazakhstan (NSARK)/Kazakhstan.

- National Space Organization (NSPO)/Chinese Taipei.

- Naval Center for Space Technology (NCST)/USA.

- Scientific and Technological Research Council of Turkey (TUBITAK)/Turkey.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- United States Geological Survey (USGS)/USA.

PREFACE

This document is a draft CCSDS Recommended Standard.    Its ‘White Book’ status indicates that its contents are not stable, and several iterations resulting in substantial technical changes are likely to occur before it is considered to be sufficiently mature to be released for review by the CCSDS Agencies.

Implementers are cautioned not to fabricate any final equipment in accordance with this document’s technical content.

Recipients of this draft are invited to submit, with their comments, notification of any relevant patent rights of which they are aware and to provide supporting documentation.

# DOCUMENT CONTROL

| Document | Title and Issue | Date | Status |
| --- | --- | --- | --- |
| CCSDS 910.NN-R-0 | Planning Information Specification, Draft 0.0 | October 2013 | White Book |
| CCSDS 910.NN-R-0.1 | Planning Information Specification, Draft 0.1 | October 2013 | White Book |
| CCSDS 910.NN-R-0.2 | Planning Data Formats, Draft 0.2 | July 2014 | White Book |
| CCSDS 902.2-W-0.03 | Planning Data Formats, Draft 0.3 – revisions to planning data format | August 2014 | White Book |
| CCSDS 902.2-W-0.04 | Planning Data Formats, Draft 0.4 – additions to planning data. Definition of planning request and planning request refinement added | November 2014 | White Book |

# CONTENTS

Section	Page

DOCUMENT CONTROL	vi

CONTENTS	vii

1	Introduction	1-11

1.1	PURPOSE AND SCOPE	1-11

1.1.1	PURPOSE	1-11

1.1.2	SCOPE	1-11

1.2	APPLICABILITY	1-12

1.3	RATIONALE	1-12

1.3.1	USE CASES	1-12

1.4	DOCUMENT STRUCTURE	1-13

1.5	DEFINITIONS	1-13

1.6	NOMENCLATURE	1-14

1.7	CONVENTIONS	1-14

1.7.1	THE UNIFIED MODELING LANGUAGE	1-14

1.8	References	1-14

2	Overview	2-1

2.1	GENERAL	2-1

2.2	Planning Data Formats	2-1

2.3	MAPPING TO W3C XML SCHEMA	2-1

3	Planning REQUEST	3-1

3.1	Planning Request CONTENT/STRUCTURE	3-1

3.1.1	CLASS SPlanningRequestHeader PARAMETERS	3-2

3.1.2	Class PlanningRequest	3-3

3.1.3	Class ServiceInfo	3-4

3.1.4	Class PassStationConstraints	3-5

3.1.5	Class PassDurationConstraints	3-5

3.1.6	Class PassIntervalConstraints	3-6

3.1.7	Class PassDailyTimeConstraints	3-7

3.1.8	Class PassRangeConstraints	3-8

3.1.9	CLASS PassDefinedEventRelativeTimeConstraints	3-9

3.1.10	CLASS PasSAdditionalEventRelativeTimeConstraints	3-10

3.1.11	CLASS PassRelativeTimeConstraints	3-10

3.1.12	CLASS DefinedEventParameter	3-11

3.1.13	CLASS AdditionalEventParameter	3-12

3.1.14	CLASS EventParameter (ABSTRACT)	3-12

3.2	Planning REFINEMENT REQUEST CONTENT/STRUCTURE	3-13

3.2.1	CLASS SPlanningRequestHeader PARAMETERS	3-14

3.2.2	Class PlanningRequest	3-15

3.2.3	Class ServiceInfo	3-16

3.2.4	Class PassStationConstraints	3-17

4	Provisional Plan	4-18

4.1	General	4-18

4.2	Provisional Plan CONTENT/STRUCTURE	4-18

4.2.1	CLASS provisionalPlanHEADER	4-19

4.2.2	CLASS DefinedEvent	4-21

4.2.3	CLASS AdditionalEvent	4-21

4.2.4	CLASS Event	4-21

4.2.5	CLASS DefinedEventParameter	4-24

4.2.6	CLASS AdditionalEventParameter	4-24

4.2.7	CLASS EventParameter (ABSTRACT)	4-24

4.3	Events	4-25

4.3.1	Event type  - COMMS	4-25

4.3.2	Event type  - DATARATE	4-29

4.3.3	Event type  - RFI	4-29

4.3.4	Event type  - CONFLICTS	4-29

4.3.5	Event type  - COSTS	4-30

4.3.6	Event type  - Other	4-30

ANNEX A XML Schema for the Simple Planning Information Format  InFormative	A-1

ANNEX B Security, SANA, and Patent Considerations  (Informative)	B-1

ANNEX C ABBreviations and ACRONYMS	C-1

(Informative)	C-1

ANNEX D Informative References  (Informative)	D-1

Figure	Page

Figure 3-1:  Planning Request Class Diagram	3-1

Figure 3-2:  Refinement Request Class Diagram	3-13

Figure 4-1:  Provisional Plan Class Diagram	4-18

Table	Page

Table 3-1: Class PlanningRequestHeader Parameters	3-2

Table 3-2: Class PlanningRequest Parameters	3-3

Table 3-3: Class PassDurationsConstraints Parameters	3-5

Table 3-4: Class PassDurationsConstraints Parameters	3-5

Table 3-5: Class PassIntervalConstraints Parameters	3-6

Table 3-6: Class PassDailyTimeConstraints Parameters	3-7

Table 3-7: Class PassRangeConstraints Parameters	3-8

Table 3-8:  PassRelativeTimeConstraints Parameters	3-10

Table 3-1: Class PlanningRequestHeader Parameters	3-14

Table 3-2: Class PlanningRequest Parameters	3-15

Table 3-3: Class PassDurationsConstraints Parameters	3-17

Table 4-1:  Class ProvisonalPlanHeader Parameters	4-19

Table 4-2:  Event Parameters	4-21

Table 4-3:  Class EventParameter Parameters	4-24

Table 4-4:  Predicted communications geometry events	4-25

Table 4-5: AOS Event Parameters	4-26

Table 4-6: LOS Event Parameters	4-26

Table 4-7: Elevation-Ascending Event Parameters	4-26

Table 4-8: Elevation-Descending Event Parameters	4-26

Table 4-9: Maximum-Elevation Event Parameters	4-27

Table 4-10: Occultation-Start Event Parameters	4-27

Table 4-11: Occultation-End Event Parameters	4-27

Table 4-12: SAA Event Parameters	4-27

Table 4-13: Range Event Parameters	4-28

Table 4-14: OWLT Event Parameters	4-28

Table 4-15: Coms-Start Event Parameters	4-28

Table 4-16: Coms-End Event Parameters	4-28

Table 4-17: Keyhole Event Parameters	4-29

Table 4-18: Cable-Wrap Event Parameters	4-29

Table 4-19:  Sustainable data rates and volume estimate events	4-29

Table 4-20:  Predicted radio frequency interference events	4-29

Table 4-21:  Predicted resource conflict events	4-30

Table 4-22:  Cost Estimates	4-30

# Introduction

## PURPOSE AND SCOPE

### PURPOSE

This Planning Information Format Recommended Standard specifies a standard format for use in transferring planning information related to groundstations and/or relay satellites between space agencies and commercial or governmental spacecraft operators. Such exchanges are used in;

- Mission design, i.e. in investigating the feasibility of a mission with respect to its uplink/downlink requirements and the availability of suitable groundstation/relay satellite availability.

- Operation planning, i.e. to request the allocation of sufficient groundstation/relay satellite resources in order to carry out the planned operations, this typical is an iterative process with the details becoming more refined as the execution time of the operations approach. The operations planning often fits into 3 phases;

  - Long Term Planning – this phase is typically several months or more before the execution time of the operations

  - Medium Term Planning – typically this is a few weeks before the execution of the operations and involves a refinement of the Long term plan based on updated orbit/trajectory/attitude predictions, possible changes to science objectives etc.

  - Short Term Planning – typically this is one occurs 1 – 2 weeks before the execution of the operations and usually involves only minor refinements to the plan based on further the latest orbit/trajectory/attitude predictions.

### SCOPE

The scope of this Recommended Standard is limited to the exchange of Planning Information required in the context of CCSDS Service Management.

#### Planning Requests

TBW – should be consistent with section 5.2 of Green Book

#### Provisional Plans

TBW – should be consistent with section 5.3 of Green Book

## APPLICABILITY

This Recommended Standard is applicable only to the planning data formats and contents, but not to its transmission. With respect to the transmission of the Planning Information between agencies and operators there are two scenarios:

- The first is where the Planning Information is exchanged within the context of Service management, in this case the transmission mechanism is described in [TBD].

- The second deals with the case where the Planning Information is exchanged outwith the scope of Service Management. Here the mechanism by which the Planning Information is transmitted is outside of the scope of this document and should be specified in an ICD agreed by the parties involved.

## RATIONALE

The primary goal of CCSDS is to increase the level of interoperability among Agencies.  This Recommended Standard furthers that goal by establishing the means to exchange planning information relating to where most cross support activity occurs: between the tracking stations or ground data handling systems of various Agencies and the mission specific components of a mission ground system.

The use cases described in the following sections were considered in deriving this Recommended Standard.

### USE CASES

#### Mission Design

During the design phase of a mission it is often desirable to be able to obtain some idea of the availability of ground station/relay satellite availability so that the feasibility of obtaining the required uplink and downlink bandwidth can be assessed. Typically, during the mission design phase, the information required relates to periods several years in the future.  Currently there is no standardized way for specifying the mission requirements and constraints between different agencies.

Whilst this recommended standard does not address the mechanism by which the required planning information can be exchanged (this possibly being covered in the negotiations involved in establishing the service agreement), it provides a standard format in which the mission requirements and constraints can be specified.

#### Mission Planning

In the mission planning use case the user agency provides the provider agency with a set of planning information that gives the provider agency the information it requires to allocate the appropriate resources to the user agency. It should be noted that this does not imply that the user agency will be allocated all the resources it requests. The allocation made by the provider agency will also take into account the needs of all users of its network and other constraints such as any limits on usage that may have been specified in the service agreement between the agencies.

It should also be noted that the planning process will typically go through a number of cycles, starting months before the actual activities are expected to take place and being finalized a few days before execution. During these planning cycles the operations will be refined as better orbit/trajectory/attitude predictions become available and/or science objectives are modified. This leads to the necessity to supply refinements to the initial planning. The format of these planning refinements is also covered in this Recommended Standard.

## DOCUMENT STRUCTURE

This document is organized as follows:

- Section 1 provides the purpose, scope, applicability, and rationale of this Recommended Standard and identifies the conventions and references used throughout the document. This section also describes how this document is organized. A brief description is provided for each section and annex so that the reader will have an idea of where information can be found in the document. It also identifies terminology that is used in this document but is defined elsewhere.

- Section 2 provides a brief overview of the CCSDS-recommended Planning Data Formats.

- Section 3 provides details about the structure and content of the Planning Request Formats.

- Section 4 provides details about the structure and content of the Provisional Plan Format.

- Annex A provides the normative Protocol Implementation Conformance Statement (PICS) proforma.

- Annex B discusses security, SANA, and patent considerations.

- Annex C contains a list of Acronyms applicable to the Simple Schedule

- Annex D is a list of informative references.

## DEFINITIONS

For the purposes of this document, the following definitions apply:

- the word ‘agencies’ may also be construed as meaning ‘satellite operators’ or ‘satellite service providers’;

- the notation ‘n/a’ signifies ‘not applicable’;

## NOMENCLATURE

The following conventions apply throughout this Recommended Standard:

- the words ‘shall’ and ‘must’ imply a binding and verifiable specification;

- the word ‘should’ implies an optional, but desirable, specification;

- the word ‘may’ implies an optional specification;

- the words ‘is’, ‘are’, and ‘will’ imply statements of fact.

## CONVENTIONS

### THE UNIFIED MODELING LANGUAGE

The Unified Modelling Language (UML) diagrams used in the specification (including class diagrams, package diagrams, sequence diagrams and activity diagrams) follow the notation, semantics and conventions imposed by the Version 2.4.1 UML specification of the Object Management Group (OMG) [6].

Within the document use is made only of class diagrams. A UML class diagram describes the structure of a message; its parts; and how those parts interrelate. A UML class, represented in the diagram as a box, represents a data set. Class diagram conventions include composition, generalization, multiplicity and constraints. Enumeration notation is also used but only when it is involved in a composition constraint.

## References

The following publications contain provisions which, through reference in this text, constitute provisions of this document.  At the time of publication, the editions indicated were valid.  All publications are subject to revision, and users of this document are encouraged to investigate the possibility of applying the most recent editions of the publications indicated below.  The CCSDS Secretariat maintains a register of currently valid CCSDS publications.

[1]	Space Communication Cross Support—Service Management—Service Specification. Recommended Standard for Space Data System Standards, CCSDS 910.11-B-1. Blue Book. Issue 1. Washington, D.C.: CCSDS, August 2009.

[2]	Extensible Space Communication Cross Support Service Management—Concept. Draft Informational Report, CCSDS 902.0-G-0.38, Draft Green Book. April 2014.

[3]	Information Technology—8-Bit Single-Byte Coded Graphic Character Sets—Part 1: Latin Alphabet No. 1. International Standard, ISO/IEC 8859-1:1998. Geneva: ISO, 1998.

[4]	“CCSDS-910.NN-B-1_XML_schemas.”
http://public.ccsds.org/publications/archive/CCSDS-910.11-B-1_XML_schemas.zip.

[5]	Time Code Formats. Recommendation for Space Data System Standards, CCSDS 301.0-B-3. Blue Book. Issue 3. Washington, D.C.: CCSDS, January 2002.

[6]	OMG Unified Modelling Language (OMG UML), Version 2.4.1, OMG Document Number: formal/2011-08-05.

[7]	Simple Schedule Format. Recommendation for Space Data System Standards, CCSDS nnn.n-B-1. Blue Book. Issue 1. Washington, D.C.: CCSDS, xxxx 20xx.

# Overview

## GENERAL

This section provides a high-level overview of the CCSDS-recommended Planning Data  Formats, which is designed to facilitate standardized exchanges of planning information between space agencies.

## Planning Data Formats

The planning data consists of files that are XML formatted. The formats of these files are suitable for automated interaction and/or (by means of a suitable XML viewer) human interaction.

Planning data is either mandatory, in which case suitable values must be present, or optional, in which case values may be present or not. In addition it is possible to extend the contents of the various planning data formats by defining additional parameters. The content of any parameters defined is outside the scope of this document and should be documented in an ICD agreed by the involved parties.

## MAPPING TO W3C XML SCHEMA

This Recommended Standard includes the specification of a mapping to World Wide Web Consortium (W3C) Extensible Markup Language (XML) schema. The normative mapping of this Recommended Standard to XML W3C schemas is a virtual annex to this Recommended Standard and is contained in a stand-alone set of schema files (reference [4]).

NOTE – The XML schema has been elaborated on the basis of the mapping guidelines described in reference [D1].

# Planning REQUEST

Planning Requests shall consist of digital data exchanged in the form of a file. There are two types of planning data foreseen and these are discussed in the following sections.

## Planning Request CONTENT/STRUCTURE

The planning request is intended to permit the requesting of services from a service provider. Figure 3-1 shows the UML Class diagram for the Planning Request.

Figure 3-1:  Planning Request Class Diagram

The attributes of each class are described further in the following subsections and tables.

### CLASS SPlanningRequestHeader PARAMETERS

#### The PlanningRequestHeader class is mandatory and shall constitute the ‘header’ of a Planning Request.

#### The PlanningRequestHeader  class parameters specified in Table 3-1 shall be used to identify the originating organization, status of the planning request, the version, the time at which the request was generated, the time at which the request starts, the time at which it ends.

Table 3-1: Class PlanningRequestHeader Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| originatingOrganization | The organization that generated the planning request. | String1024—Permitted values registered in SANA | n/a |
| generationTime | Time at which the planning request was generated. | CCSDS ASCII Time Code B (reference [5]) | UTC |
| requestStatus | The status of the request. | Enumeration TEST indicates that the request has been generated for test purposes only. PROVISIONAL indicates that the request contained is provisional and may still be subject to change. OPERATIONAL indicates that this is an operational planning request.. |  |
| provisonalPlanVersion | The version of the request. This increments by 1 every time a request for the same request status and time range is generated (i.e., has the same requestPeriodStartTime and requestPeriodEndTime). | Positive Integer | n/a |
| requestPeriodStartTime | The earliest time to which the request applies. | CCSDS ASCII Time Code B (reference [5]) | UTC |
| requestPeriodEndTime | The latest time to which the request applies. | CCSDS ASCII Time Code B (reference [5]) | UTC |
| serviceAgreementXRef | Optional Parameter. This parameter permits the inclusion of a cross reference to the service agreement under which the request operations will be carried out. | String1024 (TBC) | n/a |

### Class PlanningRequest

#### The PlanningRequest class is mandatory and contains details of the request that is to be planned, including the minimum and maximum number of passes that are required in a specifiable time interval.

#### The parameters of the PlanningRequest class are specified in Table 3-2 below.

#### There shall be one or more instances of the PlanningRequest class for each instance of the PlanningRequestHeader class.

Table 3-2: Class PlanningRequest Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| user | The user to which the event is relevant. These will typically be spacecraft names as specified in SANA. | String1024—Permitted values registered in SANA | n/a |
| minimumNumberOfPasses | The minimum number of passes required in the specified time interval. | Integer > 0 | n/a |
| maximumNumberOfPasses | The maximum number of passes required in the specified time interval. | Integer ≥ minimumNumberOfPasses | n/a |
| typeOfTimeUnits | The type of time unit within which the minimum and maximum number of passes shall occur. | Enumeration DAY(S) indicates that the required number of passes shall occur within the specified number of days. WEEK(S) indicates that the required number of passes shall occur within the specified number of days. REQUEST PERIOD indicates that the required number of passes shall occur within the period covered by the request.. | n/a |
| numberOfTimeUnits | Optional parameter. If the typeOfTimeUnits is specified as DAY(S) or WEEK(S) then this parameter is used to specify the required number of days or weeks. If it is omitted the parameter defaults to 1. This parameter has no meaning if the typeOfTimeUnits is specified as REQUEST PERIOD. | Integer >0 Default value if omitted is 1 | n/a |

### Class ServiceInfo

#### The ServiceInfo class is mandatory and is used to specify information related to the service required in the planning request.

#### The ServiceInfo class is fully defined in section 3.2.7 of the Simple Schedule Format Blue Book, reference [7].

#### There shall be one or one instances of the ServiceInfo class for each instance of the PlanningRequest class.

### Class PassStationConstraints

#### The PassStationConstraints class is optional and  can be used to specify the groundstation at which the pass is desired.

#### The parameters of the PassStationConstraints class are specified in Table 3-3 below.

#### There shall be zero or more instances of the PassStationConstraints class for each instance of the PlanningRequest class. If no PassStationConstraints class is specified it is assumed that any station can be used

Table 3-3: Class PassDurationsConstraints Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| stationName | Name of the station (ground or spacecraft) required | String1024—Permitted values registered in SANA | n/a |
| stationPriority | Optional Parameter. This can be used to specify a preference for which station is used if more than one PassStationConstraints class is instantiated. The lower the value specified here the higher the priority, with 1 being the highest prority. | Integer >0 Default value if omitted is 1 | n/a |

### Class PassDurationConstraints

#### The PassDurationsConstraints class is optional and  can be used to permit the specification of the minimum and/or maximum duration of a pass.

#### The parameters of the PassDurationsConstraints class are specified in Table 3-4 below.

#### There shall be zero or one instances of the PassDurationsConstraints class for each instance of the PlanningRequest class.

Table 3-4: Class PassDurationsConstraints Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| minimumDuration | Optional parameter. This is used to specify the minimum duration required for a pass. | Integer ≥ 0 Default value if omitted is 0 | Seconds |
| maximumDuration | Optional parameter. This is used to specify the maximum duration required for a pass. NOTE: If both minimumDuration and maximumDuration are specified then maximumDuration ≥ minimumDuration | Integer ≥ 0 Default value if omitted is ∞ | Seconds |

### Class PassIntervalConstraints

#### The PassIntervalConstraints class is optional and  can be used to permit the specification of the minimum and/or maximum intervals between passes.

#### The parameters of the PassIntervalConstraints class are specified in Table 3-5 below.

#### There shall be zero or one instances of the PassIntervalConstraints class for each instance of the PlanningRequest class.

Table 3-5: Class PassIntervalConstraints Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| minimumIntervalBetweenPasses | Optional parameter. This is used to specify the minimum interval required between passes. | Integer ≥ 0 Default value if omitted is 0 | Seconds |
| maximumIntervalBetweenPasses | Optional parameter. This is used to specify the maximum interval required between passes. NOTE: If both minimumIntervalBetweenPasses and maximumIntervalBetweenPasses are specified then maximumIntervalBetweenPasses ≥ minimumIntervalBetweenPasses | Integer ≥ 0 Default value if omitted is ∞ | Seconds |

### Class PassDailyTimeConstraints

#### The PassDailyTimeConstraints class is optional and  can be used to permit the specification of the earliest and/or latest absolute (UTC) times for passes. The use of these constraints could be used for example to limit passes to being only during normal working hours etc..

#### The parameters of the PassDailyTimeConstraints class are specified in Table 3-6 below.

#### There shall be zero or one instances of the PassDailyTimeConstraints class for each instance of the PlanningRequest class.

Table 3-6: Class PassDailyTimeConstraints Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| earliestPassStart | Optional parameter. Used to specify (in UTC) the earliest time during the day at which a pass can start. | String8 of format hh:mm:ss Where hh = Hour in two-character subfield with values 00-23 mm = Minute in two-character subfield with values 00-59 ss = Second in two-character subfield with values 00-59 (-58 or -60 during leap seconds) | n/a |
| latestPassStart | Optional parameter. Used to specify (in UTC) the latest time during the day at which a pass can start. NOTE: If both earliestPassStart and latestPassStart are specified then latestPassStart ≥ earliestPassStart | String8 of format hh:mm:ss Where hh = Hour in two-character subfield with values 00-23 mm = Minute in two-character subfield with values 00-59 ss = Second in two-character subfield with values 00-59 (-58 or -60 during leap seconds) | n/a |
| earliestPassEnd | Optional parameter. Used to specify (in UTC) the earliest time during the day at which a pass can end. | String8 of format hh:mm:ss Where hh = Hour in two-character subfield with values 00-23 mm = Minute in two-character subfield with values 00-59 ss = Second in two-character subfield with values 00-59 (-58 or -60 during leap seconds) | n/a |
| latestPassEnd | Optional parameter. Used to specify (in UTC) the latest time during the day at which a pass can end. NOTE: If both earliestPassEnd and latestPassEnd are specified then latestPassEnd ≥ earliestPassEnd | String8 of format hh:mm:ss Where hh = Hour in two-character subfield with values 00-23 mm = Minute in two-character subfield with values 00-59 ss = Second in two-character subfield with values 00-59 (-58 or -60 during leap seconds) | n/a |

### Class PassRangeConstraints

#### The PassRangeConstraints class is optional and  can be used to permit the specification of the minimum and/or maximum range between the spacecraft and groundstation for the start and/or end of a pass.

#### The parameters of the PassRangeConstraints class are specified in Table 3-7 below.

#### There shall be zero or one instances of the PassRangeConstraints class for each instance of the PlanningRequest class.

Table 3-7: Class PassRangeConstraints Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| minimumRangeAtPassStart | Optional parameter. Used to specify the minimum range required at the pass start. | Integer ≥ 0 | Kilometres |
| maximumRangeAtPassStart | Optional parameter. Used to specify the maximum range required at the pass start. NOTE: If both minimumRangeAtPassStart and maximumRangeAtPassStart are specified then maximumRangeAtPassStart ≥ minimumRangeAtPassStart | Integer ≥ 0 | Kilometres |
| minimumRangeAtPassEnd | Optional parameter. Used to specify the minimum range required at the pass end. | Integer ≥ 0 | Kilometres |
| maximumRangeAtPassEnd | Optional parameter. Used to specify the maximum range required at the pass start. NOTE: If both minimumRangeAtPassEnd and maximumRangeAtPassEnd are specified then maximumRangeAtPassEnd ≥ minimumRangeAtPassEnd | Integer ≥ 0 | Kilometres |

### CLASS PassDefinedEventRelativeTimeConstraints

#### The PassDefinedEventRelativeTimeConstraints class is optional and may be used to specify pass start/end timing constraints with respect to Events that are defined in this recommendation.

NOTE	–	The PassDefinedEventRelativeTimeConstraints class is a specialization of class PassRelativeTimeConstraints described in section 3.1.11 below, and the description of the parameters is given in that subsection.

#### There  shall be zero or more instances of the PassDefinedEventRelativeTimeConstraints class for each instance of the PlanningRequest class.

#### The various events defined in this recommendation are as specified in section 4.3 below.

### CLASS PasSAdditionalEventRelativeTimeConstraints

#### The PassAdditionalEventRelativeTimeConstraints class is optional and may be used to specify pass start/end timing constraints with respect to Events that are not defined in this recommendation. The need for this may arise if it is found that in certain cases (or missions) the Events  defined in this recommendation are not sufficient and additional Events are required..

NOTE	–	The PassAdditionalEventRelativeTimeConstraints class is a specialization of class PassRelativeTimeConstraints described in section 3.1.11 below, and the description of the parameters is given in that subsection.

#### There  shall be zero or more instances of the PassAdditionalEventRelativeTimeConstraints class for each instance of the PlanningRequest class.

#### The usage of additional Events is not within the scope of this document and should be specified in an ICD between the relevant parties.

### CLASS PassRelativeTimeConstraints

#### The PassRelativeTimeConstraints class is mandatory and shall be used to specify pass start/end timing constraints with respect to Events.

#### The PassRelativeTimeConstraints class parameters specified in Table 3-8 below.

Table 3-8: Class PassRelativeTimeConstraints Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| event | The event. The various different events defined in this standard are described in section 4.3 below. | Enumeration. | See section 4.3 below. |
| earliestDeltaTimeForPassStart | Optional parameter. If this is specified it is added to the time at which the event occurs and this time is taken to be the earliest the pass can start relative to the event. | Integer ≥ 0 | Seconds |
| latestDeltaTimeForPassStart | Optional parameter. If this is specified it is added to the time at which the event occurs and this time is taken to be the latest the pass can start relative to the event. NOTE: If values for both earliestDeltaTimeForPassStart and latestDeltaTimeForPassStart are specified they must be such that the latest time the pass can start is after the earliest time it can start | Integer ≥ 0 | Seconds |
| earliestDeltaTimeForPassEnd | Optional parameter. If this is specified it is added to the time at which the event occurs and this time is taken to be the earliest the pass can end relative to the event. | Integer ≥ 0 | Seconds |
| latestDeltaTimeForPassEnd | Optional parameter. If this is specified it is added to the time at which the event occurs and this time is taken to be the latest the pass can end relative to the event. NOTE: If values for both earliestDeltaTimeForPassEnd and latestDeltaTimeForPassEnd are specified they must be such that the latest time the pass can end is after the earliest time it can end. | Integer ≥ 0 | Seconds |

### CLASS DefinedEventParameter

See Section 4.2.5.

### CLASS AdditionalEventParameter

See Section 4.2.6 below

### CLASS EventParameter (ABSTRACT)

See Section 4.2.7 below.

## Planning REFINEMENT REQUEST CONTENT/STRUCTURE

The Planning Refinement Request is intended to permit the refinement of planning requests which have previously been submitted and processed and the results returned to the requestor via the provisional plan discussed in section 3.2.1 below. It is expected that only minor changes will be carried out via this mechanism and consequently the only operations forseen are;

- Delete a specified pass

- Modify the start time (AOS) of a specified pass

- Modify the end time (LOS) of a specified pass

Figure 3-2 shows the UML Class diagram for the Refinement Request.

Figure 3-2:  Refinement Request Class Diagram

The attributes of each class are described further in the following subsections and tables.

### CLASS SPlanningRefinmentHeader PARAMETERS

#### The PlanningRefinementHeader class is mandatory and shall constitute the ‘header’ of a Planning Refinement Request.

#### The PlanningRefinementHeader  class parameters specified in Table 3-9 shall be used to identify the originating organization, status of the planning refinement request, the version, the time at which the request was generated, the time at which the request starts, the time at which it ends.

Table 3-9: Class PlanningRefinementHeader Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| originatingOrganization | The organization that generated the refinement request. | String1024—Permitted values registered in SANA | n/a |
| generationTime | Time at which the refinement request was generated. | CCSDS ASCII Time Code B (reference [5]) | UTC |
| requestStatus | The status of the refinement request. | Enumeration TEST indicates that the refinement request has been generated for test purposes only. PROVISIONAL indicates that the refinement request contained is provisional and may still be subject to change. OPERATIONAL indicates that this is an operational planning refinement request. |  |
| provisonalPlanVersion | The version of the request. This increments by 1 every time a request for the same refinement request status and time range is generated (i.e., has the same requestPeriodStartTime and requestPeriodEndTime). | Positive Integer | n/a |
| requestPeriodStartTime | The earliest time to which the refinement request applies. | CCSDS ASCII Time Code B (reference [5]) | UTC |
| requestPeriodEndTime | The latest time to which the r refinement equest applies. | CCSDS ASCII Time Code B (reference [5]) | UTC |
| serviceAgreementXRef | Optional Parameter. This parameter permits the inclusion of a cross reference to the service agreement under which the refinement request operations will be carried out. | String1024 (TBC) | n/a |

### Class RefinementRequest

#### The RefinementRequest class is mandatory and contains details of the request that is to be refined, specifying the AOS and LOS Events IDs and times..

#### The parameters of the RefinementRequest class are specified in Table 3-10 below.

#### There shall be one or more instances of the RefinementRequest class for each instance of the PlanningRefinementHeader class.

Table 3-10: Class RefinementRequest Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| user | The user to which the event is relevant. These will typically be spacecraft names as specified in SANA. | String1024—Permitted values registered in SANA | n/a |
| AOSEventIdentifier | This is the AOS event identifier specified in the provisional plan which is used as the basis for creating the refinement request. | String1024 | n/a |
| AOSEventTime | The time at which AOS event occurs in the provisional plan which is used as the basis for creating the refinement request. | CCSDS ASCII Time Code B (reference [5]) | UTC |
| LOSEventIdentifier | This is the LOS event identifier specified in the provisional plan which is used as the basis for creating the refinement request. | String1024 | n/a |
| LOSEventTime | The time at which LOS event occurs in the provisional plan which is used as the basis for creating the refinement request. | CCSDS ASCII Time Code B (reference [5]) | UTC |
| refinementType | Specifies the type of the refinement request. | Enumeration DELETE indicates that specified pass is not required and can be deleted. MODIFY indicates that the refinement request specifies that the AOS and/or LOS times of the pass should be modified. | n/a |

### Class ServiceInfo

#### The ServiceInfo class is mandatory and is used to specify information related to the service affected by the refinement request.

#### The ServiceInfo class is fully defined in section 3.2.7 of the Simple Schedule Format Blue Book, reference [7].

#### There shall be one or one instances of the ServiceInfo class for each instance of the RefinementRequest class.

### Class ModifiedTimes

#### The ModifiedTimes class is optional and  can be used to specify the new AOS and/or LOS times desired.

#### The parameters of the ModifiedTimes class are specified in Table 3-11 below.

#### There shall be zero or one instances of the ModifiedTimes class for each instance of the RefinementRequest class. If  the refinementType is “DELETE” then no ModifiedTimes class is required. For the refinementType of “MODIFY” one instance of the ModifiedTimes class must be specified which holds the new AOS or LOS times requested.

Table 3-11: Class PassDurationsConstraints Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| stationName | Name of the station (ground or spacecraft) required | String1024—Permitted values registered in SANA | n/a |

# Provisional Plan

## General

The Provisional Plan shall consist of digital data exchanged in the form of a file.

## Provisional Plan CONTENT/STRUCTURE

Figure 4-1 shows the UML Class diagram for the Provisional Plan.

Figure 4-1:  Provisional Plan Class Diagram

The attributes of each class are described further in the following subsections and tables.

### CLASS provisionalPlanHEADER

#### The ProvisonalPlanHeader class is mandatory and shall constitute the ‘header’ of the Provisional Plan.

#### The ProvisonalPlanHeader class parameters specified in Table 4-1 shall be used to identify the originating organization, status of the schedule, status version, the time at which the schedule was generated, the time at which the schedule starts, the time at which it ends and the type(s) of the contained Provisional Plan data.

Table 4-1:  Class ProvisonalPlanHeader Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| originatingOrganization | The organization that generated the provisional plan. | String1024—Permitted values registered in SANA | n/a |
| generationTime | Time at which the schedule was generated. | CCSDS ASCII Time Code B (reference [5]) | UTC |
| provisonalPlanStatus | The status of the provisional plan. | Enumeration TEST indicates that the provisional plan has been generated for test purposes only. PROVISIONAL indicates that the provisional plan contained is provisional and may still be subject to change. OPERATIONAL indicates that this is an operational provisional plan. |  |
| provisonalPlanVersion | The version of the provisional plan. This increments by 1 every time a provisional plan for the same provisional plan status and time range is generated (i.e., has the same provisionalPlanStartTime and provisionalPlanEndTime). | Positive Integer | n/a |
| provisonalPlanStartTime | The time at which the schedule starts. | CCSDS ASCII Time Code B (reference [5]) | UTC |
| provisonalPlanEndTime | The time at which the schedule ends. | CCSDS ASCII Time Code B (reference [5]) | UTC |
| provisonalPlanType | This specifies the type of data that is contained in the provisional plan. The various types of data that can be contained in a provisional plan are discussed in reference [2], section 5.3. A provisional plan may contain 1 or more of these different planning types. | Enumeration COMMS Predicted communications geometry events (see reference [2], section 5.6) DATARATE Sustainable data rates & volume estimate events (see reference [2], section 5.7); RFI Predicted radio frequency interference events (see reference [2], section 5.8); CONFLICTS Predicted resource conflict events (see reference [2], section 5.9) COSTS Cost estimates (see reference [2], section 5.10) | n/a |

### CLASS DefinedEvent

#### The DefinedEvent class is optional and may be used to permit the instantiation of  Events that are defined in this recommendation.

NOTE	–	The DefinedEvent class is a specialization of class Event described in 4.2.4 below, and the description of the parameters is given in that subsection.

#### There  shall be zero or more instances of the DefinedEvent class for each instance of the ProvisionalPlanHeader class.

#### The various events defined in this recommendations are as specified in section 4.3 below.

### CLASS AdditionalEvent

#### The AdditionalEvent class is optional and may be used to permit the instantiation of Events that are not defined in this recommendation. The need for this may arise if it is found that in certain cases (or missions) the Events  defined in this recommendation are not sufficient and additional Events are required..

NOTE	–	The AdditionalEvent class is a specialization of class Event described in 4.2.4 below, and the description of the parameters is given in that subsection.

#### There  shall be zero or more instances of the AdditionalEvent class for each instance of the ProvisionalPlanHeader class.

#### The usage of these additional Events is not within the scope of this document and should be specified in an ICD between the relevant parties.

### CLASS Event

#### The Event class is mandatory and shall constitute the information about an event forming part of the provisional plan..

#### The Event class parameters specified in Table 4-2 shall be used to identify the information about an event.

Table 4-2:  Event Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| user | The user to which the event is relevant. These will typically be spacecraft names as specified in SANA. | String1024—Permitted values registered in SANA | n/a |
| eventType | This specifies the type of the event. The various types of event that can be contained in a provisional plan are discussed in reference [2], section 5.3. | Enumeration COMMS Predicted communications geometry events (see reference [2], section 5.6) DATARATE Sustainable data rates & volume estimate events (see reference [2], section 5.7); RFI Predicted radio frequency interference events (see reference [2], section 5.8); CONFLICTS Predicted resource conflict events (see reference [2], section 5.9) COSTS Cost estimates (see reference [2], section 5.10) OTHER Any event type not covered by the above list. | n/a |
| event | The event. The various different events of each eventType are described in section 4.3 below. | Enumeration. For the permitted event of each eventType please see section 4.3 below. | See section 4.3 below. |
| eventIdentifier | An identifier that is unique for every occurrence of a particular event in a provisional plan. NOTE – If a provisional plan is regenerated, then the eventIdentifier for a particular event may change. | String1024 | n/a |
| eventTime | The time at which either: The event occurs or The start time of the event. | CCSDS ASCII Time Code B (reference [5]) | UTC |
| eventDuration | Optional parameter. In the case where an event has a non-zero duration then this parameter is used to specify the length of the event. | Any suggestions for an appropriate format, Picoseconds maybe ? (I’m not really sure any of the CCSDS time formats are suitable). | TDB |
| eventOrbitNumber | Optional parameter. The Orbit Number on which the eventTime (see Table 4-2) occurs. If this is not relevant (e.g., deep space missions) or not available, this parameter shall be omitted. | Non-Negative Integer | n/a |
| timelineId | Optional parameter. A provisional plan can be considered as being composed of a number of timelines, where each timeline refers only to the occurrences of one particular event (and its counterpoint event if appropriate, e.g. AOS/LOS). This parameter can optionally be used to specify which timeline the event actually belongs to. NOTE: This parameter will only be useful in the case where use is being made of any timeline standard that is defined by CCSDS. | String1024 ??? | n/a |

### CLASS DefinedEventParameter

#### The DefinedEventParameter class is optional and may be used to permit the instantiation of parameters for an Event that is defined in this recommendation..

NOTE	–	The DefinedEventParameter class is a specialization of class EventParameter described in 4.2.7 below, and the description of the parameters is given in that subsection.

#### There  shall be zero or more instances of the DefinedEventParameter class for each instance of the DefinedEvent class.

#### The parameters that are expected to be associated with the various events defined in this recommendations are as specified in section 4.3 below.

### CLASS AdditionalEventParameter

#### The AdditionalEventParameter class is optional and may be used to permit the instantiation of additional parameters for an Event. The need for this may arise if it is found that in certain cases (or missions) the parameters defined in this recommendation are not sufficient and additional information is required.

NOTE	–	The AdditionalEventParameter class is a specialization of class Parameter described in 4.2.7 below, and the description of the parameters is given in that subsection.

#### There  shall be zero or more instances of the AdditionalEventParameter class for each instance of the DefinedEvent class.

#### There  shall be zero or more instances of the AdditionalEventParameter class for each instance of the AdditionalEvent class.

#### The usage of these additional parameters is not within the scope of this document and should be specified in an ICD between the relevant parties.

### CLASS EventParameter (ABSTRACT)

#### The EventParameter class shall be used to permit the instantiation of parameters for an Event by allowing the specification of parameter name/value pairs using the parameters specified in Table 4-3.

Table 4-3:  Class EventParameter Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| parameterName | Name of the parameter. | String1024 | n/a |
| parameterValue | The value of the required parameter. | As required by the additional parameter | As required by the additional parameter |

## Events

### Event type  - COMMS

This event type deals with predicted communications geometry events (see reference [2], section 5.6) and are as specified in Table 4-4:

Table 4-4:  Predicted communications geometry events

| Event | Description | Defined Parameter(s) |
| --- | --- | --- |
| AOS | Acquisition of signal by station (ground or spacecraft) | See section 4.3.1.1 below |
| LOS | Loss of signal by station (ground or spacecraft) | See section 4.3.1.2 below |
| Elevation-Ascending | Ascending angle of elevation with respect to station (ground or spacecraft) | See section 4.3.1.3 below |
| Elevation-Descending | Descending angle of elevation with respect to station (ground or spacecraft) | See section 4.3.1.4 below |
| Maximum-Elevation | Maximum elevation with respect to station (ground or spacecraft) | See section 4.3.1.5 below |
| Occultation-Start | Start of occultation with respect to station (ground or spacecraft) | See section 4.3.1.6 below |
| Occultation-End | End of occultation with respect to station (ground or spacecraft) | See section 4.3.1.7 below |
| SAA | Sun alignment angle | See section 4.3.1.8 below |
| Range | Distance with respect to station (ground or spacecraft) | See section 4.3.1.9 below |
| OWLT | One Way Light Time with respect to station (ground or spacecraft) | See section 4.3.1.10 below |
| Coms-Start | Start of possible communication window with respect to station (ground or spacecraft) | See section 4.3.1.11 below |
| Coms-End | End of possible communication window with respect to station (ground or spacecraft) | See section 4.3.1.12 below |
| Keyhole | Keyhole occurrence at station (ground or spacecraft) | See section 4.3.1.13 below |
| Cable-Wrap | Cable wrap occurrence at station (ground or spacecraft) | See section 4.3.1.14 below |

#### AOS Event Parameters

Table 4-5: AOS Event Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| stationName | Name of the station (ground or spacecraft) with which the AOS is with. | String1024—Permitted values registered in SANA | n/a |

#### LOS Event Parameters

Table 4-6: LOS Event Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| stationName | Name of the station (ground or spacecraft) with which the LOS is with. | String1024—Permitted values registered in SANA | n/a |

#### Elevation-Ascending Event Parameters

Table 4-7: Elevation-Ascending Event Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| stationName | Name of the station (ground or spacecraft) for which the ascending elevation is specified. | String1024—Permitted values registered in SANA | n/a |
| angle | Elevation angle | Float 0 ≤ Angle ≤ 90 | Degrees |

#### Elevation-Descending Event Parameters

Table 4-8: Elevation-Descending Event Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| stationName | Name of the station (ground or spacecraft) for which the descending elevation is specified. | String1024—Permitted values registered in SANA | n/a |
| angle | Elevation angle | Float 0 ≤ Angle ≤ 90 | Degrees |

#### Maximum-Elevation Event Parameters

Table 4-9: Maximum-Elevation Event Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| stationName | Name of the station (ground or spacecraft) for which the maximum elevation is specified. | String1024—Permitted values registered in SANA | n/a |
| angle | Elevation angle | Float 0 ≤ Angle ≤ 90 | Degrees |

#### Occultation-Start Event Parameters

Table 4-10: Occultation-Start Event Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| stationName | Name of the station (ground or spacecraft) for which the occultation start is specified.. | String1024—Permitted values registered in SANA | n/a |
| celestialBody | Celestial body causing the occultation. | String1024 | n/a |

#### Occultation-End Event Parameters

Table 4-11: Occultation-End Event Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| stationName | Name of the station (ground or spacecraft) for which the occultation end is specified.. | String1024—Permitted values registered in SANA | n/a |
| celestialBody | Celestial body causing the occultation. | String1024 | n/a |

#### SAA Event Parameters

Table 4-12: SAA Event Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| angle | Sun Alignment Angle | Float 0 ≤ Angle ≤ 180 | Degrees |

#### Range Event Parameters

Table 4-13: Range Event Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| stationName | Name of the station (ground or spacecraft) for which the occultation end is specified.. | String1024—Permitted values registered in SANA | n/a |
| Distance | Distance with respect to the station | Positive Number | Metres |

#### OWLT Event Parameters

Table 4-14: OWLT Event Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| stationName | Name of the station (ground or spacecraft) for which the OWLT is specified.. | String1024—Permitted values registered in SANA | n/a |
| duration | Time taken for light to travel one way with respect to station | Any suggestions for an appropriate format, Picoseconds maybe ? (I’m not really sure any of the CCSDS time formats are suitable). | TDB |

#### Coms-Start Event Parameters

Table 4-15: Coms-Start Event Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| stationName | Name of the station (ground or spacecraft) for which the Coms-Start is specified.. | String1024—Permitted values registered in SANA | n/a |

#### Coms-End Event Parameters

Table 4-16: Coms-End Event Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| stationName | Name of the station (ground or spacecraft) for which the Coms-End is specified.. | String1024—Permitted values registered in SANA | n/a |

#### Keyhole Event Parameters

Table 4-17: Keyhole Event Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| stationName | Name of the station (ground or spacecraft) for which the Keyhole is specified.. | String1024—Permitted values registered in SANA | n/a |

#### Cable-Wrap Event Parameters

Table 4-18: Cable-Wrap Event Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| stationName | Name of the station (ground or spacecraft) for which the Cable-Wrap is specified.. | String1024—Permitted values registered in SANA | n/a |

### Event type  - DATARATE

This event type deals with sustainable data rates and volume estimate events (see reference [2], section 5.7) and are as specified in Table 4-19;

Table 4-19:  Sustainable data rates and volume estimate events

| Event | Description | Defined Parameter(s) |
| --- | --- | --- |
|  |  | See section |

### Event type  - RFI

This event type deals with predicted radio frequency interference events (see reference [2], section 5.8) and are as specified in Table 4-20;

Table 4-20:  Predicted radio frequency interference events

| Event | Description | Defined Parameter(s) |
| --- | --- | --- |
|  |  | See section |

### Event type  - CONFLICTS

This event type deals with predicted resource conflict events (see reference [2], section 5.9) and are as specified in Table 4-21;

Table 4-21:  Predicted resource conflict events

| Event | Description | Defined Parameter(s) |
| --- | --- | --- |
|  |  | See section |

### Event type  - COSTS

This event type deals with cost estimates (see reference [2], section 5.10) and are as specified in Table 4-22;

Table 4-22:  Cost Estimates

| Event | Description | Defined Parameter(s) |
| --- | --- | --- |
|  |  | See section |

### Event type  - Other

This event type consists of those events which are not covered by the above definitions. No such events are defined in this recommendation, however this category is defined as it may be useful in the definition of Additional Events.

XML Schema for the Simple Planning Information Format

InFormative

Schema Organization And Packaging

Security, SANA, and Patent Considerations

(Informative)

SecuRity Considerations

ANALYSIS OF SECURITY CONSIDERATIONS

This section presents the results of an analysis of security considerations applied to the technologies specified in this Recommended Standard.

CONSEQUENCES OF NOT APPLYING SECURITY TO THE TECHNOLOGY

The consequences of not applying security to the systems and networks on which this Recommended Standard is implemented could include potential loss, corruption, and theft of data. Since it is possible to utilize these messages in preparing and disseminating schedules relating to the availability of communications and tracking resources for spacecraft, the consequences of not applying security to the systems and networks on which this Recommended Standard is implemented could include compromise or loss of the mission if malicious tampering of a particularly severe nature occurs.

POTENTIAL THREATS AND ATTACK SCENARIOS

Potential threats or attack scenarios include, but are not limited to, (a) unauthorized access to the programs/processes that generate and interpret the messages, and (b) unauthorized access to the messages during transmission between exchange partners. Protection from unauthorized access during transmission is especially important if the mission utilizes open ground networks such as the Internet to provide ground station connectivity for the exchange of data formatted in compliance with this Recommended Standard. It is strongly recommended that potential threats or attack scenarios applicable to the systems and networks on which this Recommended Standard is implemented be addressed by the management of those systems and networks.

security concerns RELATED TO THIS RECOMMENDED STANDARD

Data Privacy

Privacy of data formatted in compliance with the specifications of this Recommended Standard should be assured by the systems and networks on which this Recommended Standard is implemented.

Data Integrity

Integrity of data formatted in compliance with the specifications of this Recommended Standard should be assured by the systems and networks on which this Recommended Standard is implemented.

Authentication of Communicating Entities

Authentication of communicating entities involved in the transport of data which complies with the specifications of this Recommended Standard should be provided by the systems and networks on which this Recommended Standard is implemented.

DATA TRANSFER BETWEEN COMMUNICATING ENTITIES

The transfer of data formatted in compliance with this Recommended Standard between communicating entities should be accomplished via secure mechanisms approved by the Information Technology Security functionaries of exchange participants.

Control of Access to Resources

Control of access to resources should be managed by the systems upon which provider formatting and recipient processing are performed.

Auditing of Resource Usage

Auditing of resource usage should be handled by the management of systems and networks on which this Recommended Standard is implemented.

UNAUTHORIZED ACCESS

Unauthorized access to the programs/processes that generate and interpret the messages should be prohibited in order to minimize potential threats and attack scenarios.

DATA SECURITY IMPLEMENTATION SPECIFICS

Specific information-security interoperability provisions that apply between agencies and other independent users involved in an exchange of data formatted in compliance with this Recommended Standard should be specified in an ICD.

SANA Considerations

[Instructions for completing the SANA Considerations subsection are contained in CCSDS 313.0-Y-1, Space Assigned Numbers Authority (SANA)—Role, Responsibilities, Policies, and Procedures (Yellow Book, Issue 1, July 2011)]

NOTE: This probably needs to be updated in view of the recent discussions about XML namespace management etc. Anybody got any ideas what the relevant references are/will be ?

Patent Considerations

No patent rights are known to adhere to any of the specifications of the proposed draft Recommended Standard.

ABBreviations and ACRONYMS

(Informative)

| ASCII | American Standard Code for Information Interchange |
| --- | --- |
| CCSDS | Consultative Committee on Space Data Systems |
| ICD | Interface Control Document |
| OMG | Object Management Group |
| SANA | Space Assigned Numbers Authority |
| TBD | To Be Decided |
| UML | Unified Modelling Language |
| UTC | Coordinated Universal Time |
| W3C | World Wide Web Consortium |
| XML | eXtensible Markup Language |

Informative References

(Informative)

[D1]	Space Communication Cross Support—Service Management—Operations Concept. Report Concerning Space Data Systems Standards, CCSDS 910.14-G-1. Green Book. Issue 1. Washington, D.C.: CCSDS, May 2011.

# Comments

No real problem with the description but it does make me wonder if there are going to be any differences in the planning data format based upon the different time frames. I suspect not really. But it does strike me that there may be a relationship with the grade of the trajectory/ephemeris input information as to how accurate the various timestamps in the planning data etc. are.  Perhaps that relationship needs to be captured relatively early in the document? That's also something perhaps to capture in the overall inter-recommendations tracking.

It seems to me that this does not quite capture the distinctions we need to make. I think it's quite possible that this is in the context of service management but that we are not necessarily using the management services in which case in ICD is still applicable for the transport. In other words, yes there is a service agreement but were not using the "automation" that CCSDS has (eventually) standardized.

I think we need to be careful here… This is really more about what is physically feasible rather than actual mission requirements and constraints although certainly physical feasibility is a part of that. And I would read it really as more constraints in that the mission cannot just simply utilize a ground station at any time without regard to the laws of physics etc.

Hours or minutes even?

I think this is deviating from the concept book… I don't believe the standing order is one of the information entities identified for standardization. The term does occur but only once in the concept book but not as a standard information entity.  From the concept book it says…

The Planning Request contains (directly or by reference) requests for Communications

Geometry information (5.7), Sustainable Data Rates & Volume Estimates (5.8), Radio

Frequency Interference information (5.9) Resource Conflicts (5.10) and/or Cost Estimates

(5.11). The Planning Request may allow for specific Provider CSSS resources to be

requested (for example to exclude or include particular apertures).

On the other hand if this is stating constraints re type of geometry info to return, etc., then okay, but I think we need to discuss this further.

Oh… wow. It actually is almost ready made standing order/shopping list request for Schedule (or service), or? At least look like a lot of “re-use” possible.

If it is needed to that extent for planning… I do not know. For LEO missions rather not.

What I miss here is the differentiation what kind of planning info types we actually request. Is it at all selectable (i.e. I want to get the geometric visibilities, but RFI does not interest me)?

The “S” in front is probybly a typo

“S” in front is a typo?

Per email exchange last month I think there are a couple different schools of thought as to how to structure this. On the one hand is the notion of a "freeform" that does not include any plan type identification such that RFI, communication geometry, costing etc. "events" can be freely intermixed (although you still might have these events somehow “typed” at lower-level) Another approach is to structure this so that events all of one type are contained within one particular list. There are clearly pluses and minuses either way and I think this needs to be further discussed.

In terms of naming of elements, if this is all understood to be a provisional plan from the outset, I don't think that we need to repeat the word "provisional" in each of the elements/parameter definitions.

Need to think about this a bit. What statuses make sense for a provisional plan ?

Cut-and-paste from the schedule of services book? In this case I think it should say when the plan starts, correct

Is this needed if we have the eventType in the Event class ?

Is this needed if we have the provisionalPlanType in the provisionalPlanHeader class ?

Do we actually need  event duration ?. I would like to get rid of this !

I know it will not help ;-) but I’m afraid when we release the book next year, this will bring a lot of questions (as timelines are – let’s say – not yet very popular). Other words, wo go with this BB already ahead of things which will come first later…

I think the description captures what we discussed at the spring meeting but any clarifications are more than welcome.

Any idea where we could get a list of names for celestial bodies ???

Any idea where we could get a list of names for celestial bodies ???