Draft Recommendation for
Space Data System Standards

Simple Schedule Format Specification

Draft Recommended Standard

CCSDS 902.1-R-1.06

Red Book

April 2015

AUTHORITY

|  | Issue: | Red Book, Draft 1.06 |  |
| --- | --- | --- | --- |
|  | Date: | April 2015 |  |
|  | Location: | Not Applicable |  |

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF AUTHORITY:)

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and represents the consensus technical agreement of the participating CCSDS Member Agencies.  The procedure for review and authorization of CCSDS documents is detailed in Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-4), and the record of Agency participation in the authorization of this document can be obtained from the CCSDS Secretariat at the e-mail address below.

This document is published and maintained by:

CCSDS Secretariat

National Aeronautics and Space Administration

Washington, DC, USA

E-mail: secretariat@mailman.ccsds.org

STATEMENT OF INTENT

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF INTENT:)

The Consultative Committee for Space Data Systems (CCSDS) is an organization officially established by the management of its members. The Committee meets periodically to address data systems problems that are common to all participants, and to formulate sound technical solutions to these problems. Inasmuch as participation in the CCSDS is completely voluntary, the results of Committee actions are termed Recommended Standards and are not considered binding on any Agency.

This Recommended Standard is issued by, and represents the consensus of, the CCSDS members.  Endorsement of this Recommendation is entirely voluntary. Endorsement, however, indicates the following understandings:

o	Whenever a member establishes a CCSDS-related standard, this standard will be in accord with the relevant Recommended Standard. Establishing such a standard does not preclude other provisions which a member may develop.

o	Whenever a member establishes a CCSDS-related standard, that member will provide other CCSDS members with the following information:

--	The standard itself.

--	The anticipated date of initial operational capability.

--	The anticipated duration of operational service.

o	Specific service arrangements shall be made via memoranda of agreement. Neither this Recommended Standard nor any ensuing standard is a substitute for a memorandum of agreement.

No later than five years from its date of issuance, this Recommended Standard will be reviewed by the CCSDS to determine whether it should: (1) remain in effect without change; (2) be changed to reflect the impact of new technologies, new requirements, or new directions; or (3) be retired or canceled.

In those instances when a new version of a Recommended Standard is issued, existing CCSDS-related member standards and implementations are not negated or deemed to be non-CCSDS compatible.  It is the responsibility of each member to determine when such standards or implementations are to be modified.  Each member is, however, strongly encouraged to direct planning for its new standards and implementations towards the later version of the Recommended Standard.

FOREWORD

Through the process of normal evolution, it is expected that expansion, deletion, or modification of this document may occur.  This Recommended Standard is therefore subject to CCSDS document management and change control procedures, which are defined in the Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-4).  Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be sent to the CCSDS Secretariat at the e-mail address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- China National Space Administration (CNSA)/People’s Republic of China.

- Deutsches Zentrum für Luft- und Raumfahrt (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (FSA)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

- UK Space Agency/United Kingdom.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- China Satellite Launch and Tracking Control General, Beijing Institute of Tracking and Telecommunications Technology (CLTC/BITTT)/China.

- Chinese Academy of Sciences (CAS)/China.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- Danish National Space Center (DNSC)/Denmark.

- Departamento de Ciência e Tecnologia Aeroespacial (DCTA)/Brazil.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Geo-Informatics and Space Technology Development Agency (GISTDA)/Thailand.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Korea Aerospace Research Institute (KARI)/Korea.

- Ministry of Communications (MOC)/Israel.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic and Atmospheric Administration (NOAA)/USA.

- National Space Agency of the Republic of Kazakhstan (NSARK)/Kazakhstan.

- National Space Organization (NSPO)/Chinese Taipei.

- Naval Center for Space Technology (NCST)/USA.

- Scientific and Technological Research Council of Turkey (TUBITAK)/Turkey.

- South African National Space Agency (SANSA)/Republic of South Africa.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- Swiss Space Office (SSO)/Switzerland.

- United States Geological Survey (USGS)/USA.

PREFACE

This document is a draft CCSDS Recommended Standard.  Its ‘Red Book’ status indicates that the CCSDS believes the document to be technically mature and has released it for formal review by appropriate technical organizations.  As such, its technical contents are not stable, and several iterations of it may occur in response to comments received during the review process.

Implementers are cautioned not to fabricate any final equipment in accordance with this document’s technical content.

Recipients of this draft are invited to submit, with their comments, notification of any relevant patent rights of which they are aware and to provide supporting documentation.

# DOCUMENT CONTROL

| Document | Title | Date | Status |
| --- | --- | --- | --- |
| CCSDS 902.1-R-1 | Simple Schedule Format Specification, Draft Recommended Standard, Issue 1 | September 2014 | Red book for Agency review |
| CCSDS 902.1-R-1.02 | Simple Schedule Format Specification, Draft Recommended Standard, Draft 1.02 | December 2014 | Updated as per RIDs from Agency review. |
| CCSDS 902.1-R-1.03 | Simple Schedule Format Specification, Draft Recommended Standard, Draft 1.03 | January 2015 | Update to ICS section to be consistent with rest of document. |
| CCSDS 902.1-R-1.05 | Simple Schedule Format Specification, Draft Recommended Standard, Draft 1.04 | April 2015 | Editorial updates Inserted new Annex C for description of SM information Entity Header schema with separate name space Inserted new Annex D for description of Simple Schedule schema with separate name space |
| CCSDS 902.1-R-1.06 | Simple Schedule Format Specification, Draft Recommended Standard, Draft 1.05 | April 2015 | Makes clear mandatory naute of XML schema and points to SANA XML Schema registry. (sections, 1.4 (c), (d), (f), and (g), 3.1, new 3.6, new A3,) |

# CONTENTS

Section	Page

1	Introduction	1-1

1.1	PURPOSE AND SCOPE	1-1

1.2	APPLICABILITY	1-2

1.3	RATIONALE	1-3

1.4	DOCUMENT STRUCTURE	1-5

1.5	DEFINITIONS	1-5

1.6	NOMENCLATURE	1-6

1.7	CONVENTIONS—THE UNIFIED MODELING LANGUAGE	1-6

1.8	References	1-7

2	Overview	2-1

2.1	GENERAL	2-1

2.2	SIMPLE SCHEDULE	2-1

2.3	MAPPING TO W3C XML SCHEMA	2-1

3	Simple Schedule	3-1

3.1	GENERAL	3-1

3.2	SIMPLE SCHEDULE CONTENT/STRUCTURE	3-2

3.3	Permitted combinations of parameters SimpleScheduleHeader – status, ScheduledPackage - user, ServiceInfo - Servicetype and ScheduledActivty –activityStatus.	3-13

3.4	Ordering of Scheduled Packages	3-14

3.5	USAGE OF SIMPLE SCHEDULE FOR Specifing ANTENNA Available FREE TIME	3-16

ANNEX A Service Management Information Entity  (Normative)	A-1

ANNEX B Implementation Conformance Statement (ICS) proforma  (Normative)	B-1

ANNEX C XML Schema for the Simple Schedule Format  (InFormative)	D-1

ANNEX D Security, SANA, and Patent Considerations  (Informative)	E-1

ANNEX E ABBreviations and ACRONYMS  (INFORMATIVE)	F-1

ANNEX F Informative References  (Informative)	G-1

ANNEX G Frequency Band Definitions  (Informative)	H-1

Figure

1-1	Simple Schedule Format in the Context of Space Communication Cross Support  Service Management.	1-2

3-1	Simple Schedule Class Diagram	3-2

3-2	Example of Ordering of Scheduled Packages in Simple Schedule	3-15

3-3	Schematic of Schedule to Illustrate Use of Simple Schedule for Antenna Free Time	3-17

C-1	XML Schema for the Simple Schedule: SimpleSchedule, ScheduledPackage, and ServicePackageXRef Types	D-2

C-2	XML Schema for the Simple Schedule: ScheduledActivity, ServiceInfo, AdditionalServiceParameter, and AdditionalActivityParameter Types	D-3

C-3	XML Spy Grid View of Example XML Document for Simple Schedule Format Schema V1.0	D-3

Table

3-1	Class SimpleSchedule Parameters	3-3

3-2	Class SimpleSchedule Parameters	3-3

3-3	Class ScheduledPackage Parameters	3-6

3-4	Class ServicePackageXRef Parameters	3-7

3-5	Class ScheduledActivity Parameters	3-8

3-6	Class ServiceInfo Parameters	3-11

3-7	Class AdditionalParameter Parameters	3-13

C-1	SimpleSchedule Parameters	D-5

C-2	ScheduledPackage Parameters	D-5

C-3	ServicePackageXRef Parameters	D-5

C-4	ScheduledActivity Parameters	D-6

C-5	ServiceInfo Parameters	D-7

C-6	AdditionalParameter Type	D-8

# Introduction

## PURPOSE AND SCOPE

### PURPOSE

This Simple Schedule Format Recommended Standard specifies a standard format for use in transferring scheduling information related to ground stations and/or relay satellites between space agencies and commercial or governmental spacecraft operators. Such exchanges are used in:

- mission design, e.g., in investigating the feasibility of a mission with respect to its uplink/downlink requirements and the availability of suitable ground station/relay satellite availability;

- mission planning, e.g., to ensure that there are sufficient ground station/relay satellite resources available to carry out the planned operations;

- mission operations, e.g., to

  - inform the spacecraft operator of the actual allocation of ground station/relay satellites to their mission;

  - inform the spacecraft operator of any unused times of the ground stations and/or relay satellites.

  - return the results of a query about ground station and/or relay satellites schedules.

### SCOPE

The scope of this Recommended Standard is limited to the exchange of Simple Schedule information. The contents of the simple schedule format described here were derived from the analysis of the standard schedule formats used by a number of space agencies/parts of space agencies. This analysis lead to the identification of a ‘core’ content that was (almost) universally present in all schedules analyzed. It was however also identified that there was a need to permit some extension to the core content to cover some use cases. Consequently an extension mechanism has been provided that can be used to add further information in the eventuality that the core content is insufficient for the required purpose.

Definition of the extended content for any specific case is outside the scope of this Recommended Standard and should be specified in an Interface Control Document (ICD) agreed between the involved parties.

While this Recommended Standard has been developed within the scope of the Space Communication Cross Support Service Management (SCCS SM) (references [G1] and [G2]) activity, it is intended that the Simple Schedule Format can be used to exchange schedule information where no other use of SCCS SM is made. In view of this, schedule data that is only of relevance when used in the scope of SCCS SM has been made optional. Thus there is no limiting dependency on Service Management in the Simple Schedule Format specification.

The following figure puts the Simple Schedule Format Specification into context with the various standards that together form the Space Communication Cross Support  Service Management.

Figure 1-1:  Simple Schedule Format in the Context of Space Communication Cross Support  Service Management.

## APPLICABILITY

This Recommended Standard is applicable only to the schedule format and content, but not to its transmission. With respect to the transmission of the Simple Schedule between agencies and operators there are two scenarios:

- The first involves exchange of the Simple Schedule within the context of SCCS SM.

- The second involves exchange of the Simple Schedule outside the scope of SCCS SM. Here the mechanism by which the Simple Schedule is transmitted is outside of the scope of this document and should be specified in an ICD agreed by the parties involved.

## RATIONALE

### General

The primary goal of CCSDS is to increase the level of interoperability among agencies.  This Recommended Standard furthers that goal by establishing the means to exchange schedule information where most cross support activity occurs: between the tracking stations or ground data handling systems of various agencies and the mission-specific components of a mission ground system.

The use cases described in the following subsections were considered in deriving this Recommended Standard.

### USE CASES

#### Mission Design

During the design phase of a mission it is often desirable to be able to obtain some idea of the availability of ground station/relay satellite availability so that the feasibility of obtaining the required uplink and downlink bandwidth can be assessed. Typically, during the mission design phase, the information required relates to periods several years in the future.  Currently there is no standardized way for obtaining this information from different agencies.

While this Recommended Standard does not address the mechanism by which the required schedule information can be requested (this possibly being covered in the negotiations involved in establishing the service agreement), it provides a standard format in which the possible availability of ground stations/relay satellites can be returned.

#### Mission Planning

In the mission planning use case the provider agency provides the user agency with a schedule that gives the user agency the information it requires to plan its spacecraft operations with respect to the availability of uplink/downlink resources. The means by which the provider agency determines the availability for the user agency can be either:

- derived from a request from the user agency;

NOTE	–	The contents and format of such a request are outside the scope of this Recommended Standard (although this may be addressed elsewhere in the SCCS SM Recommended Standard at a later date).

- derived from what is specified in the service agreement between the agencies.

The planning process will typically go through a number of cycles, starting months before the actual activities are expected to take place and being finalized a few days before execution. During these planning cycles the status of the schedule can change with the initial exchanges being of a ‘provisional’ schedule that will probably change. The final schedule provided is typically considered as ‘operational’ and can be expected to provide the actual schedule that will be executed, subject to unexpected events such as equipment failure or spacecraft emergencies.

#### Dissemination of Provider Cross Support Service System (CSSS) Schedules

It is desirable that a standardized approach be available for disseminating Provider CSSS schedules, both between agencies and also within agencies. This Recommended Standard aims to provide that. There are however differences in policies between agencies with regard to the contents of distributed schedules. Some agencies provide complete schedules to all users, containing information regarding all spacecraft supported by the agency (and possibly unallocated time as well). At the other extreme, other agencies provide only details regarding a spacecraft’s allocation to the operators of that mission.

In view of this, this Recommended Standard has been designed to be flexible enough to be able to cope with the different policies of the various agencies with respect to the information they wish to provide in disseminating their schedules.

#### Dissemination of Unallocated Time Schedules

Some agencies publish a list of unallocated time of the ground stations/relay satellites in their network. This information can be used by missions to see if it is possible to request additional coverage by using resources during periods when they would otherwise be unused.

Although not addressing the method by which the usage of unallocated resources can be requested, this Recommended Standard can be used to publish a Provider CSSS unallocated time schedule. It can also be used to inform a mission of the result of a request to use an unallocated resource.

#### Response to Schedule Query

The final use case of the Simple Schedule Format is to return schedule information resulting from a query about resource availability. While the contents and format of such a query are outside the scope of this Recommended Standard, the Simple Schedule Format provides a standard mechanism by which the information can be returned to the requestor. The ability to submit queries and indeed the contents of these. will depend on the capabilities and policies of the agency, but, for example and providing the agencies policy permits, it could be used by a mission to find unallocated antenna times which they could then request the use of.

## DOCUMENT STRUCTURE

This document is organized as follows:

- Section 1 provides the purpose, scope, applicability, and rationale of this Recommended Standard and identifies the conventions and references used throughout the document. This section also describes how this document is organized. A brief description is provided for each section and annex so that the reader will have an idea of where information can be found in the document. It also identifies terminology that is used in this document but is defined elsewhere.

- Section 2 provides a brief overview of the CCSDS-recommended Simple Schedule Format.

- Section 3 provides details about the structure and content of the Simple Schedule Format and specifies the normative files that define the XML schemas that govern the content of the XML instance documents that carry Simple Schedules.

- Annex A defines the standard Service Management information entity and specifies the normative files that define the XML schemas that govern the content and format that are common to all Service Management Information Entity XML instance documents.

- Annex B provides the normative Implementation Conformance Statement (ICS) proforma.

- ANNEX C provides an informative description of the normative eXtensible Markup language (XML) schema data types that realize the classes that comprise the abstract Service Management Information Entity as defined in ANNEX A.

- ANNEX D provides an informative description of the normative XML schema data types that realize the classes that comprise the Simple Schedule Format as defined in section 3.

- ANNEX E discusses security, SANA, and patent considerations.

- ANNEX F contains a list of Acronyms applicable to the Simple Schedule Format.

- ANNEX G is a list of informative references.

- ANNEX H contains the definition of the frequency bands used in the Recommended Standard.

## DEFINITIONS

For the purposes of this document, the following definitions apply:

- the word ‘agencies’ may also be construed as meaning ‘satellite operators’ or ‘satellite service providers’;

- the notation ‘n/a’ signifies ‘not applicable’.

## NOMENCLATURE

### Normative Text

The following conventions apply for the normative specifications in this Recommended Standard:

- the words ‘shall’ and ‘must’ imply a binding and verifiable specification;

- the word ‘should’ implies an optional, but desirable, specification;

- the word ‘may’ implies an optional specification;

- the words ‘is’, ‘are’, and ‘will’ imply statements of fact.

NOTE	–	These conventions do not imply constraints on diction in text that is clearly informative in nature.

### Informative Text

In the normative sections of this document, informative text is set off from the normative specifications either in notes or under one of the following subsection headings:

- Overview;

- Background;

- Rationale;

- Discussion.

## CONVENTIONS—THE UNIFIED MODELING LANGUAGE

The Unified Modeling Language (UML) diagrams used in the specification (including class diagrams, package diagrams, sequence diagrams, and activity diagrams) follow the notation, semantics, and conventions imposed by the Version 2.4.1 UML specification of the Object Management Group (OMG) (reference [4]). An overview of UML diagramming conventions can be found in Annex E of reference [1].

Within the document use is made only of class diagrams. A UML class diagram describes the structure of a message, its parts, and how those parts interrelate. A UML class, represented in the diagram as a box, represents a data set. Class diagram conventions include composition, generalization, multiplicity, and constraints. Enumeration notation is also used but only when it is involved in a composition constraint.

## References

The following publications contain provisions which, through reference in this text, constitute provisions of this document.  At the time of publication, the editions indicated were valid.  All publications are subject to revision, and users of this document are encouraged to investigate the possibility of applying the most recent editions of the publications indicated below.  The CCSDS Secretariat maintains a register of currently valid CCSDS publications.

[1]	Space Communication Cross Support—Service Management—Service Specification. Issue 1. Recommendation for Space Data System Standards (Blue Book), CCSDS 910.11-B-1. Washington, D.C.: CCSDS, August 2009.

[2]	“CCSDS-910.11-B-1_XML_schemas.”  http://public.ccsds.org/publications/archive/CCSDS-910.11-B-1_XML_schemas.zip.

[3]	Time Code Formats. Issue 4. Recommendation for Space Data System Standards (Blue Book), CCSDS 301.0-B-4. Washington, D.C.: CCSDS, November 2010.

[4]	Unified Modeling Language (UML). Version 2.4.1. Needham, Massachusetts: Object Management Group, August 2011.

# Overview

## GENERAL

This section provides a high-level overview of the CCSDS-recommended Simple Schedule Format, which is designed to facilitate standardized exchanges of ground station and/or relay satellite schedule information between space agencies.

## SIMPLE SCHEDULE

A Simple Schedule file is XML formatted. The format of the Simple Schedule file is suitable for automated interaction and/or (by means of a suitable XML viewer) human interaction.

Data in the Simple Schedule is either mandatory, in which case suitable values must be present, or optional, in which case values may be present or not. In addition it is possible to extend the contents of the Simple Schedule by defining additional parameters. The content of any additional parameters so defined is outside the scope of this document and should be documented in an ICD agreed by the involved parties.

## MAPPING TO W3C XML SCHEMA

This Recommended Standard includes the specification of a mapping to World Wide Web Consortium (W3C) extensible Markup Language (XML) schema. The normative mapping of this Recommended Standard to XML W3C schemas is a virtual annex to this Recommended Standard and is contained in a stand-alone set of schema files (reference [2]).

NOTE	–	The XML schema has been elaborated on the basis of the mapping guidelines described in reference [G1].

# Simple Schedule

## GENERAL

The Simple Schedule shall consist of digital data exchanged in the form of a file containing an XML instance document. Section 3.6 identifies the files that contain the normative Simple Schedule XML schemas. It should be noted that the naming conventions for the files containing the Simple Schedule XML instance documents are outside of the scope of this recommended standard.

## SIMPLE SCHEDULE CONTENT/STRUCTURE

### Overview

Figure 3-1 shows the UML Class diagram for the Simple Schedule. It should be noted that for clarity abstract classes for highlighted in green

Figure 3-1:  Simple Schedule Class Diagram

The attributes of each class are described further in the following subsections and tables.

### CLASS SimpleSchedule

The SimpleSchedule class is mandatory and shall constitute the Simple Schedule information entity.

NOTE	–	The SimpleSchedule class is a specialization of class SrvMgtInfoEntity described in ANNEX A below and the generic description of the parameters is given in that subsection.

Table 3-1 specifies the use of the parameters in the SrvMgtInfoEntity in the scope of the Simple Schedule.

Table 3-1:  Class SimpleSchedule Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| srvMgtEntityType | See Table A-1. | String1024—For the Simple Schedule the only permitted value for this parameter is the string “SIMPLE_SCHEDULE” | See Table A-1. |

### CLASS SimpleScheduleHeader

The SimpleScheduleHeader class is mandatory and shall constitute the ‘header’ of the Simple Schedule.

NOTE	–	The SimpleScheduleHeader class is a specialization of class SrvMgtHeader described in ANNEX A below and the generic description of the parameters is given in that subsection.

Table 3-2 specifies the use of the parameters in the SrvMgtHeader in the scope of the Simple Schedule.

Table 3-2:  Class SimpleScheduleHeader Parameters

The parameters for the SimpleScheduleHeader class as are as per Table A-2 except for the following:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| status | See Table A-2. | String32 – For the simple Schedule the only permitted values are TEST indicates that the schedule has been generated for test purposes only. PROVISIONAL indicates that the schedule contained is provisional and may still be subject to change. OPERATIONAL indicates that this is an operational schedule. OTHER indicates that this message has been generated for other purposes. In this case the optional parameter purpose can be used to further specify the purpose of the message. | See Table A-2. |
| startTime | Mandatory parameter for the Simple Schedule. The start time of the simple schedule contained. | CCSDS ASCII Time Code B (reference [3]) | UTC |
| endTime | Mandatory parameter for the Simple Schedule. The end time of the simple schedule contained. | CCSDS ASCII Time Code B (reference [3]) | UTC |

Permitted combinations of parameters SimpleScheduleHeader – status, ScheduledPackage - user, ServiceInfo - Servicetype and ScheduledActivty –activityStatus are as illustrated in Table 3-8 below.

### CLASS ScheduledPackage

The ScheduledPackage class is optional and may be used to specify the information for service packages that have been scheduled in the time interval bounded by the SimpleSchedule parameters startTime and endTime.

NOTE	–	The ScheduledPackage class is a specialization of class SrvMgtData described in ANNEX A below. The abstract SrvMgtData class contains zero parameters.

Service Packages that start before the startTime but end after the startTime will be included in the schedule information.

Service Packages that end after the endTime but start before the endTime will be included in the schedule information.

There  shall be zero or more instances of the ScheduledPackage class for each instance of the SimpleSchedule class.

The ScheduledPackage class extends SrvMgtData class with the parameters specified in table 3-3. These parameters are used to identify the Scheduled Package, the user of the service package and, optionall,y provide other ad-hoc information.

scheduledPackageID must be unique for every scheduled package in a schedule.

The user shall be one of

- a spacecraft (the typical case);

- PROVIDER-CSSS (indicating that the time is allocated to the Provider CSSS for tests, maintenance, upgrades etc.); or

- UNALLOCATED (indicating that the antenna/relay satellite is unallocated during the specified time range).

It should be noted that case for zero instances of the ScheduledPackage is where a Simple Schedule has been returned as a result of a query. In this case it is possible that no ScheduledPackages are scheduled in the time range specified. As noted in section 1.3.2.5 the contents and format of such a query are outside the scope of this Recommended Standard.

Table 3-3:  Class ScheduledPackage Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| scheduledPackageId | An identifier that is unique for every ScheduledPackage in a schedule. NOTE – If a schedule is regenerated, then the scheduledPackageID for a particular Scheduled Package may change. | String1024 | n/a |
| user | The user of the scheduled package. These will typically be spacecraft names as specified in SANA, but also PROVIDER-CSSS and UNALLOCATED with the meanings indicated in the adjacent column. | String1024—Permitted values registered in SANA The following strings are also permitted values with the meaning indicated; UNALLOCATED used to indicate that the time is unallocated. PROVIDER-CSSS used to indicate that the time is allocated to the Provider CSSS (e.g. for tests, maintenance, upgrades etc.). | n/a |
| originatingRequestID | Optional parameter: if present must echo the identifier from the request that caused the scheduled package to be generated. | String1024 | n/a |
| comment | Optional parameter: may be used for the provision of "informal" spacecraft names or other ad hoc information. | String8096 Exact use of this may be specified in an ICD between relevant parties | n/a |

Permitted combinations of parameters SimpleScheduleHeader – status, ScheduledPackage - user, ServiceInfo - Servicetype and ScheduledActivty –activityStatus are as illustrated in Table 3-8 below.

### CLASS ServicePackageXRef

The ServicePackageXRef class is optional and may be used to map the contents of the Simple Schedule to the appropriate SCCS SM service packages.

There  shall be zero or one instance of the ServicePackageXRef class for each instance of the ScheduledPackage class.

The ServicePackageXRef class shall include the parameters specified in table 3-4.

NOTE	–	The contents of the ServicePackageXRef class are relevant only when the Simple Schedule is used in the context of SCCS SM.

Table 3-4:  Class ServicePackageXRef Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| serviceAgreementRef | The Service Agreement (as per CCSDS 910.11-B-1, reference [1]; see also reference [G2] for additional information) to which the following servicePackageRef applies. | String1024 | n/a |
| servicePackageRef | Cross-reference to the service package (as per CCSDS 910.11-B-1, reference [1]; see also reference [G2] for additional information), where the station allocation is contained in the event that the station allocation was obtained via SCCS SM. NOTE – Several ScheduledActivity instances may have the same servicePackageRef since one service package can contain a number of station allocations. | String1024 | n/a |

### CLASS ScheduledActivity

The ScheduledActivity class shall contain the details of the scheduled activity and shall include parameters specified in table 3-5.

The ScheduledActivity class shall include two time windows,

- the interval within which the station is allocated (optional);

- the interval within the first window within which the spacecraft is actually being tracked by the ground station/relay satellite.

There shall be at least one instance of the ScheduledActivity class for each instance of the ScheduledPackage class.

Table 3-5:  Class ScheduledActivity Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| scheduledActivityID | An identifier that is unique for every ScheduledActivity in a schedule. It should be noted that if a schedule is regenerated then the scheduledActivityID for a particular Scheduled Activity may change | String1024 | n/a |
| activityStatus | This parameter is used to indicate how firm the commitment to the activity is. | Enumeration: COMMITTED indicates that barring unforeseen circumstances the activity will be supported. TENTATIVE indicates that the activity is currently scheduled but may still be subject to change. In addition to the above the 1 of the following 2 values must be used permitted when the ScheduledPackage user parameter is UNALLOCATED and the ServiceInfo ServiceType is UNUSED. AVAILABLE indicates that the antenna could be scheduled during the UNUSED time. UNAVAILABLE indicates that the antenna is completely unavailable during the UNUSED time. | n/a |
| stationRef | The ground station or relay satellite to which the scheduled activity applies | String1024—Permitted values registered in SANA | n/a |
| antennaRef | Identifier specifying which antenna at a particular ground station or relay satellite is to be used. | String1024—Permitted values registered in SANA | n/a |
| beginningOfActivity | Optional parameter: must be present if endOfActivity parameter is present. Time at which the allocation of the station/antenna starts. This is assumed to allow for all necessary setup activities, etc. Where available this time should be supplied subject to agency policy. If it is not possible to specify the actual value this parameter shall be omitted. | CCSDS ASCII Time Code B (reference [3]) | UTC |
| beginningOfTrack | Time at which tracking the spacecraft is scheduled to start. | CCSDS ASCII Time Code B (reference [3]) | UTC |
| endOfTrack | Time at which tracking the spacecraft is scheduled to end. | CCSDS ASCII Time Code B (reference [3]) | UTC |
| endOfActivity | Optional parameter: must be present if beginningOfActivity parameter is present. Time at which the allocation of the station/antenna ends. This is assumed to allow for all necessary teardown activities, etc. Where available this time should be supplied subject to agency policy. If it is not possible to specify the actual value this parameter shall be omitted. | CCSDS ASCII Time Code B (reference [3]) | UTC |
| orbitNumber | Optional parameter. The Orbit Number on which the beginningOfTrack occurs. If this is not relevant (e.g., deep space missions) or not available, this parameter shall be omitted. | Non-Negative Integer | n/a |

Permitted combinations of parameters SimpleScheduleHeader – status, ScheduledPackage - user, ServiceInfo - Servicetype and ScheduledActivty –activityStatus are as illustrated in Table 3-8 below.

### CLASS AdditionalActivityParameter

The AdditionalActivityParameter class is optional and may be used to permit the instantiation of additional parameters for a ScheduledActivity.

NOTE	–	The AdditionalActivityParameter class is a specialization of class AdditionalParameter described in 3.2.10 below, and the description of the parameters is given in that subsection.

There  shall be zero or more instances of the AdditionalActivityParameter class for each instance of the ScheduledActivity class.

The usage of these additional parameters is not within the scope of this document and should be specified in an ICD between by the relevant parties.

### CLASS ServiceInfo

The ServiceInfo class shall be used to provide information about the type of operations to be carried out during a pass.

The ServiceInfo class shall use the parameters specified in table 3-6 to specify the type of service and frequency band to be used.

There shall be at least one instance of the ServiceInfo class for each instance of the ScheduledActivity class.

NOTE	–	Multiple instances of the ServiceInfo Class are required where more than one service is provided during a pass, e.g.

- Telemetry and telecommanding services are provided

- Telemetry is downlinked on both X- and S-band simultaneously

Table 3-6:  Class ServiceInfo Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| serviceType | The type of service that will be carried out during an activity. It should be noted that: APA-AZ/EL indicates Antenna Pointing Angles, Azimuth/Elevation APA-X/Y indicates Antenna Pointing Angles, X/Y VLBI indicates Very-Long-Baseline Interferometry. | Enumeration: APA-AZ/EL APA-X/Y DELTADOR DOPPLER OFFLINE-TM-RECORDING OFFLINE-TM-PROVISION RF-ONLY RANGING RESERVED TBD TELECOMMAND TELEMETRY TEST UNUSED VLBI | n/a |
| frequencyBand | The frequency band that will be used by the service. If the frequency band is not relevant the value N/A (not applicable) shall be used. (See annex H for a definition of the frequencies each band refers to.) | Enumeration: VHF UHF C-BAND KA-BAND KU-BAND L-BAND S-BAND V-BAND X-BAND OPTICAL N/A ALL | n/a |

For the case of unused time it is possible (but mandatory) to specify a frequency band . To specify the unused time on a particular band of an Antenna the following need to be specified;

- ScheduledPackage user parameter set to UNALLOCATED

- ScheduledActivity stationRef parameter set as appropriate

- ScheduleActivity antennaRef parameter set as appropriate

- serviceInfo serviceType parameter set to UNUSED

- ServiceInfo frequencyBand set to either

- The appropriate frequency band as contained in Table 3-6 above.

- The value ALL if all frequency band supported by the antenna are UNUSED

Permitted combinations of parameters SimpleScheduleHeader – status, ScheduledPackage - user, ServiceInfo - Servicetype and ScheduledActivty –activityStatus are as illustrated in Table 3-8 below.

### CLASS AdditionalserviceParameter

The AdditionalServiceParameter class is optional and may be used to permit the instantiation of additional parameters for a ServiceInfo.

NOTE	–	The AdditionalServiceParameter class is a specialization of class AdditionalParameter described in 3.2.10 below, and the description of the parameters is given in that subsection.

There  shall be zero or more instances of the AdditionalServiceParameter class for each instance of the ServiceInfo class.

The usage of these additional parameters is not within the scope of this document and should be specified in an ICD between by the relevant parties.

### CLASS AdditionalParameter (ABSTRACT)

The AdditionalParameter class shall be used to permit the instantiation of additional parameters for a ScheduledActivity or ServiceInfo by allowing the specification of parameter name/value pairs using the parameters specified in table 3-7.

The usage of these additional parameters is not within the scope of this document and should be specified in an ICD between by the relevant parties.

Table 3-7:  Class AdditionalParameter Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| parameterName | Name of the additional parameter. This is used to enable the specification of additional parameters if these are required on a bilateral basis. | String1024 | n/a |
| parameterValue | The value of the required parameter. | As required by the additional parameter | As required by the additional parameter |

It should be noted that each AddtionalParameter can itself have AdditionalParameters, i.e. the nesting of AddtionalParameters is supported.

## Permitted combinations of parameters SimpleScheduleHeader – status, ScheduledPackage - user, ServiceInfo - Servicetype and ScheduledActivty –activityStatus.

The following table specifies the permitted combinations of the following parameters:

- SimpleScheduleHeader – status,

- ScheduledPackage – user,

- ServiceInfo – serviceType,

- ScheduledActivity – activityStatus

Table 3-8: Permitted combinations of parameters SimpleScheduleHeader – status, ScheduledPackage - user, ServiceInfo - Servicetype and ScheduledActivty – activityStatus

| SimpleScheduleHeader – status value | ScheduledPackage – user value | ServiceInfo – Servicetype value | ScheduledActivty – activityStatus value |
| --- | --- | --- | --- |
| TEST | Any permitted value | Any permitted value | Any permitted value |
| PROVISIONAL | Spacecraft—Permitted values registered in SANA | Any permitted value | TENTATIVE |
|  | UNALLOCATED | UNUSED | AVAILABLE |
|  |  |  | UNAVAILABLE |
|  | PROVIDER-CSSS | Any permitted value | TENTATIVE |
| OPERATIONAL | Spacecraft—Permitted values registered in SANA | Any permitted value | TENTATIVE |
|  |  |  | COMMITTED |
|  | UNALLOCATED | UNUSED | AVAILABLE |
|  |  |  | UNAVAILABLE |
|  | PROVIDER-CSSS | Any permitted value | TENTATIVE |
|  |  |  | COMMITTED |
| OTHER | Any permitted value, although this may be further constrained in an ICD between relevant parties | Any permitted value, although this may be further constrained in an ICD between relevant parties | Any permitted value, although this may be further constrained in an ICD between relevant parties |

## Ordering of Scheduled Packages

The ordering of ScheduledPackages in a file containing a Simple Schedule shall be by increasing order of the earliest beginningOfTrack times of all the ScheduledActivities contained in a ScheduledPackage.

In the event that two or more ScheduledPackages contain ScheduledActivities that have the same earliest beginningOfTrack times, the user value of ScheduledPackage shall be used as a secondary key in increasing alphabetic order.

NOTE	–	Figure 3-2 is an example of how the order of ScheduledPackages should appear. For clarity not all parameters of ScheduledActivities are shown.

ScheduledPackage

scheduledPackageID	= Package-A

user				= Mission-A

ScheduledActivity

scheduledActivityID	= Activity-A1

beginningOfTrack		= 2020-123T12:00:00.000Z

.

.

ScheduledActivity

scheduledActivityID	= Activity-A2

beginningOfTrack		= 2020-123T12:30:00.000Z

.

.

ScheduledPackage

scheduledPackageID	= Package-B

user				= Mission-B

ScheduledActivity

scheduledActivityID	= Activity-B1

beginningOfActivity	= 2020-123T12:15:00.000Z

beginningOfTrack		= 2020-123T12:30:00.000Z

.

.

ScheduledPackage

scheduledPackageID	= Package-C

user				= Mission-C

ScheduledActivity

scheduledActivityID	= Activity-C1

beginningOfActivity	= 2020-123T12:00.00.000Z

beginningOfTrack		= 2020-123T12:30:00.000Z

.

.

ScheduledActivity

scheduledActivityID	= Activity-C2

beginningOfActivity	= 2020-123T12:10:00.000Z

beginningOfTrack		= 2020-123T12:40:00.000Z

.

.

ScheduledPackage

scheduledPackageID	= Package-D

user				= Mission-A

ScheduledActivity

scheduledActivityID	= Activity-A3

beginningOfTrack		= 2020-123T13:00:00.000Z

.

.

ScheduledActivity

scheduledActivityID	= Activity-A4

beginningOfTrack		= 2020-123T13:30:00.000Z

.

.

Figure 3-2:  Example of Ordering of Scheduled Packages in Simple Schedule

## USAGE OF SIMPLE SCHEDULE FOR Specifing ANTENNA Available FREE TIME

### Discussion

Antenna Free Time, for the purposes of the Simple Schedule, is defined as those time periods outside of scheduled activities, following on from this

- Antenna Available Free Time is antenna free time which is available for scheduling

- Antenna Unavailable Free Time is antenna free time which is not available for scheduling.

The objective of using the simple schedule to disseminate Antenna Available Free Time is to provide a standard mechanism by which, subject to the Provider-CSSS policies, missions can be informed of time slots on antennas which are currently unused and are available for use. A detailed description of how Antenna Available Free Time can be specified is contained in Section Error! Reference source not found..

It is possible for the PROVIDER-CSSS to disseminate a combined schedule that contains scheduled antenna time, i.e. time allocated to specific users, as well as Antenna Available Free Time.

The Antenna Available Free Time is specified as a UTC time range. It is not orbit or spacecraft specific. It should be noted that the Antenna Available Free Time may not all be available for tracking of a spacecraft, e.g. time may be required at the start and end of the time interval for station configuration, teardown etc. and/or antenna slewing in the case of relay satellites.

Figure 3-3 below indicates, diagrammatically, what is meant by Antenna Available Free Time. It should be noted that in this diagram it is assumed that all Antenna Free Time is available for use.

Figure 3-3:	Schematic of Schedule to Illustrate Use of Simple Schedule for Antenna Free Time

### Specification of Antenna Available Free Time.

As of this issue, Antenna Available Free Time is not user-/spacecraft-specific.

When specifying Antenna Available Free Time in the Simple Schedule Format:

- the ScheduledPackage user parameter shall be specified as ‘UNALLOCATED’;

- the ScheduledActivity activityStatus parameter shall be specified as ‘AVAILABLE’;

- the ScheduledActivity beginningOfTrack parameter shall be set to the UTC time as which the Antenna Available Free Time starts.

- the ScheduledActivity endOfTrack parameter shall be set to the UTC time as which the Antenna Available Free Time ends.

- The ScheduledActivity beginningOfActivty and endOfActvity parameters shall be omitted.

- the ServiceInfo serviceType parameter shall be set to ‘UNUSED’;

- the ServiceInfo frequencyBand parameter shall be set either to

- ‘ALL’ indicating that all frequency bands supported by the antenna are available.

- A specific frequency band (see Table 3-6 above for allowed values) indicating that the antenna is free to support that frequency band only.

## XML SchemaS for the SIMPLE SCHEDULE

Each Simple Schedule Information Entity shall conform to the XML schemas specified in the files ‘SchemaCssmSimpleSchedule-v1_0_0.xsd’, ‘SchemaCssmSmInfoEntityHeader-v1_0_0.xsd’, and ‘SchemaCssmCcsdsTimecodes-v1_0_0.xsd’. The normative source of these files shall be the SANA SCCS-SM Information Entity XML Schemas resistry: <registry URL>.

ANNEX D provides an informative description of the Simple Schedule XML schemas.

RED BOOK REVIEW NOTE - While this Recommended Standard is being developed, the schema files are available from the CWE/Cross Support Services Area (CSS)/Documents/CSS-SM/Red Book XML Schemas folder at URL
http://cwe.ccsds.org/css/docs/Forms/AllItems.aspx?RootFolder=%2Fcss%2Fdocs%2FCSS%2DSM%2FRed%20Book%20XML%20Schemas&FolderCTID=0x012000A2CFA608DF169C4EB988261660CEFAEB&View={8045374D-F8E0-4356-83CA-993252A38FE8}

Service Management Information Entity

(Normative)

GENERAL

The Service Management Information Entity forms the basis for defining information entities required by service management.

Service Management Information Entity CONTENT/STRUCTURE

Overview

Figure A-1 shows the UML Class diagram for the Service Management Information Entity. It should be noted that for clarity abstract classes for highlighted in green

Figure A-1: Service Management Information Entity Class Diagram

The attributes of each class are described further in the following subsections and tables.

Class SrvMgtInfoEntity (Abstract)

The SrvMgtInfoEntity is an abstract class which is used to instantiate the various classes of information entity required by service management.

The SrvMgtInfoEntity class parameters specified in Table A-1 shall be used to identify the information entity type.

Table A-1: Class SrvMgtInfoEntity Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| srvMgtEntityType | The type of service management information entity contained. | Enumeration — Permitted values registered in SANA. The following list identifies the currently foreseen values but this may be extended in future: ACCOUNTING_REP CONFIG_PROFILE COST_ESTIMATES EVENT_SEQUENCE PLANNING_REQUEST PROVISIONAL_PLAN RES_AVAILABILITY SERV_PACKAGE SERV_PACKAGE_EXE SERV_PACKAGE_REQ SERVICE_AGREEMENT SERVICE_CATALOG SIMPLE_SCHEDULE TRAJ_PREDICTION | n/a |

Class SrvMgtHeader (Abstract)

The SrvMgtHeader is an abstract class which is used to instantiate the header required by service management.

The SrvMgtHeader class parameters specified in Table A-2 shall be used to identify the originating organization, status of the schedule, status. version, the time at which the information entity was generated, the start time to which the information entity applies, and the end time to which it applies. Optional parameters allow for further definition of the purpose of the message and a description of its contents

Table A-2: Class SrvMgtHeader Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| originatingOrganization | The organization that generated the information entity. | String1024—Permitted values registered in SANA | n/a |
| generationTime | Time at which the information entity was generated. | CCSDS ASCII Time Code B (reference [3]) | UTC |
| status | The status of the information entity. | String32 — The permitted values for the string will be dependent on the type of information entity instantiated and are therefore specified in the various information entity specifications. |  |
| version | The version of the information entity. This increments every time a information entity of the same srvMgtEntityType, status and time range is generated (i.e., has the same startTime and endTime). NOTE: the version may increment by 1 every time but is not constrained to do so. The only constraint is that each version number is greater than the previous. | Positive Integer | n/a |
| startTime | Optional parameter: The start time to which the information entity applies. NOTE: for certain Service Management Information Entity types use of this parameter is mandatory. | CCSDS ASCII Time Code B (reference [3]) | UTC |
| endTime | Optional parameter: The end time to which the information entity applies. NOTE: for certain Service Management Information Entity types use of this parameter is mandatory. | CCSDS ASCII Time Code B (reference [3]) | UTC |
| purpose | Optional parameter: may be used to further specify the purpose of the information entity in the event that the status specified is “OTHER”. | String1024 Exact use of this may be specified in an ICD between relevant parties | n/a |
| description | Optional parameter: may be used to describe the contents of the information entity, e.g. any filter criteria used in the generation of the information entity etc.. | String8096 Exact use of this may be specified in an ICD between relevant parties | n/a |

Class SrvMgtData (Abstract)

The SrvMgtData is an abstract class which is used to instantiate the various classes of data required by service management.

The SrvMgtData class contains no parameters.

XML SchemaS for the Service Management Information Entity

Each Service Management Information Entity shall conform to the XML schemas specified in the files ‘SchemaCssmSmInfoEntityHeader-v1_0_0.xsd’ and ‘SchemaCssmCcsdsTimecodes-v1_0_0.xsd’. The normative source of these files shall be the SANA SCCS-SM Information Entity XML Schemas resistry: <registry URL>.

ANNEX C provides an informative description of the Simple Schedule XML schemas.

Implementation Conformance Statement (ICS) proforma

(Normative)

INTRODUCTION

OVERVIEW

This annex provides the Implementation Conformance Statement (ICS) Requirements List (RL) for an implementation of the Simple Schedule Format Specification (CCSDS 902.1-R-1). The ICS for an implementation is generated by completing the RL in accordance with the instructions below. An implementation shall satisfy the mandatory conformance requirements referenced in the RL.

The RL in this annex is blank. An implementation’s completed RL is called the ICS. The ICS states which capabilities and options have been implemented. The following can use the ICS:

- the implementer, as a checklist to reduce the risk of failure to conform to the standard through oversight;

- a supplier or potential acquirer of the implementation, as a detailed indication of the capabilities of the implementation, stated relative to the common basis for understanding provided by the standard ICS proforma;

- a user or potential user of the implementation, as a basis for initially checking the possibility of interworking with another implementation (it should be noted that, while interworking can never be guaranteed, failure to interwork can often be predicted from incompatible ICSes);

- a tester, as the basis for selecting appropriate tests against which to assess the claim for conformance of the implementation.

ABBREVIATIONS AND CONVENTIONS

General

The RL consists of information in tabular form. The status of features is indicated using the abbreviations and conventions described below.

Item Column

The item column contains sequential numbers for items in the table.

Feature Column

The feature column contains a brief descriptive name for a feature. It implicitly means ‘Is this feature supported by the implementation?’

NOTE –	The features itemized in the RL are elements of the Simple Schedule Format. Therefore support for a mandatory feature indicates that a generated file will include that feature, and support for an optional feature indicates that generated files can include that feature.

Class Column/Parameters

The Class/Parameters column contains, where applicable, the Simple Schedule Format class associated with the feature.

Reference Column

The reference column indicates the relevant subsection or table in the Simple Schedule Format Specification (CCSDS 902.1-R-1) (this document).

Status Column

The status column uses the following notations:

M	mandatory.

O	optional.

It should be noted that a parameter may be marked as M(andatory) while the class that contains it is marked O(ptional). This should be interpreted to mean that while the class is optional if it is present then the parameter must be present.

Support Column Symbols

The support column is to be used by the implementer to state whether a feature is supported by entering Y, N, or N/A, indicating:

Y	Yes, supported by the implementation.

N	No, not supported by the implementation.

N/A	Not applicable.

INSTRUCTIONS FOR COMPLETING THE RL

An implementer shows the extent of compliance to the Recommended Standard by completing the RL; that is, the state of compliance with all mandatory requirements and the options supported are shown. The resulting completed RL is called an ICS. The implementer shall complete the RL by entering appropriate responses in the support or values supported column, using the notation described in B1.2. If a conditional requirement is inapplicable, N/A should be used. If a mandatory requirement is not satisfied, exception information must be supplied by entering a reference Xi, where i is a unique identifier, to an accompanying rationale for the noncompliance.

ICS Proforma for Simple Schedule Format

General Information

Identification of ICS

| Date of Statement (DD/MM/YYYY) |  |
| --- | --- |
| ICS serial number |  |
| System Conformance statement cross-reference |  |

Identification of Implementation Under Test (IUT)

| Implementation name |  |
| --- | --- |
| Implementation version |  |
| Special Configuration |  |
| Other Information |  |

Identification of Supplier

| Supplier |  |
| --- | --- |
| Contact Point for Queries |  |
| Implementation Name(s) and Versions |  |
| Other Information necessary for full identification, e.g., names(s) and version(s) for machines and/or operating systems; |  |

Document Version

| CCSDS 902.1-R-1, draft issue 1 |  |
| --- | --- |
| Have any exceptions been required? (Note: A YES answer means that the implementation does not conform to the Recommended Standard. Non-supported mandatory capabilities are to be identified in the ICS, with an explanation of why the implementation is non-conforming | Yes _____ No _____ |

Requirements List

Class SimpleSchedule

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | SimpleSchedule | 3.2.2 | M |  |

Class SimpleSchedule Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | srvMgtEntityType | Table 3-1 | M |  |

Class SimpleScheduleHeader

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | SimpleScheduleHeader | 3.2.3 | M |  |

Class SrvMgtHeader Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | originatingOrganization | Table 3-2 | M |  |
|  | generationTime | Table 3-2 | M |  |
|  | status | Table 3-2 | M |  |
|  | version | Table 3-2 | M |  |
|  | startTime | Table 3-2 | M |  |
|  | endTime | Table 3-2 | M |  |
|  | purpose | Table 3-2 | O |  |
|  | description | Table 3-2 | O |  |

Class ScheduledPackage

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | ScheduledPackage | 3.2.3.3 | O |  |

Class ScheduledPackage Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | scheduledPackageID | Table 3-3 | M |  |
|  | user | Table 3-3 | M |  |
|  | originatingRequestID | Table 3-3 | O |  |
|  | comment | Table 3-3 | O |  |

Class ServicePackageXRef

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | ServicePackageXRef | 3.2.4.9 | O |  |

Class ServicePackageXRef Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | serviceAgreementRef | Table 3-4 | M |  |
|  | servicePackageRef | Table 3-4 | M |  |

Class ScheduledActivity

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | ScheduledActivity | 3.2.6 | C1 |  |

C1: If a ScheduledPackage class is contained in the Simple Schedule then there must be at least one ScheduledActivity for each ScheduledPackage.

Class ScheduledActivity Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | scheduledActivityID | Table 3-5 | M |  |
|  | activityStatus | Table 3-5 | M |  |
|  | stationRef | Table 3-5 | M |  |
|  | antennaRef | Table 3-5 | M |  |
|  | beginningOfActivity | Table 3-5 | O |  |
|  | beginningOfTrack | Table 3-5 | M |  |
|  | endOfTrack | Table 3-5 | M |  |
|  | endOfActivity | Table 3-5 | O |  |
|  | orbitNumber | Table 3-5 | O |  |

Class AdditionalActivityParameter

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | AdditionalActivityParameter | 3.2.6.4 | O |  |

Class AdditionalActivityParameter Parameters

The AdditionalActivityParameter class is used to specify additional parameters for ScheduledActivity. The additional parameters and permitted values for these should be specified in table Table B-1 below.

In the following Table B-1 the columns have the following use:

- parameterName	This column is used to specify the names of the additional parameter(s).

- Description	This column is used to enter the description of what the additional parameter(s) is/are.

- parameterValueType	This column is used to specify what type the parameterValue is, e.g., String1024, Integer, Unsigned Integer, Real, CCSDS ASCII Time Code B, etc.

- Permitted Values	This column is used to specify the values that are permitted for the additional parameter(s).

- Data units	This column is used to specify the Data Unit of the additional parameter(s), e.g., Seconds, Hertz, Volts, UTC, etc.

Table B-1: Class AdditionalParameter Instantiated for Class AdditionalActivityParameter

| parameterName | Description | parameterValue Type | Permitted Values | Data units |
| --- | --- | --- | --- | --- |

Class AdditionalActivityParameter Nested AdditionalActivityParameters

If any of the AdditionalActivityParameters themselves contain further parameters (i.e. nested parameters) then additional tables shall be added as required to document these.

Class ServiceInfo

General

| Item | Class | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | ServiceInfo | 3.2.8 | C2 |  |

C2: If a ScheduledActivity class is contained in the Simple Schedule then there must be at least one ServiceInfo for each ScheduledActivity.

Class ServiceInfo Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | serviceType | Table 3-6 | M |  |
|  | frequencyBand | Table 3-6 | M |  |

Class AdditionalServiceParameter

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | AdditionalServiceParameter | 3.2.8.4 | O |  |

Class AdditionalServiceParameter Parameters

If this class is used to specify additional parameters for ServiceInfo, the additional parameters and permitted values for these should be specified in Table B-2 below.

In the following Table B-2 the columns have the following use:

- parameterName	This column is used to specify the names of the additional parameter(s).

- Description	This column is used to enter the description of what the additional parameter(s) is/are.

- parameterValueType	This column is used to specify what type the parameterValue is, e.g., String1024, Integer, Unsigned Integer, Real, CCSDS ASCII Time Code B, etc.

- Permitted Values	This column is used to specify the values that are permitted for the additional parameter(s).

- Data units	This column is used to specify the Data Unit of the additional parameter(s), e.g., Seconds, Hertz, Volts, UTC, etc.

Table B-2: Class AdditionalParameter Instantiated for Class AdditionalServiceParameter

| parameterName | Description | parameterValue Type | Permitted Values | Data units |
| --- | --- | --- | --- | --- |

Class AdditionalServiceParameter Nested AdditionalServiceParameters

If any of the AdditionalServiceParameters themselves contain further parameters (i.e. nested parameters) then additional tables shall be added as required to document these.

Class AdditionalParameter

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | AdditionalParameter | 3.2.10 | O |  |

NOTES

- If this class is used to specify additional parameters for ScheduledActivity, the additional parameters and permitted values for these should be specified in B2.1.5.6.2.

- If this class is used to specify additional parameters for ServiceInfo the additional parameters and permitted values for these should be specified in B2.1.5.8.2.

Class AdditionalParameter Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | parameterName | Table 3-7 | M |  |
|  | parameterValue | Table 3-7 | M |  |

XML Schema Types for the Service Management Information Entity Header

(InFormative)

Purpose

This annex provides an informative description of the normative eXtensible Markup language (XML) schema data types that realize the classes that comprise the abstract Service Management Information Entity as defined in ANNEX A. The Service Management Information Entity Header XML 3C schema types and global elements are used to construct the schemas for individual Service Management Information Entities.

Schema Organization And Packaging

The normative Service Management Information Entity Header schema types and global elements are contained in the file ‘SchemaCssmSmInfoEntityHeader-v1_0_0.xsd’.

The SM Information Entity Header types and global elements are registered in the ‘urn:ccsds:schema:cssm:smInfoEntHeader:1.0.0’ name space.

The SM Information Entity Header schema imports the CcsdsAsciiTimeCodeBType type, which is registered in the ‘urn:ccsds:schema:cssm:ccsdsTimecodes:1.0.0’ name space and defined in the file ‘SchemaCssmCcsdsTimecodes-v1_0_0.xsd’.

The source of the SchemaCssmSmInfoEntityHeader-v1_0_0.xsd and SchemaCssmCcsdsTimecodes-v1_0_0.xsd files is the SANA SCCS-SM Information Entity XML Schemas resistry: <registry URL>.

RED BOOK REVIEW NOTE - While this Recommended Standard is being developed, the schema files are available from the CWE/Cross Support Services Area (CSS)/Documents/CSS-SM/Red Book XML Schemas folder at URL
http://cwe.ccsds.org/css/docs/Forms/AllItems.aspx?RootFolder=%2Fcss%2Fdocs%2FCSS%2DSM%2FRed%20Book%20XML%20Schemas&FolderCTID=0x012000A2CFA608DF169C4EB988261660CEFAEB&View={8045374D-F8E0-4356-83CA-993252A38FE8}

The SM Information Entity Header types consist of the SrvMgtInfoEntityType, SrvMgtHeaderType, and SrvMgtDataType types, and the srvMgtEntityType, srvMgtHeader, srvMgtData and status global elements. Figure C-1 is the XMLSpy graphical representation of the SrvMgtInfoEntityType, SrvMgtHeaderType, and SrvMgtDataType types and their relationships in forming the top-level structure of an Information Entity.

As shown in Figure C-1, the SrvMgtInfoEntityType contains one instance of the srvMgtEntityType element (parameter), one instance of the srvMgtHeader element (of type SrvMgtHeaderType), and zero or more instances of the srvMgtData elements (of type SrvMgtDataType).

Figure C-1:	XML Schema for the Information Entity Header Group: SrvMgtInfoEntityType, SrvMgtHeaderType, and SrvMgtDataType Types

The following subsections describe the XML types that comprise the Information Entity Header group and relate the parameters of those types to the corresponding UML classes in ANNEX A.

NOTE	-	In the flowing subsections, string types of restricted length are indicated by the notation “xsd:string[length]”.So for example, a string type that is limited to 1024 characters is designated by “xsd:string[1024]”.

SrvMgtInfoEntityType Type

SrvMgtInfoEntityType is an abstract XML schema type; it cannot be instantiated. It serves as a base type from which Information Entity-specific types may be derived.

Table C-1 lists the parameters of the SrvMgtInfoEntityType XML schema type and the XML schema types of those parameters. The srvMgtEntityType parameter of the SrvMgtInfoEntityType XML schema type has the same name, definition, and data units as the corresponding parameter of the SrvMgtInfoEntity UML class defined in A1.1.2. The srvMgtHeader and srvMgtData parameters represent the containment of the SrvMgtHeader and SrvMgtData UML classes (respectively) by the SrvMgtInfoEntity UML class.

Table C-1:  SrvMgtInfoEntityType Parameters

| Parameter | Data Type |
| --- | --- |
| srvMgtEntityType | SrvMgtEntityTypeType |
| srvMgtHeader | SrvMgtHeaderType |
| srvMgtData | SrvMgtDataType |

The srvMgtEntityType, srvMgtHeader, and srvMgtData elements are all references to global elements of the same names. This allows these elements to serve as head elements for Information Entity-specific substitution groups. How this substitution is performed is illustrated in ANNEX D.

SrvMgtHeaderType Type

SrvMgtHeaderType is an abstract XML schema type; it cannot be instantiated. It serves as a base type from which Information Entity-specific types may be derived.

Table C-2 lists the parameters of the SrvMgtHeaderType XML schema type and the XML schema types of those parameters. The parameters of the SrvMgtHeaderType XML schema type has the same name, definition, and data units as the corresponding parameters of the SrvMgtHeader UML class defined in A1.1.3.

Table C-2:  SrvMgtHeaderType Parameters

| Parameter | Data Type |
| --- | --- |
| originatingOrganization | xsd:string[1024] |
| generationTime | CcsdsAsciiTimeCodeBType |
| status | StatusType |
| version | xsd:positiveInteger |
| startTime | CcsdsAsciiTimeCodeBType |
| endTime | CcsdsAsciiTimeCodeBType |
| purpose | xsd:string[1024] |
| description | xsd:string[896] |

NOTE	–	The CcsdsAsciiTimeCodeBType simple XML type, which is registered in the ‘urn:ccsds:schema:cssm:ccsdsTimecodes:1.0.0’ name space, is defined with the regular expression pattern ‘\d{4}-\d{3}T\d{2}:\d{2}:\d{2}\.\d+Z?’, which represents CCSDS ASCII Time Code B (YYYY-DDDThh:mm:ss.d->dZ). The generationTime, startTime, and endTime parameters are cast as CcsdsAsciiTimeCodeBType.This regular expression does not enforce the ranges of the field; e.g., it will accept 537 as a ‘day of year’.

The status element is a reference to a global element of the same name. This allows this element to serve as head element for substitution groups that contain Information Entity-specific status enumerated values. How this substitution is performed is illustrated in ANNEX D.

SrvMgtDataType Type

SrvMgtDataType is an abstract XML schema type; it cannot be instantiated. It corresponds to the SrvMgtData UML class defined in A1.1.4 and therefore has no parameters. It serves as a base type from which Information Entity-specific types may be derived such that they can substitute for it in Information Entity-specific schemas.

XML Schema for the Simple Schedule Format

(InFormative)

Purpose

This annex provides an informative description of the normative XML schema data types that realize the classes that comprise the Simple Schedule Format as defined in section 3.

Schema Organization And Packaging

The XML schemas for the Simple Schedule are contained in the file ‘SchemaCssmSimpleSchedule-v1_0_0.xsd’. The root element of the SchemaCssmSimpleSchedule-v1_0_0 schemas is the simpleSchedule element.

The Simple Schedule types and global elements are registered in the ‘urn:ccsds:schema:cssm:simple_schedule:1.0.0’ name space.

The Simple Schedule schema imports (a) Service Management Information Entity Header types and global elements that are registered in the ‘urn:ccsds:schema:cssm:smInfoEntHeader:1.0.0’ name space and defined in the file ‘SchemaCssmSmInfoEntityHeader-v1_0_0.xsd’, and (b) the CcsdsAsciiTimeCodeBType type, which is registered in the ‘urn:ccsds:schema:cssm:ccsdsTimecodes:1.0.0’ name space and defined in the file ‘SchemaCssmCcsdsTimecodes-v1_0_0.xsd’.

The source of the SchemaCssmSimpleSchedule-v1_0_0.xsd , SchemaCssmSmInfoEntityHeader-v1_0_0.xsd, and SchemaCssmCcsdsTimecodes-v1_0_0.xsd files is the SANA SCCS-SM Information Entity XML Schemas resistry: <registry URL>.

RED BOOK REVIEW NOTE - While this Recommended Standard is being developed, the schema files are available from the CWE/Cross Support Services Area (CSS)/Documents/CSS-SM/Red Book XML Schemas folder at URL
http://cwe.ccsds.org/css/docs/Forms/AllItems.aspx?RootFolder=%2Fcss%2Fdocs%2FCSS%2DSM%2FRed%20Book%20XML%20Schemas&FolderCTID=0x012000A2CFA608DF169C4EB988261660CEFAEB&View={8045374D-F8E0-4356-83CA-993252A38FE8}

For ease in reading, the graphical representation of the corresponding XML schema has been split into two diagrams. Figure D-1 is the XMLSpy graphical representation of the SimpleSchedule, ScheduledPackage, and ServicePackageXRef components. As shown in figure D-1, the ScheduledPackage contains one or more instances of ScheduledActivity.

Figure D-1:	XML Schema for the Simple Schedule: SimpleSchedule, ScheduledPackage, and ServicePackageXRef Types

Figure D-2 is the XMLSpy graphical representation of the ScheduledActivity, ServiceInfo, AdditionalServiceParameter, and AdditionalActivityParameter components.

Figure D-2:	XML Schema for the Simple Schedule: ScheduledActivity, ServiceInfo, AdditionalServiceParameter, and AdditionalActivityParameter Types

The following subsections describe the XML types that make up the Simple Schedule XML schema and relate the parameters of those types to the corresponding UML classes in section 3.

SimpleScheduleType Type

The SimpleScheduleType type is a specialization of the SrvMgtInfoEntityType type described in C3. However, rather than directly inheriting the parameters of that parent class without change, each of the parameters of the SimpleScheduleType type is derived in some manner from a corresponding parameter of the SrvMgtInfoEntityType type. The following subsections describe these derivations.

srvMgtEntityType Parameter

The srvMgtEntityType parameter that is contained by the SimpleScheduleType type is a concrete substitution for the abstract srvMgtEntityType parameter of the SrvMgtInfoEntityType type. Whereas the srvMgtEntityType parameter of the SrvMgtInfoEntityType type enumerates all possible Information Entity Types, the srvMgtEntityType parameter of the SimpleScheduleType type is restricted to one value, ‘SIMPLE_SCHEDULE’, as specified for the srvMgtEntityType parameter of the SimpleSchedule class  in 3.2.2.

simpleScheduleHeader Parameter

The simpleScheduleHeader parameter that is contained by the SimpleScheduleType type is a concrete substitution for the abstract parameter srvMgtHeader of type SrvMgtHeaderType (see C4). The simpleScheduleHeader parameter is of type SimpleScheduleHeaderType (see D4).

scheduledPackage Parameter

The scheduledPackage parameter that is contained by the SimpleScheduleType type is a concrete substitution for the abstract parameter srvMgtData of type SrvMgtDataType (see C4). The scheduledPackage parameter is of type ScheduledPackageType (see D5).

SimpleScheduleHeaderType Type

The SimpleScheduleHeaderType type is a specialization of the SrvMgtHeaderType type described in C4. All parameters of the SimpleScheduleHeaderType XML schema type have the same names, definitions, and data units as the corresponding parameters of the SrvMgtHeaderType type, except for the status, startTime, and endTime parameters. The following subsections describe these deviations.

The status parameter that is contained by the SimpleScheduleHeaderType type is a concrete substitution for the abstract status parameter of the SrvMgtInfoEntityType type. Whereas the status parameter of the SrvMgtHeaderType type is simply cast as an xsd:string of length 32, the status parameter of the SimpleScheduleHeaderType restricts the value of that string to four enumerated values: ‘TEST’, ‘OPERATIONAL’, ‘PROVISIONAL’, and ‘OTHER’, as specified for the status parameter of the SimpleScheduleHeader class in 3.2.3.

startTime and endTime Parameters

The startTime and endTime parameters of the SrvMgtHeaderType type are defined with cardinality [0..1], meaning that they are each optional. For the SimpleScheduleHeader, these parameters are defined as mandatory in 3.2.3. However, as these parameters are inherited by the SimpleScheduleHeaderType type from the SrvMgtHeaderType type, they are still optional in the SimpleScheduleHeaderType type. Therefore the presence of the startTime and endTime parameters in a Simple Schedule XML instance document cannot be enforced by XML validation and must rely on application-level processing.

ScheduledPackageType Type

The ScheduledPackageType type is a specialization of the SrvMgtDataType type described in C5. Because the SrvMgtDataType type has no parameters of its own, all parameters of the ScheduledPackageType type are defined by that derived type.

Table D-1 lists the parameters ScheduledPackageType type and the XML schema types of those parameters. All parameters of the ScheduledPackage XML schema type have the same names, definitions, and data units as the corresponding parameters of the ScheduledPackage UML class defined in 3.2.4, except the servicePackageXref and scheduledActivity parameters, which represents the containment of the ServicePackageXRef and ScheduledActivity UML classes, respectively, by the ScheduledPackage UML class.

Table D-1:  ScheduledPackageType Parameters

| Parameter | XML Data Type |
| --- | --- |
| scheduledPackageId | xsd:string[1024] |
| user | xsd:string[1024] |
| originatingRequestId | xsd:string[1024] |
| comment | xsd:string[8096] |
| servicePackageXRef | ServicePackageXRef |
| scheduledActivity | ScheduledActivity |

ServicePackageXRef type

Table D-2 lists the parameters of the ServicePackageXRef type and the XML schema types of those parameters. All parameters of the ServicePackageXRef XML schema type have the same names, definitions, and data units as the corresponding parameters of the ServicePackageXRef UML class as defined in 3.2.5.

Table D-2:  ServicePackageXRef Parameters

| Parameter | Data Type |
| --- | --- |
| serviceAgreementRef | xsd:string[1024] |
| servicePackageRef | xsd:string[1024] |

ScheduledActivityType type

Table D-3 lists the parameters of the ScheduledActivityType XML type and the XML schema types of those parameters. All parameters of the ScheduledActivityType XML schema type have the same names, definitions, and data units as the corresponding parameters of the ScheduledActivity UML class defined in 3.2.6, except the serviceInfo and additionalActivityParameter parameters, which represents the containment of the ServiceInfo and AdditionalActivityParameter UML classes, respectively, by the ScheduledActivity UML class.

Table D-3:  ScheduledActivity Parameters

| Parameter | Data Type |
| --- | --- |
| scheduledActivityId | xsd:string[1024] |
| activityStatus | xsd:string with values restricted to the enumeration values: COMMITTED TENTATIVE AVAILABLE UNAVAILABLE |
| stationRef | xsd:string[1024] |
| antennaRef | xsd:string[1024] |
| beginningOfActivity | CcsdsAsciiTimeCodeBType. The element is defined as optional: the NULL value is represented by the absence of this element. |
| beginningOfTrack | CcsdsAsciiTimeCodeBType |
| endOfTrack | CcsdsAsciiTimeCodeBType |
| EndOfActivity | CcsdsAsciiTimeCodeBType. The element is defined as optional: the NULL value is represented by the absence of this element. |
| orbitNumber | xsd:NonNegativeInteger. The element is defined as optional: the NULL value is represented by the absence of this element. |
| serviceInfo | ServiceInfo |
| additionalActivity-Parameter | AdditionalActivityParameter |

ServiceInfoType type

Table D-4 lists the parameters of the ServiceInfoType XML type and the XML schema types of those parameters. All parameters of the ServiceInfoType XML schema type have the same names, definitions, and data units as the corresponding parameters of the ServiceInfo UML class defined in 3.2.8, except the additionalServiceParameter parameter, which represents the containment of the AdditionalServiceParameter UML class by the ServiceInfo UML class.

Table D-4:  ServiceInfoType Parameters

| Parameter | Data Type |
| --- | --- |
| serviceType | xsd:string with values restricted to the enumeration values: APA-AZ/EL APA-X/Y DELTADOR DOPPLER OFFLINE-TM-RECORDING OFFLINE-TM-PROVISION RF-ONLY RANGING RESERVED TBD TELECOMMAND TELEMETRY TEST UNUSED VLBI |
| frequencyBand | xsd:string with values restricted to the enumeration values: VHF UHF C-BAND Ka-BAND Ku-BAND L-BAND S-BAND V-BAND X-BAND OPTICAL N/A ALL |
| additionalServiceParameter | AdditionalServiceParameter |

AdditionalActivityParameter type

The AdditionalActivityParameter XML schema type is a subtype of the AdditionalParameter type, without extension or modification.

AdditionalServiceParameter type

The AdditionalServiceParameter XML schema type is a subtype of the AdditionalParameter type, without extension or modification.

AdditionalParameter type

Table D-5 lists the parameters of the AdditionalParameter XML type and the XML schema types of those parameters. All parameters of the AdditionalParameter XML schema type have the same names, definitions, and data units as the corresponding parameters of the AdditionalParameter UML class.

Table D-5:  AdditionalParameter Type

| Parameter | Data Type |
| --- | --- |
| parameterName | xsd:string[1024] |
| parameterValue | choice between a xsd:string[256] value and an xsd:any value. |

Example XML Document

Listing D-1 is an example XML document that conforms to version 1.0.0 of the Simple Schedule Format XML schema. It is pretty-printed to show the nesting of the type elements.

Figure D-3 is the XML Spy grid view of the example XML document.

Listing D-1: Example XML Document for Simple Schedule Format Schema V1.0.0

<?xml version="1.0" encoding="UTF-8"?>

<simpleSchedule xsi:schemaLocation="urn:ccsds:schema:cssm:simpleSchedule:1.0.0 SchemaCssmSimpleSchedule-v1_0_0.xsd" xmlns="urn:ccsds:schema:cssm:simpleSchedule:1.0.0" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xmlns:smInfoEntHeader="urn:ccsds:schema:cssm:smInfoEntHeader:1.0.0">

<srvMgtEntityType>SIMPLE_SCHEDULE</srvMgtEntityType>

<simpleScheduleHeader>

<smInfoEntHeader:originatingOrganization>WOTIS</smInfoEntHeader:originatingOrganization>

<smInfoEntHeader:generationTime>2006-257T15:11:28.2Z</smInfoEntHeader:generationTime>

<status>OPERATIONAL</status>

<smInfoEntHeader:version>1</smInfoEntHeader:version>

<smInfoEntHeader:startTime>2006-265T22:18:35.0Z</smInfoEntHeader:startTime>

<smInfoEntHeader:endTime>2006-266T00:01:47.0Z</smInfoEntHeader:endTime>

<smInfoEntHeader:purpose>To illustrate the form and content of a Simple Schedule XML instance document</smInfoEntHeader:purpose>

<smInfoEntHeader:description>Example of a Simple Schedule XML instance document</smInfoEntHeader:description>

</simpleScheduleHeader>

<scheduledPackage>

<scheduledPackageId>SOLB-15</scheduledPackageId>

<user>SOLB-SSOC</user>

<servicePackageXRef>

<serviceAgreementRef>WOTIS:SOLB-1</serviceAgreementRef>

<servicePackageRef>SOLB-15</servicePackageRef>

</servicePackageXRef>

<scheduledActivity>

<scheduledActivityId>2012-244-5</scheduledActivityId>

<activityStatus>COMMITTED</activityStatus>

<stationRef>MGS</stationRef>

<antennaRef>S-1</antennaRef>

<beginningOfActivity>2006-265T21:58:35.0Z</beginningOfActivity>

<beginningOfTrack>2006-265T22:18:35.0Z</beginningOfTrack>

<endOfTrack>2006-265T22:28:34.0Z</endOfTrack>

<endOfActivity>2006-265T22:33:34.0Z</endOfActivity>

<orbitNumber>10982</orbitNumber>

<serviceInfo>

<serviceType>TELEMETRY</serviceType>

<frequencyBand>S-BAND</frequencyBand>

</serviceInfo>

<additionalActivityParameter>

<parameterName>supportActivityCode</parameterName>

<parameterValueString>TR1</parameterValueString>

</additionalActivityParameter>

</scheduledActivity>

</scheduledPackage>

</simpleSchedule>

Figure D-3:	XML Spy Grid View of Example XML Document for Simple Schedule Format Schema V1.0.0

Security, SANA, and Patent Considerations

(Informative)

SecuRity Considerations

Overview

This section presents the results of an analysis of security considerations applied to the technologies specified in this Recommended Standard.

CONSEQUENCES OF NOT APPLYING SECURITY TO THE TECHNOLOGY

The consequences of not applying security to the systems and networks on which this Recommended Standard is implemented could include potential loss, corruption, and theft of data. Since it is possible to utilize these messages in preparing and disseminating schedules relating to the availability of communications and tracking resources for spacecraft, the consequences of not applying security to the systems and networks on which this Recommended Standard is implemented could include compromise or loss of the mission if malicious tampering of a particularly severe nature occurs.

POTENTIAL THREATS AND ATTACK SCENARIOS

Potential threats or attack scenarios include, but are not limited to, (a) unauthorized access to the programs/processes that generate and interpret the messages, and (b) unauthorized access to the messages during transmission between exchange partners. Protection from unauthorized access during transmission is especially important if the mission utilizes open ground networks such as the Internet to provide ground station connectivity for the exchange of data formatted in compliance with this Recommended Standard. It is strongly recommended that potential threats or attack scenarios applicable to the systems and networks on which this Recommended Standard is implemented be addressed by the management of those systems and networks and the utilization of adequate authentication, suitable protocols, and secured interfaces for the exchange of this information.

security concerns RELATED TO THIS RECOMMENDED STANDARD

Data Privacy

Privacy of data formatted in compliance with the specifications of this Recommended Standard should be assured by the systems and networks on which this Recommended Standard is implemented.

Data Integrity

Integrity of data formatted in compliance with the specifications of this Recommended Standard should be assured by the systems and networks on which this Recommended Standard is implemented.

Authentication of Communicating Entities

Authentication of communicating entities involved in the transport of data which complies with the specifications of this Recommended Standard should be provided by the systems and networks on which this Recommended Standard is implemented.

DATA TRANSFER BETWEEN COMMUNICATING ENTITIES

The transfer of data formatted in compliance with this Recommended Standard between communicating entities should be accomplished via secure mechanisms approved by the Information Technology Security functionaries of exchange participants.

Control of Access to Resources

Control of access to resources should be managed by the systems upon which provider formatting and recipient processing are performed.

Auditing of Resource Usage

Auditing of resource usage should be handled by the management of systems and networks on which this Recommended Standard is implemented.

UNAUTHORIZED ACCESS

Unauthorized access to the programs/processes that generate and interpret the messages should be prohibited in order to minimize potential threats and attack scenarios.

DATA SECURITY IMPLEMENTATION SPECIFICS

Specific information-security interoperability provisions that apply between agencies and other independent users involved in an exchange of data formatted in compliance with this Recommended Standard should be specified in an ICD.

SANA Considerations

General

The recommendations of this document request SANA to create the registries described below. New assignments in these registries will be shown at the SANA registry Web site: http://sanaregistry.org. Therefore, the reader shall look at the SANA Web site for all the assignments contained in these registries.

Already registered values shall not be affected by the extension of this Recommended Standard and definition of new services.

Requests to add assignments to these registries shall be submitted to SANA and shall come from a member Agency, or an observer Agency, or a CCSDS Associate, or an industry partner supported by a member Agency. The request shall be related to a cross support activity. After evaluation of the request and approval by the CSS Area Director (AD) or CSS Area Deputy Area Directory (DAD) or a person duly authorized by the AD or DAD her/him, a new value will be allocated and added to the appropriate registry.

SCCS-SM originatingOrganization Registry

The registry named ‘SCCS-SM originatingOrganization’ consists of a list of organizations (see table 3-2) along with a description:

| originatingOrganization: | a string of between 1 and 1024 characters in length. |
| --- | --- |
| Description: | a string of text describing the originatingOrganization. |

SCCS-SM USER REGISTRY

The registry named ‘SCCS-SM user’ consists of a list of users  (see table 3-3) along with a description:

| user: | a string of between 1 and 1024 characters in length. |
| --- | --- |
| Description: | a string of text describing the user. |

The initial registry should be filled with the following values:

| user | Description |
| --- | --- |
| UNALLOCATED | Indicates that the time is unallocated. |
| PROVIDER-CSSS | Indicates that the time is allocated for the Provider CSSS. |

In addition to the above values in the ‘user’ column, any value contained in the SANA Spacecraft Identifiers Registry (http://sanaregistry.org/r/spacecraftid/spacecraftid.html) column ‘Spacecraft Name’ is also a valid value for the user parameter described in table 3-3 of this document.

For details of the governance policy of the Spacecraft Identifiers Registry please refer to http://sanaregistry.org/r/spacecraftid/spacecraftid.html.

SCCS-SM stationAndAntennaRef Registry

The registry named ‘SCCS-SM stationAndAntennaRef’ consists of a list of station references (see table 3-5) with (optionally) associated antenna references (see table 3-5)  along with a description:

| stationRef: | a string of between 1 and 1024 characters in length. |
| --- | --- |
| antennaRef: | a string of between 1 and 1024 characters in length. |
| Description: | a string of text describing the stationRef and antennaRef. |

NOTES

- If a particular station has only one antenna, then the antennaRef field may have the same value as the stationRef.

- If a particular station has two or more antennas then there shall be as many entries for the station in the registry as there are antennas, with each of the stationRef entries having a unique antennaRef.

The following table presents examples of how this registry should be populated.

| stationRef | antennaRef | Description |
| --- | --- | --- |
| STATION-1 | STATION-1 | An example of a station with only 1 antenna. In this case the antennaRef has been given the same value as stationRef. |
| STATION-2 | ANTENNA-1 | An example of a station with only 1 antenna. In this case the antennaRef has been specified with a value different to that of stationRef. |
| STATION-3 | ANTENNA-1 | This example is of a station which has 3 antennas. This entry refers to antenna-1 at that station. |
| STATION-3 | ANTENNA-2 | This example is of a station which has 3 antennas. This entry refers to antenna-2 at that station. |
| STATION-3 | ANTENNA-3 | This example is of a station which has 3 antennas. This entry refers to antenna-3 at that station. |

Patent Considerations

No patent rights are known to adhere to any of the specifications of the Recommended Standard.

ABBreviations and ACRONYMS

(INFORMATIVE)

| AD | Area Director |
| --- | --- |
| ASCII | American Standard Code for Information Interchange |
| CCSDS | Consultative Committee on Space Data Systems |
| CSS | Cross Support Services |
| CSSS | Cross Support Service System |
| DAD | Deputy Area Director |
| e.g. | exempli gratia. Means “for example” |
| ICD | Interface Control Document |
| ICS | Implmentation Conformance Statement |
| i.e. | Id est. Means “that is” |
| IUT | Identification of implementation Under Test |
| M | Mandatory |
| N | No |
| n/a | Not applicable |
| OMG | Object Management Group |
| O | Optional |
| RL | Requirements List |
| SANA | Space Assigned Numbers Authority |
| SCCS SM | Space Communication Cross Support Service Management |
| TBD | To Be Decided |
| UML | Unified Modeling Language |
| UTC | Coordinated Universal Time |
| VLBI | Very-Long-Baseline Interferometry |
| W3C | World Wide Web Consortium |
| XML | eXtensible Markup Language |
| Y | Yes |

Informative References

(Informative)

[G1]	Space Communication Cross Support—Service Management—Operations Concept. Issue 1. Report Concerning Space Data System Standards (Green Book), CCSDS 910.14-G-1. Washington, D.C.: CCSDS, May 2011.

[G2]	Extensible Space Communication Cross Support—Service Management—Concept. Report Concerning Space Data System Standards (Green Book). Washington, D.C.: CCSDS, forthcoming.

Frequency Band Definitions

(Informative)

NOTE	–	The frequency bands definitions below are for informative purposes only; the actual details of the specific frequencies used for uplink, downlink, etc., will be specified in the service agreement. The following definitions, which do not distinguish between uplink or downlink or specify sub-bands, are thus sufficient for the purposes of this Recommended Standard.

| Band | Range (MHz) | Comment |
| --- | --- | --- |
| VHF | 30 – 300 |  |
| UHF | 300 - 1000 |  |
| C-Band | 3400 - 6725 |  |
| Ka-Band | 18000 - 35000 |  |
| Ku-Band | 10700 - 14500 |  |
| L-Band | 1215 - 1850 |  |
| S-Band | 2025 - 2400 |  |
| V-Band | 37500 - 50200 |  |
| X-Band | 7025 - 8500 |  |
| Optical |  | This is essentially a placeholder. May need further refinement as Optical communications standards mature. |

# Footnotes

A Provider Cross Support Service System is often colloquially referred to as a Network.

# Comments

RID CSSM-076

RID CSSM-062

RID CSSM-046

RID CSSM-064

RID CSSM-049

RID CSSM-052

RIDs CSSM-006, CSSM-018, CSSM-021, CSSM-011, CSSM-045, CSSM-056, CSSM067

RID CSSM018

RID CSSM-014 + CSSM-020

RID CSSM-049

RID CSSM-055

RID CSSM-056

RID CSSM-015

RID CSSM-045

RID CSSM-011

RID CSSM-067

RID CSSM-070

RID CSSM-070

RID CSSM-007

RID CSSM-029

RID CSSM-070

RID CSSM-024

RID CSSM-073

RID CSSM-043

RID CSSM-043

RID CSSM-006

RID CSSM-072

RID CSSM-027

RIDs CSSM-025, CSSM-072

New section to make the schemas normative.

RID CSSM-052

I think that this should be A2, and the subparagraphs promoted accordingly

RID CSSM-019

RID CSSM-018

RID CSSM-021

New section to make the schemas normative.

RID CSSM-018

RID CSSM-021

RID CSSM-045

RID CSSM-011

RID CSSM-067

RID CSSM-006

RID CSSM-006

RID CSSM-049

RID CSSM-067

RID CSSM-067

RID CSSM-067

RID CSSM-067

RID CSSM-049

RID CSSM-049

RID CSSM-049

RID CSSM-049

RID CSSM-049

RID CSSM-049

RID CSSM-049

RID CSSM-024