Draft Recommendation for
Space Data System Standards

Service Management Utilization Request Formats

Draft Recommended Standard

CCSDS 902.9-W-0.01

White Book

November 2015

AUTHORITY

|  | Issue: | White Book, Draft 0.01 |  |
| --- | --- | --- | --- |
|  | Date: | November 2015 |  |
|  | Location: | Not Applicable |  |

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF AUTHORITY:)

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and represents the consensus technical agreement of the participating CCSDS Member Agencies.  The procedure for review and authorization of CCSDS documents is detailed in Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-4), and the record of Agency participation in the authorization of this document can be obtained from the CCSDS Secretariat at the e-mail address below.

This document is published and maintained by:

CCSDS Secretariat

National Aeronautics and Space Administration

Washington, DC, USA

E-mail: secretariat@mailman.ccsds.org

STATEMENT OF INTENT

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF INTENT:)

The Consultative Committee for Space Data Systems (CCSDS) is an organization officially established by the management of its members. The Committee meets periodically to address data systems problems that are common to all participants, and to formulate sound technical solutions to these problems. Inasmuch as participation in the CCSDS is completely voluntary, the results of Committee actions are termed Recommended Standards and are not considered binding on any Agency.

This Recommended Standard is issued by, and represents the consensus of, the CCSDS members.  Endorsement of this Recommendation is entirely voluntary. Endorsement, however, indicates the following understandings:

o	Whenever a member establishes a CCSDS-related standard, this standard will be in accord with the relevant Recommended Standard. Establishing such a standard does not preclude other provisions which a member may develop.

o	Whenever a member establishes a CCSDS-related standard, that member will provide other CCSDS members with the following information:

--	The standard itself.

--	The anticipated date of initial operational capability.

--	The anticipated duration of operational service.

o	Specific service arrangements shall be made via memoranda of agreement. Neither this Recommended Standard nor any ensuing standard is a substitute for a memorandum of agreement.

No later than five years from its date of issuance, this Recommended Standard will be reviewed by the CCSDS to determine whether it should: (1) remain in effect without change; (2) be changed to reflect the impact of new technologies, new requirements, or new directions; or (3) be retired or canceled.

In those instances when a new version of a Recommended Standard is issued, existing CCSDS-related member standards and implementations are not negated or deemed to be non-CCSDS compatible.  It is the responsibility of each member to determine when such standards or implementations are to be modified.  Each member is, however, strongly encouraged to direct planning for its new standards and implementations towards the later version of the Recommended Standard.

FOREWORD

Through the process of normal evolution, it is expected that expansion, deletion, or modification of this document may occur.  This Recommended Standard is therefore subject to CCSDS document management and change control procedures, which are defined in the Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-4).  Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be sent to the CCSDS Secretariat at the e-mail address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- China National Space Administration (CNSA)/People’s Republic of China.

- Deutsches Zentrum für Luft- und Raumfahrt (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (FSA)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

- UK Space Agency/United Kingdom.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- China Satellite Launch and Tracking Control General, Beijing Institute of Tracking and Telecommunications Technology (CLTC/BITTT)/China.

- Chinese Academy of Sciences (CAS)/China.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- Danish National Space Center (DNSC)/Denmark.

- Departamento de Ciência e Tecnologia Aeroespacial (DCTA)/Brazil.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Geo-Informatics and Space Technology Development Agency (GISTDA)/Thailand.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Korea Aerospace Research Institute (KARI)/Korea.

- Ministry of Communications (MOC)/Israel.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic and Atmospheric Administration (NOAA)/USA.

- National Space Agency of the Republic of Kazakhstan (NSARK)/Kazakhstan.

- National Space Organization (NSPO)/Chinese Taipei.

- Naval Center for Space Technology (NCST)/USA.

- Scientific and Technological Research Council of Turkey (TUBITAK)/Turkey.

- South African National Space Agency (SANSA)/Republic of South Africa.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- Swiss Space Office (SSO)/Switzerland.

- United States Geological Survey (USGS)/USA.

PREFACE

This document is a draft CCSDS Recommended Standard.  Its ‘Red Book’ status indicates that the CCSDS believes the document to be technically mature and has released it for formal review by appropriate technical organizations.  As such, its technical contents are not stable, and several iterations of it may occur in response to comments received during the review process.

Implementers are cautioned not to fabricate any final equipment in accordance with this document’s technical content.

Recipients of this draft are invited to submit, with their comments, notification of any relevant patent rights of which they are aware and to provide supporting documentation.

# DOCUMENT CONTROL

| Document | Title | Date | Status |
| --- | --- | --- | --- |
| CCSDS 902.2-W-0.00 | Planning and Service Request Specification, Draft Recommended Standard, Draft 0.00 | November 2015 | Initial draft for working group |
| CCSDS 902.9-W-0.01 | Service Management Utilization Request Formats, Draft Recommended Standard, Draft 0.01 | November 2015 | Update after discussions at Darmstadt meeting. |

# CONTENTS

Section	Page

1	Introduction	1-11

1.1	PURPOSE AND SCOPE	1-11

1.2	APPLICABILITY	1-11

1.3	RATIONALE	1-11

1.4	DOCUMENT STRUCTURE	1-11

1.5	DEFINITIONS	1-11

1.6	NOMENCLATURE	1-11

1.7	CONVENTIONS—THE UNIFIED MODELING LANGUAGE	1-12

1.8	References	1-12

2	Overview	2-1

2.1	GENERAL	2-1

2.2	SIMPLE Planning Entity	2-1

2.3	MAPPING TO W3C XML SCHEMA	2-1

3	SERVICE MANAGEMENT UTILIZATION REQUEST FORMATS	3-1

3.1	GENERAL	3-1

3.2	Abstract Service Management Utilization Request Formats CONTENT/STRUCTURE	3-3

3.3	Service Management Utilization Request Formats Basic Constraints	3-23

3.4	Service Management Utilization Request Formats Enhanced Constraints	3-27

3.5	Submission Request	3-36

3.6	Basic Service Management Utilization Request Formats – Service Package - New Request	3-39

3.7	Basic Service Management Utilization Request Formats – Service Package - Update Request	3-42

3.8	Basic Service Management Utilization Request Formats – Planning Info Request	3-45

3.9	Service Management Utilization Request Formats – Service Package - Delete Request	3-47

3.10	Service Management Utilization Request Formats – Service Package – Select Alternate Request	3-49

3.11	Service Management Utilization Request Formats – Report Request	3-51

3.12	Service Management Utilization Request Formats – Information Request	3-52

3.13	Enhanced Service Management Utilization Request Formats – Service Package - New Request	3-54

3.14	Enhanced Service Management Utilization Request Formats – Service Package  - Update Request	3-58

3.15	Enhanced Service Management Utilization Request Formats – Planning Info Request	3-62

ANNEX A Informative References  (INFormative)	1

Figure

Figure 3-1:  Abstract Service Management Utilization Request Formats Class Diagram	3-4

Figure 3-2: Service Management Utilization Request Formats Basic Constraints Class Diagram	3-23

Figure 3-3: Service Management Utilization Request Formats Enhanced Constraints Class Diagram	3-27

Figure 3-4: Service Management Utilization Request Formats  - Submission Request Class Diagram	3-36

Figure 3-5: Basic Service Management Utilization Request Formats Service Package New Request Class Diagram	3-39

Figure 3-6: Basic Service Management Utilization Request Formats  Service Package Update Request Class Diagram	3-42

Figure 3-7: Basic Service Management Utilization Request Formats Planning Info Request Class Diagram	3-45

Figure 3-8: Service Management Utilization Request Formats Service Package Delete Request Class Diagram	3-47

Figure 3-9: Service Management Utilization Request Formats Service Package Select Alternate Request Class Diagram	3-49

Figure 3-10: Service Management Utilization Request Formats Report Request Class Diagram	3-51

Figure 3-11: Service Management Utilization Request Formats Information Request Class Diagram	3-52

Figure 3-12: Enhanced Service Management Utilization Request Formats Service Package New Request Class Diagram	3-54

Figure 3-13: Enhanced Service Management Utilization Request Formats Service Package Update Request Class Diagram	3-58

Figure 3-14: Enhanced Service Management Utilization Request Formats Planning Info Request Class Diagram	3-62

Table

Table 3-1: Class SrvMgtUtilReq Parameters	3-5

Table 3-2:  Class SrvMgtUtilReqHeader Parameters	3-5

Table 3-3: Class RequestType Parameters	3-6

Table 3-4: Class ServicePkgReq Parameters	3-7

Table 3-5: Class NewSrvPkg Parameters	3-8

Table 3-6: Class NewSrvPkg use of Class ServicePkgReq Parameters	3-8

Table 3-7: Class UpdateReq Parameters	3-8

Table 3-8: Class UpdateSrvPkg use of Class ServicePkgReq Parameters	3-9

Table 3-9: Class DeleteSrvPkg Parameters	3-9

Table 3-10: Class DeleteSrvPkg use of Class ServicePkgReq Parameters	3-9

Table 3-11: Class SelectAltSrvPkg Parameters	3-10

Table 3-12: Class SelectAltSrvPkg use of Class ServicePkgReq Parameters	3-10

Table 3-13: Class PlanningInfoReq Parameters	3-11

Table 3-14: Class reportReq Parameters	3-12

Table 3-15: Class InfoReq Parameters	3-13

Table 3-16: Class Scenario Parameters	3-14

Table 3-17: Class ServiceInfo Parameters	3-15

Table 3-18: Class ConfigurationProfileXRef Parameters	3-16

Table 3-19: Class ConfigProfileParameter Parameters	3-16

Table 3-20: Class EventSequenceXRef Parameters	3-17

Table 3-21: Class EventSeqParameter Parameters	3-17

Table 3-22: Class OIDParameter Parameters	3-18

Table 3-23: Class SubmissionReq Parameters	3-18

Table 3-24: Class TrajectoryDataSubmission Parameters	3-19

Table 3-25: Class CCSDSTrajectoryPrediction Parameters	3-20

Table 3-26: Class ConfigProfileSubmission Parameters	3-20

Table 3-27: Class EventSeqSubmission Parameters	3-21

Table 3-28: Class Constraints Parameters	3-21

Table 3-29: Class BasicStartTimeConstraint Parameters	3-24

Table 3-30: Class BasicDurationConstraint Parameters	3-25

Table 3-31: Class BasicHandoverConstraints Parameters	3-25

Table 3-32: Class BasicApertureConstraint Parameters	3-26

Table 3-33: Class StandingOrder Parameters	3-28

Table 3-34: Class PassIntervalConstraints Parameters	3-29

Table 3-35: Class PassDailyTimeConstraints Parameters	3-29

Table 3-36: Class PassRangeConstraints Parameters	3-31

Table 3-37: Class PassRelativeTimeConstraints Parameters	3-32

Table 3-38:  Class EventParameter Parameters	3-35

# Introduction

## PURPOSE AND SCOPE

### PURPOSE

### SCOPE

## APPLICABILITY

## RATIONALE

### General

### USE CASES

## DOCUMENT STRUCTURE

This document is organized as follows:

## DEFINITIONS

For the purposes of this document, the following definitions apply:

- the word ‘agencies’ may also be construed as meaning ‘satellite operators’ or ‘satellite service providers’;

- the notation ‘n/a’ signifies ‘not applicable’.

## NOMENCLATURE

### Normative Text

The following conventions apply for the normative specifications in this Recommended Standard:

- the words ‘shall’ and ‘must’ imply a binding and verifiable specification;

- the word ‘should’ implies an optional, but desirable, specification;

- the word ‘may’ implies an optional specification;

- the words ‘is’, ‘are’, and ‘will’ imply statements of fact.

NOTE	–	These conventions do not imply constraints on diction in text that is clearly informative in nature.

### Informative Text

In the normative sections of this document, informative text is set off from the normative specifications either in notes or under one of the following subsection headings:

- Overview;

- Background;

- Rationale;

- Discussion.

## CONVENTIONS—THE UNIFIED MODELING LANGUAGE

The Unified Modeling Language (UML) diagrams used in the specification (including class diagrams, package diagrams, sequence diagrams, and activity diagrams) follow the notation, semantics, and conventions imposed by the Version 2.4.1 UML specification of the Object Management Group (OMG) (reference [4]). An overview of UML diagramming conventions can be found in Annex E of reference [1].

Within the document use is made only of class diagrams. A UML class diagram describes the structure of a message, its parts, and how those parts interrelate. A UML class, represented in the diagram as a box, represents a data set. Class diagram conventions include composition, generalization, multiplicity, and constraints. Enumeration notation is also used but only when it is involved in a composition constraint.

## References

The following publications contain provisions which, through reference in this text, constitute provisions of this document.  At the time of publication, the editions indicated were valid.  All publications are subject to revision, and users of this document are encouraged to investigate the possibility of applying the most recent editions of the publications indicated below.  The CCSDS Secretariat maintains a register of currently valid CCSDS publications.

[1]	Space Communication Cross Support—Service Management—Service Specification. Issue 1. Recommendation for Space Data System Standards (Blue Book), CCSDS 910.11-B-1. Washington, D.C.: CCSDS, August 2009.

[2]	“CCSDS-910.11-B-1_XML_schemas.”  http://public.ccsds.org/publications/archive/CCSDS-910.11-B-1_XML_schemas.zip.

[3]	Time Code Formats. Issue 4. Recommendation for Space Data System Standards (Blue Book), CCSDS 301.0-B-4. Washington, D.C.: CCSDS, November 2010.

[4]	Unified Modeling Language (UML). Version 2.4.1. Needham, Massachusetts: Object Management Group, August 2011.

[5]	Service Agreement and Service Configuration. Recommendation for Space Data System Standards (Blue Book), CCSDS 902.5-B-1. Blue Book. Issue 1. Washington, D.C.: CCSDS, xxxx 20xx.

[6]	Simple Schedule Format. Recommendation for Space Data System Standards, CCSDS 902.1-B-1. Blue Book. Issue 1. Washington, D.C.: CCSDS, xxxx 20xx.

[7]	Planning Data Formats. Recommendation for Space Data System Standards, CCSDS 902.2-B-1. Blue Book. Issue 1. Washington, D.C.: CCSDS, xxxx 20xx.

# Overview

## GENERAL

## SIMPLE Planning Entity

## MAPPING TO W3C XML SCHEMA

This Recommended Standard includes the specification of a mapping to World Wide Web Consortium (W3C) extensible Markup Language (XML) schema. The normative mapping of this Recommended Standard to XML W3C schemas is a virtual annex to this Recommended Standard and is contained in a stand-alone set of schema files (reference [2]).

NOTE	–	The XML schema has been elaborated on the basis of the mapping guidelines described in reference  [A1].

# SERVICE MANAGEMENT UTILIZATION REQUEST FORMATS

## GENERAL

The Service Management Utilization Requests Formats forms the basis from which various types of requests required by Service Management are derived. These can be categorized into 5 types:

- Planning Information Request – permits the submission of a query that can request various types of planning information.

- Report Request– permits the submission of a request for a report to be returned. Currently two types of report are foreseen:

- Simple Schedule (see [6]– Simple Schedule Blue Book)

- Accounting Report (see TBD)

- Information Request – permits the submission of a request for one or more of the following types of information:

- Configuration Profile(s)

- Event Sequence(s)

- Service Agreement(s)

- Service Package(s)

- Trajectory(s)

The information that is being requested is specified by means of a cross reference to the identifier(s) of the data entity(ies) that was previously defined.

- Submission Request – permits the submission of data entities that are used as part of Service Management. Currently 3 types of submission request are foreseen:

- Trajectory Submission Request – enables the submission of a new trajectory prediction.

- Configuration Profile Submission Request – enables the submission of a new configuration profile.

- Event Sequence Submission Request – enables the submission of a new event sequence.

- Service Package Request– permits the submission of requests relating to service packages. The supported types of service package requests are:

- New Request – permits the submission of a new planning or service request.

- Update Request – permits the revision of a previously submitted request.

- Delete Request – permits the deletion of a previously submitted request.

- Select Alternate Service Package – permits the selection of a service package which was established via an alternative scenario.

## Abstract Service Management Utilization Request Formats CONTENT/STRUCTURE

### Overview

Figure 3-1 shows the UML Class diagram for the Abstract Service Management Utilization Request Formats.

Figure 3-1:  Abstract Service Management Utilization Request Formats Class Diagram

The attributes of each class are described further in the following subsections and tables.

### CLASS SrvMgtUtilReq

The SrvMgtUtilReq class is mandatory and shall constitute the Planning And Service information entity.

NOTE	–	The SrvMgtUtilReq class is a specialization and of class SrvMgtInfoEntity described in Annex A of reference [6] and the generic description of the parameters is can be found there.

Table 3-1 specifies the use of the parameters in the SrvMgtInfoEntity in the scope of the Simple Service Request.

Table 3-1: Class SrvMgtUtilReq Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| srvMgtEntityType | See Annex A of reference [6]. | String1024—For the Service Management Utilization Request Formats request the only permitted value for this parameter is the string “UTILIZATION_REQ” | See Annex A of reference [6]. |

### CLASS SrvMgtUtilReqHeader

The SrvMgtUtilReqHeader class is mandatory and shall constitute the ‘header’ of the Service Management Utilization Request Formats.

NOTE	–	The SrvMgtUtilReqHeader class is a specialization of class SrvMgtHeader described in Annex A of reference [6] and the generic description of the parameters is can be found there.

Table 3-2 specifies the use of the parameters in the SrvMgtHeader in the scope of the Service Management Utilization Request Formats.

Table 3-2:  Class SrvMgtUtilReqHeader Parameters

The parameters for the SrvMgtUtilReqHeader class are as per Annex A of reference [6] except for the following:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| status | See Annex A of reference [6]. | Enumeration – For the simple Service Management Utilization Request Formats the only permitted values are TEST indicates that the request has been generated for test purposes only. PROVISIONAL indicates that the request contained is provisional and may still be subject to change. OPERATIONAL indicates that this is an operational request. OTHER indicates that this request has been generated for other purposes. In this case the optional parameter purpose can be used to further specify the purpose of the request. | See Annex A of reference [6]. |

### CLASS RequestType (Abstract)

The RequestType is an abstract class which is used to instantiate the various classes of request  required by service management in the context of planning ansd scheduling requests.

NOTE	–	The RequestType class is a specialization and of class SrvMgtData described in Annex A of reference [6].

The RequestType class shall contain the parameters  as specified in Table 3-3.

Table 3-3: Class RequestType Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| user | The user of the requested services. These must be spacecraft names as specified in SANA. | String64—Permitted values registered in SANA | n/a |
| requestID | A unique request ID assigned by the requestor. | String1024 | n/a |
| serviceAgreementXRef | Optional Parameter. This can be used to specify a cross reference to the service agreement under which the requested services are to be provided. | String1024 | n/a |
| comment | Optional Parameter May be used for the provision of ad hoc information. | String8096 | n/a |

### CLASS ServicePkgReq (Abstract)

The ServicePkgReq is an abstract class which is used to instantiate the various classes of request required by service management for manipulating service packages.

NOTE	–	The ServicePkgReq class is a specialization and of class RequestType described in section 3.2.4 above.

The ServicePkgReq class shall contain the parameters  as specified in Table 3-4.

Table 3-4: Class ServicePkgReq Parameters

The parameters for the ServicePkgReq class as are as per Table 3-3 with the addition of the following:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| serviceReqID | Service request identifier. | String1024 | n/a |
| chainToSerPgkXRef | Optional parameter. This parameter may be used to specify a cross reference to an existing service package to which this service package should be “chained”. | String 1024 | n/a |

### CLASS NewSrvPkg

The NewSrvPkg class is optional and may be used to submit a new service request.

NOTE	–	The NewSrvPkg class is a specialization of class ServicePkgReq described in 3.2.5 and the generic description of the parameters is given in that subsection.

The NewSrvPkg class, in addition to the parameters in the abstract RequestType class described in 3.2.5  shall contain a reference to the appropriate Trajectory data. This parameters is as specified in Table 3-5.

Table 3-5: Class NewSrvPkg Parameters

The parameters for the NewSrvPkg class as are as per Table 3-3 and Table 3-4 with the addition of the following:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| trajectoryXRef | This is used to specify a reference to the trajectory data that is applicable to the user (i.e. spacecraft) for the requested services. | String1024 | n/a |

Table 3-6: Class NewSrvPkg use of Class ServicePkgReq Parameters

In the context of the NewSrvPkg class the usage of the following ServicePkgReq parameters (as described in Table 3-4) should be noted:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| serviceReqID | In the context of the NewSrvPkg class this parameter must be an identifier that has not previously been used. | String1024 | n/a |

### CLASS UpdateSrvPkg

The UpdateSrvPkg class is optional and may be used to update a new service request.

NOTE	–	The UpdateSrvPkg class is a specialization of class RequestType described in 3.2.5 and the generic description of the parameters is given in that subsection.

The UpdateSrvPkg class, in addition to the parameters in the abstract RequestType class described in 3.2.5  shall contain a reference to the appropriate Trajectory data. This parameter is as specified in Table 3-7.

Table 3-7: Class UpdateReq Parameters

The parameters for the UpdateSrvPkg class as are as per Table 3-3 and Table 3-4 with the addition of the following:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| trajectoryXRef | This is used to specify a reference to the trajectory data that is applicable to the user (i.e. spacecraft) for the requested services. | String1024 | n/a |

Table 3-8: Class UpdateSrvPkg use of Class ServicePkgReq Parameters

In the context of the UpdateSrvPkg class the usage of the following ServicePkgReq parameters (as described in Table 3-4) should be noted:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| serviceReqID | In the context of the UpdateSrvPkg class this parameter must refer to the identifier of the previously submitted request that is to be updated. | String1024 | n/a |

### CLASS DeleteSrvPkg

The DeleteSrvPkg class is optional and may be used to delete a previously submitted  service  request.

NOTE	–	The DeleteReq class is a specialization of class RequestType described in 3.2.5 and the generic description of the parameters is given in that subsection.

Table 3-9: Class DeleteSrvPkg Parameters

The parameters for the DeleteSrvPkg class are as per Table 3-3 and Table 3-4 with the addition of the following:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| Not applicable. |  |  |  |

Table 3-10: Class DeleteSrvPkg use of Class ServicePkgReq Parameters

In the context of the DeleteSrvPkg class the usage of the following ServicePkgReq parameters (as described in Table 3-4) should be noted:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| serviceReqID | In the context of the DeleteSrvPkg class this parameter must refer to the identifier of the previously submitted request that is to be deleted. | String1024 | n/a |

### CLASS SelectAltSrvPkg

The SelectAltSrvPkg class is optional and may be used to select an alternative scenario service request that has previously been submitted.

NOTE	–	The SelectAltSrvPkg class is a specialization of class RequestType described in 3.2.5 and the generic description of the parameters is given in that subsection.

Table 3-11: Class SelectAltSrvPkg Parameters

The parameters for the SelectAltSrvPkg class are as per Table 3-3 and Table 3-4 with the addition of the following:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| Not applicable. |  |  |  |

Table 3-12: Class SelectAltSrvPkg use of Class ServicePkgReq Parameters

In the context of the SelectAltSrvPkg class the usage of the following ServicePkgReq parameters (as described in Table 3-4) should be noted:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| serviceReqID | In the context of the SelectAltSrvPkg class this parameter must refer to the identifier of the previously submitted request that is to be used as the alternate scenario. | String1024 | n/a |

### CLASS PlanningInfoReq

The PlanningInfoReq class is optional and may be used to submit a query that can request various type of planning information.

NOTE	–	The PlanningInfoReq class is a specialization of class RequestType described in 3.2.4 and the generic description of the parameters is given in that subsection.

The PlanningInfoReq class, in addition to the parameters in the abstract RequestType class described in 3.2.4  shall contain the list of the requestedInfo. This parameter is as specified in Table 3-13.

Table 3-13: Class PlanningInfoReq Parameters

The parameters for the PlanningInfoReq class as are as per Table 3-3 with the addition of the following:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| requestedInfo | This specifies the type of information that is being requested and can be one or more of the information types specified in the next column. | Enumeration COMMS Predicted communications geometry events (see reference [7]) DATARATE Sustainable data rates & volume estimate events (see reference [7]) RFI Predicted radio frequency interference events (see reference [7]) CONFLICTS Predicted resource conflict events (see reference [7]) COSTS Cost estimates (see reference [7]) OTHER Any event not falling into the above categories (see reference [7]) | n/a |

### CLASS ReportReq

The ReportReq class is optional and may be used to submit a request for report.

NOTE	–	The ReportReq class is a specialization of class RequestType described in 3.2.4 and the generic description of the parameters is given in that subsection.

The ReportReq class, in addition to the parameters in the abstract RequestType class described in 3.2.4  shall contain the reportType required along with the required start and end times. These parameters are as specified in Table 3-14.

Currently two basic types of report are foreseen:

- Simple Schedule as described in Ref. [6]

- Accounting reports as described in TBD.

In the returned Simple Schedule the following should be noted;

- Service Packages that start before the startTime but end after the startTime will be included in the schedule information.

- Service Packages that start before the endTime but end after the endTime will be included in the schedule information.

Table 3-14: Class reportReq Parameters

The parameters for the reportReq class as are as per Table 3-3 with the addition of the following:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| reportType | This is used to specify the type of report required. | Enumeration SIM_SCH_SPECIFIC results in a Simple Schedule (see Ref. [6]) containing only information directly related to the requesting user SIM_SCH_COMPLETE results in a Simple Schedule (see Ref. [6]) containing a complete schedule of all station/aperture allocations insofar as this is permitted by the agencies policies. SIM_SCH_FREE results in a Simple Schedule (see Ref. [6]) containing a schedule of all aperture free times insofar as this is permitted by the agencies policies. ACCOUNTING results in an accounting report containing TBD data. | n/a |
| startTime | The start time to be used for the requested report. | CCSDS ASCII Time Code B (reference [3]) | UTC |
| endTime | The end time to be used for the requested report. | CCSDS ASCII Time Code B (reference [3]) | UTC |

### CLASS InfoReq

The InfoReq class is optional and may be used to submit a request for information about one or more of the following:

- Configuration Profile(s)

- Event Sequence(s)

- Service Agreement(s)

- Service Package(s)

- Trajectory(ies)

NOTE	–	The InfoReq class is a specialization of class RequestType described in 3.2.4 and the generic description of the parameters is given in that subsection.

The InfoReq class, in addition to the parameters in the abstract RequestType class described in 3.2.4  shall contain one or more of the parameters specified in Table 3-15.

Table 3-15: Class InfoReq Parameters

The parameters for the InfoReq class as are as per Table 3-3 with the addition of the following:

NOTE: At least one parameter must be specified.

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| configurationProfileXRef | Optional Parameter. This is used to specify a reference or references to the configuration profile(s) that the user wants the information for. | Array of String1024 The format of the configuration cross-reference is defined in reference [5] | n/a |
| eventSequenceXRef | Optional Parameter. This is used to specify a reference or references to the event sequence(s) that the user wants the information for. | Array of String1024 | n/a |
| serviceAgreementXRef | Optional Parameter. This is used to specify a reference or references to the service agreement(s) that the user wants the information for. | Array of String1024 | n/a |
| servicePackageXRef | Optional Parameter. This is used to specify a reference or references to the service package(s) that the user wants the information for. | Array of String1024 | n/a |
| trajectoryXRef | Optional Parameter. This is used to specify a reference or references to the trajectory(ies) that the user wants the information for. | Array of String1024 | n/a |

### CLASS Scenario

The Scenario class is optional and is required only if it is necessary to specify multiple requests covering the same time period so that non-nominal cases can be handled.

The Scenario class shall contain the identification of the scenario and cross reference to the prime request shall include parameters specified in Table 3-16.

Table 3-16: Class Scenario Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| scenarioID | This is defined by the request submitter and must uniquely define the scenario | String1024 | n/a |
| primeRequestIDXRef | Identifies the request that contains the request that applies to the nominal case. In the case of the nominal request itself this value must be the same as the requestID of the nominal request | String1024 | n/a |

### CLASS ServiceInfo

The ServiceInfo class shall be used to provide information about the type of operations to be carried out during a pass.

The ServiceInfo class shall use the parameters specified in Table 3-17 to specify the type of service and frequency band to be used.

There shall be one or more instances of the ServiceInfo class for each instance of the Servcies class.

Table 3-17: Class ServiceInfo Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| serviceType | The type of service that will be carried out during an activity. It should be noted that: APA-AZ/EL indicates Antenna Pointing Angles, Azimuth/Elevation APA-X/Y indicates Antenna Pointing Angles, X/Y VLBI indicates Very-Long-Baseline Interferometry. | Enumeration: APA-AZ/EL APA-X/Y DELTADOR DOPPLER OFFLINE-TM-RECORDING OFFLINE-TM-PROVISION RF-ONLY RANGING RESERVED TBD TELECOMMAND TELEMETRY TEST UNUSED VLBI | n/a |
| frequencyBand | The frequency band that will be used by the service. If the frequency band is not relevant the value N/A (not applicable) shall be used. (See annex See Annex H of reference [6]. for a definition of the frequencies each band refers to.) | Enumeration: VHF UHF C-BAND KA-BAND KU-BAND L-BAND S-BAND V-BAND X-BAND OPTICAL N/A ALL | n/a |

### CLASS ConfigurationProfileXRef

The ConfigurationProfileXRef class shall provide a cross-reference to an existing configuration profile.

The ConfigurationProfileXRef class shall use the parameters specified in Table 3-18 to provide the cross-reference to the existing configuration profile.

Table 3-18: Class ConfigurationProfileXRef Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| configurationProfileXRef | The cross- reference to an existing configuration profile. | String1024 | n/a |

### CLASS ConfigProfileParameter.

The ConfigProfileParameter class is optional and may be used to specify the values for the configuration parameters that apply to the service being requested. It is possible to use the ConfigProfileParameter class to specify values that override those specified in a ConfigurationProfileXRef class.

NOTE	–	The ConfigProfileParameter class is a specialization of class OIDParameter described in 3.2.19 below and the generic description of the parameters can be found there.

There  shall be zero or more instances of the ConfigProfileParameter class for each instance of the ConfigurationProfileXRef class.

In the context of service management it is expected that the details of which parameters of a particular Configuration Profile that are permitted to be updated will be contained in the Service Agreement (see reference [5]).

The ConfigProfileParameter class shall use the parameters specified in Table 3-19.

Table 3-19: Class ConfigProfileParameter Parameters

The parameters for the ConfigProfileParameter class are as per Table 3-22.

### CLASS EventSequenceXRef

The EventSequenceXRef class shall provide a cross-reference to an existing event sequence.

The EventSequenceXRef class shall use the parameters specified in Table 3-20 to provide the cross-reference to the existing event sequence.

Table 3-20: Class EventSequenceXRef Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| eventSequenceXRef | The cross- reference to an existing event sequence. | String1024 | n/a |

### CLASS EventSeqParameter.

The EventSeqParameter class is optional and may be used to specify the values for the  parameters that are to be used to update values in an event sequence. It is possible to use the EventSeqParameter class to specify values that override those specified in an EventSequenceXRef class.

NOTE	–	The EventSeqParameter class is a specialization of class OIDParameter described in 3.2.19 below and the generic description of the parameters can be found there.

There  shall be zero or more instances of the EventSeqParameter class for each instance of the EventSequenceXRef class.

In the context of service management it is expected that the details of which parameters of a particular Event Sequence that are permitted to be updated will be contained in the Service Agreement (see reference [5]). (TBD)

The EventSeqParameter class shall use the parameters specified in Table 3-21.

Table 3-21: Class EventSeqParameter Parameters

The parameters for the EventSeqParameter class as are as per Table 3-22.

### CLASS OIDParameter (Abstract)

The OIDParameter is an abstract class which is used to instantiate the various classes of parameter required to update values which are identified by object identifiers

The OIDParameter class shall contain the parameters  as specified in Table 3-22.

Table 3-22: Class OIDParameter Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| frInstanceNumber | The functional resource instance number | As defined in reference [5]. | n/a |
| parameterId-OID | The Object Identifier of the parameter ID | As defined in reference [5]. | As required by the additional parameter |
| parameterValue | The value for the parameter | As defined in reference [5]. | As required by the additional parameter |
| frType-OID | The Object Identifier specifying the function resource type (i.e. what type the parameter value is) | As defined in reference [5]. | As required by the additional parameter |

### CLASS SubmissionReq (Abstract)

The SubmissionReq is an abstract class which is used to instantiate the various classes of request required by service management for manipulating submitting new information entities, i.e. trajectory predictions, configuration profiles and event sequences.

NOTE	–	The SubmissionReq class is a specialization and of class RequestType described in section 3.2.4 above.

The SubmissionReq class shall contain the parameters  as specified in Table 3-23.

Table 3-23: Class SubmissionReq Parameters

The parameters for the SubmissionReq class as are as per Table 3-3 with the addition of the following:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| requestRef | This is the reference by which the information entity can later be cross-referenced by. It is the responsibility of the submitted that this reference is unique within the scope of their service agreement. | String1024 | n/a |

### CLASS TrajectoryDataSubmission (Abstract)

The TrajectoryDataSubmission is an abstract class which is used to instantiate the classes required by service management to submit trajectory prediction data.

NOTE	–	The TrajectoryDataSubmission class is a specialization and of class RequestType described in section 3.2.17 above.

The TrajectoryDataSubmission class shall contain the parameters  as specified in Table 3-24.

Table 3-24: Class TrajectoryDataSubmission Parameters

The parameters for the TrajectoryDataSubmission class as are as per Table 3-23 with the addition of the following:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| trajectoryType | This specifies the type of the Orbit Data Message used to specify the trajectory information. | String16 | n/a |
| trajectoryFormat | This specifies the format of the Orbit Data Message used to specify the trajectory information. | String16 | n/a |
| trajectoryData | This is used to hold the required trajectory data. | TBD | n/a |

### CLASS CCSDSTrajectoryPrediction

The CCSDSTrajectoryPrediction class is optional.

NOTE	–	The CCSDSTrajectoryPrediction class is a specialization of class TrajectoryDataSubmission described in 3.2.21 above and the generic description of the parameters can be found there.

Table 3-25 specifies the use of the parameters in the CCSDSTrajectoryPrediction .

Table 3-25: Class CCSDSTrajectoryPrediction Parameters

The parameters for the CCSDSTrajectoryPrediction class are as per Table 3-24 except for the following:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| trajectoryType | This specifies the type of the Orbit Data Message used to specify the trajectory information. | String16 – permitted values stored in SANA OPM – CCSDS Orbit Parameter Message, See Refs. YYY and ZZZ OMM – CCSDS Orbit Mean-Elements Message , See Refs YYY and ZZZ OEM – CCSDS Orbit Ephemeris Message, See Refs YYY and ZZZ OHM – CCSDS Orbit Ephemeris Message, See Refs YYY and ZZZ | n/a |
| trajectoryFormat | This specifies the format of the Orbit Data Message used to specify the trajectory information. | String16 – permitted values stored in SANA TEXT – text format of CCSDS Orbit Data Message, See Ref. YYY. XML – XML format of CCSDS CCSDS Orbit Data Message, See Ref. ZZZ | n/a |

### CLASS ConfigProfileSubmission

The ConfigProfileSubmission class is optional.

NOTE	–	The ConfigProfileSubmission class is a specialization of class SubmissionReq described in 3.2.17 above and the generic description of the parameters can be found there.

Table 3-26 specifies the use of the parameters in the ConfigProfileSubmission.

Table 3-26: Class ConfigProfileSubmission Parameters

The parameters for the ConfigProfileSubmission class are as per Table 3-24 with the addition of the following:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| TBD | TBD | TBD | TBD |

### CLASS ConfigurationProfileContents

The ConfigurationProfileContents class shall be used when it is required to submit  a complete configuration profile.

The ConfigurationProfileContents class is specified in reference [5].

### CLASS EventSeqSubmission

The EventSeqSubmission class is optional.

NOTE	–	The EventSeqSubmission class is a specialization of class SubmissionReq described in 3.2.17 above and the generic description of the parameters can be found there.

Table 3-27 specifies the use of the parameters in the EventSeqSubmission.

Table 3-27: Class EventSeqSubmission Parameters

The parameters for the EventSeqSubmission class are as per Table 3-24 with the addition of the following:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| TBD | TBD | TBD | TBD |

### CLASS EventSequence

The EventSequence class shall when it is required to submit a complete event sequence.

The EventSequence class is specified in reference TBD [Event Sequence Book].

### CLASS Constraints (Abstract)

The Constraints class is abstract and is used to instantiate the various constraint classes that apply to the Service Management Utilization Request Formats.

Table 3-28: Class Constraints Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| N/A | N/A | N/A | N/A |

## Service Management Utilization Request Formats Basic Constraints

### Overview

Figure 3-2 shows the UML Class diagram for the Service Management Utilization Request Formats Basic Constraints.

Figure 3-2: Service Management Utilization Request Formats Basic Constraints Class Diagram

The attributes of each class are described further in the following subsections and tables.

### CLASS Constraints (Abstract)

See section 3.2.17 for the definition of this class.

### CLASS BasicStartTimeConstraint

The BasicStartTimeConstraint class is optional and  may be used to specify the preferred start time of a pass along with the acceptable earliest and/or latest start times.

The parameters of the BasicStartTimeConstraint class are specified in Table 3-29.

There shall be zero or one instances of the BasicStartTimeConstraint class for each instance of the TimingConstraints class. If no BasicStartTimeConstraint class is specified it is assumed that any start time is acceptable.

Table 3-29: Class BasicStartTimeConstraint Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| PreferredStartTime | Used to specify (in UTC) the preferred time at which a pass starts. | CCSDS ASCII Time Code B (reference [3]) | UTC |
| earliestStartTime | Optional parameter. Used to specify (in UTC) the earliest time at which a pass can start. | CCSDS ASCII Time Code B (reference [3]) | UTC |
| latestStartTime | Optional parameter. Used to specify (in UTC) the latest time at which a pass can start. NOTE: If both earliestStartTime and latestStartTime are specified then latestStartTime ≥ earliestStartTime | CCSDS ASCII Time Code B (reference [3]) | UTC |

### CLASS BasicDurationConstraint

The BasicDurationConstraint class is optional and  may be used to specify the preferred duration of a pass along with the acceptable minimum and/or maximum duration.

The parameters of the BasicDurationConstraint class are specified in Table 3-30.

There shall be zero or one instances of the BasicDurationConstraint class for each instance of the TimingConstraints class. If no BasicDurationConstraint class is specified it is assumed that any duration is acceptable.

Table 3-30: Class BasicDurationConstraint Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| minimumDuration | Optional parameter. This is used to specify the minimum duration required for a pass. | Integer ≥ 0 Default value if omitted is 0 | Seconds |
| maximumDuration | Optional parameter. This is used to specify the maximum duration required for a pass. NOTE: If both minimumDuration and maximumDuration are specified then maximumDuration ≥ minimumDuration | Integer ≥ 0 Default value if omitted is ∞ | Seconds |

### CLASS BasicHandoverConstraint

The BasicHandoverConstraints class is optional and if not specified for a request it is assumed that a station handover is not permitted,

The BasicHandoverConstraints class shall contain the details of the constraints applying to station handovers shall include parameters specified in Table 3-31.

There shall be zero or one instances of the BasicHandoverConstraint class for each instance of the ApertureConstraints class.

Table 3-31: Class BasicHandoverConstraints Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| maximumHandovers | The maximum number of station handovers that are permitted during the requested tracking time. | Integer >0 | n/a |
| mimimumOverlap | Used to specify the minimum overlap between stations during a handover. NOTE: if this is negative then there will be a gap in the coverage provided. | Integer | Secs |
| minimunSingleDuration | Optional Parameter. This can be used to specify the acceptable minimum duration of contact on any one of the apertures used during the pass. | Integer>0 | Secs |

### CLASS BasicApertureConstraint

The BasicApertureConstraint class is optional and can be used to specify the aperture with it is desired that the service is provided.

The parameters of the BasicApertureConstraint class are specified in Table 3-32.

There shall be zero or more instances of the BasicApertureConstraint class for each instance of the ApertureConstraints class. If no BasicApertureConstraint class is specified it is assumed that any aperture specified in the service agreement can be used.

Table 3-32: Class BasicApertureConstraint Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| apertureRef | Name of the aperture | String1024—Permitted values registered in SANA | n/a |
| priority | Optional Parameter. This can be used to specify a preference for which aperture is used if more than one BasicApertureConstraint class is instantiated. The lower the value specified here the higher the priority, with 1 being the highest prority. | Integer >0 Default value if omitted is 1 | n/a |

## Service Management Utilization Request Formats Enhanced Constraints

### Overview

Figure 3-3 shows the UML Class diagram for the Service Management Utilization Request Formats Enhanced Constraints.

Figure 3-3: Service Management Utilization Request Formats Enhanced Constraints Class Diagram

The attributes of each class are described further in the following subsections and tables.

### CLASS Constraints (Abstract)

See section 3.2.17 for the definition of this class.

### CLASS StandingOrder

The StandingOrder class is and can be used to submit “repeat” requests. It allows the specification of the number of passes that are required within a specified time interval. A standing order will be repeated until the start time of the service(s) requested is after the endTime specified in the SrvMgtUtilReqHeader class.

The StandingOrder class shall include parameters specified in Table 3-33.

Table 3-33: Class StandingOrder Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| minNumOfPasses | The minimum number of passes required in the specified time interval. | Integer > 0 | n/a |
| maxNumOfPasses | The maximum number of passes required in the specified time interval. | Integer ≥ minNumOfPasses | n/a |
| typeOfTimeUnits | The type of time unit within which the minimum and maximum number of passes shall occur. | Enumeration DAY(S) indicates that the required number of passes shall occur within the specified number of days. WEEK(S) indicates that the required number of passes shall occur within the specified number of days. ORBIT(S) indicates that the required number of passes shall occur within the specified number of orbits. | n/a |
| numberOfTimeUnits | This parameter is used to specify the required number of days, weeks or orbits. | Integer >0 | n/a |

### Class PassIntervalConstraints

#### The PassIntervalConstraints class is optional and  can be used to permit the specification of the minimum and/or maximum intervals between passes.

#### The parameters of the PassIntervalConstraints class are specified in Table 3-34 below.

Table 3-34: Class PassIntervalConstraints Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| minIntBetweenPasses | Optional parameter. This is used to specify the minimum interval required between passes. | Integer ≥ 0 Default value if omitted is 0 | Seconds |
| maxIntBetweenPasses | Optional parameter. This is used to specify the maximum interval required between passes. NOTE: If both minimumIntervalBetweenPasses and maximumIntervalBetweenPasses are specified then maximumIntervalBetweenPasses ≥ minimumIntervalBetweenPasses | Integer ≥ 0 Default value if omitted is ∞ | Seconds |

### Class PassDailyTimeConstraints

#### The PassDailyTimeConstraints class is optional and  can be used to permit the specification of the earliest and/or latest absolute (UTC) times for passes. The use of these constraints could be used for example to limit passes to being only during normal working hours etc..

#### The parameters of the PassDailyTimeConstraints class are specified in Table 3-35.

#### There shall be zero or one instances of the PassDailyTimeConstraints class for each instance of the PlanningRequest class.

Table 3-35: Class PassDailyTimeConstraints Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| daysForPasses | Optional parameter. Used to specify the day(s) on which a pass can be accepted. | Enumeration MONDAY TUESDAY WEDNESDAY THURSDAY FRIDAY SATDAY SUNDAY | n/a |
| earliestPassStart | Optional parameter. Used to specify (in UTC) the earliest time during the day at which a pass can start. | String8 of format hh:mm:ss Where hh = Hour in two-character subfield with values 00-23 mm = Minute in two-character subfield with values 00-59 ss = Second in two-character subfield with values 00-59 (-58 or -60 during leap seconds) | n/a |
| latestPassStart | Optional parameter. Used to specify (in UTC) the latest time during the day at which a pass can start. NOTE: If both earliestPassStart and latestPassStart are specified then latestPassStart ≥ earliestPassStart | String8 of format hh:mm:ss Where hh = Hour in two-character subfield with values 00-23 mm = Minute in two-character subfield with values 00-59 ss = Second in two-character subfield with values 00-59 (-58 or -60 during leap seconds) | n/a |
| earliestPassEnd | Optional parameter. Used to specify (in UTC) the earliest time during the day at which a pass can end. | String8 of format hh:mm:ss Where hh = Hour in two-character subfield with values 00-23 mm = Minute in two-character subfield with values 00-59 ss = Second in two-character subfield with values 00-59 (-58 or -60 during leap seconds) | n/a |
| latestPassEnd | Optional parameter. Used to specify (in UTC) the latest time during the day at which a pass can end. NOTE: If both earliestPassEnd and latestPassEnd are specified then latestPassEnd ≥ earliestPassEnd | String8 of format hh:mm:ss Where hh = Hour in two-character subfield with values 00-23 mm = Minute in two-character subfield with values 00-59 ss = Second in two-character subfield with values 00-59 (-58 or -60 during leap seconds) | n/a |

### Class PassRangeConstraints

#### The PassRangeConstraints class is optional and  can be used to permit the specification of the minimum and/or maximum range between the spacecraft and groundstation for the start and/or end of a pass.

#### The parameters of the PassRangeConstraints class are specified in Table 3-36 below.

#### There shall be zero or one instances of the PassRangeConstraints class for each instance of the PlanningRequest class.

Table 3-36: Class PassRangeConstraints Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| minRangeAtPassStart | Optional parameter. Used to specify the minimum range required at the pass start. | Integer ≥ 0 | Kilometres |
| maxRangeAtPassStart | Optional parameter. Used to specify the maximum range required at the pass start. NOTE: If both minRangeAtPassStart and maxRangeAtPassStart are specified then maxRangeAtPassStart ≥ minRangeAtPassStart | Integer ≥ 0 | Kilometres |
| minRangeAtPassEnd | Optional parameter. Used to specify the minimum range required at the pass end. | Integer ≥ 0 | Kilometres |
| maxRangeAtPassEnd | Optional parameter. Used to specify the maximum range required at the pass start. NOTE: If both minRangeAtPassEnd and maxRangeAtPassEnd are specified then maxRangeAtPassEnd ≥ minRangeAtPassEnd | Integer ≥ 0 | Kilometres |

### CLASS PassDefinedEventRelativeTimeConstraints

#### The PassDefinedEventRelativeTimeConstraints class is optional and may be used to specify pass start/end timing constraints with respect to Events that are defined in reference [7].

NOTE	–	The PassDefinedEventRelativeTimeConstraints class is a specialization of class PassRelativeTimeConstraints described in section 3.4.9 below, and the description of the parameters is given in that subsection.

### CLASS PassAdditionalEventRelativeTimeConstraints

#### The PassAdditionalEventRelativeTimeConstraints class is optional and may be used to specify pass start/end timing constraints with respect to Events that are not defined in reference [7]. The need for this may arise if it is found that in certain cases (or missions) the Events defined in reference [7] are not sufficient and additional Events are required. See reference [7] for further information on the definition of Additional Events.

NOTE	–	The PassAdditionalEventRelativeTimeConstraints class is a specialization of class PassRelativeTimeConstraints described in section 3.4.9 below, and the description of the parameters is given in that subsection.

#### The usage of additional Events is not within the scope of this document and should be specified in an ICD between the relevant parties.

### CLASS PassRelativeTimeConstraints (Abstract)

#### The PassRelativeTimeConstraints class is mandatory and shall be used to specify pass start/end timing constraints with respect to Events.

#### The PassRelativeTimeConstraints class parameters specified in Table 3-37 below.

Table 3-37: Class PassRelativeTimeConstraints Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| event | The event - the various different events defined are described in reference [7]. | Enumeration. | See reference [7] |
| earliestDeltaTimeForPassStart | Optional parameter. If this is specified it is added to the time at which the event occurs and this time is taken to be the earliest the pass can start relative to the event. | Integer ≥ 0 | Seconds |
| latestDeltaTimeForPassStart | Optional parameter. If this is specified it is added to the time at which the event occurs and this time is taken to be the latest the pass can start relative to the event. NOTE: If values for both earliestDeltaTimeForPassStart and latestDeltaTimeForPassStart are specified they must be such that the latest time the pass can start is after the earliest time it can start | Integer ≥ 0 | Seconds |
| earliestDeltaTimeForPassEnd | Optional parameter. If this is specified it is added to the time at which the event occurs and this time is taken to be the earliest the pass can end relative to the event. | Integer ≥ 0 | Seconds |
| latestDeltaTimeForPassEnd | Optional parameter. If this is specified it is added to the time at which the event occurs and this time is taken to be the latest the pass can end relative to the event. NOTE: If values for both earliestDeltaTimeForPassEnd and latestDeltaTimeForPassEnd are specified they must be such that the latest time the pass can end is after the earliest time it can end. | Integer ≥ 0 | Seconds |

### CLASS DefinedEventParameter

#### The DefinedEventParameter class is optional and may be used to permit the instantiation of parameters for an Event that is defined in this recommendation..

NOTE	–	The DefinedEventParameter class is a specialization of class EventParameter described in 3.4.12 below, and the description of the parameters is given in that subsection.

#### There  shall be zero or more instances of the DefinedEventParameter class for each instance of the DefinedEvent class.

#### The parameters that are expected to be associated with the various defined events are specified in in reference [7].

### CLASS AdditionalEventParameter

#### The AdditionalEventParameter class is optional and may be used to permit the instantiation of additional parameters for an Event. The need for this may arise if it is found that in certain cases (or missions) the parameters defined in this recommendation are not sufficient and additional information is required.

NOTE	–	The AdditionalEventParameter class is a specialization of class Parameter described in 3.4.12 below, and the description of the parameters is given in that subsection.

#### There  shall be zero or more instances of the AdditionalEventParameter class for each instance of the DefinedEvent class.

#### There  shall be zero or more instances of the AdditionalEventParameter class for each instance of the AdditionalEvent class.

#### The usage of these additional parameters is not within the scope of this document and should be specified in an ICD between the relevant parties.

### CLASS EventParameter (ABSTRACT)

#### The EventParameter class shall be used to permit the instantiation of parameters for an Event by allowing the specification of parameter name/value pairs using the parameters specified in Table 3-38.

Table 3-38:  Class EventParameter Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| parameterName | Name of the parameter. | String1024 | n/a |
| parameterValue | The value of the required parameter. | As required by the additional parameter | As required by the additional parameter |

## Submission Request

### Overview

Figure 3-4 shows the UML Class diagram for the Service Management Utilization Request Formats Submission request.

Figure 3-4: Service Management Utilization Request Formats  - Submission Request Class Diagram

The attributes of each class are described further in the following subsections and tables.

### CLASS SrvMgtData

See reference [6], Annex A for the definition of this class.

### CLASS RequestType

See section 3.2.4 for the definition of this class.

### CLASS SubmissionReq

See section 3.2.20 for the definition of this class.

### CLASS ConfigProfileSubmission

See section 3.2.23 for the definition of this class.

### CLASS ConfigurationProfileContents

See section 3.2.24 for the definition of this class.

### CLASS EventSeqSubmission

See section 3.2.25 for the definition of this class.

### CLASS EventSequence

See section 3.2.26 for the definition of this class.

### CLASS TrajectoryDataSubmission

See section 3.2.21 for the definition of this class.

### CLASS CCSDSTrajectoryPrediction

See section 3.2.22 for the definition of this class.

## Basic Service Management Utilization Request Formats – Service Package - New Request

### Overview

Figure 3-5 shows the UML Class diagram for the Basic Service Management Utilization Request Formats Service Package New Request.

Figure 3-5: Basic Service Management Utilization Request Formats Service Package New Request Class Diagram

The attributes of each class are described further in the following subsections and tables.

### CLASS SrvMgtData

See reference [6], Annex A for the definition of this class.

### CLASS RequestType

See section 3.2.4 for the definition of this class.

### CLASS ServicePkgReq

See section 3.2.5 for the definition of this class.

### CLASS NewSrvPkg

See section 3.2.6 for the definition of this class.

### CLASS Scenario

See section 3.2.13 for the definition of this class.

### CLASS ServiceInfo

See section 3.2.14 for the definition of this class.

### CLASS ConfigurationProfileXRef

See section 3.2.15 for the definition of this class.

### CLASS ConfigProfileParameter

See section 3.2.16 for the definition of this class.

### CLASS EventSequenceXRef

See section 3.2.17 for the definition of this class.

### CLASS EventSeqParameter

See section 3.2.18 for the definition of this class.

### CLASS OIDParameter

See section 3.2.19 for the definition of this class.

### CLASS BasicStartTimeConstraint

See section 3.3.3 for the definition of this class.

### CLASS BasicDurationConstraint

See section 3.3.4 for the definition of this class.

### CLASS BasicHandoverConstraint

See section 3.3.5 for the definition of this class.

### CLASS BasicApertureConstraint.

See section 3.3.6 for the definition of this class.

## Basic Service Management Utilization Request Formats – Service Package - Update Request

### Overview

Figure 3-6 shows the UML Class diagram for the Basic Service Management Utilization Request Formats Service Package Update Request.

Figure 3-6: Basic Service Management Utilization Request Formats  Service Package Update Request Class Diagram

The attributes of each class are described further in the following subsections and tables.

### CLASS SrvMgtData

See reference [6], Annex A for the definition of this class.

### CLASS RequestType

See section 3.2.4 for the definition of this class.

### CLASS ServicePkgReq

See section 3.2.5 for the definition of this class.

### CLASS NewSrvPkg

See section 3.2.6 for the definition of this class.

### CLASS Scenario

See section 3.2.13 for the definition of this class.

### CLASS ServiceInfo

See section 3.2.14 for the definition of this class.

### CLASS ConfigurationProfileXRef

See section 3.2.15 for the definition of this class.

### CLASS ConfigProfileParameters

See section 3.2.16 for the definition of this class.

### CLASS EventSequenceXRef

See section 3.2.17 for the definition of this class.

### CLASS EventSeqParameters

See section 3.2.18 for the definition of this class.

### CLASS OIDParameter

See section 3.2.19 for the definition of this class.

### CLASS BasicStartTimeConstraint

See section 3.3.3 for the definition of this class.

### CLASS BasicDurationConstraint

See section 3.3.4 for the definition of this class.

### CLASS BasicHandoverConstraint

See section 3.3.5 for the definition of this class.

### CLASS BasicApertureConstraint.

See section 3.3.6 for the definition of this class.

## Basic Service Management Utilization Request Formats – Planning Info Request

### Overview

Figure 3-7 shows the UML Class diagram for the Basic Service Management Utilization Request Formats Planning Info Request.

Figure 3-7: Basic Service Management Utilization Request Formats Planning Info Request Class Diagram

The attributes of each class are described further in the following subsections and tables.

### CLASS SrvMgtData

See reference [6], Annex A for the definition of this class.

### CLASS RequestType

See section 3.2.4 for the definition of this class.

### CLASS PlanningInfoReq

See section 3.2.10 for the definition of this class.

### CLASS BasicStartTimeConstraint

See section 3.3.3 for the definition of this class.

### CLASS BasicDurationConstraint

See section 3.3.4 for the definition of this class.

### CLASS BasicHandoverConstraint

See section 3.3.5 for the definition of this class.

### CLASS BasicApertureConstraint.

See section 3.3.6 for the definition of this class.

## Service Management Utilization Request Formats – Service Package - Delete Request

### Overview

Figure 3-8 shows the UML Class diagram for the Service Management Utilization Request Formats Service Package Delete Request.

Figure 3-8: Service Management Utilization Request Formats Service Package Delete Request Class Diagram

The attributes of each class are described further in the following subsections and tables.

### CLASS SrvMgtData

See reference [6], Annex A for the definition of this class.

### CLASS RequestType

See section 3.2.4 for the definition of this class.

### CLASS ServicePkgReq

See section 3.2.5 for the definition of this class.

### CLASS DeleteSrvPkg

See section 3.2.8 for the definition of this class.

## Service Management Utilization Request Formats – Service Package – Select Alternate Request

### Overview

Figure 3-9 shows the UML Class diagram for the Service Management Utilization Request Formats Service Package Delete Request.

Figure 3-9: Service Management Utilization Request Formats Service Package Select Alternate Request Class Diagram

The attributes of each class are described further in the following subsections and tables.

### CLASS SrvMgtData

See reference [6], Annex A for the definition of this class.

### CLASS RequestType

See section 3.2.4 for the definition of this class.

### CLASS ServicePkgReq

See section 3.2.5 for the definition of this class.

### CLASS SelectAltSrvPkg

See section 3.2.9 for the definition of this class.

### CLASS Scenario

See section 3.2.12 for the definition of this class.

## Service Management Utilization Request Formats – Report Request

### Overview

Figure 3-10 shows the UML Class diagram for the Service Management Utilization Request Formats Report Request.

Figure 3-10: Service Management Utilization Request Formats Report Request Class Diagram

The attributes of each class are described further in the following subsections and tables.

### CLASS SrvMgtData

See reference [6], Annex A for the definition of this class.

### CLASS RequestType

See section 3.2.4 for the definition of this class.

### CLASS ReportReq

See section 3.2.11 for the definition of this class.

## Service Management Utilization Request Formats – Information Request

### Overview

Figure 3-11 shows the UML Class diagram for the Service Management Utilization Request Formats Information Request.

Figure 3-11: Service Management Utilization Request Formats Information Request Class Diagram

The attributes of each class are described further in the following subsections and tables.

### CLASS SrvMgtData

See reference [6], Annex A for the definition of this class.

### CLASS RequestType

See section 3.2.4 for the definition of this class.

### CLASS InfoReq

See section 3.2.12 for the definition of this class.

## Enhanced Service Management Utilization Request Formats – Service Package - New Request

### Overview

Figure 3-12 shows the UML Class diagram for the Enhanced Service Management Utilization Request Formats Service Package New Request.

Figure 3-12: Enhanced Service Management Utilization Request Formats Service Package New Request Class Diagram

The attributes of each class are described further in the following subsections and tables.

### CLASS SrvMgtData

See reference [6], Annex A for the definition of this class.

### CLASS RequestType

See section 3.2.4 for the definition of this class.

### CLASS ServicePkgReq

See section 3.2.5 for the definition of this class.

### CLASS NewSrvPkg

See section 3.2.6 for the definition of this class.

### CLASS Scenario

See section 3.2.13 for the definition of this class.

### CLASS ServiceInfo

See section 3.2.14 for the definition of this class.

### CLASS ConfigurationProfileXRef

See section 3.2.15 for the definition of this class.

### CLASS ConfigProfileParameters

See section 3.2.16 for the definition of this class.

### CLASS EventSequenceXRef

See section 3.2.17 for the definition of this class.

### CLASS EventSeqParameters

See section 3.2.18 for the definition of this class.

### CLASS OIDParameter

See section 3.2.19 for the definition of this class.

### CLASS BasicStartTimeConstraint

See section 3.3.3 for the definition of this class.

### CLASS BasicDurationConstraint

See section 3.3.4 for the definition of this class.

### CLASS BasicHandoverConstraint

See section 3.3.5 for the definition of this class.

### CLASS BasicApertureConstraint.

See section 3.3.6 for the definition of this class.

### CLASS StandingOrder

See section 3.4.3 for the definition of this class.

### CLASS PassIntervalConstraints

See section 3.4.4 for the definition of this class.

### CLASS PassDailyTimeConstraints

See section 3.4.5 for the definition of this class.

### CLASS PassRangeConstraints

See section 3.4.5 for the definition of this class.

### CLASS PassDefinedEventRelativeTimeConstraints

See section 3.4.7 for the definition of this class.

### CLASS PassAdditionalEventRelativeTimeConstraints

See section 3.4.8 for the definition of this class.

### CLASS PassRelativeTimeConstraints (Abstract)

See section 3.4.9 for the definition of this class.

### CLASS DefinedEventParameter

See section 3.4.10 for the definition of this class.

### CLASS AdditionalEventParameter

See section 3.4.11 for the definition of this class.

### CLASS EventParameter (Abstract)

See section 3.4.12 for the definition of this class.

## Enhanced Service Management Utilization Request Formats – Service Package  - Update Request

### Overview

Figure 3-13 shows the UML Class diagram for the Enhanced Service Management Utilization Request Formats Service Package Update Request.

Figure 3-13: Enhanced Service Management Utilization Request Formats Service Package Update Request Class Diagram

The attributes of each class are described further in the following subsections and tables.

### CLASS SrvMgtData

See reference [6], Annex A for the definition of this class.

### CLASS RequestType

See section 3.2.4 for the definition of this class.

### CLASS ServicePkgReq

See section 3.2.5 for the definition of this class.

### CLASS NewSrvPkg

See section 3.2.6 for the definition of this class.

### CLASS ServiceInfo

See section 3.2.14 for the definition of this class.

### CLASS ConfigurationProfileXRef

See section 3.2.15 for the definition of this class.

### CLASS ConfigProfileParameters

See section 3.2.16 for the definition of this class.

### CLASS EventSequenceXRef

See section 3.2.17 for the definition of this class.

### CLASS EventSeqParameters

See section 3.2.18 for the definition of this class.

### CLASS OIDParameter

See section 3.2.19 for the definition of this class.

### CLASS BasicStartTimeConstraint

See section 3.3.3 for the definition of this class.

### CLASS BasicDurationConstraint

See section 3.3.4 for the definition of this class.

### CLASS BasicHandoverConstraint

See section 3.3.5 for the definition of this class.

### CLASS BasicApertureConstraint.

See section 3.3.6 for the definition of this class.

### CLASS StandingOrder

See section 3.4.3 for the definition of this class.

### CLASS PassIntervalConstraints

See section 3.4.4 for the definition of this class.

### CLASS PassDailyTimeConstraints

See section 3.4.5 for the definition of this class.

### CLASS PassRangeConstraints

See section 3.4.5 for the definition of this class.

### CLASS PassDefinedEventRelativeTimeConstraints

See section 3.4.7 for the definition of this class.

### CLASS PassAdditionalEventRelativeTimeConstraints

See section 3.4.8 for the definition of this class.

### CLASS PassRelativeTimeConstraints (Abstract)

See section 3.4.9 for the definition of this class.

### CLASS DefinedEventParameter

See section 3.4.10 for the definition of this class.

### CLASS AdditionalEventParameter

See section 3.4.11 for the definition of this class.

### CLASS EventParameter (Abstract)

See section 3.4.12 for the definition of this class.

## Enhanced Service Management Utilization Request Formats – Planning Info Request

### Overview

Figure 3-14 shows the UML Class diagram for the Enhanced Service Management Utilization Request Formats Planning Info Request.

Figure 3-14: Enhanced Service Management Utilization Request Formats Planning Info Request Class Diagram

The attributes of each class are described further in the following subsections and tables.

### CLASS SrvMgtData

See reference [6], Annex A for the definition of this class.

### CLASS RequestType

See section 3.2.4 for the definition of this class.

### CLASS PlanningInfoReq

See section 3.2.12 for the definition of this class.

### CLASS BasicStartTimeConstraint

See section 3.3.3 for the definition of this class.

### CLASS BasicDurationConstraint

See section 3.3.4 for the definition of this class.

### CLASS BasicHandoverConstraint

See section 3.3.5 for the definition of this class.

### CLASS BasicApertureConstraint.

See section 3.3.6 for the definition of this class.

### CLASS StandingOrder

See section 3.4.3 for the definition of this class.

### CLASS PassIntervalConstraints

See section 3.4.4 for the definition of this class.

### CLASS PassDailyTimeConstraints

See section 3.4.5 for the definition of this class.

### CLASS PassRangeConstraints

See section 3.4.5 for the definition of this class.

### CLASS PassDefinedEventRelativeTimeConstraints

See section 3.4.7 for the definition of this class.

### CLASS PassAdditionalEventRelativeTimeConstraints

See section 3.4.8 for the definition of this class.

### CLASS PassRelativeTimeConstraints (Abstract)

See section 3.4.9 for the definition of this class.

### CLASS DefinedEventParameter

See section 3.4.10 for the definition of this class.

### CLASS AdditionalEventParameter

See section 3.4.11 for the definition of this class.

### CLASS EventParameter (Abstract)

See section 3.4.12 for the definition of this class.

- Informative References

(INFormative)

[A1]	Space Communication Cross Support—Service Management—Operations Concept. Issue 1. Report Concerning Space Data System Standards (Green Book), CCSDS 910.14-G-1. Washington, D.C.: CCSDS, May 2011.

[A2]	Extensible Space Communication Cross Support—Service Management—Concept. Report Concerning Space Data System Standards (Green Book). Washington, D.C.: CCSDS, forthcoming.

# Comments

I think especially in this book we can spend here some more effort. It seems that use cases may be pretty many (however not necesairly complicated).

Does this represent the types of use cases?

Minor editorial nit but technically speaking our agencies don't need CCSDS permission to do anything :-) suggest deleting "permits the"

let's keep an eye on the green book update (which I'm supposed to do anyway) -- to make sure that the various types of requests are called out properly at the concept level and then perhaps this recommendation is need to talk about things that are foreseen or not but just simply states the types of requests supported.

I think we need to be careful here. What's listed below this starts to get pretty much into management service. If we are going that route then why not include apply new trajectory and apply new event sequence. In the highly abstract version of the Smurf there was a notion of management service requests. Not sure we have this quite properly sorted out here. Unfortunately I don't have a concrete suggestion at the moment.

Do we in fact need to allow for event sequences and configuration profiles to be part of a planning request? I think some further analysis is needed for this…

We may need to do little more thinking about the organizing principles behind the diagram… Event sequence is called out as its own book but event sequence actually has a request versus an output component. Part of the planning of the event sequence is to have the mission sequence as an input and then the "expanded" or "realized" sequence produced by be TTC network service provider. So in this case we have six request and service package being split between this recommendation and the service package recommendation but that's not the same way the event sequence is being treated…

Planning and Service Request information entity?

Need to think whether these statuses are fully applicable.

Unless we want to keep it somehow consistent with SoS, in case of request I do not see any use for “provisional”. It would be something like “If I would ask you for something, not that I’m actually asking, but if, than I would ask for this and that”. And how much provisional would be the response to such provisional request? TEST, OPERATIONAL and OTHER is enough.

JP does this give you the functionality that you need.

If so maybe you can amplify a bit on what is meant by “chained” in this context.

Is there any relation information (is this SR a parent/child of another one, should be before, after,  whatever) for this chaining necessary?

Any rules on that? How I know “it has not been previously used”?

Perhaps the various types of reports could be in registry in the same way that the various information entities are in a registry…?

Where does this list of services come from? How does this square against the IOAG service catalog and what about the service catalog that Hugh is taking a look at? I notice DDOR is not here.

Table missing?

Table missing? Or table description obsolete?

“for manipulating the submission of new….”? In general I’d like to have here some better explanation for what we need it. This is a bit too short shot. Does the green book explains that somehow?

Submitter?

Not sure what the appropriate data type here is. In effect what we want to do is embed the file containing the trajectory data here. I’m not sure this is completely possible in XML but I think the CDATA construct in XML would allow us to put in the trajectory data such that it would be unparsed. This could then be extracted and parsed separately as appropriate.

John with your XML Guru hat on does this make sense or is there a better way ?

Wrong formatting?

Is this term sufficiently well understood or does there needs to be a definition of this and/or some other already defined CCSDS term used for this? (Nothing obvious shows up in SANA for the CCSDS glossary)  Also, could this not be used in part of an interval of time spanning many tracking passes – e.g, for planning requests whereby planning information for the next 30 passes/opportunities are desired?

I know it is maybe too late, as we handled it already like this In SoS, but would not be better if there would be xtra column for “Optional / Mandatory”?

In general, I think it would be good to have examples of the application of these constraints such that we have scenarios and then the example expressions of these parameters to match the scenarios. I realize this will feed into the prototype planning but I think a little upfront analysis will help everyone to understand what these parameters are about.

Here again I think we're going to have to get some good terms of reference together. I'm not sure if this is talking about a planning interval such as the next month worth of tracks or whether handovers are allowed in that time or if this talking about individual track or…?

Should this not be separate point?

Same comment as above is for the basic constraints but perhaps even more important for the enhanced constraints, and that is the need for some examples be worked and representative/typical parameter values supplied to illustrate how those examples make use of the various parameters.

Maybe would be good to add in brackets (per day, week or orbit). Just to clarify what a “specified time interval” refers to.

formatting

Presumably the CCSDS trajectory prediction would also be a blue book?  Should this have the same color coding as the configuration profile an event sequence? And perhaps we would want to call out the NDM/book number here for the trajectory stuff?

Would any of this be applicable to the planning request as well? For example, does it make sense to consider that for a fairly well developed mission that is perhaps only several months away from launch, could there in fact perhaps be a detailed configuration profile? -- But yet they are not actually making service requests just yet just doing some detailed planning analysis…?

Oh boy… The enhanced Smurf…I think we might need to spend a bit of time on what the basic request can do vs what the enhanced version can do – does it really just come down to more involved constraints?

It seems like for something as potential involved as constraints that the extensibility/additional parameter should be more than just a name and value but perhaps ability to plug-in arbitrary bits of schema…