## Slide 1: Registries for SoS (Simple Schedule of Services)
30-Nov-2016
Rev A: 4-Dec-2015: Updates based on Telecon of 30 Nov 2015
Rev B: 28-Jan-2016: Updates based on RMP (CCSDS 313.1-Y-0.1) book being conditionally approved
Rev C: 09-May-2016: Registry URLs and Status Update

## Slide 2: What is SOS?/Introduction
A data format for publication of TT&C network schedule of services
  E.g, at 1500 on Day of Year 237, ESA’s Mars Express (MEX) will have 6 hours of Telemetry, Command, and Tracking service on NASA DSN Antenna DSS-24
  Can be for as many or as few scheduled users, at publisher’s discretion
  Can be for an arbitrary amount of time
Stated in XML
  “Payload” and “supporting” XML Schemas
Utilizes several bits of registered information
  XML Schema
  Originator (e.g., ESTRACK, DSN, etc)
  User of services – typically mission spacecraft identifiers (e.g., CASS, MEX, MRO, ROSE, etc)
  Aperture identifiers (e.g, DSS-24)
  Service Management Information Entity Type (an enumerated list; e.g., “SCHEDULE”, “PLANNING REPORT”, “ACCOUNTABILITY REPORT”, etc.)
More or less in conformance with new RMP from SE Area
But we have not worked with SANA folks to get the registries defined, so
Let’s get that taken care of (I hope)…

## Slide 3: Registry 1: XML Schemas (New Registry)
3 schema files to be registered
Just simply to be put on-line with a URL that can be included in the SoS book
Descriptions:
  SchemaCssmCcsdsTimeCodes-V1_0_0.xsd -- A pattern, for validation of XML instances for expressing dates/times in the format of CCSDS timecode B (per CCSDS 301.0-B-4)
  SchemaCssmCcsdsTimecodes – a schema for CCSDS time formats used by other CSSM schemas – at this time specifically Time Code “B”
  SchemaCssmSmInfoEntityHeader -- a schema for a header for all service management messages
  SchemaCssmSimpleSchedule – a schema capturing the “on-the-wire” schedule publication conformant with (what will be) the Blue Book 902.1-B-1
Registration Policy
  Request for registry update needs to come from CSS Area, from AD, DAD, or someone duly designated (via email to SANA operator)
  Once registry is established, subsequent request will indicate how to treat any existing registry or registries.
Registry Class: RMP defines this as “global” See figure 2-2 of RMP (re XML Schema); as such, responsibility for update is delegated from CESG (see p 3-15, 1st paragraph of RMP). As no such delegation is currently in effect, request that CCS AD, DAD being the registration authority until CESG delegation as been made.
Action: Registry Name: To prepare for longer term usage, request registry name be changed from “Simple Schedule XML Schemas” to “Service Management XML Schemas”. (I anticipate several more sets of schemas and it will make sense to collect these in one regstiry.
URL: http://sanaregistry.org/r/service_management_xml_schemas/service_management_xml_schemas.html
Status: Listed on main SANA registry site as a candidate registry

## Slide 4: Registry 2: Originating Organization (augment Organizations registry)
Make use of “Name” in CCSDS Organization Registry…
  add an attribute of “serviceProvider”, composed of enumerated values
    “null” value shall be the first ordinal value of the list
Make use of the “Service Provider Registry” (See RMP 3.3.2.3)
    “SchedulePublisher” shall be added to this enumerated list as an attribute for entries in this registry in whatever order is best determined by SANA engineering
    All values that exist in this registry prior to the original (first) publication date of this recommendation shall have effectively a null value assigned for this attribute.
The procedure to follow
  Defined in Standard Formatted Data Units — Control Authority Procedures, Issue 2. CCSDS 630.0-B-2 (630.0-B-1 at the moment) Defined in the RMP, 3.3.2.3)
    And in addition, for publishers of schedules, the “serviceProvider” the “SchedulePublsher” attribute shall be set to “true” for those entries that are add that are schedule publication organizations to the enumerated value of “SchedulePublisher”.
URL: A supporting URL exists (but is only a registry for enumeration values):
http://beta.sanaregistry.org/r/service_provider_types/service_provider_types.html
Status: In progress

## Slide 5: Registry 3: User (Augment Spacecraft Identifiers)
Make use of “Spacecraft Name” in Spacecraft Identifiers registry…
In addition to the values for the “user” parameter contained in the CCSDS Spacecraft Identifiers registry, the following values shall be recognized by implementations
Perhaps this needs to be an additional/ancillary registry or?
Agreed by Erik + Colin that the “reserved” values (UNALLOCATED, PROVIDER-CSS) can just be stated in the book and will not be registered.
user | Description
UNALLOCATED | Indicates that the time is unallocated.
PROVIDER-CSSS | Indicates that the time is allocated for the Provider CSSS.
URL: [none]
Status: No registry needed; book update pending

## Slide 6: Registry 4: Site and Aperture names (Creation of Initial Sites and Apertures Registry) (1/2)
Utilizes Service Site and Aperture Registry (RMP 3.3.2.4)
Creation new Registry until more formal CCSDS recommendation exists
  Anticipate corrigendum to Schedule of Service recommendation
Fruther qualifications levied against RMP 3.3.2.4.7: For each site name that can be listed in a schedule, the following shall be supplied (seen as minimial starting point that will remain even when site/apertures specific document exists)
  Each Site Name shall have at least one or more Aperture Name sub-records that contains the following
Site Name: | a string of between 1 and 64 characters in length.
Site Name Abbreviation | a string of between 1 and 16 characters in length
Notes | a string of text of between 0 and 1024 characters in length describing the site.
Aperture Name | a string of between 1 and 64 characters in length.
Aperture Abbreviation | a string of between 1 and 16 characters in length
Notes | a string of text of between 0 and 1024 characters in length describing the aperture.
URL: http://sanaregistry.org/r/service_sites_apertures
Status: Created, currently a placeholder; to access, use “beta.sanaregistry.org” as url base

## Slide 7: Registry 4: Site and Aperture Names (Creation of Initial Site and Apertures Registry) (2/2)
  Maintenance
  Requests submitted from SANA, shall come from
    CCSDS member Agency
    CCSDS Observer Agency
    CCSDS Associate
      Industry partner of the above
  Need to check that if a new entry is being made for the purposes of inclusion in schedule publication then there does need to be at least one ApertureName sub-record
    I.e, for the purpose of registering a site that does not have resources that get scheduled, a site record can be added without any aperture sub-records
  SiteNames and abbreviations must be unique across the entire registry
  Aperture Names and abbreviations must be unique within the SiteName parent record
  The Notes fields are optional
(See RMP 3.3.2.4)

## Slide 8: Registry 5: Service Management Entity (Message) Types (New Registry)
  Create new registry to list the various type of service management information entities/message types
  Per the following table
  Update policy
    RMP Classification: local
    Submission to SANA
    Only authorized CSS Area rep
    (Above is consistent RMP)
Parameter | Description | Data Type | Data Units
srvMgtEntityType | The type of service management information entity contained. | Enumeration — Permitted values registered in SANA. The following list identifies the currently foreseen values but this may be extended in future: ACCOUNTING_REP CONFIG_PROFILE COST_ESTIMATES EVENT_SEQUENCE PLANNING_REQUEST PROVISIONAL_PLAN RES_AVAILABILITY SERV_PACKAGE SERV_PACKAGE_EXE SERV_PACKAGE_REQ SERVICE_AGREEMENT SERVICE_CATALOG SIMPLE_SCHEDULE TRAJ_PREDICTION | n/a
URL: http://sanaregistry.org/r/service_management_entity_types/service_management_entity_types.html
Status: Status: Listed on main SANA registry site as a candidate registry