## Slide 1: DDOR Lifecycle and CSSM Info Entities
Preliminary Analysis
Response to AI: 2016-0408-4
(Develop sketch of DDOR SM lifecycle model)
E. Barkley NASA/JPL
23 August 2016

## Slide 2: Background
At Cleveland/Spring 2016 meeting at a joint session with DDOR WG
  Agreed that the general issue to work on is the overall enterprise/lifecycle model in terms of sequence of steps and how the various information entities can and can not support the DDOR activities
Following is the preliminary analysis in respone to the above

## Slide 3
Identify apertures
Execute DDOR Activities
Develop DDOR Details
Info Entities:
Goal:
Communication Geometry (Candidate times for Targets: S/C(s), Quasar(s))
Inputs
Trajectory [SMURF: Submission]
Quasar ID (or RA/DEC) [?]
Outputs
Reserve Apertures
Comments:
Identify apertures for which DDOR view is physically feasible for particular time and duration
Request for Comm Geom needs to allow for Quasar reference(s) (?)
Request for Comm Geom needs to allow for multiple spacecraft to be stated (or at least multiple S/C trajectory references)
Goal:
Reserve apertures identified as being suitable
Unhandled at the moment: check for sufficient gain for DOR Tones or PC/N0 if no DOR Tones being used – ie no SNR consideration addressed here
Presumably S/C config profiles available – if needed this is not accommodated in planning request just yet (but something like this will be needed for data volume estimates)
Info Entities:
(Potentially) SOS Unused Time
Inputs
Service Package Request
Outputs
Service Package Result
SOS
Comments:
May be multi-pass SP requests to reserve for DDOR independently or TLM/CMD/TRK services (or vice versa)
SP Result will have detailed event sequence deferred at this point
Also EVT Seq Ref not included yet
Goal:
Provide resolved sequence planned for DDOR observation activities
Info Entities:
Inputs
Mission Event Sequence (via SMURF submission request)
Outputs
Provider Event Sequence
Comments:
Assumed that the negotiation as to when to sequence various spacecraft and their ordering in that sequence is handled by means outside of the CSSM recommendations (ie., this negotiation is covered by DDOR recommendations/practices)
Unclear yet as to what the behavior is in terms of event sequence output – SM B1 would have this as part of the service package result – needs to be worked.
Presumably the SP Result if queried at this point will have the detailed sequence attached.
Suspect that alternate scenarios, for practical purposes, will be limited to doing/not doing DDOR observation (ie., not changes in sequence and/or quasars) – need to verify with DDOR WG
Goal:
Execute DDOR activities
Info Entities:
Inputs
Potentially SPR – Select Alternate Scenario (as part of SMURF)
Outputs
Potentially update service package results
Comments:
Not sure how likely alternate scenarios are
Probably need to have a discussion re CSTS recommendations
Does/will SC-CSTS have an ability to control DDOR service execution?
Will multiple instance of MD-CSTS be needed – e.g., from each agency;
Any coordination re TD-CSTS outputs (e.g, antenna angles?)
SMURF: Planning Request
PIF: Comm Geometry
CP: Config Profile?
SMURF: SP Request; SOS Request
Svc Pkg: Service Package Result
SMURF: ES Submission (mission sequence)
ES: ES output (provider sequence)
None (CSSM) ?
CSTS Stds – just configuration for output?