## Slide 1: Response to AI 2017-0512-02
Provide Planning Products for the Mars relay to Rover for the PIF
(Subsequently interpreted to mean provide an overview and initial analysis and questions)

## Slide 2: Background
Current in-progress book deals with communication geometry
At San Antonio meetings there were three use cases identified:
  Earth’s surface to spacecraft
  Planetary surface other than earth to spacecraft
  Spacecraft to spacecraft
Per the 11 July 2017 splinter teleconference
  The use cases are also classified along the lines of
    Trajectory driven events
    Supplying, directly, a trajectory or set of trajectories
  Agreement was that supplying the trajectories/set of trajectories is not to be included in the scope of the PIF
NASA currently operates a Mars coordination relay system and this represents events in the planetary surface other than earth category and this is done via supplying trajectory driven events

## Slide 3: Current PIF Overview
UML Model as of v 15 of the white book (March 2017)
This leads to a partial XML instance on the next slide
  Per San Antonio meetings, azimuth, elevation and RTLT are to be added to every event (ie., part of event definition)

## Slide 4
XML Example Instance, ~current PIF

## Slide 5: NASA Mars Relay Coordination Planning Data Overview
Consists of a Header…
SCET == Spacecraft Ephemeris Time

## Slide 6: NASA Mars Relay Coordination Planning Data Overview
…and Body

## Slide 7: Observations, questions, comments
Mars relay coordination has to consider that view location is moving – rover on the surface of Mars – hence the location coordinates
  PIF assumes aperture registered in SANA and fixed
    As NASA SN TDRSS considered to be vectors/trajectory data, not really addressed in PIF Should it be? Optional data?
Meta data has a bit more “provenance” behind it than PIF
  Does PIF need to indicate trajectory used in driving event outputs?
  Suspect that program producing event output does not really need to be identified?
Although not formally identified in documentation I read, in practice, it appears that events are listed in a strict increasing temporal order
  Similar to current mandatory section in PIF that just contains temporally ordered events
Specialized events for orbiters – orbital events are included
  No equivalent in PIF
  By the same token, Mars relay coordination does not allow for/consider occultations (phobos travels really fast around mars, and is very small, so maybe not really an issue unless doing something like tracking behind another planet from Mars)

## Slide 8: Preliminary thoughts on accommodating this uses case
Observer location coordinate and coordinate system identification could be added as optional meta-data
  Although it would probably be required for this use case
Orbital elements could be added as optional meta-data
  Perhaps this could also be of use for near-earth spacecraft (?)
  Note that this occurs only for rise of an obiter for the Mars relay coordination