Draft Recommendation for
Space Data System Standards

Service Management Utilization Request Formats

Draft Recommended Standard

CCSDS 902.9-W-0.19

White Book

November 2021

AUTHORITY

|  | Issue: | White Book, Draft 0.19 |  |
| --- | --- | --- | --- |
|  | Date: | November 2021 |  |
|  | Location: | Not Applicable |  |

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF AUTHORITY:)

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and represents the consensus technical agreement of the participating CCSDS Member Agencies.  The procedure for review and authorization of CCSDS documents is detailed in Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-4), and the record of Agency participation in the authorization of this document can be obtained from the CCSDS Secretariat at the e-mail address below.

This document is published and maintained by:

CCSDS Secretariat

National Aeronautics and Space Administration

Washington, DC, USA

E-mail: secretariat@mailman.ccsds.org

STATEMENT OF INTENT

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF INTENT:)

The Consultative Committee for Space Data Systems (CCSDS) is an organization officially established by the management of its members. The Committee meets periodically to address data systems problems that are common to all participants, and to formulate sound technical solutions to these problems. Inasmuch as participation in the CCSDS is completely voluntary, the results of Committee actions are termed Recommended Standards and are not considered binding on any Agency.

This Recommended Standard is issued by, and represents the consensus of, the CCSDS members.  Endorsement of this Recommendation is entirely voluntary. Endorsement, however, indicates the following understandings:

o	Whenever a member establishes a CCSDS-related standard, this standard will be in accord with the relevant Recommended Standard. Establishing such a standard does not preclude other provisions which a member may develop.

o	Whenever a member establishes a CCSDS-related standard, that member will provide other CCSDS members with the following information:

--	The standard itself.

--	The anticipated date of initial operational capability.

--	The anticipated duration of operational service.

o	Specific service arrangements shall be made via memoranda of agreement. Neither this Recommended Standard nor any ensuing standard is a substitute for a memorandum of agreement.

No later than five years from its date of issuance, this Recommended Standard will be reviewed by the CCSDS to determine whether it should: (1) remain in effect without change; (2) be changed to reflect the impact of new technologies, new requirements, or new directions; or (3) be retired or canceled.

In those instances when a new version of a Recommended Standard is issued, existing CCSDS-related member standards and implementations are not negated or deemed to be non-CCSDS compatible.  It is the responsibility of each member to determine when such standards or implementations are to be modified.  Each member is, however, strongly encouraged to direct planning for its new standards and implementations towards the later version of the Recommended Standard.

FOREWORD

Through the process of normal evolution, it is expected that expansion, deletion, or modification of this document may occur.  This Recommended Standard is therefore subject to CCSDS document management and change control procedures, which are defined in the Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-4).  Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be sent to the CCSDS Secretariat at the e-mail address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- China National Space Administration (CNSA)/People’s Republic of China.

- Deutsches Zentrum für Luft- und Raumfahrt (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (FSA)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

- UK Space Agency/United Kingdom.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- China Satellite Launch and Tracking Control General, Beijing Institute of Tracking and Telecommunications Technology (CLTC/BITTT)/China.

- Chinese Academy of Sciences (CAS)/China.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- Danish National Space Center (DNSC)/Denmark.

- Departamento de Ciência e Tecnologia Aeroespacial (DCTA)/Brazil.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Geo-Informatics and Space Technology Development Agency (GISTDA)/Thailand.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Korea Aerospace Research Institute (KARI)/Korea.

- Ministry of Communications (MOC)/Israel.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic and Atmospheric Administration (NOAA)/USA.

- National Space Agency of the Republic of Kazakhstan (NSARK)/Kazakhstan.

- National Space Organization (NSPO)/Chinese Taipei.

- Naval Center for Space Technology (NCST)/USA.

- Scientific and Technological Research Council of Turkey (TUBITAK)/Turkey.

- South African National Space Agency (SANSA)/Republic of South Africa.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- Swiss Space Office (SSO)/Switzerland.

- United States Geological Survey (USGS)/USA.

PREFACE

This document is a draft CCSDS Recommended Standard.  Its ‘Red Book’ status indicates that the CCSDS believes the document to be technically mature and has released it for formal review by appropriate technical organizations.  As such, its technical contents are not stable, and several iterations of it may occur in response to comments received during the review process.

Implementers are cautioned not to fabricate any final equipment in accordance with this document’s technical content.

Recipients of this draft are invited to submit, with their comments, notification of any relevant patent rights of which they are aware and to provide supporting documentation.

# DOCUMENT CONTROL

| Document | Title | Date | Status |
| --- | --- | --- | --- |
| CCSDS 902.2-W-0.00 | Planning and Service Request Specification, Draft Recommended Standard, Draft 0.00 | November 2015 | Initial draft for working group |
| CCSDS 902.9-W-0.01 | Service Management Utilization Request Formats, Draft Recommended Standard, Draft 0.01 | November 2015 | Update after discussions at Darmstadt meeting. |
| CCSDS 902.9-W-0.02 | Service Management Utilization Request Formats, Draft Recommended Standard, Draft 0.02 | March 2016 | Updated after working group review. |
| CCSDS 902.9-W-0.03 | Service Management Utilization Request Formats, Draft Recommended Standard, Draft 0.03 | September 2016 | Updated after discussions at Cleveland meeting. |
| CCSDS 902.9-W-0.04 | Service Management Utilization Request Formats, Draft Recommended Standard, Draft 0.04 | April 2017 | Updated after discussions at Rome meeting. |
| CCSDS 902.9-W-0.05 | Service Management Utilization Request Formats, Draft Recommended Standard, Draft 0.05 | March 2018 | Updated after discussions at San Antonio and Den Haag meetings. |
| CCSDS 902.9-W-0.06 | Service Management Utilization Request Formats, Draft Recommended Standard, 0.06 | July 2018 | Updated after discussions at Gaithersburg meeting. |
| CCSDS 902.9-W-0.07 | Service Management Utilization Request Formats, Draft Recommended Standard, Draft 0.07 | December 2018 | Updated after discussions at Berlin meeting. |
| CCSDS 902.9-W-0.08 | Service Management Utilization Request Formats, Draft Recommended Standard, Draft 0.08 | May 2019 | Updated after discussions at preceding telecons. |
| CCSDS 902.9-W-0.09 | Service Management Utilization Request Formats, Draft Recommended Standard, Draft 0.09 | May 2019 | Updated after discussions at Mountain View meeting. |
| CCSDS 902.9-W-0.09.1 | Service Management Utilization Request Formats, Draft Recommended Standard, Draft 0.09.1 | August 2019 | Editorial updates plus addition of ICS. |
| CCSDS 902.9-W-0.10 | Service Management Utilization Request Formats, Draft Recommended Standard, Draft 0.10 | January 2020 | Minor tweaks to SANA registry URLs and naming conventions for Schema files. Plus modification of Basic Constraints. |
| CCSDS 902.9-W-0.11 | Only UML Model and Schema updated |  |  |
| CCSDS 902.9-W-0.12 | Only UML Model and Schema updated |  |  |
| CCSDS 902.9-W-0.13 | Only UML Model and Schema updated |  |  |
| CCSDS 902.9-W-0.14 | Only UML Model and Schema updated |  |  |
| CCSDS 902.9-W-0.15 | Only UML Model and Schema updated |  |  |
| CCSDS 902.9-W-0.16 | Service Management Utilization Request Formats, Draft Recommended Standard, Draft 0.16 | July 2021 | Updated to bring in line with current version of UML model and schema, including latest W/G input. |
| CCSDS 902.9-W-0.17 | Service Management Utilization Request Formats, Draft Recommended Standard, Draft 0.17 | August 2021 | Deleted parameter srvPkgReqVersion from class ServicePkgReq. Deleted XML examples and added pointer to SANA registry holding location of git registry with examples. |
| CCSDS 902.9-W-0.18 | Service Management Utilization Request Formats, Draft Recommended Standard, Draft 0.18 | November 2021 | Updates as per discussions at Fall 2021 meeting. |
| CCSDS 902.9-W-0.19 | Service Management Utilization Request Formats, Draft Recommended Standard, Draft 0.19 | November 2021 | Service Package name changed to ServicePackageType1 |

# CONTENTS

Section	Page

1	Introduction	1-13

1.1	PURPOSE AND SCOPE	1-13

1.2	APPLICABILITY	1-15

1.3	RATIONALE	1-16

1.4	DOCUMENT STRUCTURE	1-19

1.5	DEFINITIONS	1-19

1.6	NOMENCLATURE	1-20

1.7	CONVENTIONS—THE UNIFIED MODELING LANGUAGE	1-20

1.8	References	1-21

2	Overview	2-1

2.1	GENERAL	2-1

2.2	Service Management Utilization Request Formats	2-1

2.3	MAPPING TO W3C XML SCHEMA	2-1

3	SERVICE MANAGEMENT UTILIZATION REQUEST FORMATS	3-1

3.1	GENERAL	3-1

3.2	Service Management Utilization Request Formats Content/Structure	3-2

3.3	Planning Information Request	3-7

3.4	Report Request	3-10

3.5	Information Request	3-14

3.6	Online New and Replace Service Package Requests	3-17

3.7	Offline New and Replace Service Package Requests	3-23

3.8	Delete Service Package Request, Delete Service Package and Replace Service Package	3-27

3.9	Submission Requests	3-33

3.10	Service Management Utilization Request Formats Basic Constraints	3-39

3.11	Service Management Utilization Request Formats Enhanced Constraints	3-44

ANNEX A Implementation Conformance Statement (ICS) Proforma  (Normative)	A-0

ANNEX B Security, SANA, and Patent Considerations  (Informative)	B-31

ANNEX C XML Schema Organization, Packaging and Examples For The Service Managment Utilization Request Formats.  (Informative)	C-1

ANNEX D Abbreviations and Acronyms  (Informative)	D-3

ANNEX E Informative References  (Informative)	E-1

Figure

Figure 1-1 Service Management Utilization Requests Formats in the Context of Space Communication Cross Support Service Management.	1-15

Figure 3-1:  Service Management Utilization Request Formats Class Diagram	3-3

Figure 3-2:  Service Management Utilization Request Formats Planning Information Request Class Diagram	3-7

Figure 3-3:  Service Management Utilization Request Formats Report Request Class Diagram	3-10

Figure 3-4:  Service Management Utilization Request Formats Information Request Class Diagram	3-14

Figure 3-5:  Service Management Utilization Request Formats Online New and Replace Service Package Requests Class Diagram	3-18

Figure 3-6:  Service Management Utilization Request Formats Offline New and Replace Service Package Requests Class Diagram	3-23

Figure 3-7:  Service Management Utilization Request Formats Delete Service Package Request, Delete Service Package and Replace Service Package Class Diagram	3-27

Figure 3-8:  Service Management Utilization Request Formats Submission Requests Class Diagram	3-33

Figure 3-9: Service Management Utilization Request Formats Basic Constraints Class Diagram	3-39

Figure 3-10: Service Management Utilization Request Formats Enhanced Constraints Class Diagram	3-44

Table

Table 3-1:  Class SrvMgtUtilReqHeader Additional Parameters	3-5

Table 3-2: Class RequestType Parameters	3-5

Table 3-3: Class ServicePkgReq Parameters	3-6

Table 3-4: Class PlanningInfoReq Parameters	3-8

Table 3-5: Class ReportReq Parameters	3-11

Table 3-6: Class SimpleScheduleRepReq Additional Parameters	3-12

Table 3-7: Class InfoReq Parameters	3-15

Table 3-8: Class NewOnlineSrvPkgReq use of Class ServicePkgReq Parameters	3-20

Table 3-9: Class ReplaceOnlineSrvPkgReq use of Class ServicePkgReq Parameters	3-20

Table 3-10: Class NewOfflineSrvPkgReq use of Class ServicePkgReq Parameters	3-25

Table 3-11: Class ReplaceOfflineSrvPkgReq use of Class ServicePkgReq Parameters	3-25

Table 3-12: Class DeleteSrvPkgReq Parameters	3-28

Table 3-13: Class DeleteSrvPkgReq use of Class ServicePkgReq Parameters	3-28

Table 3-14: Class DeleteSrvPkg Parameters	3-29

Table 3-15: Class DeleteSrvPkg use of Class ServicePkgReq Parameters	3-29

Table 3-16: Class ReplaceSrvPkg Parameters	3-30

Table 3-17: Class ReplaceSrvPkg use of Class ServicePkgReq Parameters	3-30

Table 3-18: Class SubmissionReq Parameters	3-34

Table 3-19: Class BasicPass Parameters	3-41

Table 3-20: Class ApertureSelection Parameters	3-42

Table 3-21: Class StandingOrder Parameters	3-45

Table 3-22: Class Handover Parameters	3-46

Table 3-23: Class TimeWindows Parameters	3-47

Table 3-24: Class TimeWindow Parameters	3-47

Table 3-25: Class PassRange Parameters	3-48

Table 3-26: Class PassInterval Parameters	3-49

Table 3-27: Class PassDuration Parameters	3-50

Table 3-28: Class PassDailyTime Parameters	3-51

# Introduction

## PURPOSE AND SCOPE

### PURPOSE

The Service Management Utilization Request Format (SMURF) Recommended Standard specifies the formats of the data entities that are used to submit requests in the scope of CCSDS Service Management.

These requests can be categorized into 5 types:

- Planning Information Request – can be used to submit a query for various types of planning information.

- Report Request– can be used to submit a request for a report to be returned. Currently two types of report are supported:

- Simple Schedule (see Ref. [4])

- Accounting Report (see TBD)

- Information Request – can be used to submit a request for one or more of the following types of information:

- Configuration Profile(s)

- Event Sequence(s)

- Service Agreement(s)

- Service Package(s)

- Trajectory(s)

- Scenario Set(s)

- DDOR Scan Pattern(s)

- Service Instance Configuration File(s) (SICF)

The information that is being requested is specified by means of a cross reference to the identifier(s) of the data entity(ies) that was previously defined.

- Service Package Request– can be used to submit requests relating to service packages. The supported types of service package requests are:

- New Online Request – allows the submission of a new online service package request.

- Replace Online Request – allows the replacement of a previously submitted online service package request.

- New Offline Request – allows the submission of a new offline service package request.

- Replace Offline Request – allows the replacement of a previously submitted offline service package request.

- Replace Service Package Request – allows the replacement of a service package resulting from a previously submitted request.

- Delete Service Package Request Request – allows the deletion of a previously submitted request.

- Delete Service Package Request – allows the deletion of some or all of the service packages resulting from a previously submitted request.

- Set Active Scenario – allows the selection of a service package which was established as part of a set of scenarios.

- Submission Request – can be used to submit data entities that are used as part of Service Management. Currently 5 types of submission request a in re foreseen:

- Trajectory Submission Request – enables the submission of a trajectory prediction. If the ID of the Trajectory Submission request matches that of one previously submitted then the previous trajectory data is overwritten with the newly specified data.

- Configuration Profile Submission Request – enables the submission of a configuration profile. If the ID of the Configuration Profile Submission request matches that of one previously submitted then the previous Configuration Profile data is overwritten with the newly specified data.

- Event Sequence Submission Request – enables the submission of a event sequence. If the ID of the Event Sequence Submission request matches that of one previously submitted then the previous Event Sequence data is overwritten with the newly specified data.

- DDOR Scan Pattern Submission Request – enables the submission of a DDOR Scan Pattern. If the ID of the DDOR Scan Pattern Submission request matches that of one previously submitted then the previous DDOR Scan Pattern data is overwritten with the newly specified data.

- Service Instance Configuration File (SICF) Submission Request – enables the submission of a SICF. If the ID of the SICF Submission request matches that of one previously submitted then the previous Event Sequence data is overwritten with the newly specified data.

### SCOPE

The scope of this Recommended Standard is limited to the exchange of Service Management Utilization Requests required in the context of CCSDS Service Management. In the following figure the SMURF Recommendation is put into context with the various standards that together form the Space Communication Cross Support Service Management.

Figure 1-1 Service Management Utilization Requests Formats in the Context of Space Communication Cross Support Service Management.

## APPLICABILITY

This Recommended Standard is applicable only to the Service Management Utilization Requests Formats and contents, but not to its transmission. With respect to the transmission of the Planning Information between agencies and operators there are two scenarios:

- The first is where the service management utilization request is exchanged within the context of Service management, in this case the transmission mechanism is described in [TBD].

- The second deals with the case where the service management utilization request is exchanged outwith the scope of Service Management. Here the mechanism by which the Planning Information is transmitted is outside of the scope of this document and should be specified in an ICD agreed by the parties involved.

## RATIONALE

### General

The primary goal of CCSDS is to increase the level of interoperability among Agencies.  This Recommended Standard furthers that goal by establishing the means to exchange planning information relating to where most cross support activity occurs: between the tracking stations or ground data handling systems of various Agencies and the mission specific components of a mission ground system.

The use cases described in the following sections were considered in deriving this Recommended Standard.

### USE CASES

The Service Management Utilization Request Formats (SMURF) information entity serves a number of use cases. These can be categorized by the various types of requests defined by the SMURF and are discussed below.

#### Planning Information Request

The Planning Information Request support the submission of a query for various types of planning information as defined in reference [5].

The Planning Information Request allows the specification of constraints that can be used to determine the suitability of tracking assets, and also permits cross-referencing to trajectory and configure profiles so that the requested planning information can be accurately calculated. Planning information can be useful in the following cases:

##### Mission Design

During the mission design phase the planning information request can be used to obtain an idea of the feasibility of the required support, for instance by checking that there is sufficient coverage available from tracking assets to support the mission needs. It would also be possible, depending on the capabilities of the Provider CSSS, to obtain estimates of the data rates that and be supported and check if there were any issues with RFI. In the longer term it would also be possible to obtain an estimate of the costs inherent in the tracking coverage being requested from the Provider CSSS.

##### Mission Planning

During the planning phase the planning information request provides the mechanism for the User CSSS to obtain data about feasible tracking coverage, data rates, RFI issues or other conflicts (again depending on the capabilities of the Provider CSSS) that would then be fed into the detailed planning process for the mission.

The output from the User CSSS planning process would then be Service Package Requests (see Section – below).

#### Report Request

The Report Request enable a User CSSS to request a report from the Provider CSSS covering a specified time range. Currently two types of report are foreseen:

- Simple Schedule (see Ref. [4])

- Accounting Report (see TBD)

Here the uses cases are that by obtaining a Simple Schedule report a user CSSS is able to see (depending on the capabilities of the Provider CSSS) what the schedule of the Provider CSS tracking assets is and if there are any unallocated tracking opportunities that could be utilized to provide additional coverage.

The accounting report, when available, will enable a User CSSS to verify that the support provided was in line with what is in the service agreement with respect to data volume returned, lost TM frames, lost commands etc.

#### Information Request

The Information Request is intended as a mechanism that enables the User CSSS to request various types of information from the Provider CSSS. Each Information Request can specify that one or more of the following types of information be provided:

- Configuration Profile(s)

- Event Sequence(s)

- Service Agreement(s)

- Service Package(s)

- Trajectory(s)

- Scenario Set(s)

- DDOR Scan Pattern(s)

- Service Instance Configuration File(s) (SICF)

The information that is being requested is specified by means of a cross reference to the identifier(s) of the data entity(ies) that was previously defined.

Using the Information Request it is possible for the User CSSS to check that the information that the Provider CSSS has is correct.

#### Submission Request

In the scope of service management in order for the Provider CSSS to carry out the required calculations for scheduling tracking passes, configuring the equipment and carrying out activities during a pass it is necessary for the appropriate information to be provided from the User CSSS. Some of this information may be defined when the Service Agreement is set up (e.g. configuration profiles) but this may need to be adjusted during the lifetime of a mission. Other information will need to be updated on a more regular basis, e.g. trajectory information and event sequences.

With this in mine the Submission Request allows the User CSSS to submit data entities to the provider CSSS. Currently 5 types of submission request are foreseen:

- Trajectory Submission Request – enables the submission of a new trajectory prediction.

- Configuration Profile Submission Request – enables the submission of a new configuration profile.

- Event Sequence Submission Request – enables the submission of a new event sequence.

- DDOR Scan Pattern Submission Request – enables the submission of a new DDOR Scan Pattern.

- Service Instance Configuration File (SICF) Submission Request – enables the submission of a new SICF.Service Package Request

#### Service Package Request

Service Package requests allow the User CSSS to submit requests to the Provider CSSS that are related to service packages.

Typically Service Package Requests are issued during the mission planning process of the User CSSS and may be (but not mandatorily) based on plans that have been produced by the User CSSS using Planning Information obtained by means of prior Planning Information requests.

The Service Packages Requests allow the detailed specification of tracking constraints, equipment configuration and pass operations (via event sequences). The generation of Service Packages Requests may go through a number of cycles, starting months before the actual activities are expected to take place and being finalized a few days before execution, hence the need for the Update Request. During these planning cycles the status of the Service Package Request can change with the initial submission being of a ‘provisional’ request that will probably change. The final request provided is typically considered as ‘operational’ and can be expected to result in the actual Service Package that will be executed, subject to unexpected events such as equipment failure or spacecraft.

## DOCUMENT STRUCTURE

This document is organized as follows:

- Section 1 provides the purpose, scope, applicability, and rationale of this Recommended Standard and identifies the conventions and references used throughout the document. This section also describes how this document is organized. A brief description is provided for each section and annex so that the reader will have an idea of where information can be found in the document. It also identifies terminology that is used in this document but is defined elsewhere.

- Section 2 provides a brief overview of the CCSDS-recommended Service Management Utilization Request formats.

- Section 3 provides details about the structure and content of the Service Management Utilization Request.

- ANNEX A contains the Implementation Conformance Statement (ICS) proforma.

- ANNEX B discusses security, SANA and patent considerations.

- ANNEX C provides an informative description of the XML schema organization and packaging as well as the location of examples for the Service Management Utilization Request formats.

- ANNEX D contains a list of Acronyms applicable to the Service Management Utilization Request formats.

- ANNEX E is a list of informative references.

## DEFINITIONS

For the purposes of this document, the following definitions apply:

- the word ‘agencies’ may also be construed as meaning ‘satellite operators’ or ‘satellite service providers’;

- the notation ‘n/a’ signifies ‘not applicable’.

- the term “Pass” in this document may be construed as meaning a spacecraft  being tracked by a one or more ground or space based apertures. During this tracking one or more services are provided between the spacecraft and the aperture(s). These services may be telemetry, telecommanding, tracking, Delta Dor etc..

## NOMENCLATURE

### Normative Text

The following conventions apply for the normative specifications in this Recommended Standard:

- the words ‘shall’ and ‘must’ imply a binding and verifiable specification;

- the word ‘should’ implies an optional, but desirable, specification;

- the word ‘may’ implies an optional specification;

- the words ‘is’, ‘are’, and ‘will’ imply statements of fact.

NOTE	–	These conventions do not imply constraints on diction in text that is clearly informative in nature.

### Informative Text

In the normative sections of this document, informative text is set off from the normative specifications either in notes or under one of the following subsection headings:

- Overview;

- Background;

- Rationale;

- Discussion.

## CONVENTIONS—THE UNIFIED MODELING LANGUAGE

The Unified Modeling Language (UML) diagrams used in the specification (including class diagrams, package diagrams, sequence diagrams, and activity diagrams) follow the notation, semantics, and conventions imposed by the Version 2.4.1 UML specification of the Object Management Group (OMG) (reference [2]).

Within the document use is made only of class diagrams. A UML class diagram describes the structure of a message, its parts, and how those parts interrelate. A UML class, represented in the diagram as a box, represents a data set. Class diagram conventions include composition, generalization, multiplicity, and constraints. Enumeration notation is also used but only when it is involved in a composition constraint.

## References

The following publications contain provisions which, through reference in this text, constitute provisions of this document.  At the time of publication, the editions indicated were valid.  All publications are subject to revision, and users of this document are encouraged to investigate the possibility of applying the most recent editions of the publications indicated below.  The CCSDS Secretariat maintains a register of currently valid CCSDS publications.

[1]	Time Code Formats. Issue 4. Recommendation for Space Data System Standards (Blue Book), CCSDS 301.0-B-4. Washington, D.C.: CCSDS, November 2010.

[2]	Unified Modeling Language (UML). Version 2.4.1. Needham, Massachusetts: Object Management Group, August 2011.

[3]	Service Agreement and Service Configuration Profile Data Formats. Recommendation for Space Data System Standards (Blue Book), CCSDS 902.5-B-1. Blue Book. Issue 1. Washington, D.C.: CCSDS, Forthcoming.

[4]	Simple Schedule Format. Recommendation for Space Data System Standards, CCSDS 902.1-B-1. Blue Book. Issue 1. Washington, D.C.: CCSDS, May 2018.

[5]	Planning Information Formats. Recommendation for Space Data System Standards, CCSDS 902.2-B-1. Blue Book. Issue 1. Washington, D.C.: CCSDS, xxxx 20xx.

[6]	Abstract Event Definition. Recommended Practice for Space Data Systems (Magenta Book), CCSDS 902.13-M-1, Magenta Book, Issue 1. Washington, D.C.: CCSDS, February 2021.

[7]	Service Management Common Data Entities. Draft Recommended Practice for Space Data Systems (Magenta Book) 902.12-M-2, Magenta Book, Issue 2. Washington, D.C.: CCSDS, Forthcoming.

[8]	Space Link Event Sequence Data Format. Recommendation for Space Data System Standards (Blue Book), CCSDS 902.6-B-1, Blue Book, Issue 1. Washington, D.C.: CCSDS, Forthcoming.

# Overview

## GENERAL

This section provides a high-level overview of the CCSDS-recommended Service Management Utilization Request Formats, which is designed to facilitate standardized exchanges of  service management utilization requests between space agencies.

## Service Management Utilization Request Formats

The service management utilization requests consists of files that are XML formatted. The formats of these files are suitable for automated interaction and/or (by means of a suitable XML viewer) human interaction.

Service management utilization requests information is either mandatory, in which case suitable values must be present, or optional, in which case values may be present or not. In addition it is possible to extend the contents of the various service management utilization formats by defining additional parameters. The content of any parameters defined is outside the scope of this document and should be documented in an ICD agreed by the involved parties.

## MAPPING TO W3C XML SCHEMA

This Recommended Standard includes the specification of a mapping to World Wide Web Consortium (W3C) extensible Markup Language (XML) schema. The normative mapping of this Recommended Standard to XML W3C schemas is a virtual annex to this Recommended Standard and is contained in a stand-alone set of schema files.

NOTE	–	The XML schema has been elaborated on the basis of the mapping guidelines described in reference [E1].

# SERVICE MANAGEMENT UTILIZATION REQUEST FORMATS

## GENERAL

The Service Management Utilization Requests Formats forms the basis from which various types of requests required by Service Management are derived.

## Service Management Utilization Request Formats Content/Structure

### Overview

Figure 3-1:  Service Management Utilization Request Formats Class Diagram

The attributes of each class are described further in the following subsections and tables.

### CLASS SrvMgtUtilReq

#### The SrvMgtUtilReq class is mandatory and shall constitute the Service Management Utilization Request information entity.

NOTE	–	The SrvMgtUtilReq class is a specialization and of class SrvMgtInfoEntity described in reference [7] and the generic description of the parameters can be found there.

#### A SrvMgtUtilReq class shall contain the following;

- One, and only one, instance of the SrvMgtUtilReqHeader class.

- One or more instances of a class derived from the abstract RequestType class.

#### The SrvMgtUtilReq class contains no additional parameters.

### CLASS SrvMgtUtilReqHeader

#### The SrvMgtUtilReqHeader class is mandatory and shall constitute the ‘header’ of the Service Management Utilization Request Formats.

NOTE	–	The SrvMgtUtilReqHeader class is a specialization of class SrvMgtHeader described in reference [7] and the generic description of the parameters can be found there.

#### Each instance of the SrvMgtUtilReqHeader class may have 0 or more  instances of parameter classes derived from the abstract SrvMgtAbstractEvent class described in reference [7]. Usage of any additional parameters so specified is not within the scope of this document and should be specified in an ICD between by the relevant parties.

#### The use of the parameters in the SrvMgtHeader class in the scope of  the SrvMgtUtilReqHeader class are as per reference [7], with the following exceptions;

- startTime –  Usage of this parameter is request type dependent and is described in the sections on the various request types.

- endTime – Usage of this parameter is request type dependent and is described in the sections on the various request types.

#### Table 3-1 specifies the additional parameter defined for the SrvMgtUtilReqHeader class.

Table 3-1:  Class SrvMgtUtilReqHeader Additional Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| utilizationReqStatus | The status of the service management utilization request. | Enumeration The following values are permitted TEST indicates that the request has been generated for test purposes only. OPERATIONAL indicates that this is an operational request. | n/a |

### CLASS RequestType (Abstract)

#### The RequestType is an abstract class which is used to instantiate the various classes of request  required by service management in the context of planning and scheduling requests.

NOTE	–	The RequestType class is a specialization and of class SrvMgtData described in reference [7].

#### The RequestType class shall contain the parameters as specified in Table 3-2.

Table 3-2: Class RequestType Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| requestID | A unique request ID assigned by the requestor. | xsd:string | n/a |
| serviceAgreementRef | Optional Parameter. This can be used to specify a reference to the service agreement under which the requested services are to be provided. | xsd:string | n/a |
| comment | Optional Parameter May be used for the provision of ad hoc information. | xsd:string | n/a |

### CLASS ServicePkgReq (Abstract)

#### The ServicePkgReq is an abstract class which is used to instantiate the various classes of request required by service management for manipulating service packages.

NOTE	–	The ServicePkgReq class is a specialization and of class RequestType described in section 3.2.4 above.

#### The ServicePkgReq class shall contain the parameters as specified in Table 3-3.

Table 3-3: Class ServicePkgReq Parameters

The parameters for the ServicePkgReq class as are as per Table 3-2 with the addition of the following:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| spaceUserNode | The user of the requested services. These must be spacecraft names as specified in SANA. | xsd:string—Permitted values registered in SANA (see B2.3 for further information). | n/a |
| serviceReqID | Service request identifier. | xsd:string | n/a |

## Planning Information Request

### Overview

The following UML diagram shows the subset of classes that are applicable to the Planning Information Request:

Figure 3-2:  Service Management Utilization Request Formats Planning Information Request Class Diagram

#### Usage of SrvMgtUtilReqHeader startTime and endTime Parameters.

In the context of the Planning Information Request the SrvMgtUtilReqHeader startTime and endTime parameters are optional. If either startTime or endTime is specified they are interpreted as follows;

- startTime –  if specified no planning information will be returned that has a time earlier than the time specified by this parameter.

- endTime – if specified no planning information will be returned that has a time later than the time specified by this parameter

### CLASS PlanningInfoReq

#### The PlanningInfoReq class is optional and may be used to submit a query that can request various type of planning information.

NOTE	–	The PlanningInfoReq class is a specialization of class RequestType described in 3.2.4 and the generic description of the parameters is given in that subsection.

#### Each instance of the PlanningInfoHeader class must contain 1 and only 1 instance of the PlanningInfoTypeList as described in reference [7].

#### The PlanningInfoReq class , in addition to the parameters in the abstract RequestType class described in 3.2.4  shall contain the additional parameters as specified in Table 3-4.

Table 3-4: Class PlanningInfoReq Parameters

The parameters for the PlanningInfoReq class as are as per Table 3-2 with the addition of the following:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| spaceUserNode | The user of the requested services. These must be spacecraft names as specified in SANA. | xsd:string—Permitted values registered in SANA (see B2.3 for further information). | n/a |
| trajectoryRef | This is used to specify a reference to the trajectory that the spaceUserNode wants the planning information for. | xsd:string | n/a |
| configurationProfileRef | Optional Parameter. This is used to specify a reference to the configuration profile that the user wants the information for. NOTE: this parameter is mandatory for the following requestedInfo types: DATARATE RFI | xsd:strings The format of the configuration reference is defined in reference [3] | n/a |

### CLASS PlanningInfoTypeList

#### The PlanningInfoTypeList class allows the specification of a list of Planning Info Types and is fully described in reference [7].

### CLASS Constraints (Abstract)

See section 3.10.2 for the definition of this class.

## Report Request

### Overview

The following UML diagram shows the subset of classes that are applicable to the Report Request:

Figure 3-3:  Service Management Utilization Request Formats Report Request Class Diagram

#### Usage of SrvMgtUtilReqHeader startTime and endTime Parameters.

In the context of the Report Request the SrvMgtUtilReqHeader startTime and endTime parameters are not required and should not be specified. If specified they will be ignored.

### CLASS ReportReq (Abstract)

#### The ReportReq class is an abstract class that may be used to instantiate concrete report request classes.

NOTE	–	The ReportReq class is a specialization of class RequestType described in 3.2.4 and the generic description of the parameters is given in that subsection.

#### The ReportReq class, in addition to the parameters in the abstract RequestType class described in 3.2.4  shall contain the reportType required along with the required start and end times. These parameters are as specified in Table 3-5.

Table 3-5: Class ReportReq Parameters

The parameters for the reportReq class as are as per Table 3-2 with the addition of the following:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| spaceUserNode | The user of the requested services. These must be spacecraft names as specified in SANA. At least one spaceUserNode must be specified. | Array of xsd:strings —Permitted values registered in SANA (see B2.3 for further information). | n/a |
| startTime | The start time to be used for the requested report. | CCSDS ASCII Time Code B (reference [1]) | UTC |
| endTime | The end time to be used for the requested report. | CCSDS ASCII Time Code B (reference [1]) | UTC |

### CLASS SimpleScheduleRepReq

#### The SimpleScheduleRepReq class is an optional class that may be used to request Simple Schedule reports.

NOTE	–	The SimpleScheduleRepReq class is a specialization of class ReportReq described in 3.4.1.1 and the generic description of the parameters is given in that subsection.

#### Each instance of the SimpleScheduleRepReq class may contain 0 or more instances of the ApertureReference class, that is derived from the abstract ApertureLocation class..

#### In the returned Simple Schedule the following should be noted;

- Service Packages that start before the startTime but end after the startTime will be included in the schedule information.

- Service Packages that start before the endTime but end after the endTime will be included in the schedule information.

#### The SimpleScheduleRepReq class, in addition to the parameters in the abstract RequestType class described in 3.2.4  shall contain the additional parameters as specified in Table 3-6.

Table 3-6: Class SimpleScheduleRepReq Additional Parameters

The parameters for the SimpleScheduleRepReq class as are as per Table 3-5 with the addition of the following:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| reportType | This is used to specify the type of report required. | Enumeration – Currently supported values for simple schedule reports are; SIM_SCH_SPECIFIC results in a Simple Schedule (see Ref. [4]) containing only information directly related to the requested spaceUserNode(s) SIM_SCH_FREE results in a Simple Schedule (see Ref. [4]) containing a schedule of all aperture free times insofar as this is permitted by the agencies policies. For this type of report there must be exactly one spaceUserNode specified and the value for this shall be UNALLOCATED | n/a |

### CLASS ApertureLocation (Abstract)

#### ApertureLocation is an abstract class which is used to instantiate the various classes of aperture location required by service management and is fully described in reference [7].

### CLASS ApertureReference

#### The ApertureReference class allows the specification of the location of an aperture by the site name where it is located and the name of the aperture and is fully described in reference [7].

NOTE	–	The ApertureReference class is a specialization of class ApertureLocation mentioned in 3.4.4 and fully defined in reference [7].

### CLASS ApertureCelestialBodyPosition

#### The ApertureCelestialBodyPosition class allows the specification of the location of an aperture by the site name where it is located and the name of the aperture and is fully described in reference [7].

NOTE	–	The ApertureCelestialBodyPosition class is a specialization of class ApertureLocation mentioned in 3.4.4 and fully defined in reference [7].

## Information Request

### Overview

The following UML diagram shows the subset of classes that are applicable to the Information Request:

Figure 3-4:  Service Management Utilization Request Formats Information Request Class Diagram

#### Usage of SrvMgtUtilReqHeader startTime and endTime Parameters.

In the context of the Information Request the SrvMgtUtilReqHeader startTime and endTime parameters are not required and should not be specified. If specified they will be ignored.

### CLASS InfoReq

#### The InfoReq class is optional and may be used to submit a request for information about one or more of the following:

- Configuration Profile(s)

- Event Sequence(s)

- Service Agreement(s)

- Service Package(s)

- Trajectory(ies)

- Delta DOR Scan Pattern(s)

- Service Instance Configuration File(s)

NOTE	–	The InfoReq class is a specialization of class RequestType described in 3.2.4 and the generic description of the parameters is given in that subsection.

#### It is expected that the an Information Request will result in those data entities matching the request criteria being returned to the requestor.

#### The InfoReq class, in addition to the parameters in the abstract RequestType class described in 3.2.4  shall contain one or more of the parameters specified in Table 3-7.

Table 3-7: Class InfoReq Parameters

The parameters for the InfoReq class as are as per Table 3-2 with the addition of the following:

NOTE: At least one parameter must be specified.

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| spaceUserNode | The user of the requested services. These must be spacecraft names as specified in SANA. | xsd:string—Permitted values registered in SANA (see B2.3 for further information). | n/a |
| configurationProfileRef | Optional Parameter. This is used to specify a reference or references to the configuration profile(s) that the spaceUserNode wants the information for. | Array of xsd:strings The format of the configuration cross-reference is defined in reference [3] | n/a |
| eventSequenceRef | Optional Parameter. This is used to specify a reference or references to the event sequence(s) that the spaceUserNode wants the information for. | Array of xsd:strings | n/a |
| serviceAgreementRef | Optional Parameter. This is used to specify a reference or references to the service agreement(s) that the spaceUserNode wants the information for. | Array of xsd:strings | n/a |
| servicePackageRef | Optional Parameter. This is used to specify a reference or references to the service package(s) that the spaceUserNode wants the information for. | Array of xsd:strings | n/a |
| trajectoryRef | Optional Parameter. This is used to specify a reference or references to the trajectory(ies) that the spaceUserNode wants the information for. | Array of xsd:strings | n/a |
| ddorScanPatternRef | Optional Parameter. This is used to specify a reference or references to the Delta DOR scan pattern(s) that the spaceUserNode wants the information for. | Array of xsd:strings | n/a |
| sicfRef | Optional Parameter. This is used to specify a reference or references to the Service Instance Configuration File(s) that the spaceUserNode wants the information for. | Array of xsd:strings | n/a |

## Online New and Replace Service Package Requests

### Overview

The following UML diagram shows the subset of classes that are applicable to the Online New and Replace Service Package Requests:

Figure 3-5:  Service Management Utilization Request Formats Online New and Replace Service Package Requests Class Diagram

#### Usage of SrvMgtUtilReqHeader startTime and endTime Parameters.

In the context of the Online New and Replace Service Package Request the SrvMgtUtilReqHeader startTime and endTime parameters are optional. If either startTime or endTime is specified they are interpreted as follows;

- startTime –  if specified no service package will be produced that has a start time earlier than the time specified by this parameter.

- endTime – if specified no servicepackage will be produced that has an end time later than the time specified by this parameter

### CLASS OnlineSrvPkgReq (Abstract)

#### The OnlineSrvPkgReq class is an abstract class and is used to derive the classes required to submit a new online service package request or replace an existing online service package request.

NOTE	–	The OnlineSrvPkgReq class is a specialization of class ServicePkgReq described in 3.2.5 and the generic description of the parameters is given in that subsection.

#### Each instance of a class derived from the OnlineSrvPkgReq class shall contain 1, and only 1, instance of a class derived from the AbstractOnlineSrvPkg class described in section 3.6.6.

#### Each instance of a class derived from the OnlineSrvPkgReq class may  contain 0 or more instances of classes derived from the Constraints class described in section 3.6.12.

#### The use of the parameters in the ServicePkgReq class in the scope of the OnlineSrvPkgReq class are as per Table 3-2 and Table 3-3.

### CLASS NewOnlineSrvPkgReq

#### The NewOnlineSrvPkgReq class is optional and may be used to submit a new online service package request.

NOTE	1 –	The NewOnlineSrvPkgReq class is a specialization of class OnlineSrvPkgReq described in 3.6.1.1 and the generic description of the parameters is given in that section.

NOTE	2 –	The OnlineSrvPkgReq class is itself a specialization of class ServicePkgReq described in 3.2.5 and the generic description of the parameters is given in that subsection.

#### The NewOnlineSrvPkgReq class contains the parameters in the abstract OnlineSrvPkgReq class described in 3.6.1.1.

#### Usage of the OnlineSrvPkgReq and ServicePkgReq parameters in the context of the NewOnlineSrvPkgReq class is as specified in Table 3-8.

Table 3-8: Class NewOnlineSrvPkgReq use of Class ServicePkgReq Parameters

In the context of the NewOnlineSrvPkgReq class the usage of the following ServicePkgReq parameters (as described in Table 3-3) should be noted:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| serviceReqID | In the context of the NewOnlineSrvPkgReq class this parameter must be an identifier that has not previously been used.1 | xsd:string | n/a |

1It is the responsibility of the User CSSS to ensure that the serviceReqID is unqiue for the spaceUserNode that the request is being submitted for. The provider CSSS can then assume that the combination of spaceUserNode and serviceReqID constitutes a unique identifier for a service request.

### CLASS ReplaceOnlineSrvPkgReq

#### The ReplaceOnlineSrvPkgReq class is optional and may be used to replace an existing online service package request.

NOTE	1 –	The ReplaceOnlineSrvPkgReq class is a specialization of class OnlineSrvPkgReq described in 3.6.1.1 and the generic description of the parameters is given in that subsection.

NOTE	2 –	The OnlineSrvPkgReq class is itself a specialization of class ServicePkgReq described in 3.2.5 and the generic description of the parameters is given in that subsection.

#### The ReplaceOnlineSrvPkgReq class contains the parameters in the abstract OnlineSrvPkgReq class described in 3.6.1.1.

#### Usage of the OnlineSrvPkgReq and ServicePkgReq parameters in the context of the ReplaceOnlineSrvPkgReq class is as specified in Table 3-8.

Table 3-9: Class ReplaceOnlineSrvPkgReq use of Class ServicePkgReq Parameters

In the context of the ReplaceOnlineSrvPkgReq class the usage of the following ServicePkgReq parameters (as described in Table 3-3) should be noted:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| serviceReqID | In the context of the ReplaceOnlineSrvPkgReq class this parameter must refer to the identifier of the previously submitted request that is to be updated. | xsd:string | n/a |

### CLASS AbstractSrvPkg (Abstract)

#### The AbstractSrvPkg class is abstract and is used to derive the various service package classes required in service management.

#### The AbstractSrvPkg class is fully described in reference [7].

### CLASS AbstractOnlineSrvPkg (Abstract)

#### The AbstractOnlineSrvPkg class is abstract and is used to derive the various online service package classes required in service management.

NOTE –	The AbstractOnlineSrvPkg class is a specialization of class AbstractSrvPkg described in 3.6.5.

#### The AbstractSrvPkg class is fully described in reference [7].

### CLASS OnlineSrvPkyType1

#### The OnlineSrvPkyType1 class is used to specify the contents of an online service package.

NOTE –	The OnlineSrvPkyType1 class is a specialization of class AbstractOnlineSrvPkg described in 3.6.6.

#### The OnlineSrvPkyType1 class is fully described in reference [7].

### CLASS OnlineSrvPkyType1Details

#### The OnlineSrvPkyType1Details class is used to specify details relevant to an online service package.

#### The OnlineSrvPkyType1Details class is fully described in reference [7].

### CLASS DDORScanPatternDetails

#### DDORScanPatternDetails class is used to specify a reference to an existing DDOR Scan Pattern.

#### The DDORScanPatternDetails class is fully described in reference [7].

### CLASS ModResParm

#### The ModResParm class allows the modification of the value of a parameter of a resource. The Resource for which the parameter value is to be modified is specified by the resource name.

#### The ModResParm class is fully described in reference [7].

### CLASS AbstractParameter (ABSTRACT)

#### The AbstractParameter class is abstract and optional and may be used to derive parameters.

#### The AbstractParameter class is fully described in reference [6].

### CLASS Constraints (Abstract)

See section 3.10.2 for the definition of this class.

## Offline New and Replace Service Package Requests

### Overview

The following UML diagram shows the subset of classes that are applicable to the Offline New and Replace Service Package Requests:

Figure 3-6:  Service Management Utilization Request Formats Offline New and Replace Service Package Requests Class Diagram

#### Usage of SrvMgtUtilReqHeader startTime and endTime Parameters.

In the context of the Offline New and Replace Service Package Request the SrvMgtUtilReqHeader startTime and endTime parameters are optional. If either startTime or endTime is specified they are interpreted as follows;

- startTime –  if specified no service package will be produced that has a start time earlier than the time specified by this parameter.

- endTime – if specified no servicepackage will be produced that has an end time later than the time specified by this parameter

### CLASS OfflineSrvPkgReq (Abstract)

#### The OfflineSrvPkgReq class is an abstract class and is used to derive the classes required to submit a new online service package request or replace an existing offline service package request.

NOTE	–	The OfflineSrvPkgReq class is a specialization of class ServicePkgReq described in 3.2.5 and the generic description of the parameters is given in that subsection.

#### Each instance of a class derived from the OfflineSrvPkgReq class shall contain 1, and only 1, instance of the OfflineSrvPkg class described in section 3.7.5.

#### Each instance of a class derived from the OfflineSrvPkgReq class may  contain 0 or more instances of classes derived from the ConstraintsAlsoSuitableForOffline class described in section 3.7.10.

#### The OfflineSrvPkgReq class contains the parameters in the abstract ServicePkgReq class described in 3.2.5.

### CLASS NewOfflineSrvPkgReq

#### The NewOfflineSrvPkgReq class is optional and may be used to submit a new offline service package request.

NOTE 1 –	The NewOfflineSrvPkgReq class is a specialization of class OfflineSrvPkgReq described in 3.7.1.1 and the generic description of the parameters is given in that subsection.

NOTE	2 –	The OfflineSrvPkgReq class is itself a specialization of class ServicePkgReq described in 3.2.5 and the generic description of the parameters is given in that subsection.

#### The NewOfflineSrvPkgReq class contains the parameters in the abstract OfflineSrvPkg class described in 3.7.1.1.

#### Usage of the OfflineSrvPkgReq and ServicePkgReq parameters in the context of the NewOfflineSrvPkgReq class is as specified in Table 3-10.

Table 3-10: Class NewOfflineSrvPkgReq use of Class ServicePkgReq Parameters

In the context of the NewOfflineSrvPkgReq class the usage of the following ServicePkgReq parameters (as described in Table 3-3) should be noted:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| serviceReqID | In the context of the NewOfflineSrvPkgReq class this parameter must be an identifier that has not previously been used.1 | Xsd:string | n/a |

1It is the responsibility of the User CSSS to ensure that the serviceReqID is unqiue for the spaceUserNode that the request is being submitted for. The provider CSSS can then assume that the combination of spaceUserNode and serviceReqID constitutes a unique identifier for a service request.

### CLASS ReplaceOfflineSrvPkgReq

#### The ReplaceOfflineSrvPkgReq class is optional and may be used to replace an existing offline service package request.

NOTE	1 –	The ReplaceOnlineSrvPkReqg class is a specialization of class OfflineSrvPkgReq described in 3.7.1.1 and the generic description of the parameters is given in that subsection.

NOTE	2 –	The OfflineSrvPkgReq class is itself a specialization of class ServicePkgReq described in 3.2.5 and the generic description of the parameters is given in that subsection.

#### The ReplaceOfflineSrvPkgReq class contains the parameters in the abstract OfflineSrvPkg class described in 3.7.1.1.

#### Usage of the OfflineSrvPkgReq and ServicePkgReq parameters in the context of the ReplaceOfflineSrvPkgReq class is as specified in Table 3-11.

Table 3-11: Class ReplaceOfflineSrvPkgReq use of Class ServicePkgReq Parameters

In the context of the ReplaceOfflineSrvPkgReq class the usage of the following ServicePkgReq parameters (as described in Table 3-3) should be noted:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| serviceReqID | In the context of the ReplaceOfflineSrvPkgReq class this parameter must refer to the identifier of the previously submitted request that is to be updated. | Xsd:string | n/a |

### CLASS AbstractSrvPkg (Abstract)

#### The AbstractSrvPkg class is abstract and is used to derive the various service package classes required in service management.

#### The AbstractSrvPkg class is fully described in reference [7].

### CLASS OfflineSrvPkyType1

#### The OfflineSrvPkyType1 class is used to specify the contents of an offline service package.

NOTE –	The OfflineSrvPkyType1 class is a specialization of class AbstractSrvPkg described in 3.7.5.

#### The OfflineSrvPkyType1 class is fully described in reference [7].

### CLASS ModResParm

#### The ModResParm class allows the modification of the value of a parameter of a resource. The Resource for which the parameter value is to be modified is specified by the resource name. This class is fully described in reference [7].

### CLASS AbstractParameter (ABSTRACT)

#### The AbstractParameter class is abstract and optional and may be used to derive parameters.

The AbstractParameter class is specified in reference [6].

### CLASS Constraints (Abstract)

See section 3.10.2 for the definition of this class.

### CLASS ConstraintsAlsoSuitableForOffline (Abstract)

See section 3.10.3 for the definition of this class.

## Delete Service Package Request, Delete Service Package and Replace Service Package

### Overview

The following UML diagram shows the subset of classes that are applicable to the Delete Service Package Request, Delete Service Package, Replace Service Package and Set Active Scenario:

Figure 3-7:  Service Management Utilization Request Formats Delete Service Package Request, Delete Service Package and Replace Service Package Class Diagram

#### Usage of SrvMgtUtilReqHeader startTime and endTime Parameters.

In the context of the Delete Service Package Request, Delete Service Package and Replace Service Package Requests the SrvMgtUtilReqHeader startTime and endTime parameters are not required and should not be specified. If specified they will be ignored.

### CLASS DeleteSrvPkgReq

#### The DeleteSrvPkgReq class is optional and may be used to delete a previously submitted service  request.

NOTE	–	The DeleteSrvPkgReq class is a specialization of class ServicePkgReq described in 3.2.5 and the generic description of the parameters is given in that subsection.

#### The use of the DeleteSrvPkgReq will cause the specified Service Package request to be deleted and can also specify if all service packages that have been generated as a result of the deleted service package request should be deleted.

Table 3-12: Class DeleteSrvPkgReq Parameters

The parameters for the DeleteSrvPkg class are as per Table 3-2 and Table 3-3 with the addition of the following:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| deletePending | This is a Boolean flag that is used to specify whether pending Service Packages (i.e. Service packages that have been generated but not yet executed) resulting from the service package request specified for deletion should also be deleted. If the flag is set TRUE all pending Service Packages that resulted from the service package request are deleted. If the flag is set FALSE any pending service packages are not deleted. | xsd:boolean | n/a |

Table 3-13: Class DeleteSrvPkgReq use of Class ServicePkgReq Parameters

In the context of the DeleteSrvPkgReq class the usage of the following ServicePkgReq parameters (as described in Table 3-3) should be noted:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| serviceReqID | In the context of the DeleteSrvPkgReq class this parameter must refer to the identifier of the previously submitted request that is to be deleted. | xsd:string | n/a |

### CLASS DeleteSrvPkg

#### The DeleteSrvPkg class is optional and may be used to delete a service package that was generated by a previously submitted service request. It should be noted that DeleteSrvPkg will only result in the deletion of service packages that have not been, or are not currently being, executed.

NOTE	–	The DeleteSrvPkg class is a specialization of class ServicePkgReq described in 3.2.5 and the generic description of the parameters is given in that subsection.

Table 3-14: Class DeleteSrvPkg Parameters

The parameters for the DeleteSrvPkg class are as per Table 3-2 and Table 3-3 with the addition of the following:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| srvPkgRef | This is used to specify the references(s) of the service package(s) that is(are) to be deleted. | xsd:string | n/a |

Table 3-15: Class DeleteSrvPkg use of Class ServicePkgReq Parameters

In the context of the DeleteSrvPkg class the usage of the following ServicePkgReq parameters (as described in Table 3-3) should be noted:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| serviceReqID | In the context of the DeleteSrvPkg class this parameter must refer to the identifier of the request that resulted in the generation of the service package(s) that is(are) now to be deleted. | xsd:string | n/a |

### CLASS ReplaceSrvPkg

#### The ReplaceSrvPkg class is optional and may be used to replace a service package that was generated by a previously submitted service request.

NOTE	–	The ReplaceSrvPkg class is a specialization of class ServicePkgReq described in 3.2.5 and the generic description of the parameters is given in that subsection.

#### Submitting a ReplaceSrvPkg request does not guarantee that the Provider CSSS will actually be able to carry out the replacement. Depending on the elements of the service package that are changed there may be conflicts with existing scheduled service package(s) for other users which preclude the replace operation being carried out.

#### Each instance of the ReplaceSrvPkg class must contain exactly 1 instance of a class derived from the AbstractSrvPkg class (see section 3.8.5 below) which fully describes the service package to be used as a replacement.

Table 3-16: Class ReplaceSrvPkg Parameters

The parameters for the ReplaceSrvPkg class are as per Table 3-2 and Table 3-3 with the addition of the following:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| srvPkgRef | This is used to specify the reference of the service package that is to be replaced. | xsd:string | n/a |

Table 3-17: Class ReplaceSrvPkg use of Class ServicePkgReq Parameters

In the context of the ReplaceSrvPkg class the usage of the following ServicePkgReq parameters (as described in Table 3-3) should be noted:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| serviceReqID | In the context of the ReplaceSrvPkg class this parameter must refer to the identifier of the request that resulted in the generation of the service package that is now to be replaced. | xsd:string | n/a |

### CLASS AbstractSrvPkg (Abstract)

#### The AbstractSrvPkg class is abstract and is used to derive the various service package classes required in service management.

#### The AbstractSrvPkg class is fully described in reference [7].

### CLASS AbstractOnlineSrvPkg (Abstract)

#### The AbstractOnlineSrvPkg class is abstract and is used to derive the various online service package classes required in service management.

NOTE –	The AbstractOnlineSrvPkg class is a specialization of class AbstractSrvPkg described in 3.8.5.

#### The AbstractSrvPkg class is fully described in reference [7].

### CLASS OnlineSrvPkyType1

#### The OnlineSrvPkyType1 class is used to specify the contents of an online service package.

NOTE –	The OnlineSrvPkyType1 class is a specialization of class AbstractOnlineSrvPkg described in 3.8.6.

#### The OnlineSrvPkyType1 class is fully described in reference [7].

### CLASS OnlineSrvPkyType1Details

#### The OnlineSrvPkyType1Details class is used to specify details relevant to an online service package.

#### The OnlineSrvPkyType1Details class is fully described in reference [7].

### CLASS OfflineSrvPkyType1

#### The OfflineSrvPkyType1 class is used to specify the contents of an offline service package.

NOTE –	The OfflineSrvPkyType1 class is a specialization of class AbstractSrvPkg described in 3.8.5.

#### The OfflineSrvPkg class is fully described in reference [7].

### CLASS DDORScanPatternDetails

#### DDORScanPatternDetails class is used to specify a reference to an existing DDOR Scan Pattern.

#### The DDORScanPatternDetails class is fully described in reference [7].

### CLASS ModResParm

#### The ModResParm class allows the modification of the value of a parameter of a resource. The Resource for which the parameter value is to be modified is specified by the resource name.

#### The ModResParm class is fully described in reference [7].

### CLASS AbstractParameter (ABSTRACT)

#### The AbstractParameter class is abstract and optional and may be used to derive parameters.

#### The AbstractParameter class is fully described in reference [6].

## Submission Requests

### Overview

The following UML diagram shows the subset of classes that are applicable to the Submission Requests:

Figure 3-8:  Service Management Utilization Request Formats Submission Requests Class Diagram

#### Usage of SrvMgtUtilReqHeader startTime and endTime Parameters.

In the context of the Sumission Request the SrvMgtUtilReqHeader startTime and endTime parameters are not required and should not be specified. If specified they will be ignored.

### CLASS SubmissionReq

#### The SubmissionReq is a class to submit new information entities, i.e. trajectory predictions, configuration profiles. event sequences, DDOR scan patterns and service instance configuration files (SICF).

NOTE	–	The SubmissionReq class is a specialization and of class RequestType described in section 3.2.4 above.

#### The SubmissionReq class shall contain 1, and only 1, instance of a class derived from the AbstractDataSubWrapper described in 3.9.3.

#### The SubmissionReq class shall contain the parameters as specified in Table 3-18.

Table 3-18: Class SubmissionReq Parameters

The parameters for the SubmissionReq class as are as per Table 3-2 with the addition of the following:

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| spaceUserNode | The user of the requested services. These must be spacecraft names as specified in SANA. | xsd:string—Permitted values registered in SANA (see B2.3 for further information). | n/a |

### CLASS AbstractDataSubWrapper (Abstract)

#### AbstractDataSubWrapper is an abstract class that is used to instantiate the wrapper classes required to encapsulate data entities that may be used in submission requests.

NOTE	–	The AbstractDataSubWrapper class is a specialization of class AbstractDataWrapper described in reference [7] and the generic description of the parameters is given in that document.

#### The AbstractDataSubWrapper class is fully described in reference [7].

### CLASS AbstractEventSeqWrapper (Abstract)

#### AbstractEventSeqWrapper is an abstract class that is used to instantiate the wrapper classes required for Event Sequence data entities.

NOTE	–	The AbstractEventSeqWrapper class is a specialization of class AbstractDataSubWrapper described in 3.9.3 and the generic description of the parameters is given in that subsection.

#### The AbstractEventSeqWrapper class is fully described in reference [7].

NOTE	–	For a fully compliant CCSDS Submission Request for an Event Sequence it is required that the concrete Event Sequence Wrapper derived from the AbstractEventSeqWrapper class is as specified in Ref.  [8]. It is further required that this Event Sequence Wrapper contains one, and only one, instance of the Event Sequence class defined in Ref.  [8].

### CLASS AbstractTrajDataWrapper (Abstract)

#### AbstractTrajDataWrapper is an abstract class that is used to instantiate the wrapper classes required for Trajectory data entities.

NOTE	–	The AbstractTrajDataWrapper class is a specialization of class AbstractDataSubWrapper described in 3.9.4 and the generic description of the parameters is given in that subsection.

#### The AbstractTrajDataWrapper class is fully described in reference [7].

### CLASS OemWrapper

#### The OemWrapper is a class that is used to wrap an OEM data entity.

NOTE	–	The OemWrapper class is a specialization of class AbstractTrajDataWrapper described in 3.9.5 and the generic description of the parameters is given in that subsection.

#### The OemWrapper class is fully described in reference [7].

### CLASS OmmWrapper

#### The OmmWrapper is a class that is used to wrap an OMM data entity.

NOTE	–	The OmmWrapper class is a specialization of class AbstractTrajDataWrapper described in 3.9.5 and the generic description of the parameters is given in that subsection.

#### The OmmWrapper class is fully described in reference [7].

### CLASS OpmWrapper

#### The OpmWrapper is a class that is used to wrap an OPM data entity.

NOTE	–	The OpmWrapper class is a specialization of class AbstractTrajDataWrapper described in 3.9.5 and the generic description of the parameters is given in that subsection.

#### The OpmWrapper class is fully described in reference [7].

### CLASS TleWrapper

#### The TleWrapper is a class that is used to wrap a TLE data entity.

NOTE	–	The TleWrapper class is a specialization of class AbstractTrajDataWrapper described in 3.9.5 and the generic description of the parameters is given in that subsection.

#### The TleWrapper class is fully described in reference [7].

### CLASS Tle

#### Tle is used to specify trajectory data in the TLE format.

NOTE	–	The TLE format is not a CCSDS recommendation. It is therefore strongly recommended that, if at all feasible, that one of the OEM, OMM or OPM formats be used instead.

#### The Tle class is fully described in reference [7].

### CLASS OtherTrajWrapper

#### The OtherTrajWrapper is a class that is used to wrap an arbitrary format trajectory data entity. This is done by using the type xsd:any to hold the required trajectory data, because of this an additional schema must be defined to specify the data that is stored in the xsd:any element.

NOTE	–	The OtherTrajWrapper class is a specialization of class AbstractTrajDataWrapper described in 3.9.5 and the generic description of the parameters is given in that subsection.

#### The OtherTrajWrapper class is fully described in reference [7].

### CLASS AbstractConfigProfileWrapper (Abstract)

#### AbstractConfigProfileWrapper is an abstract class that is used to instantiate the wrapper classes required for Configuration Profile data entities.

NOTE	–	The AbstractConfigProfileWrapper class is a specialization of class AbstractDataSubWrapper described in 3.9.3 and the generic description of the parameters is given in that subsection.

#### The AbstractConfigProfileWrapper class is fully described in reference [7].

#### NOTE	–	For a fully compliant CCSDS Submission Request for a Configuration Profile it is required that the concrete Configuration Profile Wrapper derived from the AbstractConfigProfileWrapper class is as specified in Ref. [3]. It is further required that this Configuration Profile Wrapper contains one, and only one, instance of the Configuration Profile class defined in Ref. [3].

### CLASS AbstractDDORScanPatternWrapper (Abstract)

#### AbstractDDORScanPatternWrapper is an abstract class that is used to instantiate the wrapper classes required for DDOR Scan Pattern data entities.

NOTE	–	The AbstractDDORScanPatternWrapper class is a specialization of class AbstractDataSubWrapper described in 3.9.3 and the generic description of the parameters is given in that subsection.

#### The AbstractDDORScanPatternWrapper class is fully described in reference [7].

### CLASS DDORScanPatternWrapper

#### The DDORScanPatternWrapper is a class that is used to wrap a Delta DOR Scan Pattern data entity.

NOTE	–	The DDORScanPatternWrapper class is a specialization of class AbstractDDORScanPatternWrapper described in 3.9.13 and the generic description of the parameters is given in that subsection.

#### The DDORScanPatternWrapper class is fully described in reference [7].

### CLASS AbstractSICFWrapper (Abstract)

#### AbstractSICFWrapper is an abstract class that is used to instantiate the wrapper classes required for Service Instance Configuration File (SICF) data entities.

As there is no standard specification for SICF it is necessary to derive an Agency (or mission) specific SICF Wrapper class from this class.

NOTE	–	The AbstractSICFWrapper class is a specialization of class AbstractDataSubWrapper described in 3.9.3 and the generic description of the parameters is given in that subsection.

#### The AbstractSICFWrapper class is fully described in reference [7].

### CLASS AsciiSICFWrapper

#### Whilst, as noted above, there is no standard format for SICFs, the vast majority of these are at least expressed in ASCII. The AsciiSICFWrapper is a class that may used to wrap an arbitrary format SICF that is in ASCII format.

NOTE	–	The AsciiSICFWrapper class is a specialization of class AbstractSICFWrapper described in 3.9.15 and the generic description of the parameters is given in that subsection.

#### The AsciiSICFWrapper class is fully described in reference [7].

## Service Management Utilization Request Formats Basic Constraints

Basic constraints are intended to be used to request a single tracking pass of a spacecraft. This single tracking pass may involve the use of one or more ground stations and/or relay satellites apertures to provide the required coverage. It is therefore possible to specify handover constraints between apertures.

### Overview

Figure 3-9 shows the UML Class diagram for the Service Management Utilization Request Formats Basic Constraints.

Figure 3-9: Service Management Utilization Request Formats Basic Constraints Class Diagram

The attributes of each class are described further in the following subsections and tables.

### CLASS Constraints (Abstract)

#### The Constraints class is abstract and is used to instantiate the various constraint classes that apply to the Service Management Utilization Request Formats.

#### The abstract Constraint class does not contain any parameters.

### CLASS ConstraintsAlsoSuitableForOffline (Abstract)

#### The ConstraintsAlsoSuitableForOffline class is abstract and is used to instantiate the various constraint classes that can be used for offline as well as other Service Management Utilization Request Formats.

NOTE	–	The ConstraintsAlsoSuitableForOffline class is a specialization of class Constraints described in 3.10.2 and the generic description of the parameters can be found there.

#### The abstract ConstraintsAlsoSuitableForOffline class does not contain any parameters.

### CLASS BasicPass

#### The BasicPass class is optional and  may be used to specify the preferred start time and duration of a pass along with the acceptable earliest and/or latest start times and minimum and/or maximum acceptable duration..

NOTE	–	The BasicPass class is a specialization of class ConstraintsAlsoSuitableForOffline described in 3.10.3 and the generic description of the parameters can be found there.

#### The parameters of the BasicPass class are specified in Table 3-19.

Table 3-19: Class BasicPass Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| PreferredStartTime | Used to specify (in UTC) the preferred time at which a pass starts. NOTE 1: If an earliestStartTime is specified then PreferredStartTime ≥ earliestStartTime NOTE 2: If a latestStartTime is specified then PreferredStartTime ≤ latestStartTime | CCSDS ASCII Time Code B (reference [1]) | UTC |
| earliestStartTime | Optional parameter. Used to specify (in UTC) the earliest time at which a pass can start. | CCSDS ASCII Time Code B (reference [1]) | UTC |
| latestStartTime | Optional parameter. Used to specify (in UTC) the latest time at which a pass can start. NOTE: If both earliestStartTime and latestStartTime are specified then latestStartTime ≥ earliestStartTime | CCSDS ASCII Time Code B (reference [1]) | UTC |
| preferredDuration | This is used to specify the preferred duration of a pass. NOTE 1: If a minimumDuration is specified then preferredDuration ≥ minimumDuration NOTE 2: If a maximumDuration is specified then preferredDuration ≤ maximumDuration | xsd:unsignedInt | Secs |
| minimumDuration | Optional parameter. This is used to specify the minimum duration required for a pass. | xsd:unsignedInt Default value if omitted is 0 | Secs |
| maximumDuration | Optional parameter. This is used to specify the maximum duration required for a pass. NOTE: If both minimumDuration and maximumDuration are specified then maximumDuration ≥ minimumDuration | xsd:unsignedInt Default value if omitted is ∞ | Secs |

### CLASS ApertureSelection

#### The ApertureSelection class is optional and can be used to specify an aperture with which it is desired that the service is provided.

NOTE	–	The ApertureSelection class is a specialization of class Constraints described in 3.10.2 and the generic description of the parameters can be found there.

#### Each instance of the ApertureSelection class, in this context,  must contain 1 and only 1 instance of the ApertureReference class, that is derived from the abstract ApertureLocation class.

#### The parameters of the ApertureSelection class are specified inTable 3-20.

Table 3-20: Class ApertureSelection Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| priority | Optional Parameter. This can be used to specify a preference for which aperture is used if more than one ApertureSelection class is instantiated. The lower the value specified here the higher the priority, with 1 being the highest prority. | xsd:integer >0 Default value if omitted is 1 | n/a |

### CLASS ApertureLocation (Abstract)

#### ApertureLocation is an abstract class which is used to instantiate the various classes of aperture location required by service management and is fully described in reference [7].

### CLASS ApertureReference

#### The ApertureReference class allows the specification of the location of an aperture by the site name where it is located and the name of the aperture and is fully described in reference [7].

NOTE	–	The ApertureReference class is a specialization of class ApertureLocation mentioned in 3.10.6 and fully defined in reference [7].

### CLASS ApertureCelestialBodyPosition

#### The ApertureCelestialBodyPosition class allows the specification of the location of an aperture by the site name where it is located and the name of the aperture and is fully described in reference [7].

NOTE	–	The ApertureCelestialBodyPosition class is a specialization of class ApertureLocation mentioned in 3.10.6 and fully defined in reference [7].

## Service Management Utilization Request Formats Enhanced Constraints

The enhanced constraints are intended to provide additional flexibility when requesting tracking passes of a spacecraft and allow the possibility for “standing orders” to be defined that request of a number of passes within a specified time range subject to the same constraints. It should be noted that the use of basic and enhanced constraints is not mutually exclusive as the enhanced constraints effectively extends the functionality provided by the basic constraints.

### Overview

Figure 3-10 shows the UML Class diagram for the Service Management Utilization Request Formats Enhanced Constraints.

Figure 3-10: Service Management Utilization Request Formats Enhanced Constraints Class Diagram

The attributes of each class are described further in the following subsections and tables.

### CLASS Constraints (Abstract)

See section 3.10.2 for the definition of this class.

### CLASS StandingOrder

#### The StandingOrder class is optional and can be used to submit “repeat” requests. It allows the specification of the number of passes that are required within a specified time interval.

NOTE	–	The StandingOrder class is a specialization of class Constraints described in 3.10.2 and the generic description of the parameters can be found there.

#### The StandingOrder class shall include parameters as specified in Table 3-21.

Table 3-21: Class StandingOrder Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| standingOrderStartTime | Used to specify (in UTC) the start time of the standing order. That is the earliest time at which a service package generated as a result of the standing order may start. | CCSDS ASCII Time Code B (reference [1]) | UTC |
| standingOrderDuration | Used to specify the duration of the standing order. | xsd:unsignedInt | Secs |
| minNumOfPasses | Optional parameter. This may be used to specify the minimum number of passes required in the specified time interval. | xsd:integer > 0 | n/a |
| maxNumOfPasses | Optional parameter. This may be used to specify the maximum number of passes required in the specified time interval. NOTE: if both minNumOfPasses and maxNumOfPasses are specified then maxNumOfPasses ≥ minNumOfPasses | xsd:integer ≥ 0 | n/a |

### CLASS Handover

#### The Handover class is optional and if not specified for a request it is assumed that a station handover is not permitted,

NOTE	–	The Handover class is a specialization of class Constraints described in 3.10.2 and the generic description of the parameters can be found there.

#### The Handover class shall contain the details of the constraints applying to station handovers and shall include parameters specified in Table 3-22.

Table 3-22: Class Handover Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| maximumHandovers | The maximum number of station handovers that are permitted during the requested tracking time. | xsd:integer >0 | n/a |
| mimimumOverlap | Used to specify the minimum overlap between stations during a handover. NOTE: if this is negative then there will be a gap in the coverage provided. | xsd:integer | Secs |
| maximumOverlap | Optional Parameter This can be used to specify the maximum overlap between stations during a handover. | xsd:integer ≥ mimimumOverlap | Secs |
| minimunSingleDuration | Optional Parameter. This can be used to specify the acceptable minimum duration of contact on any one of the apertures used during the pass. | Xsd:integer>0 | Secs |

### CLASS TimeWindows

#### The TimeWindows class is optional and may be used to submit a set of time windows.

#### Each instance of the TimeWindows class must contain 1 or more instances of the TimeWindow class described in section 3.11.6.

NOTE	–	The TimeWindows class is a specialization of class Constraints described in 3.10.2 and the generic description of the parameters can be found there.

#### The use of the TimeWindows class allows the specification of a set of one or more time windows that must either all be included or all excluded in the resulting schedule.

#### Table 3-23 specifies the use of the parameters in the TimeWindows.

Table 3-23: Class TimeWindows Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| includeWindow | If true indicates that the time range specified by the window is considered to be included. If false indicates that the time range specified by the window is considered to be excluded. | xsd:Boolean | n/a |

### CLASS TimeWindow

#### The TimeWindow class is used to specify time windows that can be included in a set of time windows represented by the TimeWindows class described in section 3.11.4.

#### Table 3-24 specifies the use of the parameters in the TimeWindow.

Table 3-24: Class TimeWindow Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| startOfWindow | Used to specify (in UTC) the start time of the window. | CCSDS ASCII Time Code B (reference [1]) | UTC |
| endOfWindow | Used to specify (in UTC) the end time of the window. | CCSDS ASCII Time Code B (reference [1]) | UTC |

### CLASS PassRange

#### The PassRange class is optional and can be used to permit the specification of the minimum and/or maximum range between the spacecraft and aperture for the start and/or end of a pass.

NOTE	–	The PassRange class is a specialization of class Constraints described in 3.10.2 and the generic description of the parameters can be found there.

#### The parameters of the PassRange class are specified in Table 3-25.

Table 3-25: Class PassRange Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| minRangeAtPassStart | Optional parameter. Used to specify the minimum range required at the pass start. | xsd:unsignedInt | Kilometres |
| maxRangeAtPassStart | Optional parameter. Used to specify the maximum range required at the pass start. NOTE: If both minRangeAtPassStart and maxRangeAtPassStart are specified then maxRangeAtPassStart ≥ minRangeAtPassStart | xsd:unsignedInt | Kilometres |
| minRangeAtPassEnd | Optional parameter. Used to specify the minimum range required at the pass end. | xsd:unsignedInt | Kilometres |
| maxRangeAtPassEnd | Optional parameter. Used to specify the maximum range required at the pass start. NOTE: If both minRangeAtPassEnd and maxRangeAtPassEnd are specified then maxRangeAtPassEnd ≥ minRangeAtPassEnd | xsd:unsignedInt | Kilometres |

### CLASS PassInterval

#### The PassInterval class is optional and  can be used to permit the specification of the minimum and/or maximum intervals between passes.

NOTE	–	The PassInterval class is a specialization of class Constraints described in 3.10.2 and the generic description of the parameters can be found there.

#### The parameters of the PassInterval class are specified in Table 3-26 below.

Table 3-26: Class PassInterval Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| minIntBetweenPasses | Optional parameter. This is used to specify the minimum interval required between passes. | xsd:unsignedInt Default value if omitted is 0 | Secs |
| maxIntBetweenPasses | Optional parameter. This is used to specify the maximum interval required between passes. NOTE: If both minimumIntervalBetweenPasses and maximumIntervalBetweenPasses are specified then maximumIntervalBetweenPasses ≥ minimumIntervalBetweenPasses | xsd:unsignedInt Default value if omitted is ∞ | Secs |

### CLASS PassDuration

#### The PassDuration class is optional and can be used to permit the specification of the minimum and/or maximum duration of passes.

NOTE	–	The PassDuration class is a specialization of class Constraints described in 3.10.2 and the generic description of the parameters can be found there.

#### The parameters of the PassDuration class are specified in Table 3-27.

Table 3-27: Class PassDuration Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| minPassDuration | Optional parameter. This is used to specify the minimum duration of a pass. | xsd:unsignedInt Default value if omitted is 0 | Secs |
| maxPassDuration | Optional parameter. This is used to specify the maximum duration of a pass. NOTE: If both minPassDuration and maxPassDuration are specified then minPassDuration ≥ maxPassDuration | xsd:unsignedInt Default value if omitted is ∞ | Secs |

### CLASS PassDailyTime

#### The PassDailyTime class is optional and can be used to permit the specification of the earliest and/or latest absolute (UTC) times for passes. These constraints can be used to limit passes to being only during normal working hours etc..

NOTE	–	The PassDailyTime class is a specialization of class Constraints described in 3.10.2 and the generic description of the parameters can be found there.

#### The parameters of the PassDailyTime class are specified in Table 3-28.

Table 3-28: Class PassDailyTime Parameters

| Parameter | Description | Data Type | Data Units |
| --- | --- | --- | --- |
| daysForPasses | Optional parameter. Used to specify the day(s) on which a pass can be accepted. | Enumeration MONDAY TUESDAY WEDNESDAY THURSDAY FRIDAY SATURDAY SUNDAY | n/a |
| earliestPassStart | Optional parameter. Used to specify (in UTC) the earliest time during the day at which a pass can start. | xsd:time restricted to hh:mm:ssZ | n/a |
| latestPassStart | Optional parameter. Used to specify (in UTC) the latest time during the day at which a pass can start. NOTE: If both earliestPassStart and latestPassStart are specified then latestPassStart ≥ earliestPassStart | xsd:time restricted to hh:mm:ssZ | n/a |
| earliestPassEnd | Optional parameter. Used to specify (in UTC) the earliest time during the day at which a pass can end. | xsd:time restricted to hh:mm:ssZ | n/a |
| latestPassEnd | Optional parameter. Used to specify (in UTC) the latest time during the day at which a pass can end. NOTE: If both earliestPassEnd and latestPassEnd are specified then latestPassEnd ≥ earliestPassEnd | xsd:time restricted to hh:mm:ssZ | n/a |

Implementation Conformance Statement (ICS) Proforma

(Normative)

INTRODUCTION

OVERVIEW

This annex provides the Implementation Conformance Statement (ICS) Requirements List (RL) for an implementation of the Planning Information Formats Specification (CCSDS 902.2-R-1). The ICS for an implementation is generated by completing the RL in accordance with the instructions below. An implementation shall satisfy the mandatory conformance requirements referenced in the RL.

The RL in this annex is blank. An implementation’s completed RL is called the ICS. The ICS states which capabilities and options have been implemented. The following can use the ICS:

- the implementer, as a checklist to reduce the risk of failure to conform to the standard through oversight;

- a supplier or potential acquirer of the implementation, as a detailed indication of the capabilities of the implementation, stated relative to the common basis for understanding provided by the standard ICS proforma;

- a user or potential user of the implementation, as a basis for initially checking the possibility of interworking with another implementation (it should be noted that, while interworking can never be guaranteed, failure to interwork can often be predicted from incompatible ICSes);

- a tester, as the basis for selecting appropriate tests against which to assess the claim for conformance of the implementation.

ABBREVIATIONS AND CONVENTIONS

General

The RL consists of information in tabular form. The status of features is indicated using the abbreviations and conventions described below.

Item Column

The item column contains sequential numbers for items in the table.

Feature Column

The feature column contains a brief descriptive name for a feature. It implicitly means ‘Is this feature supported by the implementation?’

NOTE –	The features itemized in the RL are elements of the Planning Information Format. Therefore support for a mandatory feature indicates that a generated file will include that feature, and support for an optional feature indicates that generated files can include that feature.

Class Column/Parameters

The Class/Parameters column contains, where applicable, the Planning Information Format class associated with the feature.

Reference Column

The reference column indicates the relevant subsection or table in the Planning Information Formats Specification (CCSDS 902.2-R-1) (this document).

Status Column

The status column uses the following notations:

M	mandatory.

O	optional.

It should be noted that a parameter may be marked as M(andatory) while the class that contains it is marked O(ptional). This should be interpreted to mean that while the class is optional if it is present then the parameter must be present.

Support Column Symbols

The support column is to be used by the implementer to state whether a feature is supported by entering Y, N, or N/A, indicating:

Y	Yes, supported by the implementation.

N	No, not supported by the implementation.

N/A	Not applicable.

INSTRUCTIONS FOR COMPLETING THE RL

An implementer shows the extent of compliance to the Recommended Standard by completing the RL; that is, the state of compliance with all mandatory requirements and the options supported are shown. The resulting completed RL is called an ICS. The implementer shall complete the RL by entering appropriate responses in the support or values supported column, using the notation described in A1.2. If a conditional requirement is inapplicable, N/A should be used. If a mandatory requirement is not satisfied, exception information must be supplied by entering a reference Xi, where i is a unique identifier, to an accompanying rationale for the noncompliance.

ICS Proforma for Service Management Utilization Request Format

General Information

Identification of ICS

| Date of Statement (DD/MM/YYYY) |  |
| --- | --- |
| ICS serial number |  |
| System Conformance statement cross-reference |  |

Identification of Implementation Under Test (IUT)

| Implementation name |  |
| --- | --- |
| Implementation version |  |
| Special Configuration |  |
| Other Information |  |

Identification of Supplier

| Supplier |  |
| --- | --- |
| Contact Point for Queries |  |
| Implementation Name(s) and Versions |  |
| Other Information necessary for full identification, e.g., names(s) and version(s) for machines and/or operating systems; |  |

Document Version

| CCSDS 920.9-W-0.09.1 draft |  |
| --- | --- |
| Have any exceptions been required? (Note: A YES answer means that the implementation does not conform to the Recommended Standard. Non-supported mandatory capabilities are to be identified in the ICS, with an explanation of why the implementation is non-conforming | Yes _____ No _____ |

Requirements List

Service Management Utilization Request Format Classes

Class SrvMgtUtilReq

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | SrvMgtUtilReq | 3.2.2 | M |  |

Class SrvMgtUtilReq Parameters

N/A

Class SrvMgtUtilReqHeader

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | SrvMgtUtilReqHeader | 3.2.3 | M |  |

Class SrvMgtUtilReqHeader Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | originatingOrganization | Ref. [7] Table 3-1 | M |  |
|  | generationTime | Ref. [7] Table 3-1 | M |  |
|  | version | Ref. [7] Table 3-1 | M |  |
|  | startTime | Ref. [7] Table 3-1 | O |  |
|  | endTime | Ref. [7] Table 3-1 | O |  |
|  | purpose | Ref. [7] Table 3-1 | O |  |
|  | description | Ref. [7] Table 3-1 | O |  |
|  | utilizationReqStatus | Table 3-1 | M |  |

Class RequestType (Abstract)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | RequestType | 3.2.4 | M |  |

Class RequestType Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | requestID | Table 3-2 | M |  |
|  | serviceAgreementRef | Table 3-2 | O |  |
|  | comment | Table 3-2 | O |  |

Class ServicePkgReq (Abstract)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | ServicePkgReq | 3.2.5 | M |  |

Class ServicePkgReq Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | requestID | Table 3-2 | M |  |
|  | serviceAgreementRef | Table 3-2 | O |  |
|  | comment | Table 3-2 | O |  |
|  | spaceUserNode | Table 3-3 | M |  |
|  | serviceReqID | Table 3-3 | M |  |

Planning Information Request Classes

Class PlanningInfoReq

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | PlanningInfoReq | 3.3.1.1 | M |  |

Class PlanningInfoReq Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | requestID | Table 3-2 | M |  |
|  | serviceAgreementRef | Table 3-2 | O |  |
|  | comment | Table 3-2 | O |  |
|  | spaceUserNode | Table 3-4 | M |  |
|  | trajectoryRef | Table 3-4 | M |  |
|  | configurationProfileRef | Table 3-4 | O |  |

Class PlanningInfoTypeList

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | PlanningInfoTypeList | 3.2.2 | M |  |

Class PlanningInfoTypeList Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | planningInfoType | Ref.[7] Table 3-7 | M |  |

Class Constraints (Abstract)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | Constraints | 3.3.4 | M |  |

Class Constraints Parameters

N/A

Report Request Classes

Class ReportReq (Abstract)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | ReportReq | 3.4.1.1 | M |  |

Class ReportReq Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | requestID | Table 3-2 | M |  |
|  | serviceAgreementRef | Table 3-2 | O |  |
|  | comment | Table 3-2 | O |  |
|  | spaceUserNode | Table 3-5 | M |  |
|  | startTime | Table 3-5 | M |  |
|  | endTime | Table 3-5 | M |  |

Class SimpleScheduleRepReq

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | SimpleScheduleRepReq | 3.4.3 | O |  |

Class SimpleScheduleRepReq Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | requestID | Table 3-2 | M |  |
|  | serviceAgreementRef | Table 3-2 | O |  |
|  | Comment | Table 3-2 | O |  |
|  | spaceUserNode | Table 3-5 | M |  |
|  | startTime | Table 3-5 | M |  |
|  | endTime | Table 3-5 | M |  |
|  | reportType | Table 3-6 | M |  |

Class ApertureLocation (Abstract)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | ApertureLocation | 3.4.4 | O |  |

Class ApertureLocation Parameters

N/A

Class ApertureReference

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | ApertureReference | 3.4.5 | O |  |

Class ApertureReference Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | apertureRef | Ref. [7] Table 3-5 | M |  |
|  | siteRef | Ref. [7] Table 3-5 | M |  |

Class ApertureCelestialBodyPosition

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | ApertureCelestialBodyPosition | 3.4.6 | M |  |

Class ApertureCelestialBodyPosition Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | celestialBody | Ref. [7] Table 3-6 | M |  |
|  | celestialBodyLat | Ref. [7] Table 3-6 | M |  |
|  | celestialBodylong | Ref. [7] Table 3-6 | M |  |
|  | celestialBodyAltitude | Ref. [7] Table 3-6 | O |  |
|  | apertureName | Ref. [7] Table 3-6 | O |  |

Information Request Classes

Class InfoReq

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | InfoReq | 3.5.1.1 | O |  |

Class InfoReq Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | requestID | Table 3-2 | M |  |
|  | serviceAgreementRef | Table 3-2 | O |  |
|  | comment | Table 3-2 | O |  |
|  | spaceUserNode | Table 3-7 | M |  |
|  | configurationProfileRef | Table 3-7 | O |  |
|  | eventSequenceRef | Table 3-7 | O |  |
|  | serviceAgreementRef | Table 3-7 | O |  |
|  | servicePackageRef | Table 3-7 | O |  |
|  | trajectoryRef | Table 3-7 | O |  |
|  | ddorScanPatternref | Table 3-7 | O |  |
|  | sicfRef | Table 3-7 | O |  |

Online New and Replace Service Package Requests Classes

Class OnlineSrvPkgReq (Abstract)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | OnlineSrvPkgReq | 3.6.1.1 | M |  |

Class OnlineSrvPkgReq Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | requestID | Table 3-2 | M |  |
|  | serviceAgreementRef | Table 3-2 | O |  |
|  | comment | Table 3-2 | O |  |
|  | spaceUserNode | Table 3-3 | M |  |
|  | serviceReqID | Table 3-3 | M |  |

Class NewOnlineSrvPkgReq

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | NewOnlineSrvPkgReq | 3.6.3 | M |  |

Class NewOnlineSrvPkgReq Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | requestID | Table 3-2 | M |  |
|  | serviceAgreementRef | Table 3-2 | O |  |
|  | comment | Table 3-2 | O |  |
|  | spaceUserNode | Table 3-3 | M |  |
|  | serviceReqID | Table 3-8 | M |  |

Class ReplaceOnlineSrvPkgReq

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | ReplaceOnlineSrvPkgReq | 3.6.4 | M |  |

Class ReplaceOnlineSrvPkgReq Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | requestID | Table 3-2 | M |  |
|  | serviceAgreementRef | Table 3-2 | O |  |
|  | comment | Table 3-2 | O |  |
|  | spaceUserNode | Table 3-3 | M |  |
|  | serviceReqID | Table 3-9 | M |  |

Class AbstractSrvPkg (ABSTRACT)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | AbstractSrvPkg | 3.6.5 | M |  |

Class AbstractSrvPkg Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | sicfRef | Ref. [7] Table 3-20 | O |  |

Class AbstractOnlineSrvPkg (ABSTRACT)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | AbstractOnlineSrvPkg | 3.6.6 | M |  |

Class AbstractOnlineSrvPkg Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | trajectoryRef | Ref. [7] Table 3-21 | O |  |

Class OnlineSrvPkyType1

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | OnlineSrvPkyType1 | 3.6.7 | M |  |

Class OnlineSrvPkyType1 Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | eventSequenceRef | Ref. [7] Table 3-22 | M |  |

Class OnlineSrvPkyType1Details

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | OnlineSrvPkyType1Details | 3.6.8 | M |  |

Class OnlineSrvPkyType1Details Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | configProfileRef | Ref. [7] Table 3-23 | M |  |

Class DDORScanPatternDetails

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | DDORScanPatternDetails | 3.6.9 | O |  |

Class DDORScanPatternDetails Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | DDORScanPatternRef | Ref. [7] Table 3-24 | M |  |

Class ModResParm

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | ModResParm | 3.6.10 | O |  |

Class ModResParm Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | resName | Ref. [7] Table 3-8 | O |  |

Class AbstractParameter (ABSTRACT)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | AbstractParameter | 3.6.11 | M |  |

Class AbstractParameter Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | name | Ref. [6] Table 3-2 | M |  |

Class Constraints (Abstract)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | Constraints | 3.6.12 | O |  |

Class Constraints Parameters

N/A

Offline New and Replace Service Package Requests Classes

Class OfflineSrvPkyType1Req (Abstract)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | OfflineSrvPkyType1Req | 3.7.1.1 | M |  |

Class OfflineSrvPkyType1Req Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | requestID | Table 3-2 | M |  |
|  | serviceAgreementRef | Table 3-2 | O |  |
|  | comment | Table 3-2 | O |  |
|  | spaceUserNode | Table 3-3 | M |  |
|  | serviceReqID | Table 3-3 | M |  |

Class NewOfflineSrvPkgReq

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | NewOfflineSrvPkgReq | 3.7.3 | M |  |

Class NewOfflineSrvPkgReq Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | requestID | Table 3-2 | M |  |
|  | serviceAgreementRef | Table 3-2 | O |  |
|  | comment | Table 3-2 | O |  |
|  | spaceUserNode | Table 3-3 | M |  |
|  | serviceReqID | Table 3-10 | M |  |

Class ReplaceOfflineSrvPkgReq

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | ReplaceOfflineSrvPkgReq | 3.7.4 | M |  |

Class ReplaceOfflineSrvPkgReq Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | requestID | Table 3-2 | M |  |
|  | serviceAgreementRef | Table 3-2 | O |  |
|  | comment | Table 3-2 | O |  |
|  | spaceUserNode | Table 3-3 | M |  |
|  | serviceReqID | Table 3-11 | M |  |

Class AbstractSrvPkg

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | AbstractSrvPkg | 3.7.5 | M |  |

Class AbstractSrvPkg Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | sicfRef | Ref. [7] Table 3-20 | O |  |

Class OfflineSrvPkyType1

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | OfflineSrvPkyType1 | 3.7.6 | M |  |

Class OfflineSrvPkyType1 Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | configProfileRef | Ref. [7] Table 3-25 | M |  |

Class ModResParm

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | ModResParm | 3.7.7 | O |  |

Class ModResParm Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | resName | Ref. [7] Table 3-8 | M |  |

Class AbstractParameter (ABSTRACT)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | AbstractParameter | 3.7.8 | M |  |

Class AbstractParameter Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | name | Ref. [6] Table 3-2 | M |  |

Class Constraints (Abstract)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | Constraints | 3.7.9 | M |  |

Class Constraints Parameters

N/A

Class ConstraintsAlsoSuitableForOffline (Abstract)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | ConstraintsAlsoSuitableForOffline | 3.7.10 | M |  |

Class ConstraintsAlsoSuitableForOffline Parameters

N/A

Delete Service Package request, Delete Service Package and Replace Service Package Classes

Class DeleteSrvPkgReq

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | DeleteSrvPkgReq | 3.8.1.1 | M |  |

Class DeleteSrvPkgReq Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | requestID | Table 3-2 | M |  |
|  | serviceAgreementRef | Table 3-2 | O |  |
|  | comment | Table 3-2 | O |  |
|  | spaceUserNode | Table 3-3 | M |  |
|  | serviceReqID | Table 3-13 | M |  |
|  | deletePending | Table 3-12 | M |  |

Class DeleteSrvPkg

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | DeleteSrvPkg | 3.8.3 | M |  |

Class DeleteSrvPkg Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | requestID | Table 3-2 | M |  |
|  | serviceAgreementRef | Table 3-2 | O |  |
|  | comment | Table 3-2 | O |  |
|  | spaceUserNode | Table 3-3 | M |  |
|  | serviceReqID | Table 3-15 | M |  |
|  | srvPkgRef | Table 3-14 | M |  |

Class ReplaceSrvPkg

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | ReplaceSrvPkg | 3.8.4 | M |  |

Class ReplaceSrvPkg Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | requestID | Table 3-2 | M |  |
|  | serviceAgreementRef | Table 3-2 | O |  |
|  | comment | Table 3-2 | O |  |
|  | spaceUserNode | Table 3-3 | M |  |
|  | serviceReqID | Table 3-17 | M |  |
|  | srvPkgRef | Table 3-16 | M |  |

Class AbstractSrvPkg (ABSTRACT)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | AbstractSrvPkg | 3.8.5 | M |  |

Class AbstractSrvPkg Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | sicfRef | Ref. [7] Table 3-20 | O |  |

Class AbstractOnlineSrvPkg (ABSTRACT)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | AbstractOnlineSrvPkg | 3.8.6 | M |  |

Class AbstractOnlineSrvPkg Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | trajectoryRef | Ref. [7] Table 3-21 | O |  |

Class OnlineSrvPkyType1

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | OnlineSrvPkyType1 | 3.8.7 | M |  |

Class OnlineSrvPkyType1 Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | eventSequenceRef | Ref. [7] Table 3-22 | M |  |

Class OnlineSrvPkyType1Details

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | OnlineSrvPkyType1Details | 3.8.8 | M |  |

Class OnlineSrvPkyType1Details Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | configProfileRef | Ref. [7] Table 3-23 | M |  |

Class OfflineSrvPkyType1

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | OfflineSrvPkyType1 | 3.8.9 | M |  |

Class OfflineSrvPkyType1 Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | configProfileRef | Ref. [7] Table 3-25 | M |  |

Class DDORScanPatternDetails

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | DDORScanPatternDetails | 3.8.10 | O |  |

Class DDORScanPatternDetails Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | DDORScanPatternRef | Ref. [7] Table 3-24 | M |  |

Class ModResParm

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | ModResParm | 3.8.11 | O |  |

Class ModResParm Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | resName | Ref. [7] Table 3-8 | O |  |

Class AbstractParameter (ABSTRACT)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | AbstractParameter | 3.8.12 | M |  |

Class AbstractParameter Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | name | Ref. [6] Table 3-2 | M |  |

Submission Requests Classes

Class SubmissionReq (ABSTRACT)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | SubmissionReq | 3.9.1.1 | M |  |

Class SubmissionReq Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | requestID | Table 3-2 | M |  |
|  | serviceAgreementRef | Table 3-2 | O |  |
|  | spaceUserNode | Table 3-18 | M |  |
|  | comment | Table 3-2 | O |  |

Class AbstractDataSubWrapper (ABSTRACT)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | AbstractDataSubWrapper | 3.9.3 | M |  |

Class AbstractDataSubWrapper Parameters

N/A

Class AbstractEventSeqWrapper (ABSTRACT)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | AbstractEventSeqWrapper | 3.9.4 | M |  |

Class AbstractEventSeqWrapper Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | eventSequenceID | Ref. [7] Table 3-10 | M |  |

Class AbstractTrajDataWrapper (ABSTRACT)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | AbstractTrajDataWrapper | 3.9.5 | M |  |

Class AbstractTrajDataWrapper Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | trajectoryID | Ref. [7] Table 3-11 | M |  |

Class OemWrapper

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | OemWrapper | 3.9.6 | M |  |

Class OemWrapper Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | trajectoryID | Ref. [7] Table 3-11 | M |  |

Class OmmWrapper

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | OmmWrapper | 3.9.7 | M |  |

Class OmmWrapper Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | trajectoryID | Ref. [7] Table 3-11 | M |  |

Class OpmWrapper

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | OpmWrapper | 3.9.8 | M |  |

Class OpmWrapper Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | trajectoryID | Ref. [7] Table 3-11 | M |  |

Class TleWrapper

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | TleWrapper | 3.9.9 | M |  |

Class TleWrapper Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | trajectoryID | Ref. [7] Table 3-11 | M |  |

Class Tle

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | Tle | 3.9.10 | M |  |

Class Tle Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | tleLine0 | Ref. [7] Table 3-12 | M |  |
|  | tleLine1 | Ref. [7] Table 3-12 | M |  |
|  | tleLine2 | Ref. [7] Table 3-12 | M |  |

Class OtherTrajWrapper

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | OtherTrajWrapper | 3.9.11 | M |  |

Class OtherTrajWrapper Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | trajectoryID | Ref. [7] Table 3-11 | M |  |
|  | trajFormat | Ref. [7] Table 3-15 | M |  |
|  | trajData | Ref. [7] Table 3-15 | M |  |

Class AbstractConfigProfileWrapper (ABSTRACT)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | AbstractConfigProfileWrapper | 3.9.12 | M |  |

Class AbstractConfigProfileWrapper Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | configurationProfileID | Ref. [7] Table 3-16 | M |  |

Class AbstractDDORScanPatternWrapper (ABSTRACT)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | AbstractDDORScanPatternWrapper | 3.9.13 | M |  |

Class AbstractDDORScanPatternWrapper Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | ddorScanPatternID | Ref. [7] Table 3-17 | M |  |

Class DDORScanPatternWrapper

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | DDORScanPatternWrapper | 3.9.14 | M |  |

Class DDORScanPatternWrapper Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | ddorScanPatternID | Ref. [7] Table 3-17 | M |  |

Class AbstractSICFWrapper (ABSTRACT)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | AbstractSICFWrapper | 3.9.15 | M |  |

Class AbstractSICFWrapper Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | sicfID | Ref. [7] Table 3-18 | M |  |

Class AsciiSICFWrapper

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | AsciiSICFWrapper | 3.9.16 | M |  |

Class AsciiSICFWrapper Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | sicfID | Ref. [7] Table 3-18 | M |  |
|  | sicfFormat | Ref. [7] Table 3-19 | M |  |
|  | sicfData | Ref. [7] Table 3-19 | M |  |

Service Management Utilization Request Formats Basic Constraints Classes

Class Constraints (Abstract)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | Constraints | 3.10.2 | M |  |

Class Constraints Parameters

N/A

Class ConstraintsAlsoSuitableForOffline (Abstract)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | ConstraintsAlsoSuitableForOffline | 3.10.3 | M |  |

Class ConstraintsAlsoSuitableForOffline Parameters

N/A

Class BasicPass

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | BasicPass | 3.10.4 | M |  |

Class BasicPass Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | preferredStartTime | Table 3-19 | M |  |
|  | earliestStartTime | Table 3-19 | O |  |
|  | latestStartTime | Table 3-19 | O |  |
|  | preferredDuration | Table 3-19 | M |  |
|  | minimumDuration | Table 3-19 | O |  |
|  | maximumDuration | Table 3-19 | O |  |

Class ApertureSelection

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | ApertureSelection | 3.10.5 | M |  |

Class ApertureSelection Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | priority | Table 3-20 | O |  |

Class ApertureLocation (Abstract)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | ApertureLocation | 3.10.6 | M |  |

Class ApertureLocation Parameters

N/A

Class ApertureReference

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | ApertureReference | 3.10.7 | M |  |

Class ApertureReference Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | apertureRef | Ref. [7] Table 3-5 | M |  |
|  | siteRef | Ref. [7] Table 3-5 | M |  |

Class ApertureCelestialBodyPosition

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | ApertureCelestialBodyPosition | 3.10.8 | M |  |

Class ApertureCelestialBodyPosition Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | celestialBody | Ref. [7] Table 3-6 | M |  |
|  | celestialBodyLat | Ref. [7] Table 3-6 | M |  |
|  | celestialBodylong | Ref. [7] Table 3-6 | M |  |
|  | celestialBodyAltitude | Ref. [7] Table 3-6 | O |  |
|  | apertureName | Ref. [7] Table 3-6 | O |  |

Service Management Utilization Request Formats Enhanced Constraints Classes

Class Constraints (Abstract)

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | Constraints | 3.11.2 | M |  |

Class Constraints Parameters

N/A

Class StandingOrder

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | StandingOrder | 3.11.3 | O |  |

Class StandingOrder Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | standingOrderStartTime | Table 3-21 | M |  |
|  | standingOrderDuration | Table 3-21 | M |  |
|  | minNumOfPasses | Table 3-21 | O |  |
|  | maxNumOfPasses | Table 3-21 | O |  |

Class Handover

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | Handover | 3.11.4 | M |  |

Class Handover Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | maximumHandovers | Table 3-22 | M |  |
|  | mimimumOverlap | Table 3-22 | M |  |
|  | maximumOverlap | Table 3-22 | O |  |
|  | minimunSingleDuration | Table 3-22 | O |  |

Class TimeWindows

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | TimeWindows | 3.11.4 | M |  |

Class TimeWindows Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | includeWindow | Table 3-23 | M |  |

Class TimeWindow

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | TimeWindow | 3.11.6 | M |  |

Class TimeWindow Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | startOfWindow | Table 3-24 | M |  |
|  | endOfWindow | Table 3-24 | M |  |

Class PassRange

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | PassRange | 3.11.7 | M |  |

Class PassRange Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | minRangeAtPassStart | Table 3-25 | O |  |
|  | maxRangeAtPassStart | Table 3-25 | O |  |
|  | minRangeAtPassEnd | Table 3-25 | O |  |
|  | maxRangeAtPassEnd | Table 3-25 | O |  |

Class PassInterval

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | PassInterval | 3.11.8 | M |  |

Class PassInterval Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | minIntBetweenPasses | Table 3-26 | O |  |
|  | maxIntBetweenPasses | Table 3-26 | O |  |

Class PassDuration

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | PassDuration | 3.11.9 | M |  |

Class PassDuration Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | minPassDuration | Table 3-27 | O |  |
|  | maxPassDuration | Table 3-27 | O |  |

Class PassDailyTime

General

| Item | Description | Ref. | Status | Support |
| --- | --- | --- | --- | --- |
|  | PassDailyTime | 3.11.10 | M |  |

Class PassDailyTime Parameters

| Item | Parameter | Ref. | Status | Item Support or Values Supported |
| --- | --- | --- | --- | --- |
|  | daysForPasses | Table 3-28 | O |  |
|  | earliestPassStart | Table 3-28 | O |  |
|  | latestPassStart | Table 3-28 | O |  |
|  | earliestPassEnd | Table 3-28 | O |  |
|  | latestPassEnd | Table 3-28 | O |  |

Security, SANA, and Patent Considerations

(Informative)

SecuRity Considerations

Overview

This annex presents the results of an analysis of security considerations applied to the technologies specified in this Recommended Standard.

CONSEQUENCES OF NOT APPLYING SECURITY TO THE TECHNOLOGY

The consequences of not applying security to the systems and networks on which this Recommended Standard is implemented could include potential loss, corruption, and theft of data. Since it is possible to utilize these messages in preparing and disseminating schedules relating to the availability of communications and tracking resources for spacecraft, the consequences of not applying security to the systems and networks on which this Recommended Standard is implemented could include compromise or loss of the mission if malicious tampering of a particularly severe nature occurs.

POTENTIAL THREATS AND ATTACK SCENARIOS

Potential threats or attack scenarios include, but are not limited to, (a) unauthorized access to the programs/processes that generate and interpret the messages, and (b) unauthorized access to the messages during transmission between exchange partners. Protection from unauthorized access during transmission is especially important if the mission utilizes open ground networks such as the Internet to provide ground station connectivity for the exchange of data formatted in compliance with this Recommended Standard. It is strongly recommended that potential threats or attack scenarios applicable to the systems and networks on which this Recommended Standard is implemented be addressed by the management of those systems and networks and the utilization of adequate authentication, suitable protocols, and secured interfaces for the exchange of this information.

security concerns RELATED TO THIS RECOMMENDED STANDARD

Data Privacy

Privacy of data formatted in compliance with the specifications of this Recommended Standard should be assured by the systems and networks on which this Recommended Standard is implemented.

Data Integrity

Integrity of data formatted in compliance with the specifications of this Recommended Standard should be assured by the systems and networks on which this Recommended Standard is implemented.

Authentication of Communicating Entities

Authentication of communicating entities involved in the transport of data which complies with the specifications of this Recommended Standard should be provided by the systems and networks on which this Recommended Standard is implemented.

Data Transfer between Communicating Entities

The transfer of data formatted in compliance with this Recommended Standard between communicating entities should be accomplished via secure mechanisms approved by the Information Technology Security functionaries of exchange participants.

Control of Access to Resources

Control of access to resources should be managed by the systems upon which provider formatting and recipient processing are performed.

Auditing of Resource Usage

Auditing of resource usage should be handled by the management of systems and networks on which this Recommended Standard is implemented.

UNAUTHORIZED ACCESS

Unauthorized access to the programs/processes that generate and interpret the messages should be prohibited in order to minimize potential threats and attack scenarios.

DATA SECURITY IMPLEMENTATION SPECIFICS

Specific information-security interoperability provisions that apply between agencies and other independent users involved in an exchange of data formatted in compliance with this Recommended Standard should be specified in an ICD.

SANA Considerations

General

The recommendations of this document rely on the SANA registries described below. New assignments in these registries, in conformance with the policies identified, will be available at the SANA registry Web site: http://sanaregistry.org. Therefore the reader shall look at the SANA Web site for all the assignments contained in these registries.

REGISTRY for originatingOrganization

See section A2.2 of Ref. [7]

REGISTRY FOR spaceUserNode

For spaceUserNode see section A2.3 of Ref. [7].

In addition to the values for the ‘spaceUserNode’ parameter contained in the CCSDS Spacecraft Identifiers registry, the following values need to be recognized by implementations (see Table 3-6):

| user | Description |
| --- | --- |
| UNALLOCATED | Indicates that the time is unallocated. |

Registry FOR siteRef and apertureRef

See section A2.4 of Ref. [7].

Use Of Unregistered Values

Only values that have been registered should be used for the originatingOrganization,  spaceUserNode, siteRef and apertureRef parameters.  Unregistered values for the originatingOrganization,  spaceUserNode, siteRef and apertureRef parameters may be used. If unregistered values are used they should be prefixed with the string ‘UNR::’.

NOTES

- ‘UNR::’  indicates an unregistered value;

- this helps eliminate potential confusion in a multi-agency cross support context;

- use of unregistered values is not recommended and should be avoided if possible.

Patent Considerations

No patent rights are known to adhere to any of the specifications of the Recommended Standard.

XML Schema Organization, Packaging and Examples For The Service Managment Utilization Request Formats.

(Informative)

Purpose

This annex provides an informative information regarding the XML Schema Organization and packaging.

Schema Organization And Packaging

The normative Service Management Utilization Request schema types and global elements are contained in the file ‘902x09w0_19-Smurf.xsd’.

The Service Management Utilization Request types and global elements are registered in the ‘urn:ccsds:schema:cssm:1.0.0’ name space.

The Service Management Utilization Request schema includes the following schemas;

- 902x12m1-SmCmnEnt-InfEntHdr.xsd

- Types and global elements in this schema are registered in the ‘urn:ccsds:schema:cssm:1.0.0’ name space.

- 902x12m1-SmCmnEnt-AbsEvnt.xsd

- Types and global elements in this schema are registered in the ‘urn:ccsds:schema:cssm:1.0.0’ name space.

- 902x12m1-SmCmnEnt-CmnClss.xsd

- Types and global elements in this schema are registered in the ‘urn:ccsds:schema:cssm:1.0.0’ name space.

- 902x12w1_04-SmCmnEnt-DataWrp.xsd

- Types and global elements in this schema are registered in the ‘urn:ccsds:schema:cssm:1.0.0’ name space.

- 902x12w1_04-SmCmnEnt-SrvPkg.xsd

- Types and global elements in this schema are registered in the ‘urn:ccsds:schema:cssm:1.0.0’ name space.

- 902x09w0_19-Smurf-EnhancedCons.xsd

- Types and global elements in this schema are registered in the ‘urn:ccsds:schema:cssm:1.0.0’ name space.

The source of the following schema files;

- 902x09w0_19-Smurf.xsd

- 902x12m1-SmCmnEnt-InfEntHdr.xsd

- 902x12m1-SmCmnEnt-AbsEvnt.xsd

- 902x12m1-SmCmnEnt-CmnClss.xsd

- 902x12w1_04-SmCmnEnt-DataWrp.xsd

- 902x12w1_04-SmCmnEnt-SrvPkg.xsd

- 902x09w0_19-Smurf-EnhancedCons.xsd

is the SANA SCCS-SM Information Entity XML Schemas registry:

http://sanaregistry.org/r/service_management_xml_schemas

Examples

Various examples of the use of SMURF are available. These are maintained in a git repository, the location of which can be found in the following SANA registry:

http://sanaregistry.org/r/git_repository_locations

Abbreviations and Acronyms

(Informative)

| ASCII | American Standard Code for Information Interchange |
| --- | --- |
| CCSDS | Consultative Committee on Space Data Systems |
| ICD | Interface Control Document |
| OMG | Object Management Group |
| SANA | Space Assigned Numbers Authority |
| TBD | To Be Decided |
| UML | Unified Modelling Language |
| UTC | Coordinated Universal Time |
| W3C | World Wide Web Consortium |
| XML | eXtensible Markup Language |

Informative References

(Informative)

[E1]   Space Communication Cross Support—Service Management—Operations Concept. Report Concerning Space Data Systems Standards, CCSDS 910.14-G-1. Green Book. Issue 1. Washington, D.C.: CCSDS, May 2011.

# Comments

Should we put in a “forthcoming” reference ?  On the other hand, this does not appear to be supported by the UML class diagram.  I think, given the lack of any real definition for the accounting at this time, its probably better just to strike this?

I think we said this is not really being supported?

I think we could just leave it as by means cross reference to data entities.

Probably remove this from the document given that we are no longer supporting scenarios?

Do we have any kind of reference for this even in formally? Or perhaps we need a little Annex just to quickly explain what this is?

Presumably this would be the forthcoming management service, right? So perhaps this could be another one of those forthcoming references?

I don't think we'll get around to including this in the planning information data format anytime soon… Maybe we can delete this?

mind

Does not include request for accounting…(so perhaps remove accounting from document)

Two comments: 1) I think we can say that if it is specified then it is requested that no information be returned earlier than the time specified by the parameter. I don't think, at the level of this data format definition, that we can say definitively that no planning information will get turned that has a time earlier than the specified start time.  2) It seems that it would be good practice to state start and end times? As in they should be mandatory for this request type?

Okay, so these are requests for information entity retrievals. It seems like the presumption is that the various identifiers are all known which is an okay assumption, but I think we have all experienced searching for things we don't quite remember the name of and we end up resorting to I know it was between two weeks ago and yesterday and searching in that time range does help sometimes. It may be that start and end time could be stated? Following on from this a bit, I'm not sure we can say that the times will be ignored given that this is a data format definition?

Ultimately, I’m okay with the presumption that the entity name is known for the SMURF definition for agency review.

Presumably this is not optional if the request is for a configuration profile…? Perhaps we need to add a clause like "mandatory if…"?

Seems like this should either say just “OnlineSrvPkg” or add a “OnlineSrvPkgType2”? Or add some other clarifying note?

What is the interpretation if start or end time is not stated?  E.g., start time is time when request is received?

I wonder if it would be better to collect these kinds of considerations in a usage consideration annex or something like that.  It seems that as a data format specification this can not really be “enforced”.  If we were to do that then I think the description gets to be more perhaps a bit more (albeit pedantically) to the point – e.g., A unique identifier for the service request.

If we put in the usage considerations annex, another item to include in that annex.

Reference 7 is for the CDE; I am not sure that is where this will end up being, but from a pragmatic point of view we may have to do something like this. The CDE on the other hand points to the 506 book which I think is ultimately the best approach.  Is the approach here essentially that given the CDE has the abstract wrapper class the SMURF points to the CDE and it is then the CDE that in turn “resolves” to the 506 book?  If so, then that might indeed be a good approach to allow ourselves the flexibility of how much of the scan pattern we define in CSSM vs DDOR WGs, etc.

For the CPIF I put in the direct github repository link (https://github.com/cssAreaGH/CSSM-XML-InstanceExamples)  We probably need to work with SANA to get this registry going.  In doing so we probably need to have a description of the sana registry git repositories (simple as it may be).