Draft Recommendation for
Space Data System Standards

Time Critical Onboard Network (TCONS) and Onboard Bus Lan (OBL) Architecture

DRAFT RECOMMENDED STANDARD

CCSDS 000.0-R-1.1

RED BOOK

September 2005

AUTHORITY

|  | Issue: | Draft Red Book, Issue 1.1 |  |
| --- | --- | --- | --- |
|  | Date: | September 2005 |  |
|  | Location: | Atlanta, USA |  |

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF AUTHORITY:)

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and represents the consensus technical agreement of the participating CCSDS Member Agencies.  The procedure for review and authorization of CCSDS Recommendations is detailed in the Procedures Manual for the Consultative Committee for Space Data Systems, and the record of Agency participation in the authorization of this document can be obtained from the CCSDS Secretariat at the address below.

This Recommendation is published and maintained by:

CCSDS Secretariat

Office of Space Communication (Code M-3)

National Aeronautics and Space Administration

Washington, DC  20546, USA

STATEMENT OF INTENT

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF INTENT:)

The Consultative Committee for Space Data Systems (CCSDS) is an organization officially established by the management of its members. The Committee meets periodically to address data systems problems that are common to all participants, and to formulate sound technical solutions to these problems. Inasmuch as participation in the CCSDS is completely voluntary, the results of Committee actions are termed Recommended Standards and are not considered binding on any Agency.

This Recommended Standard is issued by, and represents the consensus of, the CCSDS members.  Endorsement of this Recommendation is entirely voluntary. Endorsement, however, indicates the following understandings:

o	Whenever a member establishes a CCSDS-related standard, this standard will be in accord with the relevant Recommended Standard. Establishing such a standard does not preclude other provisions which a member may develop.

o	Whenever a member establishes a CCSDS-related standard, that member will provide other CCSDS members with the following information:

--	The standard itself.

--	The anticipated date of initial operational capability.

--	The anticipated duration of operational service.

o	Specific service arrangements shall be made via memoranda of agreement. Neither this Recommended Standard nor any ensuing standard is a substitute for a memorandum of agreement.

No later than five years from its date of issuance, this Recommended Standard will be reviewed by the CCSDS to determine whether it should: (1) remain in effect without change; (2) be changed to reflect the impact of new technologies, new requirements, or new directions; or (3) be retired or canceled.

In those instances when a new version of a Recommended Standard is issued, existing CCSDS-related member standards and implementations are not negated or deemed to be non-CCSDS compatible.  It is the responsibility of each member to determine when such standards or implementations are to be modified.  Each member is, however, strongly encouraged to direct planning for its new standards and implementations towards the later version of the Recommended Standard.

FOREWORD

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING FOREWORD:)

This document is a technical Recommendation for use in developing flight and ground systems for space missions and has been prepared by the Consultative Committee for Space Data Systems (CCSDS). The Time Critical Onboard Networking Services (TCONS) described herein is intended for missions that are cross-supported between Agencies of the CCSDS, in the framework of the Spacecraft Onboard Interface Services (SOIS) CCSDS area.

This Recommendation specifies an architecture and set of related services to be used by space missions to transfer space application data over an onboard network. TCONS provides time critical communications over a single sub-network onboard a spacecraft. It also provides quality of service functions for other Transport and Network protocols like SCPS TP/NP. TCONS provides a common interface to software using the TCONS services regardless of the particular type of data-link being used for communication. The aim is to increase reuse of software components onboard a spacecraft while at the same time allowing appropriate choice of communications hardware. The specified services may be implemented in a number of different ways but will support interoperability for time critical onboard applications. The Time Critical Onboard Network Services (TCONS) will provide services to the Time Critical Onboard Applications (TCOA) layer above, to various Transport and Network Protocols including CCSDS SCPS TP/NP, and/or to user applications. It will exclusively use services of the Onboard Bus and LAN (OBL) layer below

Through the process of normal evolution, it is expected that expansion, deletion, or modification of this document may occur.  This Recommendation is therefore subject to CCSDS document management and change control procedures which are defined in reference [A1].  Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be addressed to the CCSDS Secretariat at the address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- British National Space Centre (BNSC)/United Kingdom.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- Deutsches Zentrum für Luft- und Raumfahrt e.V.  (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (Roskosmos)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- Centro Tecnico Aeroespacial (CTA)/Brazil.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- Communications Research Laboratory (CRL)/Japan.

- Danish Space Research Institute (DSRI)/Denmark.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Korea Aerospace Research Institute (KARI)/Korea.

- MIKOMTEK:  CSIR (CSIR)/Republic of South Africa.

- Ministry of Communications (MOC)/Israel.

- National Oceanic & Atmospheric Administration (NOAA)/USA.

- National Space Program Office (NSPO)/Taipei.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- United States Geological Survey (USGS)/USA.

PREFACE

This document is a draft CCSDS Recommended Standard.  Its ‘Red Book’ status indicates that the CCSDS believes the document to be technically mature and has released it for formal review by appropriate technical organizations.  As such, its technical contents are not stable, and several iterations of it may occur in response to comments received during the review process.

Implementers are cautioned not to fabricate any final equipment in accordance with this document’s technical content.

DOCUMENT CONTROL

| Document | Title | Date | Status |
| --- | --- | --- | --- |
| CCSDS xxx.x-RD-0.5 | Time Critical Onboard Networking (TCONS) Architecture | August 2005 | First Draft Issue |
| CCSDS xxx.x-RD-0.6 | Time Critical Onboard Networking (TCONS) Architecture | September 2005 | Second Draft Issue |
| CCSDS xxx.x-RD-0.7 | Time Critical Onboard Networking (TCONS) Architecture | September 2005 | Third Draft Issue Corrections to title page |
| CCSDS xxx.x-RD-1.0 | Time Critical Onboard Networking (TCONS) Architecture | September 2005 | Final draft version for approval |
| CCSDS xxx.x-RD-1.1 | Time Critical Onboard Networking (TCONS) Architecture | September 2005 | Updated following comments from SIS and TCOAS |

CONTENTS

Section	Page

1	INTRODUCTION	1-1

1.1	Purpose and Scope	1-1

1.2	Applicability	1-1

1.3	Rationale	1-2

1.4	Document Structure	1-2

1.4.1	Terms	1-2

1.4.2	Nomenclature	1-4

1.5	REFERENCES	1-4

2	OVERVIEW	2-6

3	TIME CRITICAL ONBOARD network services architecture	3-8

3.1	inter-network layer	3-9

3.2	intra-network layer	3-9

3.3	tcons api	3-10

4	onboard bus and lan architecture	4-11

4.1	data link layer	4-11

4.2	redundancy function	4-13

4.3	retry function	4-13

4.4	fragmentation function	4-13

4.5	REsource Reservation function	4-14

4.6	PDU Encapsulation	4-14

4.7	address resolution function	4-14

5	network management	5-16

Table of Figures

Figure 2-1 SOIS Architecture, Responsibilities and Context	2-6

Figure 3-1 TCONS/OBL Architecture	3-8

Figure 4-1 OBL Architecture	4-12

# INTRODUCTION

## Purpose and Scope

The purpose of this Recommendation is to provide an architectural overview of the Spacecraft Onboard Interface Services (SOIS) being developed by the Time Critical Onboard Network Services (TCONS) and Onboard Bus and LAN (OBL) working groups.  These services encompass the transport, network, and data link layers.

TCONS provides time-critical network services which can operate over many different Buses/sub-networks permitting the creation of heterogeneous flight networks with common software interfaces. Time-critical means that the user of the TCONS service cares about when an item of data will be delivered. This may take the form of a deadline for delivery, of priority of delivery or of reservation of bandwidth across a network.  Time criticality is guaranteed within each bus/sub-network but not between distinct Buses/sub-networks. TCONS provides time critical quality of service functions and isolates the application or transport and network layer software from the specific bus/sub-network being used. The aim is to support software reuse while at the same time allowing the spacecraft system engineer freedom in selecting an appropriate onboard communication infrastructure.

This Recommendation defines the TCONS services in terms of:

a)  the services provided within each layer;

b)  the service access points within the architecture;

It does not specify:

a)  individual implementations or products;

b)  the implementation of service interfaces within real systems;

c)  the protocols data units employed by the services;

d)  the technologies required to perform the services;

## Applicability

This Recommendation applies to the creation of Agency standards and to future data communications over spacecraft onboard networks.  The Recommendation includes an overview of the services required for inter-Agency cross support.  It is neither a specification of, nor a design for, real systems that may be implemented for existing or future missions.

The Recommendation specified in this document is to be invoked through the normal standards programs of each CCSDS Agency and is applicable to those missions for which the services described in this Recommendation is anticipated.   Where mandatory capabilities are clearly indicated in sections of the Recommendation, they must be implemented when this document is used as a basis for cross support. Where options are allowed or implied, implementation of these options is subject to specific bilateral cross support agreements between the Agencies involved.

## Rationale

The purpose of an onboard network is to transfer data between two end systems residing on the same sub-network or on different sub-networks.  The Time Critical Onboard Network Services (TCONS) and Onboard Bus/Lan (OBL) services address the problem of transfer of information across a spacecraft onboard network comprising one or more sub-networks where the sub-networks or buses may be of vastly different types (e.g. SpaceWire and Mil-Std-1553). TCONS handles transfer of information across multiple sub-networks (Inter-network) and single sub-networks (Intra-Network). OBL provides the necessary functions for sending information across the underlying data links.  This concept allows a range of Application layer protocols and processes to be implemented over a well-defined standard set of service profiles regardless of the characteristics of the existing underlying sub-networks.

Existing protocols like TCP/IP were considered but found to lack the time-critical behaviour required for TCONS. At the same time, the importance of using common Internet protocols across the ground, space-link and spacecraft onboard networks was recognized. The use of TCP/IP and other networking protocols are permitted within the architecture. It was also realized that anyone designing a spacecraft system that supports time-critical behaviour should put all related time-critical units on the same bus/sub-network. Therefore the key responsibility of TCONS is to provide a Quality-of-Service (QoS) service to any transport or network layer within any supported bus/sub-network. The QoS functions are a range of services classified according to their time-critical behaviour and which provide a common interface to the underlying sub-networks/buses.

## Document Structure

This document is divided into two sections.  Section 2 provides an overview of the SOIS architecture and the TCONS/OBL architecture with subsections describing each layer in detail.  Section 3 provides an overview of the Onboard Bus and LAN architecture, with subsections describing each function.

### Terms

For the purpose of this document, the following definitions apply.

Best Effort – no guarantee of packet delivery or order of delivery of packets

Fragmentation – The division of Network protocol data units (PDUs) by the data link into shorter sections (fragments) that are short enough to be sent over the data link. The data link is responsible for reassembling the fragments back into Network protocol data units (datagrams) when returning to the TCONS network layer.

Heterogeneous network – a network that uses one or more underlying communications protocols e.g. part SpaceWire and part Mil-Std 1553.

Packet – Delimited octet aligned data unit.

Priority – Differentiated treatment of a SDU or PDU whereby an SDU or PDU of higher priority is handled before one of lower priority.

Protocol data unit (PDU) – A unit of data specified in a protocol and consisting of protocol-control-information and possibly user data.

Quality of Service (QoS) – The ability of a communication system to provide predictable and differentiated services. Quality of Service for a communication service may be characterised in terms of important features relevant to that communications service, for example: Reliability, Transmission rate, Effective Bandwidth and latency, Error rate.

Reliability – A quality of service parameter indicating whether or not TCONS will attempt to acknowledge the successful receipt of a packet and possibly retry sending a PDU if no acknowledge is received by the sender.

Service Data Unit (SDU) – A unit of data passed into or out of a service interface.

Time Critical – A packet must be delivered within a certain period of time, or be treated preferentially with respect to other packets.

Traffic Class – A traffic class is a category of traffic on a sub-network distinguished by its quality of service.

The following abbreviations have been used:

API		Application Programming Interface

CCSDS	Consultative Committee for Space Data Systems

IP		Internetwork Protocol

LAN		Local Area Network

NP		Networking Protocol

OBL		Onboard Bus/LAN

PDU		Protocol Data Unit

QoS		Quality of Service

RD		Reference Document

SCPS		Space Communications Protocol Specification

SDU		Service Data Unit

SIS		Space Internetworking Services

SOIS		Spacecraft Onboard Interface Services

TCOAS	Time Critical Onboard Application Services

TCONS	Time Critical Onboard Network Services

TCP		Transmission Control Protocol

UDP		User Datagram Protocol

### Nomenclature

The following conventions apply throughout this Recommended Standard:

a)  the words ‘shall’ and ‘must’ imply a binding and verifiable specification;

b)  the word ‘should’ implies an optional, but desirable, specification;

c)  the word ‘may’ implies an optional specification;

d)  the words ‘is’, ‘are’, and ‘will’ imply statements of fact.

## REFERENCES

The following documents contain provisions that, through reference in this text, constitute provisions of the Recommendation.  At the time of publication, the editions indicated were valid.  All documents are subject to revision, and users of this recommendation are encouraged to investigate the possibility of applying the most recent editions of the documents indicated below.  The CCSDS Secretariat maintains a register of currently valid CCSDS Recommendations.

[1]  SOIS Concept and Rationale, Recommendation for blah blah…., CCSDS nnn.n-G-x.  Issue x.  CCSDS, month year.

[2]  Recommendation for Time-Critical Onboard Inter-Networking Service, CCSDS nnn.n-R-x.  Issue x.  CCSDS, month year

[3]  Recommendation for Time-Critical Onboard Intra-Networking Service, CCSDS nnn.n-R-x.  Issue x.  CCSDS, month year

[4] Time Critical Onboard Networking Services Quality of Service White Paper, CCSDS nnn.n-?-x.  Issue x.  CCSDS, month year

[5]  Recommendation for Onboard Sub-Network Generic Interface Specification, CCSDS nnn.n-R-x.  Issue x.  CCSDS, month year

[6]  Recommendation for TCONS Application Programming Interface, CCSDS nnn.n-R-x.  Issue x.  CCSDS, month year

[7]   Recommendation for TCONS Network Management Service, CCSDS nnn.n-R-x.  Issue x.  CCSDS, month year

[8]   Recommendation for TCONS over SpaceWire, CCSDS nnn.n-R-x.  Issue x.  CCSDS, month year

[9]  Recommendation for TCONS over Ethernet, CCSDS nnn.n-R-x.  Issue x.  CCSDS, month year

[10]  Recommendation for TCONS over Mil-Std 1553, CCSDS nnn.n-R-x.  Issue x.  CCSDS, month year

# OVERVIEW

The SOIS architecture, shown in Figure 2-1, defines a standard set of services for use onboard spacecraft.  The services are categorized by a stack of layers where each of the layers provides a specific set of functionality.  Each functional layer is described below.

Figure 2-1 SOIS Architecture, Responsibilities and Context

- User Applications – applications that use the SOIS services.

- TCOAS (Time Critical Onboard Application Services) layer – a collection of common onboard application that need the time-critical services of TCONS.

- Inter-network layer – provides transport and inter-networking services across multiple underlying sub-networks. Other CCSDS transport/network protocols are also permitted including TCP/IP protocols.

- Intra-network layer – provides protocol multiplexing and quality of service functions for TCOAS and the inter-networking protocols.  QoS services provided by the intra-network are supported by functionality in the data link layer, such as redundancy and retry allocation. The Intra-Network layer provides a common interface to the various data link protocols.

- Data Link layer – contains the various data-links supported by SOIS. For each data link a common set of functions, represented by the Generic Data Link Abstraction block, is provided to the Intra-Network layer. The Generic Data Link Abstraction is an abstraction of all the functions in the data link (see section 4).

- Network Management Service – used to configure, monitor and control the SOIS network.

# TIME CRITICAL ONBOARD network services architecture

The inter-network, intra-network, and the network management service interfaces are illustrated in Figure 3-1. The inter-network service interface provides a means of transferring data over multiple buses/sub-networks and includes the network layer routing function. The intra-network service interface supports transfer of data over a single bus/sub-network. Quality of service is common across both of these service interfaces. The network management interface provides the means for configuring and monitoring the network and supporting QoS.

The TCONS API enables software portability across different implementations.

The inter-network, intra-network and data-link layers are also shown in Figure 3-1. These layers are described in detail in the following sections.

Figure 3-1 TCONS/OBL Architecture

## inter-network layer

The inter-network layer contains the transport and network layers. The TCP/UDP/IP protocols and their SCPS equivalents are included as CCSDS SIS preferred transport and network protocols. Other transport and network protocols may also be added in the future. TCONS specific transport and network protocols that provide time-critical services over multiple, heterogeneous sub-networks/buses may be provided in the future.

The transport layer provides end-to-end communications services from a user application on one end-system to a user application on another end-system, across one or more sub-networks. Typical network services include a best effort service, like UDP, which makes no guarantees about delivery or order of delivery of packets, or a guaranteed delivery service, like TCP, where correctly ordered delivery of packets is ensured.

The network layer is responsible for routing datagrams across heterogeneous sub-networks from a source address on one sub-network to a destination address on the same or possibly a different sub-network.

The service access point exposed by the inter-network layer is the transport layer service. A common service interface to the inter-network service is defined in the Recommendation for TCONS Inter-networking Service Red Book [RD2].  The Inter-Networking service interfaces with user applications through the TCONS API interface.  The user application must identify the QoS required for the data being transported such that the data can be classified, or “tagged”, before being passed to the intra-network layer, where it is then categorized into a traffic class.   Refer to the QoS Whitepaper [RD4] for details on packet classification and traffic class.

Since protocol multiplexing and QoS services are in the Intra-Networking service, alternate network and transport protocols can cooperatively coexist with IP/NP.  Refer to the TCONS Inter-network Service Interface Definition Red Book [RD2] for more details.

## intra-network layer

The intra-networking layer enables the multiplexing of multiple network protocols with a range of quality of service support over underlying data links.  The main function of the TCONS Intra-Network layer is to provide the Quality of Service function: prioritization of PDUs and resource reservation.  The transmit interface to the Intra-network layer accepts the PDU to be transmitted along with parameters for the protocol, destination address and traffic class.   Together, these parameters supply all the information needed for transporting the PDU across a specific bus/LAN, to its destination, with a given QoS.

The protocol multiplexing function supports the multiplexing and de-multiplexing of the different network protocols over the underlying data link links. Examples of protocols to be supported are IPv4, IPv6, and SCPS TP/NP.  When a PDU is transmitted, its protocol identifier is mapped to its standard form on the underlying bus/sub-network.  If no standard form exists, then a suitable form is defined by the SOIS mapping onto the particular underlying bus/sub-network [RD8, RD9, RD10].

The destination address is a TCONS logical address used by the transmit interface to select the appropriate bus/sub-network and then to derive the appropriate bus/sub-network-specific address for the SDU. For example, the destination address may be a 32-bit number associated with an end-point on a 1553 sub-network.  The intra-network layer uses this association to pass the SDU onto the required 1553 interface. The address translation from destination address to physical address is done in the data link layer.  In the current example it may be the 32-bit address to a 1553 RT/SA translation.

The Traffic Class defines the type of traffic being passed to TCONS and how that traffic will be treated as it passes through a particular sub-network.  The Traffic Class encompasses priority, retry, redundancy, and resource reservation in a single QoS identifier which specifies to TCONS how an SDU is to be handled. There are four principal traffic classes supported by TCONS: Best-Effort, Assured, Reserved, Guaranteed. The SOIS White book on the Quality of Service [RD4] and the TCONS Inter-network Service Interface Definition Red Book [RD2] should be consulted for more details.

Packets that arrive at their destination without error are de-multiplexed and provided to the appropriate protocol receive engine.  Data such as the traffic class, the protocol, the source address, the destination address, and the bus/sub-network type that the PDU was received on may be provided to the layer above if available.

## tcons api

The TCONS application programming interface (API) provides uniform interfaces to the Inter-Network Service, the Intra-Network Service and the Network Management Service.

The aim of the API is to provide compatibility at the software level, so that software written using one type of transport protocol can be used with another transport protocol. The API by its nature is programming language specific. The TCONS API will be written in C to provide an appropriate basis for developing similar APIs in other programming languages.

The TCONS API is a non-normative software interface to TCONS functionality that provides for application portability between implementations.  The API is presented in a C-Semantic but can be implemented in a variety of languages.  The TCONS API is a call back/ event driven interface allowing a direct link between network activity and software execution.

The Red book describing the TCONS API, “Recommendation for TCONS Application Programming Interface” [RD6] should be consulted.

# onboard bus and lan architecture

## data link layer

The data-link layer provides support to the SOIS Intra networking service and network management. It provides the means to communicate over any SOIS bus or sub-network and  provides a consistent interface by implementing functionality required by the TCONS Intra-Networking service interface that is not included by the underlying bus/sub-network. Bus/sub-network specific functions are provided for address translation, PDU encapsulation, resource reservation, fragmentation, retry and redundancy. The Generic Data Link Abstraction is an abstract representation of those functions that must be provided by each individual data-link to be SOIS compliant. It provides a consistent set of configurable parameters for each function across all data-links.

The data link layer will be defined for several buses/networks including SpaceWire, IEEE1394, CAN, 1553 and Ethernet. Not all of these standard buses/networks provide the full set of required data link functionality. The SOIS data link layer provides the missing functionality for each of the buses/networks and provides the consistent set of data-link functionality to the intra-network layer.

The data-link layer sends and receives delimited octet aligned data on a single bus/sub-network.  It provides optional link level services such as: link-level retry, link-level redundancy management, and link-level scheduling.

The Data Link Layer is expanded further in Figure 4-1.

Figure 4-1 OBL Architecture

The Data Link Service Interface provides a common interface to the various underlying buses or networks. For each of the SOIS supported buses or networks, there are two components within the data link: firstly the bus or network standard and secondly a set of SOIS functions that are necessary to provide the SOIS quality of service and communications functions using the particular underlying bus or network. The SOIS data link functions include:

a)  Redundancy

b)  Retry

c)  Fragmentation

d)  Resource Reservation

e)  PDU Encapsulation

f)  Address translation

Each of these functions is described in the following subsections.

## redundancy function

The Redundancy Model adopted by SOIS is that of equivalent data links that provide alternative paths from a source end-point to a destination end-point on a single sub-network. The architecture supports autonomous switching between equivalent data links. Non-autonomous switching of paths can be done by an application specifying the bus/link/path to be used (using different destination addresses) or reconfiguring the TCONS routing table used to select which link is used for a particular address. Applications may control autonomous redundancy and link level retry by using a management parameter associated with the transmit traffic class.  It should be noted that system management policy might uniformly dictate a redundancy policy which applications must use.

Link equivalence requires two independent paths to a destination. These redundant paths may be used in one of three ways:

a)   Sending data over both paths at the same time.

b)  Sending over the prime link and then if there is a failure using the redundant link 	     (Often used for MIL-STD-1553 bus).

c)  Sending over either link, then if failure of one link all traffic goes over the 	  	     remaining link.

The link redundancy function is bus/sub-network specific.  The SOIS documentation associated with the specific Bus should be consulted [RD8, RD9, RD10].

## retry function

The Link level Retry function provides a mechanism for resending PDUs that are incorrectly received at the other end of the data link. When the source sends a PDU, it starts a timer. When the PDU arrives at the destination, an acknowledgement is returned to the source. If the source does not receive the acknowledgement before the timer times-out, the PDU is assumed not to have arrived at the destination and the source resends the PDU.  Consideration should be given to any QoS parameters when setting the time-out and retry values, i.e. packets that have bounded latency requirements.  If multiple copies of the same PDU arrive at the destination, i.e. the first PDU arrived after the initial time-out, any duplicates are discarded.

## fragmentation function

Fragmentation is needed if the underlying bus/sub-network cannot support the maximum Intra-Network PDU size in a single packet on the bus/sub-network. It is the data link’s responsibility to fragment the PDUs if necessary and to reassemble them at the other end of the data link to reform the original PDUs before they are passed up to the inter-network layer.

## The Fragmentation function is bus/sub-network specific. The SOIS documentation associated with the specific Bus should be consulted.

## REsource Reservation function

## Resource Reservation allocates data-link resources to specific traffic classes.

## The Resource Reservation function provides support for the four TCONS traffic classes:

The Best Effort traffic class provides for non-reserved, try once communication. It makes no promises about the time of delivery, the network bandwidth available or the error rate of the traffic. Several priority levels are provided for Best Effort traffic. Traffic with a higher priority level is treated preferentially compared to traffic with a lower priority level.

The Assured traffic class provides for non-reserved communication with retries. It tries to ensure that the traffic arrives at the intended destination. If the data does not arrive safely at the destination then it is resent. To support this, the destination acknowledges the receipt of Assured traffic.  Several priority levels are provided for Assured traffic, which are the same levels as those for Best Effort traffic.

The Reserved traffic class provides for best-effort communication over a resource reserved logical link. It is able to ensure the time of delivery and the network bandwidth available, but makes no promises about the error rate of the traffic. Traffic may be lost but if it does arrive at the destination it will do so in a timely manner.

The Guaranteed traffic class provides for resource reserved communications with retries. It is able to ensure the time of delivery, the network bandwidth available, and tries to ensure that the traffic arrives at the intended destination without error.

Any combination or indeed all of these traffic classes may be used in the same SOIS system.

The Resource Reservation function is bus/sub-network specific.  The SOIS documentation associated with the specific Bus should be consulted for details [RD7, RD8, RD9].

## PDU Encapsulation

## The PDU encapsulation function encapsulates (and decapsulates) the SDU and associated parameters into a specific data-link PDU. It may take advantage of fields in the underlying data-link PDU to improve efficiency of SDU encapsulation.

## address resolution function

The address resolution function maps the TCONS logical address to the data-link specific address.

The Address translation function is bus/sub-network specific. The SOIS documentation associated with the specific Bus should be consulted [RD8, RD9, RD10].

# network management

Network management configures and monitors the Inter-Network, Intra-Network and Data-Link layers.  Specifically, the network manager configures all links and provides operational statistics and status for those links.  The network manager configures the Quality of Service function, routing and address translation tables, and monitors for fault conditions and violations of quality of service rules.

The Network Manager is an application with a user interface provided via the SOIS API. Network Management Agents are present on all SOIS units to provide local network management services.

The Red book describing the TCONS API, “Recommendation for TCONS Network Management Service” [RD7] should be consulted.

# Comments

I guess by its name, TCOAS means Time Critical, but I’m wondering if ALL the apps will use the TCONS route, i.e. File service (CFDP is not time-critical)

This is confusing. Please clarify

I think this text could use some work.  I think the current idea is all OBL’s are “route through” since the source/dest logical addresses are known at the sender & receiver.

Address translation involves translating the logical addresses into bus-specific physical addresses and vice versa.  Since the logical addresses are 32 bit ints, they could well be IP addresses from the IP protocol layer.  However this is more a question of how IP stacks are mapped onto TCONS than of address translation itself.  An alternative IP stack mapping onto TCONS could just as easily use a secondary table that translates logical addresses to fake Ethernet addresses that are used to make TCONS look like an Ethernet driver.  (GDM)