DRAFT RECOMMENDATION FOR SPACE

DATA SYSTEM STANDARDS

Spacecraft Onboard Interface Services Intra-Network Service

CCSDS xxx.x-R-1.0

DRAFT RED BOOK

September 2005

AUTHORITY

|  | Issue: | Draft Red Book, Issue 1.0 |  |
| --- | --- | --- | --- |
|  | Date: | September 2005 |  |
|  | Location: | N/A |  |

(WHEN THIS RECOMMENDATION IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF AUTHORITY :)

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and reflects the consensus of technical panel experts from CCSDS Member Agencies.  The procedure for review and authorization of CCSDS Reports is detailed in reference [2].

This document is published and maintained by:

CCSDS Secretariat

Program Integration Division (Code MT)

National Aeronautics and Space Administration

Washington, DC 20546 USA

STATEMENT OF INTENT

The Consultative Committee for Space Data Systems (CCSDS) is an organization officially established by the management of member space Agencies. The Committee meets periodically to address data systems problems that are common to all participants, and to formulate sound technical solutions to these problems. Inasmuch as participation in the CCSDS is completely voluntary, the results of Committee actions are termed Recommendations and are not considered binding on any Agency.

This Recommendation is issued by, and represents the consensus of, the CCSDS Plenary body. Agency endorsement of this Recommendation is entirely voluntary. Endorsement, however, indicates the following understandings:

- Whenever an Agency establishes a CCSDS-related standard, this standard will be in accord with the relevant Recommendation. Establishing such a standard does not preclude other provisions which an Agency may develop.

- Whenever an Agency establishes a CCSDS-related standard, the Agency will provide other CCSDS member Agencies with the following information:

  - The standard itself.

  - The anticipated date of initial operational capability.

  - The anticipated duration of operational service.

- Specific service arrangements are made via memoranda of agreement. Neither this Recommendation nor any ensuing standard is a substitute for a memorandum of agreement.

No later than five years from its date of issuance, this Recommendation will be reviewed by the CCSDS to determine whether it should: (1) remain in effect without change; (2) be changed to reflect the impact of new technologies, new requirements, or new directions; or, (3) be retired or cancelled.

In those instances when a new version of a Recommendation is issued, existing CCSDS-related Agency standards and implementations are not negated or deemed to be non-CCSDS compatible. It is the responsibility of each Agency to determine when such standards or implementations are to be modified. Each Agency is, however, strongly encouraged to direct planning for its new standards and implementations towards the later version of the Recommendation.

FOREWORD

(WHEN THIS RECOMMENDATION IS FINALIZED, IT WILL CONTAIN THE

FOLLOWING FOREWORD)

This document is a technical Recommendation for use in developing flight and ground systems for space missions and has been prepared by the Consultative Committee for Space Data Systems (CCSDS). The Time Critical Onboard Network Services (TCONS) Intra-Network described herein is intended for missions that are cross-supported between Agencies of the CCSDS, in the framework of the Spacecraft Onboard Interface Services (SOIS) CCSDS area.

This Recommendation specifies a set of related services to be used by space missions to transfer space application data over an onboard network. The SOIS Intra-Network Service provides time critical communications over a single sub-network onboard a spacecraft. It can support various transport and network protocols like TCP/IP and can directly support applications that only need to use a single sub-network. The SOIS Intra-Network Service  provides quality of service functions for  any user application and also provides a common interface to software using the SOIS Intra-Network services regardless of the particular type of data-link being used for communication. The aim is to increase reuse of software components onboard a spacecraft while at the same time allowing appropriate choice of communications hardware. The specified services may be implemented in a number of different ways but will support interoperability for time critical onboard applications. The SOIS Intra-Network Service will provide services to the Time Critical Onboard Applications (TCOA) layer above, to various Transport and Network Protocols including CCSDS SCPS TP/NP, and/or to user applications.

Through the process of normal evolution, it is expected that expansion, deletion, or modification to this Report may occur. This Report is therefore subject to CCSDS document management and change control procedures, which are defined in reference [3].  Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this report should be addressed to the CCSDS Secretariat at the address on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- British National Space Centre (BNSC)/United Kingdom.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- Deutsches Zentrum für Luft- und Raumfahrt e.V.  (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- National Aeronautics and Space Administration (NASA)/USA.

- National Space Development Agency of Japan (NASDA)/Japan.

- Russian Space Agency (RSA)/Russian Federation.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- Centro Tecnico Aeroespacial (CTA)/Brazil.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- Communications Research Centre (CRC)/Canada.

- Communications Research Laboratory (CRL)/Japan.

- Danish Space Research Institute (DSRI)/Denmark.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Federal Service of Scientific, Technical & Cultural Affairs (FSST&CA)/Belgium.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space and Astronautical Science (ISAS)/Japan.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- MIKOMTEK:  CSIR (CSIR)/Republic of South Africa.

- Korea Aerospace Research Institute (KARI)/Korea.

- Ministry of Communications (MOC)/Israel.

- National Oceanic & Atmospheric Administration (NOAA)/USA.

- National Space Program Office (NSPO)/Taipei.

- Swedish Space Corporation (SSC)/Sweden.

- United States Geological Survey (USGS)/USA.

PREFACE

This document is a draft CCSDS Recommendation. Its Red Book status indicates that the CCSDS believes the document to be technically mature and has released it for formal review by appropriate technical organizations. As such, its technical contents are not stable, and several iterations of it may occur in response to comments received during the review process.

Implementers are cautioned not to fabricate any final equipment in accordance with this document’s technical content.

DOCUMENT CONTROL

| Document | Title | Date | Status |
| --- | --- | --- | --- |
| CCSDS xxx.x-RD-0.1 | Time Critical Onboard Network Services (TCONS) Intra-Network | April 2005 | Athens Rough outline of document, based on previous TCONS draft red book |
| CCSDS xxx.x-RD-0.4 | Time Critical Onboard Network Services (TCONS) Intra-Network Service | September 2005 | Atlanta Appropriate service interfaces and parameters added to document, but still very rough |
| CCSDS xxx.x-RD-0.5 | Time Critical Onboard Network Services (TCONS) Intra-Network Service | September 2005 | Kirriemuir Document updated to reflect the technical agreement in Atlanta. Full editorial revision of document. |

CONTENTS

Section	Page

1	INTRODUCTION	1-7

1.1	purpose and scope of this document	1-7

1.2	APPLICABILITY	1-7

1.3	RATIONALE	1-7

1.4	DOCUMENT STRUCTURE	1-7

1.5	Conventions and Definitions	1-8

1.5.1	Bit numbering convention and nomenclature	1-8

1.5.2	DEFINITIONS	1-8

1.6	how this document fits into the SOIS documentation Tree	1-9

1.6.1	DOCUMENT NOMENCLATURE	1-10

1.7	REFERENCES	1-10

2	OVERVIEW	2-12

2.1	Context	2-12

2.2	Assumptions	2-13

3	INTRA-NETWORK Service	3-14

3.1	Overview	3-14

3.2	Service Parameters	3-15

3.3	best-Effort Data Delivery Service	3-17

3.3.1	best-Effort Service Overview	3-17

3.3.2	Best-Effort Service Primitives	3-17

3.4	ASSURED Data Delivery Service	3-19

3.4.1	ASSURED Service Overview	3-19

3.4.2	ASSURED Service Primitives	3-19

3.5	Reserved Data Delivery Service	3-22

3.5.1	Reserved Service Overview	3-22

3.5.2	Reserved Service Primitives	3-23

3.6	Guaranteed DATA Delivery Service	3-24

3.6.1	Guaranteed Service Overview	3-24

3.6.2	Guaranteed Service Primitives	3-25

Table of Figures

Figure 2-1:  Intra-Network Context	2-13

# INTRODUCTION

## purpose and scope of this document

The purpose of this document is to define services and service interfaces provided by the Spacecraft Onboard Interface Services (SOIS) Intra-Network to the above Network layer and/or user applications [RD6, RD7].

## APPLICABILITY

This document is a draft for agency review and should not be used as the basis for non-experimental systems.

## RATIONALE

The CCSDS believes it is important to document the rationale underlying the recommendations chosen, so that future evaluations of proposed changes or improvements will not lose sight of previous decisions.

There is need for CCSDS to provide recommendations for Spacecraft Onboard Interface Services. Today many different buses are used on Spacecraft requiring software with the same basic functionality to be rewritten for each type of bus. This then impacts on the application software resulting in custom software for almost every new mission. The Spacecraft Onboard Interface Services (SOIS) working group aims to provide a consistent interface to various onboard buses and sub-networks, enabling a common interface to the application software. The eventual goal is reusable software that can be easily ported to new missions and run on a range of onboard buses without substantial modification. The system engineer will then be able to select a bus based on its performance, power, etc and be confident that a particular choice of bus will not place excessive demands on software development.

## DOCUMENT STRUCTURE

This document is derived from the TCONS/OBL Architecture Red Book [RD6] and the Quality of Service White Book [RD7], which together describe the technical approach taken for the SOIS Intra-Network Service. The present document details the service interfaces.

The document has three major sections:

- This section, containing administrative information, definitions and references;

- Section 2, describing general concepts and assumptions;

- Section 3, containing the TCONS Intra-Network service specification.

## Conventions and Definitions

### Bit numbering convention and nomenclature

In accordance with modern data communications practice, spacecraft data fields are often grouped into 8-bit ‘words’ widely known as bytes. Throughout this Recommendation, such an eight-bit word is called an ‘octet’. The numbering for octets within a data structure starts with zero.

By CCSDS convention, any ‘spare’ bits shall be permanently set to ‘0’.

### DEFINITIONS

Within the context of this document the following definitions apply:

#### Definitions from the Open Systems Interconnection (OSI) Basic Reference Model

The TCONS Intra-Network Layer is defined using the style established by the Open Systems Interconnection (OSI) Basic Reference Model [2].  This model provides a common framework for the development of standards in the field of systems interconnection.

The following terms, used in this Report, are adapted from definitions given in [3]:

Layer: A subdivision of the architecture, constituted by subsystems of the same rank

Protocol data unit (PDU): a unit of data specified in a protocol and consisting of protocol-control-information and possibly user data.

Service: A capability of a layer (service provider) together with the layers beneath it, which is provided to the service-users.

Service data unit (SDU): An amount of information whose identity is preserved when transferred between peer entities in a given layer and which is not interpreted by the supporting entities in that layer.

#### Terms Defined in this Recommendation

For the purposes of this Recommendation, the following definitions also apply. Many other terms that pertain to specific items are defined in the appropriate sections.

Channel: An identifier for network resources associated with a resource reservation.  May be a list of time slots in a time division multiplexed system or a bandwidth limit in a bandwidth division multiplexed system. The network resources required for the communication may also be defined to allow simultaneous use of non-conflicting resources on networks that support this feature.

Delimited: Having a known (and finite) length; applies to data in the context of data handling.

Epoch: The repeat cycle time for  the Slot identifiers.

Fragmentation: The division of Network protocol data units (datagrams) by the sending data link into smaller sections (fragments) that are short enough to be sent over the data link. The receiving data link is responsible for reassembling the fragments back into link protocol data units (datagrams) when returning to the OBL. This may be considered by some to be data-link segmentation. The name “fragmentation” is used to clearly distinguish this from segmentation in a transport layer.

Maximum Data Unit: The maximum size of data that the user can give to the Intra-Network Service. Note that the MDU is required to ensure that different sources of data get fair access to the transmission medium, by multiplexing traffic on a packet by packet basis. When a large data unit is being sent, other sources can get a look in after each segment of the large data unit has been sent.

Octet: An 8-bit word commonly referred to as a byte.

Packet: Delimited octet aligned data unit.

Priority: Identifies the transmit precedence of an SDU relative to other SDUs.

QoS: See Quality of Service.

Quality of Service: The level of service that is requested / provided.

Slot: The smallest unit of time division in SOIS network.

SOIS Intra-Network Layer Service Data Unit: The user data provided to SOIS Intra-Network Layer for sending over the data-link/sub-network using one of the SOIS Intra-Network Layer services.

SDU: Service Data Unit.

Service Access Point (SAP): Identifies a SOIS Intra-Network service user entity. It is composed of the Source Address or Destination Address and the Protocol ID.

User Data: The user data, or higher-layer protocol data unit, that is being sent in the PDU.

## how this document fits into the SOIS documentation Tree

The SOIS documentation tree has an overall document [RD5] that describes the concepts and rationale for Spacecraft Onboard Interfaces and Services (SOIS).  Below this document are a set of documents that provide descriptions and requirements for each of the different areas within the scope of the SOIS work.

SOIS is composed by the following service layers:

- Time Critical Onboard Application Services

- Transport and Network Layer Services

- Time Critical Onboard Intra-Network Services

This CCSDS document provides recommendations for the SOIS Intra-Network Services, which provides time-critical services across data-links and sub-networks onboard a spacecraft. A consistent QoS for the different data-links and sub-networks is provided to the user application.

For an architectural overview of the Time Critical Onboard Intra-Network Services please refer to RD 6. To understand the QoS approach refer to RD 7.

### DOCUMENT NOMENCLATURE

The following conventions apply throughout this Recommendation:

- a) The words ‘shall’ and ‘must’ imply a binding and verifiable specification;

- b) The word ‘should’ implies an optional, but desirable, specification;

- c) The word ‘may’ implies an optional specification;

- d) The words ‘is’, ‘are’, and ‘will’ imply statements of fact.

## REFERENCES

The following documents contain provisions which, through reference in this text, constitute provisions of this Recommendation. At the time of publication, the editions indicated were valid. All documents are subject to revision, and users of this Recommendation are encouraged to investigate the possibility of applying the most recent editions of the documents indicated below. The CCSDS Secretariat maintains a register of currently valid CCSDS Recommendations.

[1] Spacecraft Onboard Interfaces Concepts and Rationale Green Book, CCSDS, CCSDS-830.0-G-0.4, Green Book, Issue TBD, Washington D.C., CCSDS, September 2003

[2] Information Technology.Open Systems Interconnection.Basic Reference Model: The Basic Model. International Standard, ISO/IEC 7498-1. 2nd ed. Geneva: ISO, 1994.

[3] Information Technology.Open Systems Interconnection.Basic Reference Model.Conventions for the Definition of OSI Services. International Standard, ISO/IEC 10731:1994. Geneva: ISO, 1994.

[4] Space Link Identifiers, CCSDS 135.0-B-1, (Future Issue)

[5] SOIS Concept and Rationale,  CCSDS nnn.n-G-x.  Issue x.  CCSDS, month year.

[6] Recommendation for Time-Critical Onboard Network Services (TCONS) and Onboard Bus/LAN (OBL) Architecture, CCSDS nnn.n-R-1.1.  Issue x.  CCSDS, September, 2005.

[7] Time Critical Onboard Networking Services Quality of Service White Paper, CCSDS nnn.n-?-x.  Issue x.  CCSDS, month year

[8] Recommendation for Onboard Sub-Network Generic Interface Specification, CCSDS nnn.n-R-x.  Issue x.  CCSDS, month year

[9] Recommendation for TCONS Application Programming Interface, CCSDS nnn.n-R-x.  Issue x.  CCSDS, month year

[10] Recommendation for TCONS Network Management Service, CCSDS nnn.n-R-x.  Issue x.  CCSDS, month year

[11] Recommendation for TCONS over SpaceWire, CCSDS nnn.n-R-x.  Issue x.  CCSDS, month year

[12] Recommendation for TCONS over Ethernet, CCSDS nnn.n-R-x.  Issue x.  CCSDS, month year

[13] Recommendation for TCONS over Mil-Std 1553, CCSDS nnn.n-R-x.  Issue x.  CCSDS, month year

# OVERVIEW

The Intra-networking Service is designed to enable multiplexing of a variety of internetworking protocols with a range of quality of service support over underlying data links.   The Intra-network service interface provides TCOAS and other users a common Quality of Service interface when transporting data across a variety of underlying data links.

## Context

The Intra-network layer provides Quality of Service functions to a variety of user applications, such as Time Critical Onboard Application Service (TCOAS), Space Internet Services (SIS), and others, for transporting data over a single sub-network onboard a single spacecraft.  Quality of Service elements supported by the Intra-network layer include:

- Priority

- Resource Reservation

- Retry/Redundancy

These three QoS elements map into four TCONS Quality of service traffic services for onboard data communications:

- Best Effort

- Assured

- Reserved

- Guaranteed

Data to be transported is passed to the Intra-network service via the Intra-network service interface with a requested QoS. The requested QoS is referred to as a traffic class which includes the type of service (Best-Effort, Assured, Reserved or Guaranteed), priority and where appropriate a channel identifier.  As shown in Figure 2-1, the data is de-multiplexed, prioritized, and the required resources for transport are allocated.  The data is then passed to the appropriate data link for transfer across the bus.  The SOIS supported data links may inherently provide the quality of service support requested by the intra-network layer.  In the case where the data link does not have the required level of support, the missing function is added by SOIS.   See the SOIS mapping documents for details of the functionality provided by SOIS for several different data links [RD 11, 12, 13].

Figure 2-1 shows the context of the Intra-Network Service. The Intra-Network Service provides Protocol Multiplexing and Quality of Service functions to support the applications using this service. Applications wishing to use the SOIS Intra-Network Service do so via that Intra-Network Service Interface which provides four distinct services: Best-Effort, Assured, Reserved and Guaranteed. A Network Management Service Interface is also provided to access the Network Management Services which are responsible for configuring, managing and collecting status information from the Intra-Network Services. The Intra-Network Service makes use of the Data Link to transfer data and control information.  Applications that may use the Intra-Network Service include the Time-Critical Onboard Network Services (TCONS), Space Internet Services (SIS), or other CCSDS transport and network protocols, the Time-Critical Onboard Applications Services (TCOAS) and user applications that wish to use the Intra-Network Services directly.

Figure 2-1:  Intra-Network Context

## Assumptions

The following assumptions have been made in designing the SOSI Intra-Network Services:

- Time critical behaviour implies operation over a single sub-network, i.e. time-critical operations take place in the Intra-Network layer. Inter-Network services are not normally time-critical.

- SOIS Intra-network services are provided across single sub-networks.

- SOIS Intra-network services are made available to protocol entities in the network and application layers.

# INTRA-NETWORK Service

In this section the SOIS Intra-Network Service is defined. The SOIS Intra-Network is a subdivision of the Network layer and provides sub-network independent convergence functionality.

First an overview of the SOIS Intra-Network Layer is given in section 3.1. The service parameters are introduced in section 3.2. The four services provided by SOIS Intra-Network Layer are then described in sections 3.3, 3.4, 3.5 and 3.6. Each of these four sections contains sub-sections providing:

- an overview of the service,

- a definition of the service primitives.

## Overview

The SOIS Intra-Network Service transfers packets of information from one end-point on a data-link/sub-network to another end-point on the same data-link/sub-network, using the SOIS data-link functions to move the information across the data-link/sub-network.

There are four communication services provided by the SOIS Intra-Network Layer:

- Best-Effort Service (Differentiated, Non-reliable)

  - Makes a single attempt to deliver data to its destination but cannot ensure that it will be delivered successfully.

  - Data is provided without errors and without duplication.

  - The order of data packets is not necessarily preserved.

  - A priority parameter is used to signal the importance of the data to the service.  This priority is common with the Assured Service priority parameter.

- Assured Service (Differentiated, Reliable)

  - Ensures delivery of data to its destination.

  - Should it not be possible to provide the assured service this is indicated to the sending entity i.e. if it is not possible to deliver data the user is informed.

  - Data is provided in sequence, complete, without errors and without duplication.

  - A priority parameter is used to signal the importance of the data to the service.  This priority parameter is common with the Best-Effort Service priority parameter.

- Reserved  Service (Differentiated, Non-Reliable, Reserved)

  - Makes a single attempt to deliver data to its destination but cannot ensure that it will be delivered successfully.

  - Data is provided in-sequence, without errors and without duplication.

  - A Channel defines the resources that are used to transmit the SDU.

  - A priority parameter is used to signal the importance of the data to the service.  This priority defines the priority of a communication within the resource reservation i.e. within a Channel.

- Guaranteed Service (Differentiated, Reliable, Reserved)

  - Ensures delivery of data to its destination.

  - Should it not be possible to provide the guaranteed service this is indicated to the sending entity i.e. the user is informed if it is not possible to deliver the data.

  - Data is provided in sequence, complete, without errors and without duplication.

  - A Channel defines the resources that are used to transmit the SDU.

  - A priority parameter is used to signal the importance of the data to the service.  This priority defines the priority of a communication within the resource reservation i.e. within a Channel.

- Features common to all TCONS services

  - SDUs extracted from PDUs containing errors will not be delivered.

  - Incompleteness of data will be signalled to the receiver whenever possible.

  - Individual Service Data Units being sent cannot be larger than the MDU.

## Service Parameters

The Service Parameters are listed in brackets following the name of the particular service.

For example:

INTRA_BE_SEND.request (Source, Destination, Protocol ID, Priority)

INTRA_BE is the name of the service.

SEND.request is the name of the primitive.

(Source Addr, Destination Addr, Protocol ID, Priority) are the parameters.

The parameters used in the Intra-Network Service are defined below:

Data

The Data parameter is the Service Data Unit (SDU) of the SOIS Intra-Network (SOIS-INTRA) service.

Source Address

The Source Address defines the data system which is the originator of the SDU. The Source Address is a logical address which may be global to a spacecraft or local to the sub-network. Reserved Source Address values are controlled by RD 4.

Destination Address

The Destination Address defines the data system which is the recipient of the SDU. The Destination Address is a logical address which may be global to a spacecraft or local to the sub-network. Reserved Destination Address values are controlled by RD 4.

Protocol ID

The Protocol ID defines the protocol entity which is the user of the SOIS Intra-Network service and which is the originator or consumer of the SOIS Intra-Network service primitives. Reserved Protocol ID values are controlled by RD 4.

Note that the Source Address and Protocol ID, taken together, constitute the address of the SOIS Intra-Network Source Service Access Point (SOIS-INTRA-SSAP) and that the Destination and Protocol ID, taken together, constitute the address of the SOIS Intra-Network Destination Service Access Point (SOIS-INTRA-DSAP)

Channel (Used for reserved or guaranteed services only)

A Channel fully specifies an end to end resource reservation for a network communication.  For Time division multiplexed (scheduled) systems, the Channel identifies a list of time slots that may be used to support transmission of the channel data.  For systems based on bandwidth reservation, the Channel identifies the percentage of network resources that may be used to support the transmission. The time-slot allocation or bandwidth reservation for each channel is defined by management parameters. This definition is referenced by the Channel number.

Priority

Priority indicates the importance of the data to the system.  Lower numbers indicate higher priority.  The Best Effort and Assured services share 16 priority levels, i.e. Best Effort priority 1 is identical to Assured Priority 1.  For resource reserved channels the specified priority allows packets within a channel to be prioritized.

Failure Metadata

Failure Metadata is information generated by the Intra-Network service provider to the sending entity to provide information related to a failure of service provision.

## best-Effort Data Delivery Service

In this section, the Best-Effort service is defined. First an overview of this service is provided, and then the service primitives are presented.

### best-Effort Service Overview

The Best-Effort data delivery service can send data from one End System to another End System on the same sub-network. An End System is a system using the SOIS Intra-Network services e.g. an application running on a processor which has the SOIS Intra-Network services installed. The Best-Effort service does not have to establish a connection between End Systems before sending data. The service offered cannot ensure delivery of information to a destination End System. The service provided is on a best effort basis, hence its name. Data that goes missing or is corrupted during its transfer across the sub-network will be lost and the source End System will not be informed that the data has been lost.

The Best-Effort service supports priority. When a packet is passed to the SOIS Intra-Network service for sending, it is assigned a priority level by the user. High priority packets are sent and forwarded before lower priority ones.

The maximum amount of data that can be sent in one packet is limited to the MDU. This is the maximum amount of data that can be passed in one go to the Best-Effort service.

Packets of data that are sent can arrive at the destination in a different order to that in which they were sent: the packet sequence may not be maintained across the sub-network.

An End System (i.e. Transport/Network Protocol, TCOAS service or user application) that wishes to receive data has to register (bind) with the Best-Effort service. This allows the End System to provide receive buffers for the information to be placed in, potentially enhancing the performance of the receiving process.

The Best-Effort service has the following features:

- Send a packet

- Receive a packet

- Maximum size of user data in a Best-Effort SDU is specified by the MDU

- No need to set up a connection before sending and receiving data

- Priority packet support

- Delivery is not ensured

- No order preservation

- Statistics maintained about errors and undelivered data.

### Best-Effort Service Primitives

In this section the service primitives for the Best-Effort service are presented.

There are two primitives used by this service:

- Send Request which requests to send an SDU,

- Receive Indication which indicates that a packet has been received and which passes the corresponding SDU to the End System.

#### Send Request

Function

The Send Data.request primitive requests the Best-Effort service to send a SDU to a destination protocol entity, which is a user of the Best-Effort service. The SDU is assigned a priority level which determines the urgency with which it will be sent and forwarded through the onboard sub-network.

Semantics

INTRA_BE_SEND.request (Source, Destination, Protocol ID, Data, Priority)

When Generated

The SEND.request primitive shall be passed to the SOIS Intra-Network Best Effort service provider to request that the Data be sent.

Effect on Receipt

Receipt of the SEND.request primitive shall cause the SOIS Intra-Network Best Effort service provider to encapsulate the SDU and to issue a PDU over the underlying data-link/sub-network.

Additional Comments

Destination is the address of the node to where the data is directed.

Source is the address of the node that sent the data.

Protocol ID identifies the protocol entity which is the user of the Best-Effort service.

Data is the information to be sent from the Source to the Destination protocol entity.

Priority indicates the level of precedence that should be given to the data compared to other SDUs being serviced or other PDUs on the sub-network.

#### Receive Indication

Function

The Receive Indication is used to pass the contents of a received Best-Effort Service PDU to the user protocol entity.

Semantics

INTRA_BE_RECEIVE.indication (Source, Destination, Protocol ID, Data)

When Generated

This primitive is issued by the service provider to the receiving application on receipt of a DATA PDU. The corresponding SDU is placed in a queue for access by the protocol identified by the Protocol ID.

Effect on Receipt

The response of the End System to a RECEIVE.indication primitive is for the data received to be read by the End System. It is then up to the End System what it does with this data.

Additional Comments

Destination is the address of the node where the data has been received.

Source is the address of the node that sent the data.

Protocol ID identifies the protocol entity which is the user of the Best Effort service.

Data is the data received by the Best-Effort service entity and directed to the specified protocol entity (End System).

## ASSURED Data Delivery Service

In this section, the assured service is defined. First an overview of this service is provided, and then the service primitives are presented.

### ASSURED Service Overview

The Assured data delivery service sends data from one End System to another End System on the same sub-network and ensures that the data arrives intact and in the same order in which it was sent.

The maximum amount of data that can be sent in one packet is limited to the Maximum Data Unit (MDU). This is the maximum amount of data that can be passed to the Assured service in one SDU.

The Assured service has the following features:

- Maximum SDU size is determined by the Maximum Data Unit (MDU) management parameter

- SDU priority supported

- Delivery ensured through retry and redundancy mechanisms

- Statistics maintained about errors and undelivered data.

### ASSURED Service Primitives

In this section the service primitives for the Assured service are presented.

There are three primitives used by this service:

- Send Request which requests to send a packet of data across a data-link/sub-network.

- Receive Indication which indicates that a packet has been received on the data-link/sub-network and is ready for the user of the Assured service to read.

- Failure Indication, which indicates that the retry limit for the sending process has been reached.

#### Send Request

Function

The Send Request primitive is used by an application to send data over the data-link/sub-network.

Semantics

INTRA_ASSURED_SEND.request (Source, Destination, Protocol ID, Priority, Data)

When Generated

The SEND.request primitive shall be passed to the Assured service provider to request that the Data be sent.

Effect on Receipt

Receipt of the SEND.request primitive shall cause the Assured service provider to issue a DATA PDU containing the data passed with the send request and addressed with the sub-network address of the destination.

Additional Comments

Destination is the address of the node to where the data is directed.

Source is the address of the node that is sending the data.

Protocol ID identifies the protocol entity which is the user of the Assured service

Data is the data to be sent from the Source to the Destination protocol entity.

Priority indicates the level of precedence that should be given to the data compared to other SDUs being serviced or other PDUs on the sub-network.

#### Receive Indication

Function

The Receive Indication is used to pass the contents of a received Assured service PDU to the user protocol entity.

Semantics

INTRA_ASSURED_RECEIVE.indication (Source, Destination, Protocol ID, Data)

When Generated

This primitive is issued by the Assured service provider to the SOIS Intra-Network Assured service user on receipt of a Data PDU. The corresponding SDU is made available to the protocol identified by the Protocol ID.

Effect on Receipt

The effect of receipt of the INTRA-ASSURED_RECEIVE.indication primitive is that the service user reads the data, informing the Assured service when the data has been read. It is up to the user of the Assured service what it does with the data once it has been read.

Additional Comments

Destination is the address of the node where the data has been received.

Source is the address of the node that sent the data.

Protocol ID identifies the protocol entity which is the user of the SOIS Intra-Network Assured service.

Data is the data received by the Assured service entity and directed to the receiving SOIS Intra-Network Assured service user protocol entity.

#### Failure Indication

Function

The Retry Failure Indication is used to indicate, to the application that requested to send data,  that it has been impossible to send and confirm delivery of a Data PDU after a maximum number of retries.

Semantics

INTRA_ASSURED_ FAILURE.Indication (Source, Destination, Failure Metadata)

When Generated

This primitive is issued by the Assured service provider to the service user when the retry limit for a PDU has been exceeded. Note that the retry limit is a managed parameter; see RD 6 and RD 10.

Effect on Receipt

The effect of receipt of the INTRA-ASSURED_FAILURE.Indication primitive is undefined, i.e. it is up to the user of the Assured service what it does when it gets a failure indication.

Additional Comments

Destination is the address of the node where the data was to be sent.

Source is the address of the node that sent the data.

Failure Metadata contains information about the type of error that occurred resulting in the failure to send and confirm delivery of the Data PDU to the specified destination.

## Reserved Data Delivery Service

In this section, the Reserved service is defined. First an overview of this service is provided, and then the service primitives are presented.

### Reserved Service Overview

The Reserved data delivery service sends data from one End System to another End System on the same sub-network using reserved resources. An End System is a system using the SOIS Intra-Network services e.g. an application running on a processor which has the SOIS Intra-Network services installed. The Reserved service assumes that the reserved resources that it wants to use have been set up by the Network Management service. The reserved resources are identified by a channel number. The Reserved service can only use pre-defined channels for communication. It cannot open new channels. The Reserved service does not ensure delivery of information to a destination End System, but it does reserve communication resources to support the communication. Data that goes missing or is corrupted during its transfer across the network will be lost and the source End System will not be informed that the data has been lost.

The Reserved service supports priority within a resource-reserved channel. When a packet is passed to the Reserved service for sending it is assigned a priority level and channel number by the user. High priority packets are sent and forwarded before lower priority ones.  All packets are sent using the sub-network resources specified by the channel number. The resources are allocated for each channel by the Network Management service [RD 10] and must be set up before the channel is used to send data.

The maximum amount of data that can be sent in one packet is limited to the MDU. This is the maximum amount of data that can be passed in one go to the Reserved service.

Packets of data that are sent can arrive at the destination in a different order to that in which they were sent: the packet sequence may not be maintained across the network.

An End System (i.e. Transport/Network Protocol, TCOAS service or user application) that wishes to receive data has to register (bind) with the Reserved service. This allows the End System to provide receive buffers for the information to be placed in, potentially enhancing the performance of the receiving process.

The Reserved service has the following features:

- Maximum size of user data in a Reserved SDU is specified by the MDU

- Channel reserving sub-network resources must be set up before sending and receiving data

- SDU priority supported within each channel

- Delivery is not ensured

- No order preservation

- Statistics maintained about errors and undelivered data.

### Reserved Service Primitives

In this section the service primitives for the Reserved service are presented.

There are two primitives used by this service:

- Send Request which requests to send an SDU through a pre-arranged channel, from a source End System to a destination End System on the same sub-network,

- Receive Indication which indicates that a PDU has been received and which passes the corresponding SDU to the End System.

#### Send Request

Function

The Send Data.request primitive requests the Reserved service to send a SDU using a specific channel to a destination protocol entity, which is a user of the Reserved service. The channel references a set of reserved resources forming a path from the source to the destination. Resources are allocated to a channel by the Network Management service [RD 10]. The SDU is assigned a priority level which determines the urgency with which it will be sent and forwarded through the onboard sub-network. The priority applies only within the channel that is being used to send the data. Since resources are reserved the SDU does not have to compete with SDUs in other channels.

Semantics

INTRA_RESERVED_SEND.request (Source, Destination, Protocol ID, Data, Priority, Channel)

When Generated

The SEND.request primitive is passed to the Reserved service provider to request that the Data be sent to the specified destination using the specified channel and priority.

Effect on Receipt

Receipt of the SEND.request primitive shall cause the SOIS Intra-Network Reserved service provider to encapsulate the SDU and to issue a corresponding PDU over the underlying data-link/sub-network.

Additional Comments

Destination is the address of the node to where the data is directed.

Source is the address of the node that sent the data.

Protocol ID identifies the protocol entity which is the user of the Reserved service

Data is the data to be sent from the Source to the Destination protocol entity.

Priority indicates the level of precedence that should be given to the data compared to other SDUs being serviced or other PDUs in the same channel on the sub-network.

Channel is the identifier of the set of reserved resources that are to be used to send the data.

#### Receive Indication

Function

The Receive Indication is used to pass the contents of a received Reserved Service PDU to the user protocol entity.

Semantics

INTRA_RESERVED_RECEIVE.indication (Source, Destination, Protocol ID, Data)

When Generated

This primitive is issued by the service provider to the receiving application on receipt of a DATA PDU. The corresponding SDU is made available to the user protocol entity identified by the Protocol ID.

Effect on Receipt

The response of the End System to a RECEIVE.indication primitive is for the data received to be read by the protocol identified by the Protocol ID. It is then up to the End System what it does with this data.

Additional Comments

Destination is the address of the node where the data has been received.

Source is the address of the node that sent the data.

Protocol ID identifies the protocol entity which is the user of the Reserved service.

Data is the data received by the Reserved service entity and directed to the specified protocol entity (End System).

## Guaranteed DATA Delivery Service

In this section, the Guaranteed service is defined. First an overview of this service is provided, and then the service primitives are presented.

### Guaranteed Service Overview

The Guaranteed data delivery service sends data from one End System to another End System on the same sub-network using reserved resources. The Guaranteed service assumes that the reserved resources that it wants to use have been set up by the Network Management service. The reserved resources are identified by a channel number. The Guaranteed service can only use pre-defined channels for communication. It cannot open new channels. The Guaranteed service ensures the data arrives intact and in the same order in which it was sent.

The Guaranteed service supports priority within a resource-reserved channel. When a packet is passed to the Guaranteed service for sending it is assigned a priority level and channel number by the user. High priority packets are sent and forwarded before lower priority ones.  All packets are sent using the sub-network resources specified by the channel number. The resources are allocated for each channel by the Network Management service [RD 10] and must be set up before the channel is used to send data.

The maximum amount of data that can be sent in one packet is limited to the Maximum Data Unit (MDU). This is the maximum amount of data that can be passed to the Assured service in one SDU.

The Guaranteed service has the following features:

- Maximum SDU size is determined by the Maximum Data Unit (MDU) management parameter

- Channel reserving sub-network resources must be set up before sending and receiving data

- SDU priority supported within each channel

- Delivery ensured through retry and redundancy mechanisms

- Statistics maintained about errors and undelivered data.

### Guaranteed Service Primitives

In this section the service primitives for the Guaranteed service are presented.

There are three primitives used by this service:

- Send Request which requests to send an SDU through a pre-arranged channel, from a source End System to a destination End System on the same sub-network,

- Receive Indication which indicates that a PDU has been received and which passes the corresponding SDU to the End System.

- Failure Indication, which indicates that the retry limit for the sending process has been reached.

#### Send Request

Function

The Send Data.request primitive requests the Guaranteed service to send a SDU using a specific channel to a destination protocol entity, which is a user of the Guaranteed service. The channel references a set of reserved resources forming a path from the source to the destination. Resources are allocated to a channel by the Network Management service [RD 10]. The SDU is assigned a priority level which determines the precendence? with which it will be sent and forwarded through the onboard sub-network. The priority applies only within the channel that is being used to send the data. Since resources are reserved the SDU does not have to compete with SDUs in other channels. It the communication fails then it is retried until either the communication is successful or until a specified number of retries has been attempted. The number of retried is a Network Management parameter [RD 10].

Semantics

INTRA_GUARANTEED_SEND.request (Source, Destination, Protocol ID, Channel, Priority, Data)

When Generated

The SEND.request primitive is passed to the Guaranteed service provider to request that the Data be sent to the specified destination using the specified channel and priority.

Effect on Receipt

Receipt of the SEND.request primitive shall cause the SOIS Intra-Network Guaranteed service provider to encapsulate the SDU and to issue a corresponding PDU over the underlying data-link/sub-network.

Additional Comments

Destination is the address of the node to where the data is directed.

Source is the address of the node that is sending the data.

Protocol ID identifies the protocol entity which is the user of the Guaranteed service.

Data is the data to be sent from the Source to the Destination protocol entity.

Priority indicates the level of precedence that should be given to the data compared to other SDUs being serviced or other PDUs in the same channel on the sub-network.

Channel is the identifier of the set of reserved resources that are to be used to send the data.

#### Receive Indication

Function

The Receive Indication is used to pass the contents of a received Guaranteed Service PDU to the user protocol entity.

Semantics

INTRA_GUARANTEED_RECEIVE.indication (Source, Destination, Protocol ID, Data)

When Generated

This primitive is issued by the service provider to the receiving application on receipt of a DATA PDU. The corresponding SDU is placed in a queue for access by the user protocol entity identified by the Protocol ID.

Effect on Receipt

The response of the End System to a RECEIVE.indication primitive is for the data received to be read by the protocol identified by the Protocol ID. It is then up to the End System what it does with this data.

Additional Comments

Destination is the address of the node where the data has been received.

Source is the address of the node that sent the data.

Protocol ID identifies the protocol entity which is the user of the Guaranteed service.

Data is the data received by the Guaranteed service entity and directed to the specified protocol entity (End System).

#### Failure Indication

Function

The Retry Failure Indication is used to indicate that it has been impossible to send and confirm delivery of a Data PDU after a maximum number of retries.

Semantics

INTRA_GUARANTEED_ FAILURE.Indication (Source, Destination, Failure Metadata)

When Generated

This primitive is issued by the Guaranteed service provider to the service user when the retry limit for a PDU has been exceeded. Note that the retry limit is a managed parameter; see RD 6 and RD 10.

Effect on Receipt

The effect of receipt of the INTRA-GUARANTEED_FAILURE.Indication primitive is undefined, i.e. it is up to the user of the Assured service what it does when it gets a failure indication.

Additional Comments

Destination is the address of the node where the data has been received.

Source is the address of the node that sent the data.

Failure Metadata contains information about the type of error that occurred resulting in the failure to send and confirm delivery of the Data PDU to the specified destination.

# Comments

What about the OBL/Data Link….isn’t that part of SOIS?  And the Management Service Interface?

This sounded like QOS across multiple links is provided.  How about this edit?

Will this be a point of argument?

I don’t understand why this is controlled by Space Link Identifiers??  I thought it was a systems engineering/management thing.  Same for destination.

In what book will how to do this be documented?

Earlier this was called data system.  We should be consistent.

We need to allow channels to be defined at initialization of a system.  Does this preclude that, i.e. static table definitions?  And why can’t we use the management service to add new channels dynamically?  Granted we might crash the system, but it also enables flexibility while on-orbit.

Do we want to specifiy failure metadata?  Otherwise, this isn’t inter-operable/re-useable.